This a Headline in two lines
Lorem Ipsum esta Dolores ned
Session 4 : GUI Extensions

---
Karabo GUI
- Control and designer modes.
- In designer mode: drag and drop device properties to the scene.
- Default widgets based on the data type are displayed.
- Contains 3 items: property name, display and edit widgets.
- Scenes are stored in project or provided by devices.

---
Karabo GUI
- Large set of built-in widgets.
- Widgets can be changed by right clicking on the widget and
  selecting Change Widget.
- Based on the data type, display types changes.
- Switching between widgets is always possible.

---
GUI Extensions
- Karabo GUI Extensions (further extensions) is a python package that compliments Karabo GUI by adding custom tailor made widgets.
- It is not part of Karabo framework and does not follow karabo release/deployment cycle and can be updated at any point.
- Gitlab link: https://git.xfel.eu/karaboDevices/guiextensions

---
Problem: Missing Widget

---
Solution: Update gui extensions
- As the extensions are frequently updated one might miss the latest widgets.
- Use Help →Check for Updates to update extensions.
- Close and open karabo gui to reload extensions.

---
Karabo GUI development environment
- Karabo GUI is installed via conda package manager and dependency tool.
- It is written in Python by using PyQt and pyqtgraph libraries.
- To prepare the development environment of gui extensions:
  1. Clone guiextensions repository
  2. Activate conda environment of the Karabo GUI.
  3. Install guiextensions python package.

---
Hands on #1 : prepare developer environment
- Open terminal
- source /opt/miniconda/bin/activate
- conda activate karabogui
- cd
- cd karabo/devices/guiextensions
- git checkout workshop
- pip install -e .
- karabo-gui (might take few sec.)

---
Hands on #2: Change widget to gui extension
- Open karabo from terminal and connect with admin rights.
- Open project SESSION_4.
- Instantiate the middlelayer device KARABO_TEST/MDL/PROPERTY_TEST.
- Create a scene SESSION_4_SCENE.
- Drag and drop a Float (Min / Max) property on the scene.
- Ungroup widgets and change the second widget to Workshop Example 1.
- Save project.

---
GUI Extensions: Building blocks
- Extension is defined as an entry point in the setup.py
- It has to have a data model
- And representation widget.

---
Hands on #3: explore gui extension
- Open visual code.
- Open folder karabo/devices/guiextensions
- Open file src/extensions/workshop/display_example_one.py

---
GUI Extensions: Building blocks
- Class is decorated with register_binding_controller.
  - ui_name appears in the gui.
  - klassname should be the same as in setup.py
  - binding_type defines data type that the controller will accept.
- Class has to be inherited from BaseBindingController.
- Has a model (for storing attributes in project) and internal objects.
- Mandotary methods that needs to be implemented:
  - create_widget returns PyQt widget object,
  - value_update callback when value proxy changes.

---
GUI Extensions: Building blocks
- Model can be used to store a gui related configuration in the Karabo project.
- Setup.py contains all entry points:
- pip install -e . to links the package. Necessary if the entry points in the setup.py change. No need to do pip install if the extension code changes.

---
Note about libraries: Qt, PyQt, qtpy and traits
- Qt is graphical library written is c++, PyQt is wrapper of Qt and qtpy handles various PyQt versions.
- QWidget is a base class of all user interface objects (QLabel, QlineEdit, QPushButton, etc.).
- Widgets are grouped in layout(s) (QHBoxLayout, QVBoxLayout, QgridLayout).
- Traits package is used to ensure data validation.
  Hint:
- PyQt provides designer tool.
- Allows to explore Qt library and create *ui files for complex widgets and layouts.

---
Designer
- Activate conda karabo environment and launch designer.

---
Hands on #4
- Currently display_example_one.py contains one label that displays a text with attribute value.
- Modify widget by adding a value input widget that displays the value.

---
Hands on #4 : steps and solution
- Add QLineEdit (widget for value input) to the imports (line 1).
- Add _value_ledit = WeakRef(QLineEdit) to internal objects (After line 18)
- Add line edit to the widget and layout (after line 25 and 28):
  - self._value_ledit = QlineEdit(parent=widget)
  - hlayout.addWidget(self._value_ledit)
- Set label and value_ledit text (after line 34):
  - self._value_ledit.setText(str(value))
  - Solution: git checkout workshop_done (close/open GUI)
  - git diff workshop workshop_done

---
Property proxies
- Property proxy links device attributes with widgets.
- It is not the device proxies used in the middlelayer context.
- All karabo data types are supported. Including nodes.
- Reimplement add_proxy to accept multiple proxies.
- add_proxy on success should return True.
- value_update will be called if any proxy has been changed.

---
Hands on # 5: Example with two proxies
- Drag and drop Float property to the scene.
- Change widget to Workshop Example 2.
- Drag and drop a String property on top of the widget.
- Text appears in the label. Hovering over the widget shows connected proxies.
- Open display_example_two.py in visual code.

---
Hands on #6
- Modify display_workshop_example_two.py.
- Implement basic interactive gui. If the float value is above 100:
  - Disable value self._value_edit (use setEnabled()).
  - Informe user that manual mode is disabled: Set tool tip of the self._value_edit.

---
Hands on #6 : steps and result
- Add code to the value_update:
  self._value_ledit.setEnabled(value < 100)
  tool_tip = "Manual mode is disabled" if value > 0 else ""
  self._value_ledit.setToolTip(tool_tip)
- Solution: git checkout workshop_done (close/open GUI)
- Difference: git diff workshop workshop_done

---
An advanced example
- Workshop example 3
- Nested layouts.
- Usage of model attributes (Traits package).
- Qt signals and slots.
- Setting attributes via proxy.
- Handling state_update.
- Calling karabo slots and handling response.
- KaraboPlotView class.

---
Hands on #7
- Drag and drop Float attribute on the scene.
- Change widget to Workshop Example 3.
- Drag and drop a second Float attribute on the scene.

---
Hands on #8
- Modify Workshop example 3
- Remove spinbox items
- biding_type should accept VectorDouble and VectorFloat attributes.
- on_value change verify that vectors have the same length.
- On each value update clean scatter graph and plot new points.

---
Hands on #8 : result

---
Further reading
- Karabo scenes: https://rtd.xfel.eu/docs/karabo/en/latest/library/gui_scene_development.html
- GUI Extensions: https://rtd.xfel.eu/docs/gui-extensions/en/latest/install_latest_version.html
- Qt: https://doc.qt.io/qt-5/qtwidgets-index.html , https://doc.qt.io/qt-5/qtwidgets-module.html
- PyQt graph: https://www.pyqtgraph.org/

---
Take Away
- Karabo GUI has a rich set of built-in widgets.
- Most of them are adjustable to fit user needs.
- Missing gui appearance and complex widgets might be achieved via gui extensions.
- Use existing set of Karabo GUI widgets, ask for support/feature or develop your gui extensions.