## Slide 1
pyAT and Matlab AT with GPU
Jean-Luc PONS E.S.R.F.
Accelerator Middle Layer Workshop
JUNE 19-21, DESY Hamburg

## Slide 2: STATUS
Standard passMethods and exact passMethods implementation done (available from github.com/atcollab/at branch gpu_tracking)
GPU tracking available from both python and matlab
Build and setup scripts available for Windows/Linux, python/matlab
MacOS development in progress
Evaluation of Metal (MSL) foreseen for MacOS (OpenCL deprecated on MacOS)
OpenCL and Cuda implemented
Parallel tracking starting from several references development in progress
Parallel tracking in multiple RING foreseen
Multiple GPU foreseen

## Slide 3: C++ IMPLEMENTATION OVERVIEW (PASS METHODS CODE GENERATION)
CavityPass
AbstractElement
RFCavityPass
IdentityPass
DriftPass
StrMPoleSymplectic4Pass
ExactDriftPass
BndMPoleSymplectic4Pass
ExactMultipolePass
ThinMPolePass
StrMPoleSymplectic4RadPass
BndMPoleSymplectic4RadPass
ExactMultipoleRadPass
AbstractElement: GPU memory transfer, access to ring data from python/matlab (method declarations)
IdentityPass: Translation, Rotation, Aperture check
StrMPoleSymplectic4Pass: Polynomial handling
PassMethodFactory: Singleton class that creates elements and generates GPU code
Lattice: Main class to run GPU kernel
Each class implemented only its specificities.

## Slide 4: C++ IMPLEMENTATION (INTERNAL)
REPR lattice loader
CudaGPU
AbstractGPU
OpenCLGPU
AbstractInterface
PyInterface
MatlabInterface
CppObject
C++ Tracking debugging purpose
AbstractGPU: GPU compilation, running, loading (method declarations)
CudaGPU: CUDA implementation
OpenCLGPU: OpenCL implementation
AbstractInterface: Access to ring data method declarations (used by pass methods)
PyInterface : Interface to python implementation
MatlabInterface : Interface to Matlab implementation

## Slide 5: CODE GENERATION
Ring parsing: 77.288ms (REPR Loader on EBS)
GPU Code generation: 0.158ms
GPU Code compilation: 17.279ms
GPU lattice loading: 1.98ms
int nb = elem->mpole.NumIntSteps;
switch(elem->SubType) {
case 1:{
for(int m = 0; m < nb; m++) {
p_norm=PNORM(r6[4]);fastdrift(r6,SL*(AT_FLOAT)0.6756035959798289,p_norm);
quadthinkickrad(r6,elem->mpole.PolynomA[0],elem->mpole.PolynomB[0],elem->mpole.K,SL*(AT_FLOAT)1.3512071919596578,elem->mpole.CRAD,p_norm);
p_norm=PNORM(r6[4]);fastdrift(r6,SL*(AT_FLOAT)-0.1756035959798289,p_norm);
quadthinkickrad(r6,elem->mpole.PolynomA[0],elem->mpole.PolynomB[0],elem->mpole.K,SL*(AT_FLOAT)-1.7024143839193155,elem->mpole.CRAD,p_norm);
p_norm=PNORM(r6[4]);fastdrift(r6,SL*(AT_FLOAT)-0.1756035959798289,p_norm);
quadthinkickrad(r6,elem->mpole.PolynomA[0],elem->mpole.PolynomB[0],elem->mpole.K,SL*(AT_FLOAT)1.3512071919596578,elem->mpole.CRAD,p_norm);
p_norm=PNORM(r6[4]);fastdrift(r6,SL*(AT_FLOAT)0.6756035959798289,p_norm);
}
GPU code for integrator loops are automatically generated for all possible configurations
Code generation overhead

## Slide 6: SYMPLECTIC INTEGRATOR
Symplectic integrator loops are automatically generated (6 integrator types supported)
1 Euler 1st
2 Optimal 2nd order from "The Accuracy of Symplectic Integrators", R. Mclachlan P Atela, 1991
3 Ruth 3rd
4 Forest/Ruth 4th
5 Optimal 4th order from "The Accuracy of Symplectic Integrators", R. Mclachlan P Atela, 1991
6 H. Yoshida 6th, "Construction of higher order symplectic integrators", 1990
  Symplecticity check (6D tracking, misalignment of 5 microns RMS, EBS lattice)
  J6 = jmat(3) # block matrix, from at.physics.amat import jmat M66 = ring.find_m66()[0] VS = (M66.T.dot(J6).dot(M66) - J6).flatten()**2 RMS66 = np.sqrt(np.sum(VS)) # should be 0 when 100% symplectic
Polynomial are optimized for basic type (KickAngle, Quad, DQ, Sextu, Octu)
RFCavity OFF, Radiation OFF, SL is the slice length
CPU(SL=0.010) RMS66=3.020310206081857e-09
GPU(SL=0.010,$Eul_{1st}) RMS66=1.7971693218050667e-09
GPU(SL=0.010,$McL_{2nd}) RMS66=3.5984645974252943e-09
GPU(SL=0.010,$Rut_{3rd}) RMS66=1.6426534063683773e-09
GPU(SL=0.010,$F/R_{4th}) RMS66=5.136143080445193e-09
GPU(SL=0.010,$McL_{4th}) RMS66=3.857426258406334e-09
GPU(SL=0.010,$Yos_{6th}) RMS66=5.755868260401188e-09
With Radiation ON, the impact of the damping is clearly visible
CPU(SL=0.010) RMS66=0.013576939942364072
GPU(SL=0.010,$Eul_{1st}) RMS66=0.012741108407377816
GPU(SL=0.010,$McL_{2nd}) RMS66=0.013472996199817283
GPU(SL=0.010,$Rut_{3rd}) RMS66=0.013577271012208037
GPU(SL=0.010,$F/R_{4th}) RMS66=0.013576940544098255
GPU(SL=0.010,$McL_{4th}) RMS66=0.013577264165442464
GPU(SL=0.010,$Yos_{6th}) RMS66=0.013576865317977516

## Slide 7: SYMPLECTIC INTEGRATOR / ACCURACY / PERFORMANCE
FMA (EBS 1024 turns) SL = slice length
Standard passMethod
CPU 14 cores (Xeon@4.1GHz) 199.4 sec
GPU (RTX A4500) 36.4 sec
GPU/Single CPU: 77.5
Exact passMethod CPU 14 cores (Xeon@4.1GHz) 265.1 sec
GPU (RTX A4500) 46.6 sec
GPU/Single CPU: 79.6
Kick/Drift
per slice
1 / 1
2 / 2
3 / 3
3 / 4
4 / 4
7 / 8
EBS DA GPU/CPU (10.000 turns) F/R4th

## Slide 8: SYMPLECTIC INTEGRATOR / ACCURACY / PERFORMANCE
CPU
GPU
FMA in tune space using F/R4th
the fitting of the killing resonance lines is good

## Slide 9: PRICE / PERFORMANCE
1 x RTX A4500 ≈ ~90 x CPU@4.1GHz (no loss particle, ~1MB lattice of ~3300 elements, GPU at 100%)
./clpeak --compute-sp --compute-dp
Platform: NVIDIA CUDA
Device: NVIDIA RTX A4500
Driver version : 535.146.02 (Linux x64)
Compute units : 56
Clock frequency : 1650 MHz
Single-precision compute (GFLOPS)
float : 23074.39
Double-precision compute (GFLOPS)
double : 426.19
RTX A4500 has 8.6 compute capabilities:
56*128 FP32 units,
56*2 FP64 units,
56*64 INT32 units
H100 has 9.0 computes capabilities:
114*128 FP32 units,
114*64 FP64 units,
114*64 INT32 units
In 2023 (ESRF price):
H100 PICe ~34.000 euros
14 cores/28 threads 3.3GHz (4.8 GHz) Desktop + 2xRTX A4500 ~4800 euros
In 2024 (ESRF price):
96 cores/192 threads 2.5GHz (5.1GHz) Desktop + RTX A4000 ~17.736 euros
https://docs.nvidia.com/cuda/cuda-c-programming-guide/index.html#compute-capabilities
Platform: NVIDIA CUDA Device: NVIDIA H100 PCIe Driver version : 535.129.03 (Linux x64) Compute units : 114 Clock frequency : 1755 MHz Single-precision compute (GFLOPS) float : 49331.30 Double-precision compute (GFLOPS) double : 25186.19

## Slide 10: PERFORMANCE MEASUREMENT AND LIMITATION
To load a GPU at 100%, it is recommended to track a number of particles which is multiple of 64 times the number of compute units. AT use BLOCK_SIZE 64.
In CUDA, A warp is an “elementary” subset of 32 threads within a thread block such that all the threads in a warp can execute a same instruction (SIMT) at the time in a single compute unit.
The RTX A4500 (8.6) has 4 warp schedulers. A compute unit can execute up to 128 threads in parallel.
56*128 (7168) threads can really be executed in parallel without serialization if required underlying units (FP32,FP64,INT32) are available.

## Slide 11: PERFORMANCE MEASUREMENT AND LIMITATION
+---------------------------------------------------------------------------------------+
| NVIDIA-SMI 535.146.02 Driver Version: 535.146.02 CUDA Version: 12.2 |
|-----------------------------------------+----------------------+----------------------+
| GPU Name Persistence-M | Bus-Id Disp.A | Volatile Uncorr. ECC |
| Fan Temp Perf Pwr:Usage/Cap | Memory-Usage | GPU-Util Compute M. |
| | | MIG M. |
|=========================================+======================+======================|
| 0 NVIDIA RTX A4500 On | 00000000:17:00.0 Off | Off |
| 30% 35C P2 73W / 200W | 198MiB / 20470MiB | 100% Default |
| | | N/A |
+-----------------------------------------+----------------------+----------------------+
| 1 NVIDIA RTX A4500 On | 00000000:65:00.0 Off | Off |
| 30% 32C P8 24W / 200W | 79MiB / 20470MiB | 0% Default |
| | | N/A |
+-----------------------------------------+----------------------+----------------------+
Do not rely on nvidia-smi for GPU usage !
+---------------------------------------------------------------------------------------+
| NVIDIA-SMI 535.146.02 Driver Version: 535.146.02 CUDA Version: 12.2 |
|-----------------------------------------+----------------------+----------------------+
| GPU Name Persistence-M | Bus-Id Disp.A | Volatile Uncorr. ECC |
| Fan Temp Perf Pwr:Usage/Cap | Memory-Usage | GPU-Util Compute M. |
| | | MIG M. |
|=========================================+======================+======================|
| 0 NVIDIA RTX A4500 On | 00000000:17:00.0 Off | Off |
| 30% 56C P2 111W / 200W | 948MiB / 20470MiB | 100% Default |
| | | N/A |
+-----------------------------------------+----------------------+----------------------+
| 1 NVIDIA RTX A4500 On | 00000000:65:00.0 Off | Off |
| 30% 34C P8 25W / 200W | 79MiB / 20470MiB | 0% Default |
| | | N/A |
+-----------------------------------------+----------------------+----------------------+
Single particle tracking
16384 particles tracking

## Slide 12: USAGE (PYTHON)
rout, *_ = ring.track(rin, nturns=nturns, use_gpu=True, gpu_pool=[0], integrator=4)
rout, *_ = ring.track(rin, nturns=nturns, use_mp=True, pool_size=16)
b2, s2, g2 = ring.get_acceptance(planes,npoints,amplitudes,
grid_mode=at.GridMode.CARTESIAN,
nturns=nturns,
use_gpu=True,
offset=np.array([1e-7,0,1e-7,0,0,0]))
Main tracking function
Acceptance
Help on function gpu_info in module at.tracking.track:
gpu_info()
:py:func:`gpu_info` returns list of GPU present on the system and their corresponding information. If GPU
support is not enabled or if no capable device are present on the system, an empty list is returned.
Returns:
gpu: [gpu name,hardware version (CUDA device),compute unit number,platform]. The number of compute
units is not the so-called number of "CUDA cores". The number of threads that can be executed simultaneously
depends on the hardware and on the type of used instructions. For best performance, it is recommended to
track a number of particles which is multiple of 64 (or 128) times the number of compute units.
>>> at.tracking.gpu_info()
[['NVIDIA RTX A4500', '8.6', 56, 'CUDA 12.2'], ['NVIDIA RTX A4500', '8.6', 56, 'CUDA 12.2']]
GPU Info

## Slide 13: USAGE (MATLAB)
Main tracking function
GPU Info
>> out = gpuinfo();
>> out{1}
ans =
struct with fields:
Name: 'NVIDIA RTX A4500'
Version: '8.6'
CoreNumber: 56
Platform: 'CUDA 12.2'
>> ring = atloadlattice("test/lattice/simple_ebs.mat");
>> rin = [0.001,0,0.001,0,0,0];
>> % rout = ringpass(ring,rin',100); % CPU Call
>> rout = ringpass(ring,rin',100,'gpuId',0);
>> rout(99*6:100*6-1)
ans =
1.0e-03 *
-0.5059 0.9495 -0.0113 0.7300 0.2937 0

## Slide 14: USAGE (PYTON EVALUTATION)
Parallel tracking starting from several refpts (development in progress)
Help on built-in function gpupass in module at.tracking.gpu:
gpupass(...)
gpupass(line: Sequence[Element], r_in, n_turns: int, refpts: Uint32_refs = [], reuse: Optional[bool] = False, omp_num_threads: Optional[int] = 0)
Track input particles r_in along line for nturns turns.
Record 6D phase space at elements corresponding to refpts for each turn.
Parameters:
…
tracking_starts: numpy array of indices of elements where tracking should start.
len(tracking_start) must divide the number of particle and it gives the stride size.
The i-th particle of rin starts at elem tracking_start[i/stride].
The behavior is similar to lattice.rotate(tracking_starts[i/stride]).
The stride size should be multiple of 64 for best performance.
…
startingElem = np.array([0,100,200,300,400,500,600,700],dtype=np.uint32)
rout, *_ = ring.track(rin, nturns=nturns, use_gpu=True, tracking_starts=startingElem)

## Slide 15: INSTALlATION
Python (https://github.com/atcollab/at/blob/gpu_tracking/docs/p/howto/multiprocessing.rst)
MATLAB (R2021b, Ubuntu 20)
>>cd /home/esrf/pons/at
>>addpath(genpath(['./atmat']))
>>addpath(genpath(['./atintegrators']))
>>atmexall -cuda /cvmfs/hpc.esrf.fr/software/packages/ubuntu20.04/x86_64/cuda/12.3.1

## Slide 16
THANKS
Jean-Luc PONS E.S.R.F.
Accelerator Middle Layer Workshop
JUNE 19-21, DESY Hamburg