## Slide 1: WP4: Linac transfer line
ESSnuSB Annual Meeting 2024
PRESENTED BY Natalia milas on behalf of WP4

## Slide 2: Why a new transfer line
  Make construction easier getting further away from the experimental hall
  Improve the old design
  Reduce costs

## Slide 3: Layout of a new transfer line

## Slide 4: Comparisons
Old Design:
  Based on a FDO lattice (two quadrupoles in between long dipoles);
  15 H dipoles, 12 V dipoles and 64 quads
  Average evelope size in both planes 2 mm (phase advance ~22.5 per cell)
  Full depth = 7.8 m
New Design:
  Based on a FODO lattice (one quadrupole in between long dipoles);
  15 H dipoles, 9 V dipoles and 41 quads
  Average evelope size in both planes 2 mm (phase advance ~22.5 per cell)
  Full depth = 7.6 m
Optics

## Slide 5: Envelope Simulations
New transfer line Lattice
Old transfer line Lattice

## Slide 6: Effects of H- stripping
  From studies before (presented in the CDR for ESSnuSB) stripping components are divided in:
    Black body stripping (temperature dependent)
    Magnetic stripping (connected to magnetic field strengths)
    Intra beam stripping (related to particle density in the beam)
  Blackbody still an issues for the current transfer as it has for the old one.
  Diploes and quadrupoles for the new design have the similar fields strength and so Magnetic stripping will also be very similar.
  For the new design the beam envelope are also similar and thus there is not increased densities for the bunches thus intra beam stripping is not expected to change considerably.
  In summary, we do not expect changes on the losses due to stripping for the new design if compared to the previous one!

## Slide 7: Transfer line vertical profile
New transfer line design
Old transfer line design

## Slide 8: Matching to the accumulator ring
Injection point
It is possible to use this last triple to match the incoming beam from the Linac to the ring

## Slide 9: Thank you! Questions?