## Slide 1: Magnetic and Mechanical Design of Large Aperture HTS Superconducting Dipole for the Muon Collider Accelerator Ring
A. Pampaloni1,5, L. Alfonso1, L. Balconi2,3, A. Bersani1, L. Bottura4, B. Caiffi1, S. Fabbri4, S. Farinon1, A. Gagno1, F. Levi1, T. Maiello1, F. Mariani2,5, S. Mariotto2,3, D. Novelli1,5, C. Santini2, S. Sorti2,3, M. Statera2
1 INFN – Genova, 2 INFN – Milano, 3 Università degli Studi di Milano, 4 CERN, 5 Sapienza Università di Roma
Main requirements of the dipole:
Large rectangular aperture (w x h): 100 x 30 mm;
Rectangular good field region (GFR) 50 x 20 mm;
Open midplane configuration;
10 T in the centre of the aperture;
Magnetic field harmonics 10 units in the GFR;
Magnetic field homogeneity 1 % in the GFR;
Operating temperature: 20 K;
Margin in temperature ;
HTS REBCO cable;
Racetracks coils.
I [A] | J | B0 [T] | Bp [T] | Top [K] | Margin [K] | Cost
2381.13 | 734.92 | 10.00 | 12.32 | 20 | >2.5 | 196.24
I [A] |  | B0 [T] | Bp [T] | Top [K] | Margin [K] | 
2381.13 | 734.92 | 10.00 | 12.32 | 20 | >2.5 | 196.24
1
2
3
Magnetic design
# racetrack | # cond. left | # cond. right | # tot. cond.
1 | 47 | 158 | 205
2 | 45 | 160 | 205
3 | 46 | 159 | 205
Cable assumptions
Mechanical assumptions:
Infinitely rigid mechanical structure;
Homogenous material for racetracks: ;
Maximum horizontal stress 400 MPa and maximum vertical stress 100 MPa;
Frictionless system;
Use of the sectors to reduce stress.
MAX
Magnetic results
Conductor [k€/m] | 159.41
Iron yoke [k€/m] | 13.65
Mechanical structure [k€/m] | 3.18
Assembly [k€/m] | 20.00
Total cost [k€/m] | 196.24
Conductor [k€/m] | 159.41
Iron yoke [k€/m] | 13.65
Mechanical structure [k€/m] | 3.18
Assembly [k€/m] | 20.00
Total cost [k€/m] | 196.24
Cost
Mechanical results
Using T-A formulation, it is possible to make a model that simulates the charging phase of the magnet.
Magnetization
The charging phase is characterized by a slope of 20 until the peak current of and the current stays constant for
Magnetization of the cable causes a different current distribution that generates a different magnetic field map
Assumption:
IMCC and MuCol annual meeting 2025
The Muon Collider complex