## Slide 1: Bunch rotation experiments and benchmarking at SNS
Austin Hoover, Vasiliy Morozov
IMCC and MuCol Annual Meeting
Hamburg, Germany
May 13, 2025

## Slide 2: Outline
SNS resembles IMCC proton driver concept
SNS has unique capabilities (bunch intensity, energy flexibility, phase space painting, diagnostics)
Feasibility of bunch compression using existing hardware
Preliminary simulations and experiments

## Slide 3: Overview of SNS accelerator and comparison to IMCC design

## Slide 4
https://arxiv.org/abs/2303.08533

## Slide 5
https://arxiv.org/abs/2303.08533

## Slide 6
https://arxiv.org/abs/2407.12450

## Slide 7
https://arxiv.org/abs/2407.12450
2-4 MW
5-10 GeV
10 Hz
2 ns

## Slide 8
2.5 MeV
RFQ
MEBT
Ion Source
Front end forms 1ms chopped H- beam (~42 mA)

## Slide 9
DTL
2.5 MeV
CCL
1050 MeV
86.8 MeV
SRF
SRF
186 MeV
387 MeV
RFQ
MEBT
Linac accelerates to 1.3 GeV
Ion Source
Front end forms 1ms chopped H- beam (~42 mA)

## Slide 10
Charge exchange + painting
Accumulator ring compresses 1 ms pulse to 700 ns
DTL
2.5 MeV
CCL
1050 MeV
86.8 MeV
SRF
SRF
186 MeV
387 MeV
RFQ
MEBT
Linac accelerates to 1.3 GeV
Ion Source
RF (h=1,2)
Front end forms 1ms chopped H- beam (~42 mA)
Notes: No acceleration in ring; rf maintains extraction gap

## Slide 11
Accumulator ring compresses 1 ms pulse to 700 ns
DTL
2.5 MeV
CCL
1050 MeV
86.8 MeV
SRF
SRF
186 MeV
387 MeV
RFQ
MEBT
Linac accelerates to 1.3 GeV
Ion Source
RF (h=1,2)
Front end forms 1ms chopped H- beam (~42 mA)
Charge exchange + painting
1.8 MW @ 60 Hz

## Slide 13
2.8 MW

## Slide 14: Collective effects can be amplified using phase space painting

## Slide 15: Collective effects can be amplified using phase space painting and beam energy reduction
Turn off cavities to lower energy (1.3  0.8 GeV)

## Slide 16: With strong compression, SNS could probe MC space charge regime
MC (~2 ns bunch)
10 GeV, 4 MW
5 GeV, 2 MW
SNS 2.8 MW
Notes: Right vertical line shows nominal bunch length relative to 250 meter SNS ring length. This assumes a uniform density bunch.
Left vertical line shows factor of 10 compression, which would be the absolute

## Slide 17: Diagnostics available to measure turn-by-turn particle distribution
Diagnostic | Measured Quantity | Operational? | Speed
Ring instability monitor (RIM) |  | Yes | Instant
Beam position monitors (BPM) |  | Yes | Instant
Beam current monitor (BCM) |  | Yes | Instant
Wire scanners (WS) |  | Yes | 5-15 mins
Electron scanner (ES) |  | No… | Instant
Diagnostic | Measured Quantity | Operational? | Speed
Ring instability monitor (RIM) |  | Yes | Instant
Beam position monitors (BPM) |  | Yes | Instant
Beam current monitor (BCM) |  | Yes | Instant
Wire scanners (WS) |  | Yes | 5-15 mins
Electron scanner (ES) |  | No… | Instant

## Slide 18: 1D measurements constrain 2D/4D phase space density of accumulated bunch
Phys. Rev. Accel. Beams 27, 122802 (2024)
Notes: https://doi.org/10.1103/PhysRevAccelBeams.27.122802
Can measure different turns

## Slide 19: Feasibility of bunch compression at SNS
Notes: Can we compress the bunch using available RF power?

## Slide 20: Goal 1: Accumulate with barrier waveform
Barrier
Barrier
Notes: Problem: no barrier cavities

## Slide 21: Goal 2: Compress with single-harmonic waveform
Barrier
H=1
Notes:   Problem: waveforms must change mid-cycle
  Problem: weak RF and limited storage time
  Problem: significant beam-cavity interaction
  …

## Slide 22: SNS uses dual-harmonic RF to maintain extraction gap and reduce peak density
Barrier
H=1,2
Notes:   Problem: waveforms must change mid-cycle
  Problem: weak RF and limited storage time
  Problem: significant beam-cavity interaction
  …

## Slide 23: 2/4 cavities used during production (6/13 kV)
H=1
H=2
H=1
H=2
Phase
RF1
RF2
RF3
RF4
Amp

## Slide 24: Feedback system modifies phases/amplitudes
Phase
RF1
RF2
RF3
RF4
Amp
Injection
Extraction

## Slide 25: Question 1: Can we approximate barrier waveforms during accumulation?
Barrier
Barrier

## Slide 26: Question 1: Can we approximate barrier waveforms during accumulation?
Idea 1: Turn off cavities

## Slide 27: Question 1: Can we approximate barrier waveforms during accumulation?
Idea 1: Turn off cavities
Idea 2: Force zero net voltage using RF feedback system

## Slide 28
Set = 1.5 kV
Set = 0.5 kV
Set = 0 kV
Notes: Beam was injected for 100 turns and then stored for 800 turns.
Initial ramp and flat-top is before beam starts injecting.
Initial spike is cased by beam; voltage/phase adjust to maintain voltage.
Want to test if this could work with higher beam intensity.
Could try using feedforward control loop to damp initial spike.

## Slide 29: Question 1: Can we approximate barrier waveforms during accumulation?
Idea 1: Turn off cavities
Idea 2: Force zero net voltage using RF feedback system
Idea 3: Approximate barrier waveforms using additional harmonics

## Slide 30: Four harmonics are enough for ~flat waveforms
Notes: There is probably an exact solution; I found these by messing around with the amplitudes.

## Slide 31: Old simulations show influence of barrier waveforms on longitudinal distribution
Holmes et al., HB 2006
Energy distribution
Waveforms
New
Old

## Slide 32: Unclear if higher harmonics are possible with existing hardware
Unsuccessful initial attempt to reach h=3 with custom waveform generator and tuning current.
Reaching h>2 may require new ferrite rings.

## Slide 33: Question 1: Can we approximate barrier waveforms during accumulation?
Idea 1: Turn off cavities
Idea 2: Force zero net voltage using RF feedback system
Idea 3: Approximate barrier waveforms using additional harmonics
Idea 4: Install new barrier cavities [$$$]

## Slide 34: Question 2: Can we compress the bunch?
Barrier
H=1

## Slide 35: Question 2: Can we compress the bunch?
Max voltage ~ 20 kV (with 2 cavities).
Synchrotron period ~ 2000 turns (at 1.3 GeV)
New custom waveform generator should allow switching waveforms mid-cycle.
Limited storage time — try to extend.
Optimal RF settings accounting for collective effects?
Notes: The RF during accumulation will determine final compression ration

## Slide 36: Initial experiment and simulation benchmarking

## Slide 37: Initial experiment injected 300 turns into 10-kV RF voltage (closed loop)
Notes: Injection time ~ 1/2 rotation time

## Slide 38: 1D simulation shows reasonable agreement with initial experiment
[MeV]
RMS length (10% thresh)
TBT profiles
Notes: Assumed ~uniform z profile; fit width of first few measured pulses.
Assumed Gaussian dE profile; adjusted by eye for closer agreement with measured rms bunch lengths.
Injected zlim ramps from 18/64 to 38/64 in first hundred turns.
Included 1D longitudinal space charge and impedance models.
Space chargeIntensity is 30% of full pulse.
Space
Initial energy spread/bunch length not optimized.
Rotation during injection leads to growth in initial energy spread.

## Slide 39: Future modeling/benchmarking considerations
Codes: (PyORBIT, ImpactX, Xsuite)
Space charge solver (3D/2.5D/2D/1D)
Wake fields, beam-cavity interaction, feedback system
Electron cloud
Cousineau et al., ECLOUD 2007
Notes: Will be more important at higher perveance
Usure if ecloud affected by short bunch length

## Slide 40: Example: tomographic measurement of space-charge-driven 4th order resonance
Measure?

## Slide 41: Example: are nonlinear space charge forces resolved properly?
Notes: Can run tomography algorithms to reconstruct z-dE, dependent on model assumptions.

## Slide 42: Conclusion
Bunch compression experiments ongoing at SNS.
Success may depend on RF engineering/hardware upgrades.
Future work: explore limits of current setup and develop simulation benchmarks.
Acknowledgements: Chip Piller, Amith Narayan, Nick Evans, Wim Blokland.

## Slide 44: With strong compression, SNS could probe MC space charge regime
MC (2-ns bunch)
10 GeV, 4 MW
5 GeV, 2 MW
SNS 1.8 MW

## Slide 45: With strong compression, SNS could probe MC space charge regime
MC (2-ns bunch)
10 GeV, 4 MW
5 GeV, 2 MW
SNS 2.8 MW

## Slide 46: 1D simulation shows reasonable agreement with initial experiment
[MeV]
Notes: Assumed ~uniform z profile; fit width of first few measured pulses.
Assumed Gaussian dE profile; adjusted by eye for closer agreement with measured rms bunch lengths.
Injected zlim ramps from 18/64 to 38/64 in first hundred turns.
Included 1D longitudinal space charge and impedance models.
Space chargeIntensity is 30% of full pulse.
Space
Initial energy spread/bunch length not optimized.
Rotation during injection leads to growth in initial energy spread.

## Slide 47: 1D simulation shows reasonable agreement with initial experiment
RMS length (10% thresh)
TBT profiles
Turn 1100
Turn 300
Notes: Injected 300 turns with synchrotron period ~ 2000 turns.
Stored beam for ~800 turns.

## Slide 48
2.4845 ns (1/402.5 MHz)
260 micro-pulses
645 ns
300 ns
945 ns (1/1.059 MHz)
1ms
16.7 ms (1/60 Hz)
15.7ms
Macro-pulse
(ion source)
Mini-pulse
(chopper)
Micro-pulse
(RFQ)

## Slide 49: SNS today: protons per pulse
1.7 MW @ 60 Hz
Experiments possible at full intensity (1 Hz)

## Slide 50: SNS soon: protons per pulse
2.8 MW @ 60 Hz (capable)
2.0 MW @ 60 Hz (target limit)
Experiments possible at full intensity (1 Hz)

## Slide 51: SNS in 10-15 years: Second Target Station
protons
2.0 MW @ 45 Hz
0.7 MW @ 15 Hz
Experiments possible at full intensity (1 Hz)

## Slide 52: Zero-space-charge simulation shows moderate compression for realistic energy spread
Notes: Zero space charge; instant RF ramp; 1.3 GeV beam energy.
[1] Minimum energy spread of 1 MeV from Holmes simulations.
[2] Zero RF voltage during accumulation (not even beam-induced voltage)
[3] Larger energy spread of 3 MeV
Conclusion: given synchrotron tune and good initial bunch, it could be possible to reach significant compression factor.

## Slide 53
Full charge
Zero charge
Notes: This simulation uses a uniform z distribution and Gaussian energy distribution. I assume the full 2.8 MW beam intensity (2.25e+14).

## Slide 54
Notes: Supplied by Chip Piller (ORNL), RF engineer
I am not an RF engineer and am just starting to learn about the system.

## Slide 55: Shorting cavities works, but can’t unshort after accumulation
Notes: Currently use mechanical relay to short cavities.
Would need some type of solid-state relay to switch mid-cycle.

## Slide 56: Beam-induced voltages limit beam intensity when operating cavities in open-loop
300-turn accumulation. Approaching 12 kV limit.

## Slide 57: Can we use multiple cavities same frequency but different phases?
Notes: Inject 100 turns with two cavities at 5 kV.
Left: same phase (approximate bunching phase)
Right: 180-degree phase shift.
Should repeat for higher intensity beam.