## Slide 1: Magnetic and mechanical design of large aperture HTS superconducting dipole for the Muon Collider accelerator ring
1 INFN – Genova, 2 INFN – Milano, 3 University of Milan, 4 CERN, 5 Sapienza Università di Roma
L. Alfonso1, L. Balconi2,3, A. Bersani1, L. Bottura4, B. Caiffi1, S. Fabbri4, S. Farinon1, A. Gagno1, F. Levi 1, T. Maiello1, F. Mariani2,5, S. Mariotto2,3, D. Novelli1,5, A. Pampaloni1,5, C. Santini2, S. Sorti2,3, M. Statera2

## Slide 2
Outline:
Requirements on the accelerator dipole
Cable assumption
Magnetic design and analysis
Magnetization analysis
Mechanical design and analysis
Heat loads
Warm-cold transitions
Future developments
L. Alfonso1, L. Balconi2,3, A. Bersani1, L. Bottura4, B. Caiffi1, S. Fabbri4, S. Farinon1, A. Gagno1, F. Levi 1, T. Maiello1, F. Mariani2,5, S. Mariotto2,3, D. Novelli1,5, A. Pampaloni1,5, C. Santini2, S. Sorti2,3, M. Statera2
1 INFN – Genova, 2 INFN – Milano, 3 University of Milan, 4 CERN, 5 Sapienza Università di Roma

## Slide 3: Requirements for the SC Dipoles
Main characteristics:
Open midplane dipole to avoid deposition of the radiation from muon decay.
10 T of central field.
Rectangular aperture of 100 mm x 30 mm.
Magnetic length of about 1.3 m.
Proposed solution:
Magnet design based on metal insulated
HTS racetracks.
Aperture
100 mm
30 mm

## Slide 4: Requirements for the SC Dipoles
Field quality requirements:
Rectangular aperture of 100 mm x 30 mm.
Field quality: units in beam radius of 10 mm.

## Slide 5: Requirements for the SC Dipoles
Field quality requirements:
Rectangular aperture of 100 mm x 30 mm.
Field homogeneity 1% in the good field region.

## Slide 6: Cable Assumptions
The conductor consists of two tapes and one SS strip.
The SC is based on a commercial YBCO tape from Fujikura.
Same assumption as for the collider studies
Cu
SC
Substrates
Ag
SS strip

## Slide 7: Magnetic Design
Three identical racetracks.
Alignment of racetracks for easier mechanical design.
Use of the sectors to reduce stress.
I [A] | Jeng | B0 [T] | Bp [T] | Top [K] | T margin [K]
2381.13 | 734.92 | 10.00 | 12.32 | 20 | ≥ 2.5
I [A] |  | B0 [T] | Bp [T] | Top [K] | T margin [K]
2381.13 | 734.92 | 10.00 | 12.32 | 20 | ≥ 2.5
# racetrack | # cond. left | # cond. right | # tot. cond.
1 | 47 | 158 | 205
2 | 45 | 160 | 205
3 | 46 | 159 | 205
Mag length [m] | Mec length [m] | Yoke radius [mm] | Cost
~1.3 | ~1.6 | 300 | 196.24
Mag length [m] | Mec length [m] | Yoke radius [mm] | 
~1.3 | ~1.6 | 300 | 196.24
1
2
3
Notes: Yoke outer radius

## Slide 8: Field Quality and Homogeneity
All harmonics greatly less then 10 units.
The harmonics higher than the 7th order less than 0.003 units.
The field homogeneity evaluated at x = 25 mm is about 0.06%.

## Slide 9: Magnetization Analysis
Using T-A formulation, it is possible to make a model that simulates the charging phase of the magnet.
Assumptions which are at the basis of the theory:
The charging phase is characterized by a slope of 20 until the peak current of and the current stays constant for .

## Slide 10: Magnetization Analysis
Magnetization of the cable causes a different current distribution that generates a different magnetic field map

## Slide 11: Mechanical Performance
1 Value taken from “Electro-mechanical properties of REBCO coated conductors from various industrial manufacturers at 77 K, self-field and 4.2 K, 19 T”
https://iopscience.iop.org/article/10.1088/0953-2048/28/4/045011
Only Lorentz forces effect evaluation:
This very simple model has the aim of evaluate the stress associated to the Lorentz forces, not for the dimensioning of the mechanical structure.
Infinitely rigid structure.
Homogenous material for racetracks:
Frictionless system.
Maximum horizontal stress 400 MPa and maximum vertical stress 100 MPa.
1
To reduce the stresses inside the conductors 5 mm thick infinitely rigid sectors were inserted which split the coils in two smaller coils.

## Slide 12: Mechanical Analysis
Racetrack | Fx |  | Fy | 
1 | 1019 | 799 | 23 | 95
2 | 993 | 698 | -93 | -378
3 | 927 | 632 | -418 | -1797
tot | 5068 |  | -2568 | 
Racetrack |  |  |  | 
1 | 1019 | 799 | 23 | 95
2 | 993 | 698 | -93 | -378
3 | 927 | 632 | -418 | -1797
tot | 5068 |  | -2568 | 
Racetrack | Peak |  | Peak |  | Peak | 
1 | -85.60 | -86.55 | -25.98 | -26.86 | 76.07 | 76.73
2 | -83.71 | -84.85 | -25.89 | -27.06 | 74.24 | 75.09
3 | -82.80 | -82.27 | -41.23 | -44.12 | 71.71 | 71.27
Racetrack |  |  |  |  |  | 
1 | -85.60 | -86.55 | -25.98 | -26.86 | 76.07 | 76.73
2 | -83.71 | -84.85 | -25.89 | -27.06 | 74.24 | 75.09
3 | -82.80 | -82.27 | -41.23 | -44.12 | 71.71 | 71.27
MAX

## Slide 13: Heat Loads (CERN siting)
1. (where is the muon mean lifetime (2.2 s), and is changing)
2.
3.
For reference, collider average power from 500 W/m
 | Acceleration time [ms] | % lost | Peak Power over accel. time [W/m] | Avg. Power at 5 Hz [W/m]
RCS1 | 0.45 | 11.9 | 1976 | 4.45
RCS2 | 2.6 | 16.1 | 517 | 6.7
RCS3 | 4.42 | 13.1 | 647 | 14

## Slide 14: Warm-Cold transitions
https://accelconf.web.cern.ch/e04/PAPERS/WEPKF015.PDF
Cold mass (1.9 K)
Room temperature (300 K)

## Slide 15: Warm-Cold transitions
Part ID | Location | Length (mm)
LHCLVTB_008 | C/W Transition CB50 Assembly type I | 1078
Part ID | Location | Length (mm)
LHCLVTB_001 | C/W Transition CB50 Assembly type C | 541
Part ID | Location | Length (mm)
LHCLVTL_001 | C/W Transition CB53 Assembly type A | 394.5
NOTE: distance is given from the end of the cold mass dome to the end of the warm flange

## Slide 16: Warm-Cold transitions
W/C transition in the LHC are 400 mm long. To this length, we need to add:
  Distance from the end of the cold magnet (end of the magnetic length) to the end of the cold mass dome: approximately 400 mm
  Distance from the warm flange to the beginning of the warm magnet (beginning of the magnetic length): approximately 200…300 mm ?
The field-free region at each W/C transition will be of the order of 1 m
Some optimization required and possible:
  Interconnects (current, fluids) will likely exit laterally
  Operation at 20 K will ease design and shorten W/C thermo-mechanical transition

## Slide 17: Conclusions and Future Developments
Conclusions:
A solid 2D magnetic design is ready and it fulfils all the requirements:
  Good field quality and homogeneity over large aperture
  Large margin at high temperature (20 K, with Tmargin 2.5 K)
A strategy to mitigate the effect of the Lorentz Forces has been studied, through stress management concept using sectors.
The value of hysteretic losses is around 50
Peak heat loads can be on the order of 2000 W/m in RCS1
Field-free region at each W/C transition will be of the order of 1 m
Next steps to be studied:
A detailed and optimized 2D and 3D mechanical design.
A 3D electromagnetic design.
An evaluation of the effect of persistent currents on the field quality.
Thermal analysis concerning both a more refined magnetization model and the effects of quench.

## Slide 18: Thanks for your attention
1 INFN – Genova, 2 INFN – Milano, 3 University of Milan, 4 CERN, 5 Sapienza Università di Roma
L. Alfonso1, L. Balconi2,3, A. Bersani1, L. Bottura4, B. Caiffi1, S. Fabbri4, S. Farinon1, A. Gagno1, F. Levi 1, T. Maiello1, F. Mariani2,5, S. Mariotto2,3, D. Novelli1,5, A. Pampaloni1,5, C. Santini2, S. Sorti2,3, M. Statera2

## Slide 19: Margin in Temperature
The temperature margin requirement of ≥ 2.5 K is met

## Slide 20: Costs
) + 20
Cond. | 8000 | 2500
Iron | 7800 | 8
SS | 7800 | 10
Cond. | 8000 | 2500
Iron | 7800 | 8
SS | 7800 | 10
Assembly
Cost | 
Conductor [k€/m] | 159.41
Iron yoke [k€/m] | 13.65
Mechanical structure [k€/m] | 3.18
Assembly [k€/m] | 20.00
Total cost [k€/m] | 196.24

## Slide 21: T-A Formulation
Using T-A formulation, it is possible to make a model that simulates the charging phase of the magnet.
Equation which are at the basis of the theory:
Assumptions which are at the basis of the theory

## Slide 22: Magnetization Analysis
Due to magnetization the requirement of field quality, in the good field region, of 10 units is not met
Notes: After the ramp..