## Slide 1
Magnet Design for the first demo cell of the 6D cooling (B5-like)
G. Scarantino, L. Bottura, M. Castoldi, S. Fabbri, L. Rossi, M. Statera 14/05/2025

## Slide 2
Outline
B5-like Demonstrator Cell Layout
Solenoid Optimization Methods
Coil Layout – Winding & Assembly
Configurations Studied
  “B5 DEMO MAG 2.3”
  “B5 DEMO MAG 2.4”
First Cell and Stand-Alone Mode
Coil Charging Transient: EM-TH Analysis
Conclusions and Next Steps
Conclusions and Next Steps

## Slide 3
Muon Cooling Demonstrator: Overview
Radio Frequency in Magnetic Field Test Facility (“RFMFTF”)
B5-like DEMO Cell
Credits: C. Rogers

## Slide 4
B5 DEMO Cell Magnets: Operational Modes
Test of each cell at full field.
A magnet design fulfilling both operative conditions looks challenging!
Nominal conditions:
periodic cell array, magnets with alternated polarity.
Different operating conditions in the magnets of the first cell in the array: unbalanced forces, no field screening on the begin-of-array side.
Test of each inter-cell module in stand-alone mode: Axial Forces increase / Invert their direction
Can it be avoided?

## Slide 5
B5 DEMO Cell Layout: “Inter-Cell Cryostat”
Cooling Cell
Target field on axis for a 1 m cell
Axial forces on coils
(lattice operation)
Target field harmonics
z
Target Field - Longitudinal Harmonics Expansion
Input for the magnet design

## Slide 6
B5 DEMO Cell – Coil Space Constraints
Space available for magnets
255 mm
337 mm
3 cavities
Outer of RF
Power in
Outer of RF + 5 mm gap for cryostat
130 mm
163 mm
45 mm
45 mm
Space for magnet structure, thermal shield, vessel.
200 mm
163 mm
Vertical space for magnet structure. For Coil2: consider space for dipole.
45 mm
45 mm
30 mm
*>30 mm
mm
Alternate configuration
Coil 1
Coil 2
Considering also the 5 mm gap from 130 mm absorber radius to the inner radius of the cryostat (135 mm).
mm
Coil 1
Coil 2
135 mm
50 mm
30 mm
Absorber

## Slide 7
B5 DEMO Cell: Magnets Design Approaches
Scan the coil parameters: 10 d.o.f.
Results compared to the target field harmonics required by the cooling lattice.
Select the optimal configuration based on relevant design parameters:
  Minimum Axial Force
  Stored Magnetic Energy <
  Minimum Conductor Volume
Grid-based Approach
Pattern Search Optimization Method
Computationally Expensive: only coarse grids scanned
Cost Function Definition
Derivative-free optimization method.
Conflict between different optimization targets  Objective weighting.
Two criteria on the minimum stored energy considered:
  limit
  Max Temperature Limit: 200 K
Converge to the optimal solution in much fewer steps!
Coil Configuration Search Assuming 6D Cooling Lattice Operation!

## Slide 8
Coil Layout: Winding & Assembly
Winding scheme: 2x HTS tapes + SS tape co-wound (ESMA-derived)  Dry-wound HTS coils (20 K operation).
Dimensions: HTS(12mm X 0.0656mm), SS(12mm X 0.026mm).
Faraday Factory Japan tape (SuperOx YBCO 2G HTS*).
Inter-turns contact resistance: .
Inter-pancake spacers dimensions:
  Best compromise in terms of field (B1, B2, focusing strength), margins (Ic) and mechanics.
SS spacer dimensions:
Coil 1: > 2 mm
Coil 2: > 2 mm
HTS
HTS
SS tape:
Conductor Section
Coil 1
Coil 2
HTS coil
SS Spacer
*Tape data from: [University of Victoria Wellington, Robinson HTS critical current database, SuperOx YBCO 2G HTS data. https://htsdb.wimbush.eu]

## Slide 9
Configurations Studied
Coil 1
Coil 2
Coil 1
Coil 2
“B5 DEMO MAG 2.3”
“B5 DEMO MAG 2.4”
Configuration considered in current integration studies (Grid-Based Coil Scan)
Better Optimized Version (Pattern Search Optimization)

## Slide 10
B5 DEMO MAG 2.3 Configuration - Results
Mag. Energy Density in Lattice (Coil1 / Coil2)
149 MJ/m3 / 92.9 MJ/m3
Total Mag. Energy - full cell
12.2 MJ
Coil Hoop Stress
Coil Radial Stress
Radial pressure applied on the external coil boundary:
10 MPa on Coil1
60MPa on Coil2
EM analysis
Mechanical Analysis
Exceedingly high margins:
not optimized!
Minimum ext. pressure:
Radial stress < 1MPa,
Hoop stress > 0 in operation
Resulting Stresses:
176 MPa peak hoop
0.98 MPa peak positive radial stress
Magnetc energy density values within target limit.
Resulting axial forces: 4.12 MN, 8.25 MN

## Slide 11
B5 DEMO MAG 2.4 Configuration - Results
EM analysis
Mechanical Analysis
Acceptable margin values!
 Better conductor usage
Note: not possible to reduce meet the requirement on the radial stress:
98 MPa peak hoop
2.4 MPa peak positive radial stress
Magnetc energy density values within target limit.
Resulting axial forces: - 4.61 MN, 11.7 MN
Mag. Energy Density (Coil 1 / Coil 2)
152 MJ/m3 / 147 MJ/m3
Total Mag. Energy - full cell
11.8 MJ
Coil Hoop Stress
Coil Radial Stress
Radial pressure applied on the external coil boundary:
- 24 MPa on Coil1
- 90 MPa on Coil2
Minimum ext. pressure:
Radial stress < 1MPa,
Hoop stress > 0 in operation

## Slide 12
Coil Support Structure: Mechanical Analysis
Von Mises Stress
Stress concentration on the inner Coil 2 corner: 410 MPa peak.
Von Mises Stress
Stress concentration on the inner Coil 2 corner: 648 MPa peak.
AISI 316LN steel structure
0.59 MN*m bending moment
0.32 MN*m bending moment
Intercept the load between the pancakes or apply axial precompression.
Total Deformation
Total Deformation
Symmetry Plane
B5 DEMO MAG 2.3
B5 DEMO MAG 2.4

## Slide 13
Summary Table
B5 DEMO MAG 2.4 option: improved performances compared to the currently integrated 2.3 design.
Significant reduction in total superconductor length.
Force direction between Coil1/Coil2 inverted in the 2.4 design: higher peak stresses on the shell structure.

## Slide 14
Begin of Cell
6D lattice
First Stage Evaluation
At full current:
Peak Field >> Target
Design of the first stage in the cell array still to be considered.
Running magnets at full current results in 10 T peak field on axis.  25% current reduction to match the peak field on axis.
Note: unbalanced forces in the first two inter-cell units!
Adiabatic matching?
Separate design of the first stage structure (first two inter-cells) needed

## Slide 15
First Stage Evaluation
Design of the first stage in the cell array still to be considered.
Running magnets at full current results in 10 T peak field on axis.  25% current reduction to match the peak field on axis.
Note: unbalanced forces in the first two inter-cell units!
Adiabatic matching?
~ Target Peak Field
< 1 MN Unbalance
Need to be supported
Separate design of the first stage structure (first two inter-cells) needed
Coil structure support feet need to be designed to withstand force unbalance of the order of 1 MN.
Margins are not critical: 25% current reduction; change in field-tape angle not critical.

## Slide 16
Inter-Cell Magnets - Stand-Alone Operation
Axial Forces:
Coil 1: 1.12 MN
Coil 2: 12.5 MN
(Pointing in outward inter-cell direction)
Coil Hoop Stress
Could we test the inter-cell modules in stand-alone mode?
20% increase in the coil peak hoop stress
1% decrease in minimum current margins

## Slide 17
Inter-Cell Magnets - Stand-Alone Operation
Increase of the peak Von Mises Stress on the structure.
Peak stress still within the material limits.
Loads intercept between each pancake?
Peak Von Mises Stress: 687 MPa

## Slide 18
B5 DEMO MAG 2.4: Coil Charging Transient
Transient Simulation of the charging of two separated non-insulated coils: magnetization loss effects accounted.
Tuning of the ramp rates in the two coils to match the same ramping time.
Characteristics time in the two magnets are very different (factor 8 difference): around 1h delay time in Coil 1.
Assumed 6h charging time: 4h current ramp in Coil 1.
Conduction cooling of the two magnets via cryocoolers*.
* Cryocooler data from:
SHI SRDK 500B2 technical specification sheet, https://shicryogenics.com/product/rdk-500b2-20k-cryocooler-series/.
Critical current fraction during charging
Assumption: periodic field conditions
 all similar magnets are ramped at the same time

## Slide 19
B5 DEMO MAG 2.4: Coil Charging Transient
Transient Simulation of the charging of two separated non-insulated coils: magnetization loss effects accounted.
Tuning of the ramp rates in the two coils to match the same ramping time.
Characteristics time in the two magnets are very different (factor 8 difference): around 1h delay time in Coil 1.
Assumed 6h charging time: 4h current ramp in Coil 1.
Conduction cooling of the two magnets via cryocoolers*.
* Cryocooler data from:
SHI SRDK 500B2 technical specification sheet, https://shicryogenics.com/product/rdk-500b2-20k-cryocooler-series/.
6.5 W Peak Losses in Coil1
Coil 1
Coil 2
32 K temperature peak in Coil1:
2 K temperature margin!
Consider longer ramp times (e.g., 6h ramp time).
Maximum local Jc fraction: 80%

## Slide 20
Conclusions and Next Steps
Engineering design of the B5-like cooling cell demonstrator magnets is proceeding. Converging to a design satisfying all the possible operational modes is challenging. Tight space constraints are limiting.
Inter-cell cryostat layout offers significant improvements in the assembly and magnet integration: strong repulsing forces sustained by a solid AISI 316LN structure.
B5 DEMO MAG 2.4 option offers a reduction in the total amount of conductor needed, with comparable stored magnetic energy within the target 150 MJ/m^3 limit.
However, axial force distribution in this configuration result in higher peak stress values on the coil structure:  design the coil supports to intercept the axial load between pancakes or apply axial precompression.
Design of the first-cell-in-array still to be considered. Is the field produced with a 25% current reduction good enough for the optics?
EM and thermal analyses of the coil charging transient showed a charging time > 6h if cryogen-free cooling option is considered.
Evaluate performances with gas-cooling with He @ 20 K.
Quench simulations are of prior importance:
  interesting dynamics during fast discharge (See T. Mulder presentation tomorrow).
  Be aware of the induced currents (hence stresses) on the RF cavities!

## Slide 21
Thank you for your attention!
giuseppe.scarantino@mi.infn.it

## Slide 22
BACKUP

## Slide 23
B5 DEMO MAG 2.3: EM Analysis Results
angular dependence considered
z
R
 | Coil 1 | Coil 2
Total Radial Resistance [mΩ] | 30.6 | 12.0
Coil Inductance (lattice op.) [H] | 29.2 | 3.39
Characteristic Time [s] | 954 | 282.6
Power dissipated @ charging [W] (ramp rate: 0.1 A/s) | 278 | 9.58
Margins exceedingly high: non-optimal conductor usage with the selected winding layout (2x 12mm HTS tape + SS tape) considering the coil protection limit (maximum stored magnetic energy density < 150 MJ/m^3).
Mag. Energy Density in Lattice (Coil1 / Coil2)
149 MJ/m3 / 92.9 MJ/m3
Total Mag. Energy - full cell
12.2 MJ

## Slide 24
B5 DEMO MAG 2.3: Mechanical Analysis Results
Coil Hoop Stress
Coil Radial Stress
Von Mises Stress SS spacers
Free radial expansion
Radial precompression
Minimum ext. pressure:
Radial stress < 1MPa,
Hoop stress > 0 in operation
Radial pressure applied on the external coil boundary:
10 MPa on Coil1
60MPa on Coil2
Coil Hoop Stress
Coil Radial Stress
Von Mises Stress SS spacers

## Slide 25
B5 DEMO MAG 2.4: EM Analysis Results
angular dependence considered
 | Coil 1 | Coil 2
Total Radial Resistance [mΩ] | 22.05 | 8.308
Coil Inductance (lattice op.) [H] | 15.84 | 0.7721
Characteristic Time [s] | 718.5 | 92.94
Mag. Energy Density (Coil 1 / Coil 2)
152 MJ/m3 / 147 MJ/m3
Total Mag. Energy - full cell
11.8 MJ
z

## Slide 26
B5 DEMO MAG 2.4: Mechanical Analysis Results
Coil Hoop Stress
Coil Radial Stress
Von Mises Stress SS spacers
Free radial expansion
Radial precompression
Minimum ext. pressure:
Radial stress < 1MPa,
Hoop stress > 0 in operation
Radial pressure applied on the external coil boundary:
- 38 MPa on Coil1
- 130 MPa on Coil2
Coil Hoop Stress
Coil Radial Stress
Von Mises Stress SS spacers

## Slide 27
B5 DEMO MAG 2.4: Mechanical Analysis Results
Coil Hoop Stress
Coil Radial Stress
Von Mises Stress SS spacers
Free radial expansion
Radial precompression
Minimum ext. pressure:
Radial stress < 1MPa,
Hoop stress > 0 in operation
Radial pressure applied on the external coil boundary:
- 38 MPa on Coil1
- 130 MPa on Coil2
Coil Hoop Stress
Coil Radial Stress
Von Mises Stress SS spacers
Minimum hoop stress values

## Slide 28
B5 DEMO MAG 2.3: Coil Support Structure
Von Mises Stress
Total Deformation
Mechanical analysis of the coil support structure in lattice operation.
8,25 MN
4,12 MN
Mechanical analysis of 1/8 shell support structure: lattice magnet operation.
Shell material: AISI 316LN steel.
Lorentz force density input from EM analysis.
0.59 MN*m bending moment on structure.
Stress concentration on the inner Coil 2 corner: 410 MPa peak.

## Slide 29
11,7 MN
4,61 MN
B5 DEMO MAG 2.4: Coil Support Structure
Von Mises Stress
Total Deformation
Peak stresses on the coil structure still within the material limits. Consider the possibility to intercept the loads between each pancake to reduce the stresses on the structure.
Mechanical analysis of 1/8 shell support structure: lattice magnet operation.
Shell material: AISI 316LN steel.
Lorentz force density input from EM analysis.
0.32 MN*m bending moment on structure.
Stress concentration on the inner Coil 2 corner: 648 MPa peak.

## Slide 30
B5 DEMO MAG 2.4: Local Stress Components
Evaluate the local stress components on the most loaded coils.
Coil#1.11
Coil#2.1
Free radial expansion
Pre-compression
Coil#1.11
Coil#2.1

## Slide 31: Lorentz force distribution on the coil pancakes
R
z
Coil 1.1
Coil 1.11
Coil 2.1
Coil 2.3
-6.28 MN
5.55 MN
7.16 MN

## Slide 32
Coil Assembly: Powering and Cooling Considerations
Each Inter-Cell module will be a self-standing unit  need to integrate electrical connections and cooling system in a tight configuration.
Conduction cooling proposal: SHI RDK 500B2 cryocoolers* considered for their optimal capacity (50W @ 20K) and cost.
Cu Electrical Connections
NI HTS Coil
Cu Cooling Plate
SS support + Insulating Layer
Coil 1
Coil 2
Coil 2
Coil 1
* Cryocooler data from:
SHI SRDK 500B2 technical specification sheet, https://shicryogenics.com/product/rdk-500b2-20k-cryocooler-series/.
Cu cooling plates terminations
Cold head interface