## Slide 1
Bernd Stechauner1,2, Bernardo Bordini2, Jose Ferreira Somoza2, Tim Mulder2,
Chris Rogers3, Jochen Schieck1,4, Daniel Schulte2 & Rebecca Taylor2
1Technische Universität, Vienna
2CERN, Geneva
3STFC Rutherford Appleton Laboratory, Didcot
4Institute of High Energy Physics (HEHPY), Vienna
Final cooling beam physics
IMCC & MuCol Annual Meeting, DESY, Hamburg, 15.05.2025

## Slide 2: Overview
Beam dynamics of a single final cooling cell.
Inclusion of significant technical components.
Thesis results and outlooks.

## Slide 3: Transverse ionization cooling
Final cooling section Small but powerful, ~100 m
One part of a final cooling cell
Goal of the final cooling section:
Minimize the norm. trans. emittance , as much as possible.
Minimize the growth of the norm. long. emittance , as much as possible.
Transverse ionization cooling:
Absorber and cavities reduce the beam divergence.
The solenoid suppresses the increase of caused by multiple Coulomb scattering.

## Slide 4: High field solenoid in the final cooling
Technical design with pancake modules [1]. See Bernardo’s talk!
Three corrector pancakes are added at both the entrance and exit of the solenoid.
Effective cooling requires strong solenoid fields to counteract the emittance heating caused by scattering.
The solenoid's field must be homogeneous at the absorber location.
G4BL simulated field

## Slide 5: Muon transport into a high-field solenoid + absorber system
Matching condition of a solenoid.
High field solenoid
Low field solenoid
Low field solenoid
Absorber
µ
Requirements:
Low-field (~4T) solenoid transport lines.
Matching coils are introduced between low-field and high-field solenoids.
Matching coil
Free parameters of a solenoid
Outer radius
Current density
Position
Inner radius
Matching coil

## Slide 6: Why correct beam matching is significant
This example demonstrates a matched solenoid beamline system.
The absorber reduces the norm. trans. emittance successfully!
A mismatch is demonstrated in the right low-field region.
increases due to beam filamentation.
Low field
Low field
High field
Matchers
Matchers
matched
matched
mismatched
blow up
Accurate solenoid matching is essential for the final cooling optics design. Without proper matching, the emittance reduced in the absorber will increase again.
Absorber
Beam dynamics evaluated with G4Beamline [3]

## Slide 7: Beam matching
Optimization by varying the outer coil radius of the matching coils.
Technical advantages:
Constant currents in matching coils.
No spacing between matching coils.
While adjusting the physical size of a solenoid in a computer simulation is straightforward, making such changes in the actual machine will be significantly more challenging.
µ-Bunch
ref. particle 2 = 115.8 MeV/c
ref. particle 1 = 109.2 MeV/c

## Slide 8: Coupled and single beam dynamics in final cooling
Single particle dynamics in solenoids:
With absorbers: Larmor radii decrease.
The helices shrink to lines for infinite beam line and without scattering.
Larmor center moves to the beam axis.

## Slide 9: Coupled and multiple particle dynamics Field flipped solenoids
Normalized canonical angular momentum [4]
Can. angl. mom. decrease focusing in the solenoids.
Less focusing -> less ionization cooling:
Better cooling with field flips

## Slide 10: RF systems in the final cooling
The energy spread can be controlled using phase-rotating cavities.
This minimizes the growth of the norm. long. emittance .
RF cavities can be positioned between the matching coils.
Previous design:
Cavities inside solenoids [5].
RF
RF
RF
µ-beam
Matchers
High field
Low field
Low field

## Slide 11: Absorber studies with windows
µ-beam
LiH window, 5mm thick
Minimize Coulomb scattering by utilizing thin windows.
Choose window materials with a low atomic number (Z).
LiH and Si₃N₄ are promising material options.
High pressure has a significant impact on the design of the final cooling channel.
To reduce pressure within the absorbers after a muon beam passes, the initial hydrogen pressure and density must be adjusted.
As a result, some absorbers may transition from a liquid to a vapor state.
See Jose’s & Valentina’s talk!
solenoid
µ-beam
Liquid
hydrogen

## Slide 12: Final cooling cell summary
A single final cooling cell consists of two window-hydrogen-window configurations within a high-field solenoid.
These configurations are separated by field-reversed solenoids.
Alternating RF cavities and matching coils are positioned between to the high-field solenoids.
Beam windows and density adjusted hydrogen absorbers are significant components.
An overview of the acceleration between two final cooling cells will be discussed during the poster session.

## Slide 13: Multiple final cooling cells
9 final cooling cells
Transverse emittance of 27 µm was reached.
After each cell, a new beam was generated in this design.

## Slide 14: Outlook
A very high performance of transmission was achieved.
Liquid H used from Cell 1-4.
Vapor H used from Cell 5-9
Final has to be reduced in future studies.
This depends on the optimum choice of the cooling rate for each cell.
More details in Taylor’s talk.

## Slide 15: Reference list
[1] B. Bordini et al., “Conceptual design of a ReBCO non/metal-insulated ultra-high gield solenoid for the Muon Collider“, 2024.
[2] J. Nelder and R. Mead, „A simplex method for function minimization“, 1965.
[3] T. Roberts, „G4Beamline users guide“, 2022.
[4] G. Penn et al., „Beam envelope equation for cooling of muons in solenboid fields“, 2000.
[5] H. Sayed et al., „High field - low energy ionization cooling “, 2015.

## Slide 16
Thank you for your attention