## Slide 1
RF breakdown studies
Juliette Plouin
Guillaume Ferrand, Claude Marchand, Sophie Pierron
CEA-Saclay

## Slide 2
3-D cavity design
Field emission in an elliptical cavity
Further studies on breakdown phenomena

## Slide 3
adapted to the MuCol stage B5 requirement in a p-mode
Task 6.2
In parallel, a 3-cells cavity has been designed by CEA, based on electric coupling, in order to allow comparison with magnetic coupling structure. A main advantage is to avoid the presence of metallic sheet (beryllium or any other metal) between the cells.
3 cells cavity based on electric coupling
R. Zhu et al., Phys. Rev. Accel. Beams 28, 041003

## Slide 4: Cavity geometry
Inner cell | Req | 0.1874
 | Riris | 0.06
 | a1 | 0.06716
 | b1 | 0.065171
 | a2 | 0.019031
 | b2 | 0.017366
Outer cells | Req | 0.1885
 | Riris | 0.06
 | a1 | 0.067582
 | b1 | 0.066989
 | a2 | 0.016716
 | b2 | 0.020453
tube | radius | 0.06
Coupler port | holeA | 0.05
 | holeB | 0.1
 | WH | 0.2
 | WA | 0.123825
 | WB | 2 x WA
Vérifier a/b
Coupler port
a1
b1
a2
b2
Riris
Req
WA
WB
holeA
holeB
*The tube length is not defined: it has been chosen to be long enough so that the boundary conditions at ends doesn’t modify the RF parameters
WH
Standard WG975

## Slide 5: Cavity RF parameters
Freq | MHz | 704.2
TTF |  | 0.674
R/Q | Ω | 287
Epeak/Eacc |  | 1.95
Epeak/Eacc | mT/(MV/m) | 7.48
Q0 (copper) |  | 36500
Lacc | m | 0.565
E0 | MV/m | 26.3
Eacc | MV/m | 17.7
V0 | MV | 14.9
Vcav | MV | 10
Pdiss | MW | 9.6
Epeak | MV/m | 34.5
Peak field is crucial for breakdown issue
Cavity shape is also important: in a cavity with non-parallel walls, the surface density of emitted electrons arriving on a cavity wall could be decreased due to the walls angle. Elliptical cavities could then be a good choice for lowering the breakdown issues.
Ez (a. u.)

## Slide 6: Kilpatrick…
0,94
0,49
1,58
1,91
Kilpatrick ratio
Kilp @ 704 MHz | MV/m | 24.7
 | MV/m | 26.3
 | MV/m | 34.5
Kilp ratio |  | 1.40
Kilp @ 704 MHz | MV/m | 24.7
 | MV/m | 26.3
 | MV/m | 34.5
Kilp ratio |  | 1.40
704 MHz
34.5 MV/m
24.7 MV/m
Kilpatrick ratio
D. Bowring et al., Phys. Rev. Accel. Beams 23, 072001
A. Moretti et al., Phys. Rev. ST Accel. Beams 8, 072001

## Slide 7
3-D cavity design
Field emission in an elliptical cavity
Further studies on breakdown phenomena

## Slide 8: DC magnetic field generated by solenoids
Distance between solenoids 0,64 m
Lcav=0,565 m
Solenoid radius = 0,35 m
CST M static solver

## Slide 9: RF electromagnetic field for the p-mode
E0 [MV/m] | 30.0
Eacc [MV/m] | 21.6
V0 [MV] | 17
Vcav [MV ] | 12
Pdiss [MW] | 12
Epk [MV] | 39.3
Stored energy | 100
CST eigensolver
*Old values

## Slide 10: Electron emission from surface
Emission from 3 points in the iris region of the cavity (where the E field is max)
Model : DC emission
Emission point area ~ 1 mm2
Initial e- energy : some eV
CST PIC Solver

## Slide 11: Electron emission with DC magnetic field and RF field
With DC magnetic field (superimposed)
Result is the same from B = 1 T
The electrons follow exactly the DC field lines.
Here, most electrons hit the facing iris, and some electron fly up to the window…
Without DC magnetic field
Electron max energy is 10 MeV (velocity close to c)
CST PIC solver with importation of M static and eigenmode solvers.

## Slide 12: Solenoid orientation
B field on axis (T)
From Lucio Rossi
Our simulation
Lattice cell
?
Solenoid current
B field on axis
B field lines followed by electrons
Electron trajectory calculation to be done

## Slide 13
3-D cavity design
Field emission in an elliptical cavity
Further studies on breakdown phenomena

## Slide 14: B field influence on the electron beamlet size
This formula gives a temperature rise.
Calculation of spatial temperature gradient could be of interest?
D. Bowring et al., Phys. Rev. Accel. Beams 24, 072001

## Slide 15: B field influence on the initial emission itself
What is the nature of ejected matter in breakdown phenomena?
Electrons ?
Plasma ?
Liquid metal ?

## Slide 16: « Fireball » emission from emitter, Abe et al.
Movie : https://www2.kek.jp/accl/eng/topics/topics190122.html
< Figure 7 > […] A flying bright object appeared near the downstream end plate (right image), moving upstream, and impacted the upstream end plate (left image) at t = 0.081 s. Breakdown occurred at the moment of impact (t = 0.081 s) […]
Fireballs speed ~few m/s, not driven by electrical field
From temperature meas (IR camera) they conclude that the flying object is not copper
RF cavity (509 MHz) equipped with high speed camera
T. Abe et al., Phys. Rev. Accel. Beams 21, 122002
No B field

## Slide 17: Atoms ejection from an emitter, Kyritsakis et al.
“In this article, we give insights to the atomic scale
processes taking place in metal nanotips under intense field emission conditions. […]. We find that when a sufficiently high electric field is applied to the tip, the emission-generated heat partially melts it and the field-induced force elongates and sharpens it.”
Molecular dynamics simulations
Static E field
Heat transfer
Formation of Taylor cones
A Kyritsakis et al, J. Phys. D: Appl. Phys. 51 225203
No B field

## Slide 18: Magneto hydrodynamical simulations from an emitter in presence of RF field and DC magnetic field
Study to be developed by a Master Student at CEA
Possible scenario ?
Effect of RF ?
Effect of B field ?
Liquid metal
Cavity
RF E,B field
BDC
Cavity
RF E,B field
BDC
Cavity
RF E,B field
BDC
time

## Slide 19: RF test facility with magnets …few considerations
cavity
cavity
Single solenoid
Bfield on axis
Lattice pair of solenoids
Bfield on axis
Should be considered ?
Cavity diagnostics
Dismountable plates for post mortem analysis
Faraday cups
Photomultipliers
Cameras
Pressure sensors
….

## Slide 20
Thank you
for attention