## Slide 1: Status of upgrades to MicroTCA at the Spallation Neutron Source
Alan Justice
Controls Hardware System Engineer
Oak Ridge National Laboratory
Spallation Neutron Source
13th Annual MicroTCA Workshop

## Slide 2: What will be covered today?
MicroTCA future at SNS
MicroTCA Systems in Production
Future Upgrades to MicroTCA
Lessons Learned

## Slide 3: MicroTCA future at SNS
VME to MicroTCA upgrades are part of the Integrated Controls Section modernization strategy at SNS
7 years of production at SNS for MicroTCA
Extensive in-house hardware & firmware expertise
Improving the reliability through extensive component health monitoring (IPMI)
  EPICS interface is deployed for production
Vadatech VT814
This Photo by Unknown Author is licensed under CC BY-SA-NC

## Slide 4: MicroTCA Applications at SNS
Currently 69 MicroTCA Systems in Production
Low Level RF
  Ring LLRF
  LINAC LLRF
Machine Protection System(MPS)
Magnet Power Supplies(PS) - Injection Kickers
  Waveform Monitor
  Waveform Generator
Personnel Protection System(PPS)
  Beam Power Limiting System

## Slide 5: Upgraded Machine Protection System
Largest deployment so far with a total of 48 systems
Master Hardware
  Vadatech VT815 Chassis
  Vadatech UTC006 MCH
  Vadatech UTC006 Crossbar/MCH
  Vadatech AMC502 carrier cards
  Vadatech FMC105 SFP transceivers
  Vadatech AMC726 Processor
Field Node Hardware
  Vadatech VT819 Chassis
  Vadatech AMC523
  Custom RTM
SNS MPS Master and Trigger Control
Notes: Crossbar reference at the bottom

## Slide 6: Beam Power Limiting System
Personnel Protection System and Machine Protection System functions
Limit Beam Power on First Target Station
Hardware
  Vadatech VT815 Chassis
  Vadatech UTC002 MCH
  Vadatech AMC560 carrier cards
  Vadatech AMC726 Processor
  FMC 155 – RS485
  FMC267 - ADC
  Custom FMC Timing Receiver

## Slide 7: Future Upgrades to MicroTCA
Timing Master
HPRF
Extraction Kicker Magnet Power Supplies
LEBT Chopper

## Slide 8: Timing Master
Replacing existing VME based custom Timing System Master
Functions
  Generate Timing Link with Events and Real Time Data
  GPS Interface for Timestamping
  Interface to Beam Monitor to provide Beam Charge Per Pulse
Hardware
  Vadatech VT815 Chassis
  Vadatech UTC006 MCH
  Vadatech AMC502 or AMC560 carrier cards
  Vadatech AMC756 Processor
  Custom FMCs
Target completion by end of 2025 and placed into production early 2026

## Slide 9: High Power RF
Upgrade from existing VME-based system to MicroTCA-based
  Existing system has 15 VME chassis; the MicroTCA-based system will have 4-5 chassis
Functions
  Control for HPRF Modulators and Transmitters
  Provides Timing to HPRF Modulators and Transmitters
  Upgrade from existing VME-based system to MicroTCA-based
Hardware
  Vadatech VT815 Chassis
  Vadatech UTC006 MCH
  Vadatech AMC756 Processor
  Vadatech AMC560
  Custom FMC Timing Receiver
  Custom FMC Fiber Fanout

## Slide 10: Extraction Kicker
Replacing existing analog solution
Function
  Digitize Extraction Kicker Charge and Fire Waveforms
  Apply Window to each and trip MPS for any fault condition
Hardware
  Vadatech VT815 Chassis
  Vadatech UTC006 MCH
  Vadatech AMC756 Processor
  Vadatech AMC560
  Vadatech FMC235 ADC
  Custom FMC Timing Receiver

## Slide 11: Lessons Learned
Plan Ahead for Hardware lead times
Be wary of obsolescence
Collaborate more
Utilize IPMI more extensively

## Slide 12: MicroTCA Working Group
Half day session at the EPICS Meeting hosted at Oak Ridge National Laboratory/Spallation Neutron Source
Over 25 participants
6 presentations
  Argonne National Laboratory
  European Spallation Source
  Facility for Rare Isotopes Beams (FRIB)
  Fermi National Accelerator Laboratory
  Spallation Neutron Source
  IPMI over EPICS
Lots of discussion and opportunities for collaboration

## Slide 13: Questions
Thanks to my colleagues Miljko Bobrek and Brian Shepetofsky for their contributions to this presentation and their work!