## Slide 1: Comments on HALHF vs CLIC power
Erik Adli, U. Oslo, 2025-01-15
Advantages PWFA vs RF:
1) High gradient
2) High efficiency? (Improved Luminosity/Power?)

## Slide 2: Efficiency RF vs PWFA
Erik Adli, U. Oslo, 2025-01-15
100%
Before the plasma interaction
DB
dump
23%
PLASMA
After the plasma interaction
50%
27%
DB
WB
100%
Before the two-beam module
DB
dump
19.1%
ACC wall
and dump
After the two-beam module
28%
53%
DB
WB
CLIC
2013 PWFA-LC
CLIC CDR
100%
Before the plasma interaction
DB
dump
20%
PLASMA
After the plasma interaction
40%
40%
DB
WB
HALHF 2.0 PWFA-LC
Assuming Gaussian bunches assumed, and transverse stability not considered.
With self-correction, and careful parameter optimzation, including transverse stability
40% > 28%
Optimized for efficiency, assuming 100 MV/m, and limited by transverse stability.

## Slide 3: HALHF 380 vs CLIC 380
Average power consumption:
HALHF 250 2.0: 106 MW (not optimized)
HALHF 380 2.0: 154 MW (not optimized)
CLIC 380 (2022): 110 MW
Luminosity per (total) power:
HALHF 250 2.0: 1.2x1034/106 = 11 x 10-3 (approx)
HALHF 380 2.0: 1.7x1034/154 = 11 x 10-3 (approx)
CLIC 380 (2022): 2.3x1034/110 = 21 x 10-3
Erik Adli, U. Oslo, 2025-01-15
HALHF: ca. 2x worse L/P than CLIC.

## Slide 4
SI_e | 1.602e-19 |  |  |  |  |  |  |  |  |  |  |  | 
SI_c | 2.998e8 |  |  |  |  |  |  |  |  |  |  |  | 
 |  | HALHF 2.0 | HALHF 380 |  | CLIC 2022 (Snowmass=) |  |  |  |  |  |  |  | 
 |  | 250 GeV | 380 GeV | 550 GeV | 380 GeV |  |  |  |  |  |  |  | 
 | avg rep rate | 1.60E+04 | 1.60E+04 | 1.60E+04 |  |  |  |  |  |  |  |  | 
 | COM, sqrt(s) | 2.50E+02 | 3.80E+02 | 550 |  |  |  |  |  |  |  |  | 
 | boost | 1.67E+00 | 1.67E+00 | 1.67E+00 |  |  |  |  |  |  |  |  | 
 | energy e- | 3.75E+02 | 5.70E+02 | 8.25E+02 |  |  |  |  |  |  |  |  | 
 | energy e+ | 4.17E+01 | 6.34E+01 | 9.17E+01 |  |  |  |  |  |  |  |  | 
 |  |  |  |  | CLIC |  |  |  |  |  |  |  | 
 | PWFA e- |  |  |  | one e- arm |  |  |  |  |  |  |  | 
 | DB wall plug |  |  |  |  |  |  | Man. calc |  |  |  |  | 
 | MB power e- | 9.61E+06 | 1.46E+07 | 2.11E+07 | 2.65E+06 | 1.39E+07 |  | 2.79E+06 |  |  |  |  | 
 | DB power e- | 2.38E+07 | 3.62E+07 | 5.24E+07 | 9.57E+06 |  |  |  |  |  |  |  | 
 | DB to MB efficiency e- | 4.04E-01 | 4.04E-01 | 4.04E-01 | 2.77E-01 | CDR 3 TeV | CDR: 0.2 |  |  |  |  |  | 
 | DB linac W2B eff | 55.0% | 55.0% | 55.0% | 4.97E-01 | CDR 3 TeV | CDR: 0.55 |  |  |  |  |  | 
 | total power e- | 4.33E+07 | 6.58E+07 | 9.52E+07 | 1.93E+07 | (without injectors) | 66000000 | 1.95E+07 | (without CR, TR) |  |  |  | 
 | Wall to MB efficiency e- | 22.2% | 22.2% | 22.2% | 1.38E-01 | Improved from 2018, will be further improved in 2025 |  | 1.43E-01 |  |  |  |  | 
 | COOL COPPER |  |  |  |  |  |  |  |  |  |  |  | 
 | MB power e+ | 3.21E+06 | 4.87E+06 | 7.05E+06 |  |  |  |  |  |  |  |  | 
 | W2B eff | 11.0% | 11.0% | 11.0% |  |  |  |  |  |  |  |  | 
 | total power e+ | 2.91E+07 | 4.43E+07 | 6.41E+07 |  |  |  |  |  |  |  |  | 
 | TOTAL LINACS |  |  |  |  |  |  |  |  |  |  |  | 
 | MB power total | 1.28E+07 | 1.95E+07 | 2.82E+07 | 5.30E+06 |  |  |  |  |  |  |  | 
 | Linac power total | 7.24E+07 | 1.10E+08 | 1.59E+08 | 3.85E+07 | (wihtout DB combination/transport) |  |  |  |  |  |  | 
 | Wall to MB total eff | 1.77E-01 | 1.77E-01 | 1.77E-01 | 1.38E-01 |  |  |  |  |  |  |  | 
 | Total power | 1.06E+08 | 1.54E+08 | 2.18E+08 | 1.10E+08 |  |  |  |  |  |  |  | 
 | DB power / total power |  | 71.5% |  | 35.0% |  |  |  |  |  |  |  | 
 | Luminosity | 1.20E+34 | 1.70E+34 | 2.05E+34 | 2.30E+34 | (with imperfections) |  | 4.50E+00 | without imperfections |  |  |  | 
 | Luminosity per linacs power | 1.66E+26 | 1.54E+26 | 1.28E+26 | 5.97E+26 | Ratio CLIC380/HALHF380: |  | 3.86E+00 | (with CLIC imperfections) |  |  |  | 
 | Luminosity per total power | 1.13E+26 | 1.10E+26 | 9.38E+25 | 2.09E+26 | Ratio CLIC380/HALHF380: |  | 1.89E+00 | (with CLIC imperfections) |  |  |  | 
 | IP beam sizes | 636 x 6.6 nm2 | 520 x 5.3 nm2 |  | 149 x 2.0 nm2 |  |  | 2.65E+00 |  |  |  |  | 
 | IP betas | 3.3 x 0.1 mm2 | 3.3 x 0.1 mm2 |  | 8 x 0.1 mm2 |  |  | 2.13E+00 |  |  |  |  | 
 | Conclusion: |  |  |  |  |  |  |  |  |  |  |  | 
 | HALHF linacs are on average more power efficienct (20%+ ish), mainly due to 40% PWFA DB2MB |  |  |  |  |  |  |  |  |  |  |  | 
 | but, |  |  |  |  |  |  |  |  |  |  |  | 
 | HALHF needs twice more beam power for the target luminosity. |  |  |  |  |  |  |  |  |  |  |  | 
 | Therefore, the total power for the target luminosity is higher |  |  |  |  |  |  |  |  |  |  |  | 
 | reason: the low positron energy ("maximum" energy assymetry not good, since lum. driven by positrons, goes down?) |  |  |  |  |  |  |  |  |  |  |  | 
 | The luminosity per power of CLIC is therefore 4-5 times higher than that of HALHF |  |  |  |  |  |  |  |  |  |  |  | 
Erik Adli, U. Oslo, 2025-01-15

## Slide 5: Beam power
Beam power (e- + e+) :
HALHF 380 2.0: 19.5 MW
CLIC 380: 5.3 MW
Linac wall-plug power (e- + e+) :
HALHF 380 2.0: 110 MW
CLIC 380: 39 MW
Total power (e- + e+) :
HALHF 380 2.0: 154 MW
CLIC 380: 110 MW
Beam sizes:
HALHF 250 2.0: 520 x 5.3 nm2
CLIC 380: 149 x 2.0 nm2
Erik Adli, U. Oslo, 2025-01-15
Large beam size driven by low-energy postitron beam. ”Helps” electron beam emittance requirements, but it is not overall positive to have large e- and e+ beams at IP.
HALHF: ⌁4x larger beam power, or ⌁3x more linac power, or ⌁2x more total power, needed to achieve similar luminosity.

## Slide 6: Conclusions
HALHF luminosity per power is a factor 2 – 4 lower than CLIC.
currently x2, realistically power should scale with beam power, so x4?
despite assuming PWFA efficiency to be higher than that of RF
Originates from requirement for large positron beam, disadvantage of the asymmetric concept.
possible that reaching sufficiently small beam emittances in PWFA will anyway be difficult
Preliminary total costing shows that advantages of more compact machine still outweights the disadvantageous L/P.
- but we should work to reduce the HALHF L/P where possible
Erik Adli, U. Oslo, 2025-01-15
HALHF: DB power is 71% of total power, CLIC, 35% of total.