## Slide 1
Concatenation Methods
Thomas Flisgen
Workshop on Higher Order Modes in Superconducting Cavities (HOMSC25)
06 - 08 October 2025
DESY, Hamburg, Germany

## Slide 2: Motivation for concatenation methods: Computation of RF Properties of electrically LARGE structure with tiny features
*E. Vogel et al.: "Status of the 3rd harmonic systems for FLASH and XFEL in summer 2008", Proc. LINAC 2008
*
E-Field of third dipole mode in Resonator
Higher modes are not necessarily localized in the individual resonators of the chain
Consideration of the entire chain is necessary for a meaningful determination of its RF properties
Fundamental waveguide mode

## Slide 3: Overview concatenation methods Developed and USED at UROS / HZB / BTU
CSC – A procedure for coupled S-parameter calculations [1]
[1] H. -W. Glock et al., "CSC - A procedure for coupled S-parameter calculations," in IEEE Transactions on Magnetics, vol. 38, no. 2, pp. 1173-1176, 2002
SCC – State-Space Concatenations [2]
[2] T. Flisgen et al., "Eigenmode compendium of the third harmonic module of the European X-ray Free Electron Laser," in Phys. Rev. Accel. Beams 20, 042002, 2017
CSCBEAM – Generalization of CSC to compute beam coupling impedances [3]
[3] T. Flisgen et al., "Generalization of coupled 𝑆-parameter calculation to compute beam impedances in particle accelerators," in Phys. Rev. Accel. Beams 23, 034601, 2020

## Slide 4: COMMON FEATURES of THE CONCATENATION METHODS CSC, SSC and CSCBEAM
Important advantages:
(numerical) treatment of segments is computationally less demanding
single treatment of identical segments
segments with simple geometry can be treated analytically, which is very fast
employment of (rotational) symmetry of segments is feasible
1. Decomposition of the Structure at Regions of Constant Cross Section

## Slide 5: COMMON FEATURES of THE CONCATENATION METHODS CSC, SSC and CSCBEAM
2. Consideration of Segments as Blocks with Terminals and Expansion of Fields on Slice Planes in terms of 2D Port Modes
Segment
E-field of first three 2D port modes
Modal voltages correspond to tangential electric fields of 2D port modes
Modal currents correspond to tangential magnetic fields of 2D port modes

## Slide 6: COMMON FEATURES of THE CONCATENATION METHODS CSC, SSC and CSCBEAM
3. Description of RF Properties of Individual Sections
wave equation (PDE):
Relationship between port quantities (and fields)
Segment

## Slide 7: COMMON FEATURES of THE CONCATENATION METHODS CSC, SSC and CSCBEAM
4. Concatenation Description of Individual Segments
Segment 1
Segment 2
Coupling equations arising from field continuity constraints
Arbitrary topologies and number of 2D port modes supported
Description of RF properties of full structure available

## Slide 8: MODAL EXPANSION AT THE SLICE PLANES
How many waveguide modes have to be considered?
Segment 1
Segment 2
Slice plane
Wave amplitudes
Number of waveguide modes required is determined by upper frequency fmax
All propagating waveguide modes must be considered (shown in blue here)
Additionally, a finite set of evanescent modes must be taken into account
The longer the region of constant cross section, the fewer waveguide modes need to be considered

## Slide 9: Overview concatenation methods Developed and USED at UROS / HZB / BTU
CSC – A procedure for coupled S-parameter calculations [1]
[1] H. -W. Glock et al., "CSC - A procedure for coupled S-parameter calculations," in IEEE Transactions on Magnetics, vol. 38, no. 2, pp. 1173-1176, 2002
SCC – State-Space Concatenations [2]
[2] T. Flisgen et al., "Eigenmode compendium of the third harmonic module of the European X-ray Free Electron Laser," in Phys. Rev. Accel. Beams 20, 042002, 2017
CSCBEAM – Generalization of CSC to compute beam coupling impedances [3]
[3] T. Flisgen et al., "Generalization of coupled 𝑆-parameter calculation to compute beam impedances in particle accelerators," in Phys. Rev. Accel. Beams 23, 034601, 2020

## Slide 10: Workflow CSC [1]
[1] H.-W. Glock, K. Rothemund, and U. van Rienen, "CSC - A procedure for coupled S-parameter calculations," in IEEE Trans. on Mag., vol. 38, no. 2, pp. 1173-1176, 2002
Scattering matrix of full structure and fields on discrete frequencies
Concatenation
Topology Information
Computation of S-Matrices on discrete frequencies

## Slide 11: COMPARISON S-PARAMETERS computed with CSC VS. MEASUREMENTS
frequency / Hz
C1
C2
C3
C4
Measurement
noise floor
first two dipole bands
fundamental band
Simulation
quadrupole modes
T. Flisgen, H.-W. Glock, P. Zhang, I. R. R. Shinton, N. Baboi, R. M. Jones, and U. van Rienen, “Scattering parameters of the 3.9 GHz accelerating module in a free-electron laser linac: A rigorous comparison between simulations and measurements”, Phys. Rev. ST Accel. Beams 17, 022003, 2014
|sC3H1,C3H2| / dB

## Slide 12: COMPARISON S-PARAMETERS computed with CSC VS. MEASUREMENTS
frequency / Hz
C1
C2
C3
C4
Measurement
noise floor
first two dipole bands
Simulation
quadrupole modes
T. Flisgen, H.-W. Glock, P. Zhang, I. R. R. Shinton, N. Baboi, R. M. Jones, and U. van Rienen, “Scattering parameters of the 3.9 GHz accelerating module in a free-electron laser linac: A rigorous comparison between simulations and measurements”, Phys. Rev. ST Accel. Beams 17, 022003, 2014
|sC1H1,C4H2| / dB

## Slide 13: Overview concatenation methods Developed and USED at UROS / HZB / BTU
CSC – A procedure for coupled S-parameter calculations [1]
[1] H. -W. Glock et al., "CSC - A procedure for coupled S-parameter calculations," in IEEE Transactions on Magnetics, vol. 38, no. 2, pp. 1173-1176, 2002
SCC – State-Space Concatenations [2]
[2] T. Flisgen et al., "Eigenmode compendium of the third harmonic module of the European X-ray Free Electron Laser," in Phys. Rev. Accel. Beams 20, 042002, 2017
CSCBEAM – Generalization of CSC to compute beam coupling impedances [3]
[3] T. Flisgen et al., "Generalization of coupled 𝑆-parameter calculation to compute beam impedances in particle accelerators," in Phys. Rev. Accel. Beams 23, 034601, 2020

## Slide 14: Workflow SCC [2]
[2] T. Flisgen, J. Heller, T. Galek, L. Shi, N. Joshi, N. Baboi, R. M. Jones, and U. van Rienen, "Eigenmode compendium of the third harmonic module of the European X-ray Free Electron Laser," in Phys. Rev. Accel. Beams 20, 042002, 2017
Model-Order Reduction

## Slide 15: Workflow SCC [2]
Model-Order Reduction
state vector:
orthogonal projection matrix:
reduced state vector:
·
=
·
=

## Slide 16: Workflow SCC [2]
[2] T. Flisgen, J. Heller, T. Galek, L. Shi, N. Joshi, N. Baboi, R. M. Jones, and U. van Rienen, "Eigenmode compendium of the third harmonic module of the European X-ray Free Electron Laser," in Phys. Rev. Accel. Beams 20, 042002, 2017
Model-Order Reduction
Concatenation
Topology Information
Reduced-Order Model of full structure
Scattering Parameters
Eigenmodes
…
Field Distributions

## Slide 17: Chain of Eight Superconducting 3rd Harmonic Cavities in XFEL
 | HOM Coupler | Cavity | HOM Coupler with Power Coupler | Bellow | HOM Coupler (rotated) | HOM Coupler with Power Coupler (rotated)
Ndof | 411,015 | 1,119,963 | 585,915 | 427,119 | 411,015 | 585,915
Ndof,red | 138 | 258 | 164 | 145 | 138 | 164
Figures of cavities E. Vogel et al.: "Status of the 3rd harmonic systems for FLASH and XFEL in summer 2008", Proc. LINAC 2008
Full model of eight cavity chain is estimated to have Ndof = 20,239,977 degrees of freedom
Reduced-order models of segments concatenated to reduced-order model of full chain with Ndof,red = 2,931 degrees of freedom

## Slide 18: Computation of Eigenmodes based on Reduced-Order Model
Computed 1,479 eigenmodes in the interval 1 GHz to 8 GHz of the chain by means of a standard workstation computer
Assembled a modal compendium for the chain with resonant frequency, external quality factor, R/Q, and electric field distribution of each mode
In total, the compendium consists of 137 pages

## Slide 19: External Quality Factors in Chain of Eight 3rd Harmonic Cavities
monopole bands
Figures of cavities courtesy of E. Vogel / DESY
dipole bands
quadrupole bands

## Slide 20: Pure Bellow Modes (Inter-Cavity Modes) at 5.1524 GHz
The plots show the absolute value of the electric field.

## Slide 21: Overview concatenation methods Developed and USED at UROS / HZB / BTU
CSC – A procedure for coupled S-parameter calculations [1]
[1] H. -W. Glock et al., "CSC - A procedure for coupled S-parameter calculations," in IEEE Transactions on Magnetics, vol. 38, no. 2, pp. 1173-1176, 2002
SCC – State-Space Concatenations [2]
[2] T. Flisgen et al., "Eigenmode compendium of the third harmonic module of the European X-ray Free Electron Laser," in Phys. Rev. Accel. Beams 20, 042002, 2017
CSCBEAM – Generalization of CSC to compute beam coupling impedances [3]
[3] T. Flisgen et al., "Generalization of coupled 𝑆-parameter calculation to compute beam impedances in particle accelerators," in Phys. Rev. Accel. Beams 23, 034601, 2020

## Slide 22: Workflow CSCBEAM [3]
Computation of generalized S-Matrices on discrete frequencies
[3] T. Flisgen, E. Gjonaj, H.-W. Glock, and A. Tsakanian, "Generalization of coupled 𝑆-parameter calculation to compute beam impedances in particle accelerators," in Phys. Rev. Accel. Beams 23, 034601, 2020

## Slide 23: Workflow CSCBEAM [3]
[3] T. Flisgen, E. Gjonaj, H.-W. Glock, and A. Tsakanian, "Generalization of coupled 𝑆-parameter calculation to compute beam impedances in particle accelerators," in Phys. Rev. Accel. Beams 23, 034601, 2020
commonly known scattering parameters
coupling between scattered waves and beam current
commonly know beam coupling impedance
  Decomposition
contribution of incident waves to voltage “seen” by beam
  Description of r-th Segment with Generalized Matrix
  (Beam is an Additional Port)
  Concatenation of Generalized Matrices

## Slide 24: Workflow CSCBEAM [3]
Computation of generalized S-Matrices on discrete frequencies
Concatenation
Topology Information
Generalized S-matrix of full structure (including beam-coupling impedances) on discrete frequencies
[3] T. Flisgen, E. Gjonaj, H.-W. Glock, and A. Tsakanian, "Generalization of coupled 𝑆-parameter calculation to compute beam impedances in particle accelerators," in Phys. Rev. Accel. Beams 23, 034601, 2020

## Slide 25: Playground example CSCBEAM [3]
[3] T. Flisgen, E. Gjonaj, H.-W. Glock, and A. Tsakanian, "Generalization of coupled 𝑆-parameter calculation to compute beam impedances in particle accelerators," in Phys. Rev. Accel. Beams 23, 034601, 2020

## Slide 26: Summary
Concatenation methods are powerful tools to determine RF properties of (higher-order) modes of complex structures (long chains of cavities with power and HOM couplers) using workstation computers
CSC, SSC and CSCBEAM are based on a non-overlapping domain decomposition and expansion of field at slice planes using waveguide modes
Schemes differ in the way how segments are described and what quantities are delivered
Further research on generalized matrices required, i.e. how they can be effectively determined

## Slide 28: CSCBEAM TESLA CAVITY example [3]
[3] T. Flisgen, E. Gjonaj, H.-W. Glock, and A. Tsakanian, "Generalization of coupled 𝑆-parameter calculation to compute beam impedances in particle accelerators," in Phys. Rev. Accel. Beams 23, 034601, 2020
18 port modes used for the field expansion
dimension of generalized matrices for each segment: 37 x 37
  Courtesy of Erion Gjonaj

## Slide 29: CSCBEAM TESLA CAVITY example [3]
[3] T. Flisgen, E. Gjonaj, H.-W. Glock, and A. Tsakanian, "Generalization of coupled 𝑆-parameter calculation to compute beam impedances in particle accelerators," in Phys. Rev. Accel. Beams 23, 034601, 2020