## Slide 1: Beam Stability in the EIC ESR: Contribution of the 591 MHz RF Cavities
Oct. 6-8, 2025
Alexei Blednykh
Pre-Operations System Manager

## Slide 2: Outline
Beam Intensity Parameters
Impedance Modeling and Database
Wakefield Simulations of the 2-Cavity String
Total Wakefileds
Instability Threshold Analysis
Summary
International Workshop on Higher Order Modes in Superconducting Cavities (HOMSC2025)
Alexei Blednykh

## Slide 3: EIC Project Overview
Electron Injection System
  DC Photoelectron Gun
    320 keV, ~85% polarization, 1.5 nC per bunch
  S-band LINAC
    750 MeV energy, normalized emittance: ~80 μm (x), ~50 μm (y)
Beam Accumulator Ring (BAR, C50 m)
  750 MeV energy, single-bunch accumulation: 28 nC
  Design lead by the NSLS-II team
Rapid Cycling Synchrotron (RCS, C1.4 km)
  0.75018 GeV in 100 ms, 1 Hz
  Spin-transparent lattice, 28 nC, normalized εₙ: 16-24 nm (x), 1.4-2.4 nm (y)
Electron Storage Ring (ESR, C3.8 km)
  Beam energy: 5-18 GeV, current : up to 2.5 A, SR power: up to 10 MW
  Polarized bunches, swap-out injection
Hadron Storage Ring (HSR, C3.8 km)
  Beam energy: Injection at 23.8 GeV, accelerated to 41-275 GeV
  Beam current: up to 1 A / 0.7 A with M = 1160 / 290 bunches
  Crossing angle: 25 mrad with crab cavities
  Spin rotators (longitudinal) for p, d, He3
  Cooler: low-energy electron and stochastic cooling
  Luminosity: up to 10³³-10³⁴ cm⁻²s⁻¹
Alexei Blednykh
International Workshop on Higher Order Modes in Superconducting Cavities (HOMSC2025)
ESR: 591 MHz
HSR: 24.8 MHz, 49 MHz, 98 MHz, 197 MHz and 591 MHz

## Slide 4: Ultimate Beam Intensity Parameters
Alexei Blednykh
 | 5 GeV | 10 GeV | 18 GeV
Num. of electrons per bunch, | 1.72x1011 |  | 6.25x1010
Bunch Charge, | 28 nC |  | 11 nC
Number of Bunches, | 1160 |  | 290
Single Bunch Current, | 2.2 mA |  | 0.8 mA
Bunch Length, | 22.7 ps | 25.4 ps | 30 ps
Peak Bunch Current, | 484 A | 433 A | 155 A
Average Current, | 2.5 A | 2.5 A | 0.23 A
 | 5 GeV | 10 GeV | 18 GeV
 | 1.72x1011 |  | 6.25x1010
 | 28 nC |  | 11 nC
 | 1160 |  | 290
 | 2.2 mA |  | 0.8 mA
 | 22.7 ps | 25.4 ps | 30 ps
 | 484 A | 433 A | 155 A
 | 2.5 A | 2.5 A | 0.23 A
High intensity beams at 5 GeV and 10 GeV
International Workshop on Higher Order Modes in Superconducting Cavities (HOMSC2025)

## Slide 5: ESR Vacuum System Component Database
Alexei Blednykh
Accelerator Physics
Xiaofeng Gu, Gang Wang, … .
Vacuum System
Mathew Mahony, Charlez Hetzel, … .
Mechanical Design
George Dacos (IR10), Sankar Poopalasingam, Kentaro Matsushima, … .
Instrumentation System
David Gassner, … .
RF System
Zack Conway, , Wencan Xu, Jiquan Guo, … .
International Workshop on Higher Order Modes in Superconducting Cavities (HOMSC2025)

## Slide 6: List of Vacuum Components and Their Status
Alexei Blednykh
Total wakefield simulations for the ESR are in progress.
80 mm
36 mm
ESR Vacuum Chamber Profile
International Workshop on Higher Order Modes in Superconducting Cavities (HOMSC2025)

## Slide 7: IR10 SRF and Beam Line System
Alexei Blednykh
Components | Abbreviation | Previous Number | New Number
IR10 |  |  | 
591 MHz RF Cavity | CAV | 17 | 18
Bellows, 274 mm aperture | BLW 274 | 17 | 18
Bellows, 180 mm aperture | BLW 180 | 0 | 40
Bellows, 150 mm aperture | BLW 150 | 17 | 0
Tapered Transition | TPRD | 19 | 2
Gate Valve, 180 mm aperture | GV 180 | 0 | 20
Gate Valve, 150 mm aperture | GV 150 | 17 | 0
Beam Line Absorbers, 274 mm aperture | BLA 274 | 17 | 9
Beam Line Absorbers, 150 mm aperture | BLA 150 | 17 | 0
Beam Pipes,180 mm aperture, L~5 m | BP 180 | 0 | 10
Beam Pipes, 150 mm aperture, L~2.5 m | BP 150 | 18 | 0
International Workshop on Higher Order Modes in Superconducting Cavities (HOMSC2025)

## Slide 8: Two Back-to-Back 591 MHz Cavities
Alexei Blednykh
Longitudinal Wakefield
Vertical Dipole Wakefield
Large-aperture connection eliminates tapered transitions between cryomodules.
~40% reduction in and from old to present geometry
Design meets ESR wakefield requirements
Gang Wang
International Workshop on Higher Order Modes in Superconducting Cavities (HOMSC2025)

## Slide 9: Wakefield Simulations for 2-Cavity String
Alexei Blednykh
Simulated Vacuum Components
  Two Back-to-Back 591 MHz RF Cavities
  Beam Line Absorbers, 274 mm aperture
Remaining Components to Simulate
  Bellows, 274 mm aperture
  Tapered Transition (Arc to Straight Section)
  Gate Valve, 180 mm aperture
  Beam Pipes,180 mm aperture, L~5 m
Beam Line Absorber
Two Back-To-Back Cavities
No significant impact is expected from adding and of the remaining cryomodule components to the total wakefield.
International Workshop on Higher Order Modes in Superconducting Cavities (HOMSC2025)

## Slide 10: Breakdown of Wakefields by Component
Alexei Blednykh
Longitudinal Wakefield
Vertical Dipole Wakefield
Quadrupole Wakefield
Wakefields have been simulated for a 0.5 mm bunch length (Pseudo Green Functions).
International Workshop on Higher Order Modes in Superconducting Cavities (HOMSC2025)

## Slide 11: Main Parameters At 5 GeV
Alexei Blednykh
Energy, |  | 5
Average Current, |  | 2.5
Revolution Period, |  | 12.79
Gammat |  | 29.6
Momentum Compaction, |  | 1.14x10-3
Number of Bunches, |  | 1160
Energy Loss, |  | 1.2
RF Voltage, |  | 12
RF Acceptance |  | 1.2
Synchrotron Tune, |  | 0.057
Damping Time, |  | 54, 27
Energy Spread, |  | 4.93x10-4
Bunch Length, |  | 6.0
 |  | 5
 |  | 2.5
 |  | 12.79
Gammat |  | 29.6
 |  | 1.14x10-3
 |  | 1160
 |  | 1.2
 |  | 12
RF Acceptance |  | 1.2
 |  | 0.057
 |  | 54, 27
 |  | 4.93x10-4
 |  | 6.0
Lattice v6.3
CSR
Geom.+RW
A safety factor of 2 was applied to the Geom. + RW Wakefield.
International Workshop on Higher Order Modes in Superconducting Cavities (HOMSC2025)

## Slide 12: ELEGANT Simulations of MWI
Alexei Blednykh
mA
mA
MWI threshold,
Chart: Energy Spread
| 0 | 2 | 4 | 5 | 6 | 8 | 10
 | 0.00049408 | 0.00049715 | 0.00050056 | 0.00050267 | 0.00053936 | 0.00058932 | 0.00060509
Chart: Bunch Length
| 0 | 2 | 4 | 5 | 6 | 8 | 10
 | 6.0042 | 7.2651 | 8.354 | 8.8635 | 9.6567 | 10.9366 | 11.8491
Energy Spread
Bunch Lengthening
International Workshop on Higher Order Modes in Superconducting Cavities (HOMSC2025)

## Slide 13: Coupled Bunch Instabilities at 5 GeV
Alexei Blednykh
Longitudinal multiple coupled-bunch modes are unstable at 2.5 A average current. The growth time is 20 ms.
Longitudinal bunch-by-bunch feedback (damper) is required
The beam is stable against vertical coupled-bunch instabilities during beam-beam collision.
The vertical shunt impedance <12 MΩ/m (Eng. def.).
Cross-checking beam stability, RW+HOM’s w/o beam-beam collision.
Michael Blaskiewicz
-=
CST (Frequency Domain)
ECHO (Time Domain)
Wencan Xu
Gang Wang
Vertical bunch-by-bunch feedback is under investigation
International Workshop on Higher Order Modes in Superconducting Cavities (HOMSC2025)

## Slide 14: Summary
Alexei Blednykh
2-cavity 591 MHz string contribution analyzed for single-bunch dynamics and HOM-driven effects.
Wakefield and Stability Analysis:
  A longitudinal damper is required to suppress coupled-bunch instabilities driven by HOMs from the 2-cavity string.
  A transverse damper is under investigation to address potential transverse coupled-bunch instabilities (without beam-beam effect)
  The beam is single-bunch stable
Cryomodule impedance meets the requirements
  Remaining components will be incorporated into the impedance budget; No significant impact is expected due to their shielded and standardized designs.
International Workshop on Higher Order Modes in Superconducting Cavities (HOMSC2025)