## Slide 1
NUMERICAL ANALYSIS OF HIGHER-ORDER MODE COUPLERS
Sosoho-Abasi Udongwo, Thomas Flisgen

## Slide 2: Wakefields
Wakefields
  Generated by the beam as it moves through the cavity structure
  Superposition of several modes
    Lower-Order modes (LOMs)
    Accelerating mode
    Higher-Order modes (HOMs)
Electric field magnitude of fields excited by beam moving through the cavity

## Slide 3: Beamline absorbers
Typically lossy ceramic or ferrite material
Advantages
  Simple, robust and broadband
  Minimal impact on the accelerating mode
  Compact
Disadvantages
  Ineffective for trapped HOMs

## Slide 4: Waveguide couplers
Extract HOM power above waveguide cutoff frequency
Advantages
  Broadband
  Minimal impact on accelerating mode
Disadvantages
  Typically bulky
Quad-ridged waveguide
Rectangular waveguide

## Slide 5: Coaxial hom couplers
Use coaxial line with an antenna or loop near cavity to couple to HOM fields
Advantages
  Can damp trapped modes
Disadvantages
  Usually narrowband
  Complex geometry
  Risk of multipacting
  Usually requires multiple couplers per cavity

## Slide 6: Coaxial HOM Coupler Design
Parameterisation of some coaxial HOM couplers
Parameterise geometry
Modelling

## Slide 7: Coaxial HOM Coupler Design
Roughly synthesise equivalent circuit model
Estimate equivalent circuit element values and bounds from 3D model
Tune equivalent circuit model
Surrogate Modelling

## Slide 8: Sensitivity analysis
l
l
SALib, UQPy, Dakota Engine, etc
l
l
3D model variable sensitivities
Equivalent circuit model variable sensitivities

## Slide 9: Sobol’ Indices
Convergence of Sobol‘ main indices S1 for equivalent circuit model
S1
N= samples are analysed increasing the value of to study the convergence
Total number of samples analysed is where D is the number of input variables
For and the number of evaluations are 20480

## Slide 10: Initial optimisation
Transmission curves for a typical coaxial HOM coupler

## Slide 11: optimisation
Transmission parameter depend on orientation of coaxial HOM coupler
It is therefore necessary to reoptimise the HOM coupler in the cavity-coupler assembly

## Slide 12: HOM coupler configurations
j

## Slide 13: Uncertainty quantification
Double Quarter-Wave HOM Coupler
Hook-Type HOM Coupler

## Slide 14: Uncertainty quantification
A tensor product is constructed from Gaussian quadrature points for the three geometric parameters
Each dimension has four Gaussian nodes 64 total design points
Guarantees integration accuracy up to polynomial order 7
Method

## Slide 15: Uncertainty quantification
Accelerating mode frequency change in tens of kilohertz
Maximum FM frequency change across all variables is about 10 kHz
Accelerating mode frequency

## Slide 16: Uncertainty quantification
Negligible effect on the fundamental mode
All in the same order of magnitude as the nominal value
Accelerating mode external quality factor

## Slide 17: Uncertainty quantification
Non-negligible effect on the maximum first dipole passband impedance
Impedance value can go as high as 3.5 times the nominal value
Max Transverse Impedance – First HOM Dip. Passband

## Slide 18: Summary
In this presentation I showed
  Equivalent circuit modelling
  Sensitivity analysis and
  Uncertainty quantification of some coaxial HOM couplers
outlook
Development of an efficient procedure for synthesising and tuning equivalent circuit models

## Slide 19
Brandenburgische Technische Universität Cottbus – Senftenberg
Fakultät/Institut/Verwaltungsbereich
Fachgebiet/Abteilung
Sosoho-Abasi Udongwo
E udongwo@b-tu.de