## Slide 1
PROGRESS OF HOM COUPLERS FOR PERLE SRF CAVITIES
Patricia Duchesne, Sébastien Blivet, Akira Miyazaki, Gilles Olivier, Guillaume Olry, Hervé Saugnac IJCLab
Yolanda Gomez Martinez LPSC
Carmelo Barbagallo, Karin Canderan CERN
Haipeng Wang JLab
Work supported by funding from the European Union’s program Horizon-INFRA-2023-TECH-01 under GA No 101131435 – iSAS
International Workshop
HOMSC2025
Hamburg, Germany @ DESY
October 6-8, 2025

## Slide 2: CONTEXT: ERL PERLE
PERLE (Powerful Energy Recovery Linac for Experiments)
Linac cryomodule
(Four 5-cell SRF cavities)
Booster
Beam dump
Injection line
Recirculating arc (x3)
DC Photogun
HV system
ERL PERLE 250 MeV
Demonstrate multi-turn and high current operation
Validate important technical choices
Host experiments of interest for our lab and institute
Target Parameters (2030) | Unit | Value
Injection energy | MeV | 7
Electron beam energy | MeV | 250
Normalized emittance | mm mrad | 6
Average beam current Ib,0 | mA | 20
Bunch charge Qb | pC | 500
Longitudinal bunch length z | mm | 3
RF frequency | MHz | 801.58
Duty factor | - | CW
2025
2026
2027
2028
2029
2030
20
500
PERLE 3 turns @500 MeV
PERLE 3 turns @250 MeV
250
PERLE 1 turn @89 MeV

## Slide 3: CAVITY AND HOM COUPLER DEVELOPMENT FOR PERLE
First Nb 802 MHz 5-cell cavity fabricated @JLab
PERLE 5-cell CAVITY & HOM COUPLERS
  Cavity RF Design by CERN & Jefferson Lab: optimized for an ERL at high beam currents (High Q0, efficient HOMs extraction), prototype manufactured and tested successfully (Q0@2K = 3e10 @27 MV/m)
Jacketed Nb 802 MHz 5-cell cavity
Cavity mechanical design: mechanical and RF sensitivity analyses
Cavity made of Niobium RRR250
Titanium He Tank including the beam pipes
4 HOM ports + 1 High Power Coupler port + 1 pickup port
HOM port (x4)
HPC port
pickup port
120°
  First PERLE HOM Coupler Prototypes
    3D-printed epoxy & copper coated couplers at CERN
    Successfully tested on 5-cell copper cavity at Jlab
  HOM Damping scheme for PERLE (C. Barbagallo, PhD Thesis, 2024):
    Coaxial couplers to damp the trapped HOMs (4 max / cavity)
    Beam-line absorbers to damp the HOMs propagating through the beam pipes (cold / warm BLA)
Linac cryomodule PERLE

## Slide 4: DAMPING SCHEME: REQUIREMENTS
DAMPING REQUIREMENT
BBU (Beam BreakUp instability) studies from an analytical method (C. Barbagallo, PhD Thesis, 2024)
Machine configuration | (/m) | () /
PERLE 3 turns @500 MeV @20 mA | 1.41E9 | 1.13E8
PERLE 3 turns @250 MeV @20 mA | 4.88E7 | 1.36E8
PERLE 1 turn @89 MeV @5 mA | 1.24E10 | 8.72E10
Machine configuration |  | 
PERLE 3 turns @500 MeV @20 mA | 1.41E9 | 1.13E8
PERLE 3 turns @250 MeV @20 mA | 4.88E7 | 1.36E8
PERLE 1 turn @89 MeV @5 mA | 1.24E10 | 8.72E10
PERLE 250 MeV
Cryo_start
Cryo_end
1,2,3
Cryomodule 1
Dump
  HOM requirements depending on the machine configuration:
Monopole mode n:
Dipole mode n:
Impedance threshold:
CM1_start
CM1_end
CM2_end
Cryomodule 1
Cryomodule 2
1,3,5
2,4,6
Dump
PERLE 500 MeV
Threshold current Ith for a multi-pass machine:

## Slide 5: DAMPING SCHEME FOR THE TRAPPED HOMs
CHOICE OF THE HOM DAMPING SCHEME
Identification of the dangerous HOMs of the 5-cell cavity
Simulation with CST
(eigenmode + wakefield solvers)
Example with 2 hook & 2 probe couplers:
Evaluation of the HOM power (for one cavity) PERLE 3-turns
PL [0; 2.5 GHz] | PM [2.5; 4 GHz] | PH [4; 40 GHz] | PHOM | 2 Beam pipes | FPC | 2 Hook | 2 Probe
3.5 W | 12 W | 114 W | 130 W | 113 W | 13 W | 1 W | 2.5 W
HOM Power (Wakefield):
=
Parameter | Symbol | Value
Longitudinal bunch length | z | 3mm
Bunch charge | Qb | 500 pC
Average beam current | Ib,0 | 20 mA
Operating beam current | Ib,op | 120 mA
Total longitudinal loss factor | k∥ | 2.304 V/pC
Loss factor of FM k∥,0 | k∥,0 | 0.594 V/pC
With 2H2P:
Approximation by considering three frequency ranges (Low, Medium, High) (C. Barbagallo):
Almost all of the HOM power goes into the beam pipes (85%). Only several watts are extracted by the HOM couplers
  with high R/Q values, close to a beam harmonic (a multiple of 40 MHz), confined within the cavity
    Several trapped modes: monopoles TM011 and dipoles TE111 & TM110
    Monopole modes far from beam harmonics
    Dipole modes only 1 to 2 MHz away from beam harmonics
Evaluation of the impedances
  with different HOM couplers (HOOK, PROBE, DQW)
    Two efficient damping schemes: 4DQW / 2H2P
  Average HOM Power:

## Slide 6: DAMPING SCHEME FOR THE TRAPPED HOMs
HOM DAMPING SCHEME ADOPTED FOR PERLE
  4H damping scheme is the ideal choice (same fabrication, less cost by mass production)
  Start PERLE with only 2 HOOK couplers (one on each side of the cavity oriented at 120° to each other), 2 ports left empty for upgrade
Mechanical considerations associated with the integration into the cryomodule
  Risk of thermal instability due to dynamic heat loads of the fundamental mode
  Integration of the couplers on the cavity equipped with its helium vessel
    Only Hook and Probe couplers are possible options
    Comparison of the impedances between 2H2P, 4H, 2H
Probe couplers don’t damp enough the monopole modes
Monopole modes are far from beam harmonics
Minimum ratio for 2H > 10
Higher impedances were achieved through more detailed simulations (complete HPC, 2 cavities)
Ratio = Zcalc / Zth
Longitudinal impedance of dangerous monopole modes:
Dipole modes well damped by Hook couplers
Dipole modes are quite close to the beam harmonics
Minimum ratio for 2H > 7
Transversal impedance of dangerous dipole modes:

## Slide 7: DESIGN OF THE HOM COUPLER
5-cell cavity with 2 Hook couplers in the cryomodule
FROM THE RF DESIGN TO THE MECHANICAL DESIGN
Coupler with a High RRR Nb antenna :
  A standard RF feedthrough
  A Helium tank to provide an active cooling circuit@2K
  CF flanges to have a precise positioning
  The closest position to the endcell while allowing the integration of the helium vessel of the cavity
Sensitivity studies performed on geometrical parameters to define requirements on the geometrical tolerances
Validation of the mechanical design: iterative process combining RF, thermal and mechanical analyses
Based on 800 MHz Hook coupler for HL-LHC optimized:
  The best transmission at TE111 & TM110 passbands
  The rejection of the Fundamental mode
  Including some geometrical constraints
Standard RF feedthrough
Cu top antenna
Nb antenna
Nb Outer conductor
Helium Tank
CF50 Flange
CF16 Flange
Hook Coupler for PERLE:

## Slide 8: RF CABLE
Static heat loads: Thermal conduction from the ambient temperature
  No thermalization of the RF cable: 145 mW @2K
  With a thermalization at 50K: < 100 mW @2K
Type RG142
As the extracted HOM power by the coupler is evaluated to a few watts, a RF cable type RG142 is being considered:
  Its small diameter limits the static heat loads,
  Its length is limited to reduce the dynamic heat contribution.
CHOICE OF THE RF CABLE
Dynamic heat loads: RF losses along the RF cable
Dynamic heat loads:
    with Pext = Extracted RF power by the HOM coupler (=2W)
0,83 dB/m @RT
0,25 dB/m @2K
Evaluation of the attenuation of the RF cable as a function of temperature
Attenuation @3GHz
No thermalization of the RF cable: 420 mW @2K, T°max = 380K
With a thermalization at 50K: < 150 mW @2K, T°max = 300K
T = 337K
T = 476K = 203°C
T = 364K
Thermalization at the centre
Temperature of the cable inside the cryomodule as a function of HOM power extracted
Extremity on the Cryomodule side
Extremity on the HOM coupler side
Thermal. 50K
Measurements will be realized in cryostat to validate the choice of RF cables
Thermal straps @2K will be also added to reduce heat loads on the HOM coupler

## Slide 9: MECHANICAL DESIGN OF THE HOM COUPLER
Thermal and Mechanical analyses
        Resistance to the helium bath pressure (MAWP=1,5 barg)
        Low temperature range achieved
        Acceptable thermal contractions and stresses
Cooling down (static heat loads, no LHe in the coupler tank):
Static heat loads [mW] | 100
Dynamic heat loads [mW] | 490+150
 Total heat loads [mW] | 740
Dissipated by: | 
Cavity LHe@2K [mW] | 5
Coupler LHe@2K [mW] | 735
Gap reduction 0.06mm
Gap reduction 0.05mm
Gap reduction 0.04mm
2.8K
4.8 K
30K
No liquid helium
        Static heat loads
        = 100 mW
Cavity @2K
Thermal contractions
T° achieved after cooling down
4.8K
        all heat loads
        = 100 mW + 150 mW
Liquid helium
Cavity @2K
T° in nominal condition
Nominal condition (all heat loads, LHe in the coupler tank):
  Heat loads from the RF cable: 100 mW + 150 mW
  Dynamic heat loads due to fundamental mode (FM) on walls and dielectrics (strongly depend on the Niobium T°)
H field & E field @Eacc = 22.4 MV/m
Hmax = 1.6x104A/m
Bmax = 21mT
In the ceramic
Emax = 0.05 MV/m
        Niobium parts remain superconducting
        Dynamic heat loads due to FM: 490 mW (including 40mW on hook antenna)
        Heat loads dissipated in LHe tank: 735 mW

## Slide 10: COOLING CIRCUIT
COOLING CIRCUIT @2K
Heat extraction capacity
  Evaluation of the maximum heat flux extracted before boiling:
He II
He I
Vapor
Tsat
Psat
T
Psat + gh
  Hydrostatic pressure gives the maximum variation of temperature T
Capacity of heat transport limited by the section 1
  if 2-phase tube is half full
  if 2-phase tube is quarter full
Capacity of heat transport = 2 to 3 times the total heat loads (735 mW)
Section 2
Section 3
H2
Section 1
H1
H3
100
Cooling circuit for HOM coupler
2-phase tube
Pipe 16
Single pipe connecting the coupler helium vessel to the 2-phase tube (saturated helium bath)
  Use of the equivalent thermal conductivity of Superfluid Helium in a channel:
Gorter-Mellink law:
He II
Tw
Tc
L

## Slide 11: CONCLUSION and OUTLOOK
A damping scheme with only 2 Hook couplers is selected to start PERLE
A mechanical design of Hook coupler equipped with a helium tank is proposed
The heat extraction capacity of the cooling circuit is compatible with the estimated static and dynamic heat loads
Fabrication of 4 HOM Couplers by CERN:
  Detailed manufacturing studies in progress
  Manufacturing in 2026
Test of HOM couplers at IJCLab scheduled for the end of 2026:
  Measurement campaign on the copper 5-cell cavity at room T°, based on
  the experimental setup proposed by C. Barbagallo and H. Wang (2023)
Fabrication of a mock-up helium tank and its circuit to validate the cooling system (Beginning of 2026)
Integration on the cavity string (End of 2027)
Copper 5-cell cavity fabricated at Jlab (2023)

## Slide 12
Thank you for your attention