## Slide 1: Evanescent mode coupling in coaxial HOM filters
Kai Papke
DESY
ICFA Workshop on High Order Modes in Superconducting Cavities 2025
DESY, Hamburg, Germany - 6-8.10.2025
Acknowledgments:
Thomas Flisgen1, Frank Gerigk2, Graeme Burt3, Ursula van Rienen4, Hermann Pommerenke2
1BTU Cottbus and FBH, 2CERN, 3Lancaster University, 4University of Rostock

## Slide 2: Introduction

## Slide 3: Introduction
Some thoughts on the course of history
[E. Haebel, Part. Accel. 40, 141 (1992)]

## Slide 4: Introduction
Era of Numerical simulations tools yield a zoo of coaxial HOM couplers but ...
  Choice a suitable topology remains doubtful
  Systematic design typically based on exhaustive parameter variations
  Black box behavior hinder in understanding the origin of particular filter characteristics (parasitic and non-parasitic phenomena)
Some thoughts on the course of history
LHC HOM couplers [CERN]
B. P. Xiao, et al. DQW-CC HOM Coupler,
De Silvia, et al., RFD-CC HHOM Coupler
Q. Wu, et. al., HOM Damper for 56MHz SRF Cavity for RHIC
J. Sekutowicz, et. al. , HERA, TESLA, ...
Notes: no conclusions on topology or topological improvements
Most designs quite similar from from the equivalent circuit
Basic equivalent elements are shunt L, series C and shunt LC (shunt = connection inner and outer conductor, series = along the inner conductor)
Some combinations cause parasitic intersection of stop eventually narrowing the notch filter (TESLA and DQWCC HOM couplers)
Coupling of evanescent modes is another phenomenon but non-parasitic
New Class of coaxial filters with canonical topology and elaborated design procedures given complete understanding

## Slide 5: Introduction
Common to many HOM couplers is a parasitic behavior below notch
Notch filter seem to be placed within the pass-band of a high-pass filter
Intrinsic property given by combination series notch filter (L0C0) and fixing of inner conductor (L1)
Motivation
W. Xu, et. al., in Proc. PAC 2011 , TUP060
J. Mitchel, PhD thesis 2019
RF Transmission of modified TESLA Coupler
RF Transmission of DQWCC HOM Coupler
How to avoid this combination?
K. Watanabe, et. al., NIM Sec. A, 2008
Notes: rf transmission by means of the examples on the left
Some words on equivalent elements:
  Fixing of inner conductor equivalent to inductance
  Notch filter in most designs equivalent to Series LC circuit connecting inner and outer conductor
How to avoid this combination?
  Fixing strictly necessary to hold inner conductor
  Abandon notch filter makes coaxial HOM couplers useless; other damping schemes more preferable (e.g. rect. or ridged wg)

## Slide 6: Introduction
Motivation
R. Ainsworth, in Proc. IPAC2012, WEEPPB008
W. Xu, in Proc. PAC2011, TUP060
Q. Wu, et. al., HOM Damper Design ..., BNL, 2010
Q. Wu, et. al., Operation of the 56 MHz superconducting rf cavity in RHIC with higher order mode damper, PRAB 22, 102001 (2019)
Some HOM couplers reveal an “unusual” notch characteristic
In contradiction to equivalent circuits based on alternating shunt inductance and series capacitance (only notch at f = 0 Hz possible)
What is the origin of the notch(es)?
Notes: Couplers 1 and 2 do NOT suffer from parasitic behavior of previous slide

## Slide 7: Phenomenological investigations
Towards an understanding of the “unusual” notch in coaxial lines

## Slide 8: Phenomenological investigations
Analysis of waveguide obstacles and discontinuities by numerous model fits
Focus on elements that are appropriate for high-pass filters, i.e. equivalent behavior of:
Ladder of shunt inductance and series capacitance will NOT introduce a notch at a frequency > 0
Topology, filter components, and equivalent circuits
f0 = 0
f0 = 0
f0 > 0
f0 > 0
Coaxial guide with capacitive gap between two inductive posts
Notes: Simplest microwave structure common to previous designs on primary focus
Angle variation not present in Wu’s and Ainsworth’s designs
Fit by intuitive equivalent circuit fails -> assumption by previous authors definitely wrong

## Slide 9: Phenomenological investigations
Analysis of waveguide obstacles and discontinuities by numerous model fits
Focus on elements that are appropriate for high-pass filters, i.e. equivalent behavior of:
Parallel LC resonator yield perfect match between equivalent circuit model and simulation data over large frequency range
Topology, filter components, and equivalent circuits
f0 = 0
f0 = 0
f0 > 0
f0 > 0
Coaxial guide with capacitive gap between two inductive posts
Notes: Perfect match of parallel LC applies of course only up to a certain frequency as shown later
Hovever, below that frequency, the fit appears to be exact

## Slide 10: Phenomenological investigations
Canonical 3rd-order high-pass filter with finite transmission zero at f0 >= 0
Remarkable variation of by orders of magnitude with dfix and α
L0 nearly constant over large frequency well above notch frequency -> broad band character
Indicators for coupled evanescent modes
Equivalent circuit and element characteristics
Coaxial guide with capacitive gap between two inductive posts
Dependency of notch filter elements
Notes: Actually sub-canonical since microwave structure has less physical elements than equivalent circuit
3rd order filter extendable by feed through capacitance to 4th order -> already comparable or superior to TESLA, LHC, and most other couplers
Transmission zero at f=0 if alpha = 90deg
constant L0 allows for broad band character (L1, L2, C0 are anyway constant but Tlines are the limiting factor)
small distance dﬁx favorable to reduce impact of transmission lines
Broad band matching is limited by the frequency band over with equivalent circuit elements behave constant

## Slide 11: Phenomenological investigations
Repetition of “T”-element in part analog to repetition of alternating shunt inductance and parallel LC resonator in series
Scalability of the filter order
3rd order filter
5th order filter
7th order filter
Propagation of 1st HOM
Notes: In general evanescent modes coupling occurs also between non-neighboring fixings (inductive posts)
Equivalent circuit must be reassessed but ...
There is evidence of equivalence: 3 examples indicate similar scaling behavior as alternating shunt inductance and parallel LC circuit
Bandwidth is limited by cutoff of the first HOMs

## Slide 12: Phenomenological investigations
Repetition of “T”-element in part analog to repetition of alternating shunt inductance and parallel LC resonator in series
Scalability of the filter order
3rd order filter
5th order filter
7th order filter
Notes: In general evanescent modes coupling occurs also between non-neighboring fixings (inductive posts)
Equivalent circuit must be reassessed but ...
There is evidence of equivalence: 3 examples indicate similar scaling behavior as alternating shunt inductance and parallel LC circuit
Bandwidth is limited by cutoff of the first HOMs

## Slide 13: Field Analyses
On the interference of evanescent modes in coaxial wave guides

## Slide 14: Field analyses
Concatenation procedure based on scattering properties (CSC)1
Excited modes and their superposition at a single inductive post
Inductive post defines polarization angle of the excited TEmn mode
Exploration of contributing modes
1H.-W. Glock, et. al., CSC—A Procedure for Coupled S-Parameter Calculations, IEEE Transaction on Magnetics, Vol. 38, No. 2, 2002
...
...
TEM mode
TEM mode
N modes
N modes
...
N modes
Rotation
TEM
TE11
TE21
TEM+TE11
TEM+TE11+TE21
Notes: Comparison of complete and concatenated structure with varying number of modes (N) in between the segments
Rotation matrix is analytical incorporates impact of the rotation angle alpha (only a characteristic part of the matrix is shown)

## Slide 15: Field analyses
Presence of modes depends on filter order
Coupling of evanescent modes vanishes if orthogonality applies
  @ α=45deg, Inference of TE21 disappears below its cutoff
  @ α=90deg, Inference of TE11 disappears below its cutoff
Properties related to the coupling of evanescent modes
3rd order filter
5th order filter
7th order filter
TEM
TE11
TEM
TE11
TE21
TEM
TE11
TE21
  -> Parallel LC resonator reduces C in equivalent circuit
Notes: In general evanescent modes coupling occurs also between non-neighboring fixings (inductive posts)
Equivalent circuit must be reassessed but ...
There is evidence of equivalence: 3 examples indicate similar scaling behavior as alternating shunt inductance and parallel LC circuit
Bandwidth is limited by cutoff of the first HOMs

## Slide 16: Field analyses
Consistency of L0 over notably large frequency range results from dependency of the TE11 cutoff frequency
Large adjustment range of L0 results from the nearly inverse dependency of the coupling factor between evanescent modes
Properties related to the coupling of evanescent modes
microwave structure and equivalent circuit
Coupling factor dependency
L0 Consistency and Cutoff dependency
L0 µ k-1 (coupling factor k µ cosα)
Notes: These properties are verified for the 3rd order realization

## Slide 17: Filter design
Some thoughts on rudimentary approaches

## Slide 18: Filter design
If equivalent circuits exists, methods of network synthesis can be applied, particularly by means of ladder networks
Example of a third-order elliptic high-pass filter (704 MHz SPL)
Synthesis based on fitting equivalent circuits
Approximation problem
Network synthesis
Model fitting
Notes: Transmission lines must be includes
Equivalent circuits for filter order >=5 mus be revealed
First approach for the synthesis of transfer functions by means of coaxial microwave structures
still rudimentary but the principle has been proven

## Slide 19: Filter design
Numerical optimization of parameterized segments using CSC
Fully consistent to complete structure provided the necessary modes are involved
3D field simulations replaced by matrix multiplications and solving small linear matrix equations given the minimal order representation of the problem
Synthesis based on concatenation of scattering matrices
...
...
TEM mode
TEM mode
N modes
N modes
...
N modes
Rotation
Notes: Method resulting from the angle analyses of the various structures (3rd, 5th, and 7th order)

## Slide 20: Conclusion

## Slide 21: Conclusion
Canonical topology -> Filter realization with minimal effort
High-pass realization without parasitic effects below TE11 cutoff
No need of large notch filter capacitance or series LC resonator
Remarkable larger adjustment range of filter functions (equivalent circuit elements) in comparison to existing coupler designs
In general compact design due to evanescent character
Independent treatment of beam pipe/ cavity coupling and notch
Broad band character -> matching focus: beam pipe/ cavity coupling
Dismountable coupler designs
Systematic design in principle without 3D numerical simulations
Evanescent mode coupling in coaxial HOM couplers allow for ...
W. Xu, et. al., in Proc. PAC 2011 , TUP060
B. P. Xiao, et al. DQW-CC HOM Coupler,
B. P. Xiao, et al., in Proc. SRF2013
Notes: Below TE11 cutoff can be a very large frequency range
Most existing couplers require 3D simulations

## Slide 22: Outlook
Thank you very much
Equivalent circuits including quadrupole modes and simplifications for filter synthesis
Investigate the scalability of the filter order and limits in more detail
Refine and automatize design processes from filter function to microwave structure
Experimental studies and application in real facilities
Still a lot of work to do ...

## Slide 23: Extra slides

## Slide 24: Introduction
Analysis of numerous obstacles and discontinuities by model fitting
Focus on elements that are appropriate for high-pass filters, i.e. equivalent behavior of
Ex: Capacitive gap in coaxial guide
  analytical or empirical approximation:
RF Filter Components, Equivalent Circuits, and Topology
Coaxial line with capacitive gap
LP [nH]
dgap [mm]
dgap
[Matthaei et. al, “Microwave Filters, Impedance-Matching Networks, and Coupling Structures”]

## Slide 25: Introduction
Analysis of numerous obstacles and discontinuities by model fitting
Focus on elements that are appropriate for high-pass filters, i.e. equivalent behavior of
Ex: Inductive post in coaxial guide
  analytical or empirical approximation:
Some thoughts on Filter theory and coaxial lines
Coaxial line with inductive post
LP [nH]
[Matthaei et. al, “Microwave Filters, Impedance-Matching Networks, and Coupling Structures”]

## Slide 26: Coaxial Couplers and Synthesis
No coupling due to vanishing fields at coupler location (resonance in cutoff tube)
Independent of coupler design
Influenced by waveguide, taper and coupler location
Ensure distance from HOMs
Transmission Zeros in Cutoff Tubes
TEM-TE11 transmission
TEM-TM01 transmission
Cavity side | r1 [mm] | r2 [mm] | lt [mm] | l0 [mm] | f1 [GHz]
Tuner | 65 | 40 | 28 | 30 | 1.85-1.96
FMC | 70 | 40 | 34 | 59 | 1.68-1.74
Transmission zeros of the high- SPL cutoff tubes
Probe antenna mounted on cutoff tube

## Slide 27: Coaxial Couplers and Synthesis
Analysis of numerous obstacles and discontinuities by model fitting
  understanding of individual components of HOM couplers
  basis for topological choice, synthesis, and numerical optimizations
  equivalent behavior of capacitive gap between two inductive posts as a mid-shunt ladder possibly not documented so far
First approach for the synthesis of transfer functions by means of coaxial microwave structures
  still rudimentary but the principle has been proven
Understanding of transmission zeros in cutoff tubes
  transmission zeros of SPL cutoff tubes not harmful
Summary and Conclusions

## Slide 28: Coaxial Couplers and Synthesis
non-linear least square problem
Example coaxial guide with capacitive gap between two inductive posts
Equivalent Circuit Parameter Characterization of RF Filter Components
scattering [dB]
phase shift
freq. domain simulation
2-port parameter transformation