## Slide 1
Notes: Slide 1: Company Logo Full Page
Before you start editing the slides of your talk change to the Master Slide view:
Microsoft Office :Menu: View > Slide Master;
Macintosh – View > Master > Slide Master
Edit the following items:
On the Slide Master (first master slide) – lower area
a) On the left Delete the text and write the title of the event/Conference, Location
b) On the right delete the text and write the name and surname of the speaker and the date (day, month , year)
Close Master View

## Slide 2: QMiR Cavities RF Analysis
Nuaman Shafqat
On behalf of
Elettra team
Elettra Sincrotrone Trieste
Notes: Slide 2: Title of the Presentation
Before you start editing the slides of your talk change to the Master Slide view:
Microsoft Office :Menu: View > Slide Master;
Macintosh – View > Master > Slide Master
Edit the following items:
On the Slide Master (first master slide) – lower area
a) On the left Delete the text and write the title of the event/Conference, Location
b) On the right delete the text and write the name and surname of the speaker and the date (day, month , year)
Close Master View
To start adding slides insert a new slide and select a Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank

## Slide 3
ELETTRA, 2-2.4 GeV SRLS:
in operation since 1994
FERMI, 1.5 GeV FEL:
in operation since 2010
Elettra Sincrotrone Trieste is an international multidisciplinary research centre of excellence, open to the international research community, featuring a 2.0/2.4 GeV, third-generation synchrotron light source (Elettra), a free-electron laser light source (FERMI) and a variety of support laboratories.
Shut down in July for major upgrade
Elettra Sincrotrone Trieste

## Slide 4
Almost all experimental techniques gain from either a large 6-D photon density (brilliance) or a large coherent flux (degeneracy parameter):
for
Diffraction Limit
ICS
4GSR
and
More flux at the sample, for any given -range
Higher -harmonics by means of low-gap IDs
Shorter integrated time of measurement
Micro- and nano-focusing
Transverse x&y coherence up to 1 keV
Elettra 2,0
Diffraction Limit

## Slide 5
Parameter | Elettra 2.0 | Crab Cavities | FERMI | Units
Spectral range | 0.02 - 50 | 0.1 - 10 | 0.01 – 0.7 | keV
Rep. rate | 1 – 400 | 0.1 – 1 | 0.05 | MHz
Pulse duration, rms | 30 | 0.5 – 2 | 0.005 – 0.1 | ps
Flux at sample, ave | 106 – 1013 | 105 – 109 | 109 – 1013 | ph/sec
Spectral resolution | 10-5 – 10-4 | 10-4 | 10-4 – 10-3 (w/o mono) | 
Polarization | all | all | all | 
Coherence | Hor. ≤ 1 keV | Hor. < 0.5 keV | full | 
# Beamlines / Run | 31 | < 10 | < 2 | 
Elettra 2,0
Timing Mode

## Slide 6
Two transverse deflecting cavities
Fundamental RF f = 500 MHz
For 6 and 6.5th harmonic: f1 = 3.0 GHz and f2 = 3.25 GHz
For the exact cancellation at the centre of the bunch
Deflecting slope:
: are angular wave numbers, are deflecting voltages, e is electron charge while E is beam energy.
Elettra 2.0
1- frequency tilt & cancel
The bunch is crabbed at it passes through zero-crossing of transverse deflecting cavities

## Slide 7
Fill pattern:
200 regular bunches, 2 mA/bunch, 4 ns-time sep.
1 tilted bunch, 2 mA , 32 ns time sep., 1.157 MHz
Pulse selection:
  Temporal gating
  distorted orbit
  chopper
A. Lunin et al., Phys. Proc. 79 (2015) 54.
A. Lunin, T. Khabiboulline, V. Yakovlev , “A White Paper on Design and Fabrication of SRF Deflecting Cavities for Elettra 2.0”, FNAL note.
A. Zholents, NIM A 798 (2015) 111
See also: X. Huang, PRAB 2016, 2019, 2023
Crab Cavities:
Working Principle

## Slide 8
Elettra
ANL
(A. Zholents, X. Huang)
SLAC
FERMILAB
NC
SC
SC
white papers
Panel Review
(A. Fabris chair)
Strategic Project Agreement
Strategic Project Agreement
Requirements
Voltages, frequencies
Length, size
Apertures
Material
Temperature
Loss factor, kick factor
 | Voltage (MV) | f (GHz)
Cavity 1 | < 1.5 (2.0) | 3.0
Cavity 2 | < 1.2 (1.8) | 3.25
Shunt impedance HOMs below cutoff frequency | 
Vertical plane | <1.5 (MΩ/m)
Horizental plane | <4.0 (MΩ/m)
Longitudinal plane | <0.4 (MΩ/m*GHz)
  feasibility of achieving the performance
  duration of the design work
  cost of the design work
  anticipated cost of operation and maintenance
  identify risks
Decision of SC technology
Project planning
(AF, SDM)
Beam physics
(SDM, KM & al.)
RF design
(NS)
SC & Cryogenics
(MM, PZ)
Elettra 2.0 team
Ref. A. Fabris
Project Evaluation

## Slide 9
  Optimization of the FermiLab/ANL prototype to 3.0 GHz and 3.25 GHz, larger apertures, lower HOMs, and weaker multipoles.
  RF source input power < 500 W per cavity.
  3 pure-Nb cavities @ 4,5 K (extension of the Elettra 3HC cryogenic system).
Quasi-waveguide Multicell Resonator (QMiR) designed for 2.815 GHz frequency for APS-U@ANL. Cavity successfully tested @2K in a vertical cryostat, demonstrated a 2.6 MV transverse voltage.
A. Lunin, T. Khabiboulline, V. Yakovlev , “A White Paper on Design and Fabrication of SRF Deflecting Cavities for Elettra 2.0”, FNAL
Best cancellation of residual kicks for standard bunches
QMiR Design:
FNAL-Elettra-CERN
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 10: Explanation of The Model Proposed Configuration
Available space = 2.5 m |  |  | 
 | f [GHz] | D.V. [MV] | % change in D.V. @ 5.0 mm offset
Cav. 1 | f1: 3.0 | V1: 1,5 | ≤10 %
Cav. 2 | f2: 3.25 | V2: 1.2 | ≤10 %
Shunt impedances HOMs below cutoff |  | 
Vertical | <1.5 | (MΩ/m)
Horizontal | <4.5 | (MΩ/m)
Longitudinal | <5,0 | (MΩ*GHz)
Short range wakefields |  | 
Loss factor | 4 | (V/pC)
Horizontal kick factor | 1.3 | (V/pC/mm)
Vertical kick factor | 1.3 | (V/pC/mm)
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 11: QMiR Elettra Geometry
Stub_dist
WG_l
72.136 mm
Stub_dist
Stub_dist
WG_d
WG_l | 400 mm | 400 mm
Stub_dist | 12,50 mm | 13,95 mm
WG_d | 37,86 mm | 37,86 mm
Coupler_w | 28,70 mm | 22 mm
WG_l | 400 mm | 400 mm
Stub_dist | 12,50 mm | 13,95 mm
WG_d | 37,86 mm | 37,86 mm
Coupler_w | 28,70 mm | 22 mm
Stub shape
18 mm
WG_d
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 12
QMiR Elettra
Fundamental Mode
E field (side view)
Cav.1
H field (top view)
E field (contour)
H field (contour)
Cav.2
E field (side view)
H field (top view)
E field (contour)
H field (contour)
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 13: QMiR Elettra Geometry cav1 n cav2
 | Version F @ 3.0 GHz | Version F @ 3.25 GHz | 
 | 959,30 | 587,75 | Ω
 | 22,97 | 41,13 | MV/m
 | 49,09 | 85,56 | mT
Dy variation | 5.94% | 5,98% | 
G factor | 103,87 | 112,56 | 
 | Version F @ 3.0 GHz | Version F @ 3.25 GHz | 
 | 959,30 | 587,75 | Ω
 | 22,97 | 41,13 | MV/m
 | 49,09 | 85,56 | mT
Dy variation | 5.94% | 5,98% | 
G factor | 103,87 | 112,56 | 
E_peak & B_peak are scaled for 0,75 MV for Cav.1 & 1,2 MV for Cav.2
Cav.1
Cav.2
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 14: QMiR Elettra Geometry cav1 n cav2
Cav.1
Chart: offset [mm]
| 0 | 0.25 | 0.5 | 0.75 | 1 | 1.25 | 1.5 | 1.75 | 2 | 2.25 | 2.5 | 2.75 | 3 | 3.25 | 3.5 | 3.75 | 4 | 4.25 | 4.5 | 4.75 | 5
Vy(y) | 3.3947 | 3.4012 | 3.4076 | 3.4139 | 3.4201 | 3.4262 | 3.4321 | 3.4381 | 3.4456 | 3.4545 | 3.465 | 3.4763 | 3.4869 | 3.4983 | 3.5118 | 3.5264 | 3.5411 | 3.5549 | 3.5685 | 3.5828 | 3.5984
Vy(x) | 3.3947 | 3.3944 | 3.3934 | 3.3914 | 3.3883 | 3.3841 | 3.3786 | 3.37 | 3.3601 | 3.3489 | 3.3369 | 3.3239 | 3.3099 | 3.295 | 3.2789 | 3.2613 | 3.2418 | 3.221 | 3.1951 | 3.1666 | 3.1367
Chart: offset [mm]
| 0 | 0.25 | 0.5 | 0.75 | 1 | 1.25 | 1.5 | 1.75 | 2 | 2.25 | 2.5 | 2.75 | 3 | 3.25 | 3.5 | 3.75 | 4 | 4.25 | 4.5 | 4.75 | 5
Vz(y) | 451.0389 | 58200 | 116200 | 174000 | 232000 | 291000 | 349000 | 408000 | 466000 | 525000 | 583000 | 642000 | 702000 | 762000 | 823000 | 884000 | 945000 | 1006000 | 1070000 | 1127000 | 1190000
Vz(x) | 451.0389 | 519.895 | 555.583 | 505.147 | 441.69 | 400.78 | 288.138 | 234.67 | 166.25 | 111.97 | 120.128 | 146.18 | 203.734 | 278.6468 | 347.95 | 370.466 | 249.78 | 88.68 | 103.998 | 224.42 | 233.954
Chart: offset [mm]
| 0 | 0.25 | 0.5 | 0.75 | 1 | 1.25 | 1.5 | 1.75 | 2 | 2.25 | 2.5 | 2.75 | 3 | 3.25 | 3.5 | 3.75 | 4 | 4.25 | 4.5 | 4.75 | 5
R/Qy(PW) | 564.2267 | 566.5742 | 568.729 | 570.602 | 572.1949 | 573.289 | 574.125 | 574.575 | 574.8589 | 575.059 | 575.8635 | 577.6835 | 580.1744 | 583.3668 | 586.41 | 589.059 | 591.0976 | 592.898 | 594.5597 | 595.6546
R/Qy(LM) | 564.774 | 564.774 | 564.774 | 564.774 | 564.774 | 564.774 | 564.774 | 564.774 | 564.774 | 564.774 | 564.774 | 564.774 | 564.774 | 564.774 | 564.774 | 564.774 | 564.774 | 564.774 | 564.774 | 564.774
Chart: Offset [mm]
| 0 | 0.25 | 0.5 | 0.75 | 1 | 1.25 | 1.5 | 1.75 | 2 | 2.25 | 2.5 | 2.75 | 3 | 3.25 | 3.5 | 3.75 | 4 | 4.25 | 4.5 | 4.75 | 5
Vy(x) | 4.1466 | 4.1469 | 4.1459 | 4.1438 | 4.1406 | 4.1363 | 4.1303 | 4.1211 | 4.108 | 4.093 | 4.0765 | 4.0582 | 4.0393 | 4.0188 | 3.997 | 3.9795 | 3.9495 | 3.9238 | 3.8966 | 3.8682 | 3.8375
Vy(y) | 4.1466 | 4.1534 | 4.16 | 4.1664 | 4.1726 | 4.1784 | 4.1842 | 4.1905 | 4.2022 | 4.2148 | 4.2278 | 4.2415 | 4.256 | 4.2708 | 4.2873 | 4.3078 | 4.3287 | 4.3476 | 4.3647 | 4.3794 | 4.3936
Chart: Offset[mm]
| 0 | 0.25 | 0.5 | 0.75 | 1 | 1.25 | 1.5 | 1.75 | 2 | 2.25 | 2.5 | 2.75 | 3 | 3.25 | 3.5 | 3.75 | 4 | 4.25 | 4.5 | 4.75 | 5
Vx(x) | 88.651 | 104.284 | 217.073 | 347.416 | 378.685 | 314.52 | 227.849 | 1.2288 | 448.971 | 8.3488 | 1145.9 | 1375.08 | 1515.25 | 1572.21 | 1444.7 | 1337.5 | 1337.5 | 1184.82 | 972.74 | 716.1 | 464.428
Vx(y) | 88.651 | 65500 | 131000 | 197000 | 262300 | 327000 | 393760 | 459655 | 526226 | 593157 | 660352 | 728000 | 795000 | 862000 | 930000 | 997000 | 1060000 | 1130000 | 1200000 | 1270000 | 1340000
Chart: offset [nmm]
| 0 | 0.25 | 0.5 | 0.75 | 1 | 1.25 | 1.5 | 1.75 | 2 | 2.25 | 2.5 | 2.75 | 3 | 3.25 | 3.5 | 3.75 | 4 | 4.25 | 4.5 | 4.75 | 5
R/Qy_LM | 912.173 | 912.173 | 912.173 | 912.173 | 912.173 | 912.173 | 912.173 | 912.173 | 912.173 | 912.173 | 912.173 | 912.173 | 912.173 | 912.173 | 912.173 | 912.173 | 912.173 | 912.173 | 912.173 | 912.173 | 912.173
R/Qy_PW | 919.135 | 919.135 | 920.803 | 921.967 | 922.664 | 923.147 | 924.207 | 925.462 | 928.703 | 932.356 | 936.035 | 939.181 | 941.468 | 943.833 | 946.612 | 947.665 | 949.731 | 951.668 | 954.057 | 957.146 | 959.3
Cav.2
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 15: QMiR Elettra Geometry (Cav.1)
Cav.1
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 16: QMiR Elettra Geometry (Cav.2)
Cav.2
Chart: Freq [GHz]
| 2.5 | 4.73698 | 4.7946600000000004 | 4.8676700000000004 | 5.4626200000000003 | 5.5841399999999997
PerfH | 234.061 | 237.32 | 1752.9 | 555.077 | 1652.38
PerfE | 6764.44 | 18931.2 | 324152 | 739.531 | 149.974 | 364.405 | 5720.06
Chart: 
| 2.5 | 4.73698 | 4.7946600000000004 | 4.8676700000000004 | 5.4626200000000003 | 5.5841399999999997
R/Qx PMC | 0.1676 | 2.3746 | 0.3002 | 1.8536 | 0.000415
R/Qy PMC | 1.37e-05 | 0.83985 | 0.04627 | 2.8568 | 0.042009
R/Qz PMC | 0.10699 | 73.3093 | 14.9073 | 98.7101 | 35.8306
R/Qx PEC | 4.24e-05 | 0.000272 | 1.35e-05 | 6.94e-08 | 3.93e-06 | 2.95e-05 | 4.31e-06
R/Qy PEC | 2.74 | 7.25 | 590.128 | 0.1298 | 0.03389 | 0.008206 | 0.001369
R/Qz PMC | 1.55e-06 | 4.39e-06 | 9.81e-07 | 1.95e-09 | 1.95e-07 | 2.99e-07 | 1.84e-06
Chart: σ=4,5mm/15ps
| 4.73698 | 4.7946600000000004 | 4.8676700000000004 | 5.4626200000000003 | 5.5841399999999997
Rz PMC | 9.7188e-05 | 0.068009 | 0.10306 | 0.22962 | 0.25063 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Rz PEC | 0 | 0 | 2.7282e-08 | 2.3242e-07 | 9.4055e-07 | 4.9675e-12 | 1.2934e-10 | 4.8535e-10 | 4.6972e-08 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Rx PMC | 0.0031886 | 0.046138 | 0.043465 | 0.090306 | 6.0797e-05 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Ry PMC | 2.6064e-07 | 0.016318 | 0.0066993 | 0.13918 | 0.0061542 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Rx PEC | 0 | 0 | 1.5631e-05 | 0.0003016 | 0.00027109 | 3.7027e-09 | 5.4594e-08 | 1.0029e-06 | 2.3044e-06 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Ry PEC | 0 | 0 | 1.0101 | 8.039 | 11850.035 | 0.0069253 | 0.00047078 | 0.00027898 | 0.00073195 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 17: QMiR Elettra 3 cav System
1
Cav.2
Cav.1
Cav.1
cav1
cav1
cav2

## Slide 18: QMiR Elettra 3 cav System (HOMs)
Cav.2
Cav.1
Chart: Freq [GHz]
R/Qx PEC | 0.00040837 | 1.49e-07 | 0.0001575 | 3.67e-05 | 0.0001877 | 0.0004725 | 0.000127 | 3.37e-05 | 1.64e-05 | 1.61e-06 | 1.33e-09 | 3.64e-06 | 5.1e-06 | 6.36e-07 | 1.62e-06 | 4.81e-06 | 4.14e-05 | 7.4e-06 | 1.96e-07 | 7.62e-06 | 2.18e-05 | 3.89e-07 | 5.01e-07 | 0.0001206 | 1.7e-05 | 1.998e-06 | 8.04e-07 | 5.14e-06 | 4.1e-10 | 2.18e-07 | 2.93e-06 | 1.23e-06 | 3.29e-07 | 3.75e-05 | 1.65e-06 | 3.36e-07 | 5.37e-07 | 1.27e-06 | 2.28e-06
R/Qy PEC | 0.51458 | 4.6879 | 2.79 | 2.5589 | 18.41 | 954.5898 | 959.555 | 7.1504 | 589.78 | 0.2334 | 0.002983 | 1.258 | 1.7171 | 0.43506 | 0.881 | 15.553 | 0.0037586 | 31.3259 | 0.087278 | 0.64029 | 1.1059 | 0.1349 | 6.1336 | 33.035 | 5.52 | 65.8 | 0.06383 | 0.0012644 | 0.0234 | 0.0169 | 13.25 | 0.021176 | 0.00095579 | 4.439 | 0.03179 | 4.63e-06 | 0.00125 | 1.0554 | 2.1742
R/Qz PEC | 1.14e-06 | 3.5855e-05 | 6.45e-06 | 5.65e-06 | 1.98e-07 | 2.43e-05 | 1.1235e-05 | 1.042e-05 | 1.44e-05 | 6.198e-07 | 5.123e-09 | 5.26e-07 | 9.4e-07 | 2.85e-07 | 3.19e-07 | 3.47e-06 | 8.18e-06 | 8.46e-07 | 1.01e-08 | 4.22e-06 | 7.48e-06 | 3.67e-06 | 8.23e-07 | 3.076e-05 | 3.4e-07 | 1.13e-05 | 2.7e-07 | 6.05e-08 | 6.95e-07 | 1.56e-06 | 2.73e-06 | 1.31e-06 | 7.78e-08 | 1.43e-06 | 8.033e-08 | 1.24e-09 | 5.7e-06 | 2.51e-07 | 6.46e-07
Chart: Freq [GHz]
Q_ext PEC | 5629 | 5629.75 | 6766.43 | 24420.4 | 24420.7 | 126000 | 126000 | 18937.2 | 324000 | 333022 | 1490000 | 53489.2 | 213558 | 8759.96 | 33464.3 | 720.416 | 1491.48 | 433.389 | 256.031 | 270.998 | 123.356 | 109.258 | 93.7942 | 157.853 | 145.413 | 547.342 | 444.069 | 443.367 | 1562.11 | 1553.56 | 597.051 | 133962 | 116128 | 790.288 | 92.6525 | 335.784 | 5336.33 | 619.902 | 1057.06
Chart: σ=4,5mm/15ps

## Slide 19: QMiR Elettra 3 cav System + CPR Tapers
1
Cav.2
Cav.1
Cav.1
cav1
cav1
cav2
Eliptical Profile
RhombiodalProfile
PEC
PEC
PEC
PEC
PEC
PEC
Copper
Copper
Copper
Copper
9mm
27mm
27mm
17mm

## Slide 20: QMiR Elettra 3 cav System + CPR Tapers
450 mm
cav1
150 mm
Copper tapers (150 mm)+2 rings
Copper tapers (450 mm)+2 rings
Copper tapers (350 mm)+2 rings
1350 mm
1750 mm
1950 mm

## Slide 21: QMiR Elettra 3 cav System + Tapers + CR
Chart: Freq [GHz]
Cav.2
Cav.1
Chart: Freq [GHz]
Copper tapers (150 mm)+2 rings
Copper tapers (450 mm)+2 rings
Chart: Freq [GHz]
Copper tapers (350 mm)+2 rings

## Slide 22: QMiR Elettra 3 cav System: R/Q Comparison
Chart: Freq [GHz]
Cav.2
Cav.1
Chart: Freq [GHz]
R/Qx PEC | 1.26e-05 | 0.00256 | 3.14e-05 | 6.23e-07 | 0.0004244 | 0.003489 | 2.91e-05 | 0.0051 | 0.0001148 | 0.00010025 | 2.69e-06 | 3.9e-05 | 6.73e-05 | 2.03e-06 | 5.23e-05 | 1.1226 | 8.46e-05 | 3.67e-05 | 8.81e-06 | 1.01e-05 | 2.24e-05 | 0.0015599 | 0.00051966 | 0.000864 | 6.73e-05 | 0.0018657 | 8.01e-08 | 2.19e-06 | 0.000117 | 8.77e-07 | 6.37e-05 | 0.00044 | 0.000299 | 8.34e-05 | 0.0004268 | 0.0001243 | 1.13e-06 | 5.23e-06 | 2.21e-07 | 9.45e-06 | 0.0002009 | 8.5e-05 | 0.000149 | 0.0002268 | 5.21e-05 | 2.47e-05 | 6.65e-06 | 8.001e-85 | 1.59e-05 | 1.42e-05 | 7.55e-05 | 3.4e-06 | 2.67e-05 | 7.54e-07 | 0.0002159 | 5.01e-06 | 2.51e-05 | 2.7e-06 | 0.0002102
R/Qy PEC | 0.4475 | 8.1728 | 2.609 | 2.2147 | 18.54 | 950.575 | 966.84 | 6.879 | 586.924 | 0.2216 | 0.0028394 | 0.1067 | 0.69488 | 1.2299 | 1.7604 | 0.4941 | 0.4206 | 0.4247 | 0.8531 | 0.11738 | 0.19749 | 14.75 | 1.9694 | 1.9279 | 0.0672 | 31.69 | 13.43 | 0.52906 | 0.00796 | 2.1756 | 2.4685 | 3.9694 | 1.1028 | 0.50305 | 11.3519 | 0.41399 | 5.5716 | 36.8353 | 2.715 | 2.7 | 0.2426 | 14.511 | 60.419 | 2.33e-05 | 0.005119 | 0.002356 | 0.041129 | 9.873 | 0.00756 | 0.0076 | 3.7569 | 13.6504 | 5.1768 | 0.0002125 | 0.001039 | 1.045 | 1.8674 | 8.2e-06 | 2.8325
R/Qz PEC | 6.84e-07 | 1.75e-07 | 6.36e-05 | 7.26e-06 | 7.01e-06 | 0.0001449 | 1.38e-06 | 8.37e-05 | 8.6e-05 | 2.73e-06 | 1.24e-07 | 5.08e-06 | 1.636e-05 | 2.61e-07 | 6.97e-07 | 9.19e-10 | 2.15e-05 | 1.4e-05 | 1.125e-05 | 3.61e-06 | 7.71e-05 | 0.00025096 | 2.266e-05 | 5.99e-05 | 1.92e-06 | 0.0001399 | 1.029e-08 | 1.96e-05 | 4.43e-07 | 1.43e-05 | 6.44e-06 | 2.45e-05 | 5.9e-07 | 2.24e-06 | 5.62e-05 | 3.19e-05 | 9.35e-07 | 2.27e-05 | 3.74e-06 | 3.35e-06 | 1.04e-05 | 3.05e-06 | 3.22e-06 | 6.05e-05 | 7.21e-06 | 2.07e-05 | 1.77e-05 | 7.11e-06 | 4.16e-07 | 1.2e-06 | 2.74e-05 | 2.22e-05 | 4.45e-08 | 8.53e-06 | 1.81e-06 | 1.5e-05 | 2.01e-06 | 6.73e-08 | 1.46e-05
Chart: Freq [GHz]
R/Qx PEC | 0.0001789 | 0.0018688 | 3.14e-05 | 5.06e-05 | 0.00074256 | 0.000158 | 0.00226 | 0.00148 | 0.000331 | 2.56e-06 | 4.39e-06 | 0.000127 | 6.32e-05 | 3.025e-05 | 6.05e-06 | 3.87e-05 | 0.000316 | 0.00018355 | 3.57e-06 | 1.01e-05 | 2.24e-05 | 8.57e-06 | 1.34e-06 | 2.64e-06 | 8.01e-08 | 2.19e-06 | 6.46e-05 | 1.95e-07 | 7.91e-06 | 2.73e-05 | 8.62e-06 | 1.22e-05 | 9.56e-05 | 0.000187 | 1.18e-06 | 0.00024 | 4.18e-05 | 5.22e-05 | 4.8e-06 | 0.00023 | 0.0001618 | 0.000442 | 0.000232 | 5.19e-07 | 4.1e-10 | 4.79e-06 | 7.97e-06 | 7.8e-09 | 1.28e-05 | 2.2e-05 | 7.16e-08 | 2.22e-06 | 1.39e-05 | 7.28e-05 | 4.48e-07 | 3.29e-07 | 3.02e-07 | 6.34e-08
R/Qy PEC | 8.4086 | 0.069966 | 2.7429 | 2.455 | 19.03 | 959.458 | 957.33 | 6.944 | 589.395 | 0.2363 | 0.00387 | 0.65104 | 0.18463 | 1.258 | 1.7423 | 0.26912 | 0.7609 | 0.4067 | 0.889 | 0.11738 | 0.19749 | 16.096 | 0.00399 | 32.981 | 13.43 | 0.52906 | 0.1231 | 4.4418 | 1.5821 | 0.93106 | 0.000138 | 0.00147 | 10.87 | 3.772 | 1.49 | 7.26 | 38.028 | 0.539 | 4.577 | 59.369 | 12.253 | 0.00101 | 0.0016 | 0.00121 | 0.001625 | 0.02925 | 12.747 | 0.000228 | 0.0147 | 4.2819 | 0.026584 | 8.3185 | 0.00144 | 0.00116 | 0.5075 | 0.9127 | 1.9022 | 1.1935
R/Qz PEC | 1.26e-05 | 2.33e-05 | 3.19e-09 | 1.96e-07 | 7e-05 | 1.15e-07 | 2.51e-05 | 2.21e-05 | 1.31e-05 | 1.3e-08 | 1.29e-08 | 4.33e-05 | 0.0001025 | 2.87e-06 | 5.15e-08 | 1.19e-07 | 7.93e-05 | 1.06e-05 | 1.41e-06 | 3.61e-06 | 7.71e-05 | 5.1e-06 | 1.34e-06 | 5.44e-06 | 1.029e-08 | 1.96e-05 | 8.59e-06 | 4.006e-05 | 1.616e-06 | 2.47e-06 | 3.3e-06 | 3.179e-06 | 1.182e-07 | 4.85e-05 | 5.03e-09 | 1.48e-06 | 3.06e-06 | 0.000128 | 9.35e-08 | 2.01e-07 | 2.65e-07 | 7.27e-07 | 9.4e-05 | 1.43e-07 | 6.95e-07 | 1.41e-07 | 5.2e-10 | 4.59e-06 | 1.19e-06 | 7.31e-06 | 2.96e-07 | 1.018e-06 | 2.4e-06 | 2.32e-08 | 0.00012765 | 2.23e-07 | 2.32e-07 | 6.73e-08
Copper tapers (350 mm)+2 rings
Copper tapers (150 mm)+2 rings
Copper tapers (450 mm)+2 rings

## Slide 23: QMiR Elettra 3 cav System: QL Comparison
Cav.2
Cav.1
Chart: Freq [GHz]

## Slide 24: QMiR Elettra 3 cav System + Tapers
1
Cav.2
Cav.1
Cav.1
cav1
cav1
cav2
Eliptical Profile
RhombiodalProfile
Copper ring
Copper ring
Quality factor Q |  |  | 
Freq CST | Q CST | Freq HFSS | Q HFSS
4,00339 | 6,45 E05 | 4,00347 | 5,45 E05
4,00341 | 6,45 E05 | 4,00349 | 5,46 E05
4,01279 | 2,33 E05 | 4,01318 | 2,08 E05
4,01345 | 5,14 E05 | 4,01384 | 3,87 E05
4,04 | 3,84 E08 | 4,03997 | 6,54 E08
Setup

## Slide 25: QMiR Elettra Wakefields (Cav.1)
Cav.1
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 26: QMiR Elettra Wakefields (Cav.2)
Cav.2
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 27: QMiR Elettra WakeImpedance from Wakefields
Cav.2
Cav.1
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 28: QMiR Elettra WakeImpedance from Wakefields
Cav.2
Cav.1
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 29: QMiR Elettra WakeImpedance from Wakefields
Cav.2
Cav.1
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 30: QMiR Elettra WakeImpedance from Wakefields
Cav.2
Cav.1
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 31: QMiR Elettra WakeImpedance from Wakefields
Cav.2
Cav.1
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 32: QMiR Elettra WakeImpedance from Wakefields
Cav.2
Cav.1
Zoomed (4,25-6,0 GHz)
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 33
Below the critical temperature or , with the critical temperature, the BCS contribution to the surface resistance dominates. The product results a characteristic of the geometry of the cavity, and only dependent from the operational temperature of the device.
Q0, RSF & Dynamic Thermal load for NB cavity @ 4K

## Slide 34
Q0versus T at 1.3 GHz from calculations based on BCS theory for Nb3Sn compared to measurement of a Nb3Sn cavity.
Scaling the BCS part from 1.3 3.0 and 3,25 GHz and adding the reported ~5 nΩ residual resistence
Q0, RSF & Dynamic Thermal load for NB3Sn cavity @ 4K

## Slide 35
The static thermal load depends only on the cryomodule cryogenic design and not on the cavity material.
Here below a rough estimation of the thermal budget @ 4K and @ thermal screen stage
Static Thermal Load

## Slide 36
The current Elettra liquefaction plant, which will also supply LHe to Elettra 2.0, does not have sufficient power to supply liquid helium to the pure Nb cavities, so it would be necessary to install a dedicated plant. The Nb3Sn cavity solution requires more time from a research and development point of view for the construction of the cavities themselves, but would have less impact on the Elettra 2.0 facility. In the long term, the cryogen-free Nb3Sn solution is more sustainable, also due to the uncertainty of the He market.
Pure Nb cavities
Nb3Sn cavities
Vs
Conclusions

## Slide 37: Acknowledgements
Special thanks to...
A. Zholents – ANL USA
A. Lunin, T. Khabiboulline, V. Yokovlev– FNAL USA
External Collaborator
RF Group CERN
A. Fabris
K. Manukyan
S. Dastan
S. Di Mitri
F. Gerigk
R. Calaga
A. Grudiev
Elettra Team
M. Zamolo
M. Modica
G.Scrimali

## Slide 38: QMiR Elettra Review Pannel Comments
Verification should be done to make sure the reasonable isolation of operating mode and no-interaction of HOMs.
Multi-pole components should be further studied and optimized
Further optimization of design should be done from wakefields point of view.
Additional reduction of both normal and skew sextuple components should be considered by poles (electrodes) shaping.
More complex HOM damping is needed as the number of on-cell waveguides increases.
Further analysis should be preformed to ensure effective damping of SOM as gaps in a bunch pattern will generate sub-harmonic.
Solely relying on R/Q of SOMs may not provide adequate solution to control the parasitic impedance. Fundamental rejection in the waveguide incorporating rejection/notch filters should be investigated.
The HOM resonant RF losses must be carefully analyzed considering the actual geometry of the adjacent sections of the vacuum chamber.
The cavity slow frequency tuner with a range of about few 100 kHz should be integrated into the CM design.
The procedure for safely parking the cavities be carefully studied. Preliminary assumption is that the system should be warmed up to room temperature when not in use. A proper mechanism of absorbing SOM/HOM power, if necessary, should be analyzed and developed.
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 39
Notes: Last Slide 1: Thanks to the audience

## Slide 40
Notes: Last Slide 2: Aerial Photo of Elettra

## Slide 41
QMiR Elettra
Post Processing
Fundamental mode @ 3.0 GHz |  | Symmetric | units
Acc. Voltage |  |  | V
Deflecting Voltage |  |  | V
R over Q |  |  | Ω
PW voltage |  |  | V
PW R over Q |  |  | Ω
 | Peak of E field |  | V/m
 | Peak of H field |  | T
Q factor |  |  | 
G factor |  |  | 
Fundamental mode @ 3.0 GHz |  | Symmetric | units
Acc. Voltage |  |  | V
Deflecting Voltage |  |  | V
R over Q |  |  | Ω
PW voltage |  |  | V
PW R over Q |  |  | Ω
 | Peak of E field |  | V/m
 | Peak of H field |  | T
Q factor |  |  | 
G factor |  |  | 
Notes: Slide 3 – (..) : Content of the presentation
Insert a new slide: Home > “New Slide” and choose a slide Layout:
For Title & Subtitle
For text with bullet points
For Text
For Picture, graphs, visuals
Two columns
Blank
If you want Copy & paste an element from the Clip Board to the particular slide: 1. Click on a box to mark it.
2. Position the mouse pointer on the box frame: Copy! 3. Click on the particular slide: Paste!
How you intend to use the elements is your choice. You can combine the text block style with the background colour in different manner.

## Slide 42
Literature Survey
Generation of Short Pulses in SPEAR3
f1
f2
f1+f2
Deflecting Voltage
-0.4 -0.2 0 0.2 0.4 0.6 0.8 1
z = cז (m)
1- frequency tilt & cancel
The bunch is crabbed at it passes through zero-crossing of transverse deflecting cavities
Two transverse deflecting cavities
6th & 6.5th harmonic of 476.3 MHz to produce “beat frequency” kick waveform that crab-kick every other bucket with a combined voltage of 2-3 MV
For the exact cancellation at the centre of bunch . The slight over-compensation with V2 helps minimizing the perturbation to the whole bunch.
Coupling strength of crab cavity is proportional to product of its frequency & deflecting voltage ()
APS-SPX
  Crab cavity frequency: 2815 MHz
  Transverse kick: 2 MV
SPEAR3
  Crab cavity frequency: 2858 MHz
  Transverse kick: 1.93 MV

## Slide 43: QMiR Elettra 3 cav System + Tapers
1
Cav.2
Cav.1
Cav.1
cav1
cav1
cav2
Eliptical Profile
RhombiodalProfile

## Slide 44: QMiR Elettra 3 cav System + Tapers (HOMs)
Cav.2
Cav.1
Chart: Freq [GHz]
R/Qx PEC | 0.00040837 | 0.0006157 | 0.0001575 | 3.67e-05 | 0.0001877 | 0.0004725 | 0.000127 | 3.37e-05 | 1.64e-05 | 1.61e-06 | 1.33e-09 | 5.12e-07 | 1.15e-07 | 3.64e-06 | 5.1e-06 | 2.51e-06 | 3.96e-07 | 6.36e-07 | 1.62e-06 | 1.58e-06 | 2.47e-06 | 4.81e-06 | 5.86e-07 | 1.81e-05 | 8.01e-08 | 2.19e-06 | 9.42e-06 | 1.06e-06 | 7.91e-06 | 2.73e-05 | 2.47e-05 | 1.22e-05 | 1.38e-07 | 1.18e-06 | 3.61e-05 | 4.18e-05 | 1.88e-05 | 4.8e-06 | 9.92e-07 | 5.2e-05 | 7.72e-06 | 1.98e-06 | 5.19e-07 | 4.1e-10 | 4.79e-06 | 7.97e-06 | 1.86e-05 | 1.17e-05 | 3.32e-06 | 2.62e-06 | 2.54e-05 | 3.36e-07 | 1.71e-05 | 4.48e-07 | 3.13e-06 | 7.1e-06 | 6.34e-08
R/Qy PEC | 0.51458 | 7.8721 | 2.79 | 2.5589 | 18.41 | 954.5898 | 959.555 | 7.1504 | 589.78 | 0.2334 | 0.002983 | 0.67721 | 0.1457 | 1.258 | 1.7171 | 0.29127 | 0.78206 | 0.43506 | 0.881 | 0.089725 | 0.2334 | 16.096 | 0.005613 | 33.139 | 12.959 | 0.94082 | 0.0714 | 4.1987 | 1.5821 | 1.0576 | 0.002206 | 0.003569 | 4.4788 | 1.86 | 7 | 38.028 | 0.1554 | 4.577 | 59.369 | 12.253 | 0.0428 | 0.0025885 | 0.00121 | 0.0234 | 0.02925 | 12.747 | 1.74e-07 | 0.01842 | 4.2819 | 0.02542 | 8.3185 | 0.000809 | 0.001396 | 1.0586 | 0.9127 | 1.9022 | 1.1935
R/Qz PEC | 1.14e-06 | 3.5855e-05 | 6.45e-06 | 5.65e-06 | 1.98e-07 | 2.43e-05 | 1.1235e-05 | 1.042e-05 | 1.44e-05 | 6.198e-07 | 5.123e-09 | 1.14e-08 | 4.82e-09 | 5.26e-07 | 9.4e-07 | 1.07e-07 | 1.29e-07 | 2.85e-07 | 3.19e-07 | 4.85e-07 | 2.51e-06 | 3.47e-06 | 8.18e-06 | 3.04e-07 | 7.08e-07 | 2.58e-06 | 3.57e-06 | 2.05e-08 | 1.616e-06 | 2.47e-06 | 9.65e-06 | 3.179e-06 | 1.184e-09 | 5.03e-09 | 1.48e-06 | 3.06e-06 | 1.17e-06 | 9.35e-08 | 2.01e-07 | 2.65e-07 | 7.27e-07 | 2.24e-06 | 1.43e-07 | 6.95e-07 | 1.41e-07 | 1.225e-07 | 2.79e-07 | 1.71e-06 | 1.88e-06 | 6.09e-08 | 1.018e-06 | 2.15e-06 | 5.194e-10 | 8.71e-08 | 2.23e-07 | 2.32e-07 | 6.73e-08
Chart: Freq [GHz]
Q_ext PEC | 5629 | 5629.75 | 6766.43 | 24420.4 | 24420.7 | 126000 | 126000 | 18937.2 | 324000 | 356000 | 2110000 | 129000 | 1290000 | 53489.2 | 370000 | 16037.2 | 15674.1 | 8759.96 | 69237.2 | 1201.14 | 1108.89 | 859.135 | 5837.9 | 650.251 | 107.595 | 107.695 | 8957.88 | 4279.51 | 448.987 | 432.887 | 306.126 | 332.79 | 9474.48 | 136.254 | 161.703 | 242.084 | 223.681 | 163.616 | 748.591 | 207.09 | 221.44 | 364.857 | 389.311 | 1562.11 | 1440.61 | 636.195 | 104659 | 138543 | 818.49 | 93.3284 | 433.329 | 335.784 | 5328.18 | 455.265 | 610.513 | 1037.72 | 510.362
Chart: σ=4,5mm/15ps

## Slide 45: QMiR Elettra 3 cav System + Tapers + 2CR
Cav.2
Cav.1
Chart: Freq [GHz]
R/Qx PEC | 0.0001789 | 0.0018688 | 3.14e-05 | 5.06e-05 | 0.00074256 | 0.000158 | 0.00226 | 0.00148 | 0.000331 | 2.56e-06 | 4.39e-06 | 0.000127 | 6.32e-05 | 3.025e-05 | 6.05e-06 | 3.87e-05 | 0.000316 | 0.00018355 | 3.57e-06 | 1.01e-05 | 2.24e-05 | 8.57e-06 | 1.34e-06 | 2.64e-06 | 8.01e-08 | 2.19e-06 | 6.46e-05 | 1.95e-07 | 7.91e-06 | 2.73e-05 | 8.62e-06 | 1.22e-05 | 9.56e-05 | 0.000187 | 1.18e-06 | 0.00024 | 4.18e-05 | 5.22e-05 | 4.8e-06 | 0.00023 | 0.0001618 | 0.000442 | 0.000232 | 5.19e-07 | 4.1e-10 | 4.79e-06 | 7.97e-06 | 7.8e-09 | 1.28e-05 | 2.2e-05 | 7.16e-08 | 2.22e-06 | 1.39e-05 | 7.28e-05 | 4.48e-07 | 3.29e-07 | 3.02e-07 | 6.34e-08
R/Qy PEC | 8.4086 | 0.069966 | 2.7429 | 2.455 | 19.03 | 959.458 | 957.33 | 6.944 | 589.395 | 0.2363 | 0.00387 | 0.65104 | 0.18463 | 1.258 | 1.7423 | 0.26912 | 0.7609 | 0.4067 | 0.889 | 0.11738 | 0.19749 | 16.096 | 0.00399 | 32.981 | 13.43 | 0.52906 | 0.1231 | 4.4418 | 1.5821 | 0.93106 | 0.000138 | 0.00147 | 10.87 | 3.772 | 1.49 | 7.26 | 38.028 | 0.539 | 4.577 | 59.369 | 12.253 | 0.00101 | 0.0016 | 0.00121 | 0.001625 | 0.02925 | 12.747 | 0.000228 | 0.0147 | 4.2819 | 0.026584 | 8.3185 | 0.00144 | 0.00116 | 0.5075 | 0.9127 | 1.9022 | 1.1935
R/Qz PEC | 1.26e-05 | 2.33e-05 | 3.19e-09 | 1.96e-07 | 7e-05 | 1.15e-07 | 2.51e-05 | 2.21e-05 | 1.31e-05 | 1.3e-08 | 1.29e-08 | 4.33e-05 | 0.0001025 | 2.87e-06 | 5.15e-08 | 1.19e-07 | 7.93e-05 | 1.06e-05 | 1.41e-06 | 3.61e-06 | 7.71e-05 | 5.1e-06 | 1.34e-06 | 5.44e-06 | 1.029e-08 | 1.96e-05 | 8.59e-06 | 4.006e-05 | 1.616e-06 | 2.47e-06 | 3.3e-06 | 3.179e-06 | 1.182e-07 | 4.85e-05 | 5.03e-09 | 1.48e-06 | 3.06e-06 | 0.000128 | 9.35e-08 | 2.01e-07 | 2.65e-07 | 7.27e-07 | 9.4e-05 | 1.43e-07 | 6.95e-07 | 1.41e-07 | 5.2e-10 | 4.59e-06 | 1.19e-06 | 7.31e-06 | 2.96e-07 | 1.018e-06 | 2.4e-06 | 2.32e-08 | 0.00012765 | 2.23e-07 | 2.32e-07 | 6.73e-08
Chart: Freq [GHz]
Q_ext PEC | 5637.32 | 5637.49 | 6775.24 | 24448.7 | 24448.1 | 125914 | 125900 | 18959.6 | 324854 | 235319 | 519989 | 129474 | 129366 | 59416.3 | 361013 | 15985.9 | 15756.1 | 9870.59 | 64373.1 | 1179.6 | 1129 | 859.135 | 5810.44 | 650.251 | 107.392 | 107.919 | 8430.28 | 5319.34 | 445.599 | 430.477 | 303.902 | 333.019 | 2269.31 | 10845.2 | 137.104 | 159.452 | 230.063 | 238.851 | 164.137 | 736.846 | 208.258 | 219.891 | 368.973 | 387.91 | 1367.88 | 1443.12 | 635.094 | 104659 | 133252 | 822.083 | 92.742 | 461.8 | 335.585 | 5345.33 | 459.906 | 612.915 | 1032.38 | 510.362
Chart: σ=4,5mm/15ps

## Slide 46: QMiR Elettra 3 cav System + Tapers
1
Cav.2
Cav.1
Cav.1
cav1
cav1
cav2
Eliptical Profile
RhombiodalProfile
Copper ring
Copper ring
cav1
cav1
cav2
Copper ring
Copper ring
Copper ring
Copper ring

## Slide 47: QMiR Elettra 3 cav System + Tapers + 4CR
Cav.2
Cav.1
Chart: Freq [GHz]
R/Qx PEC | 0.0001789 | 0.0018688 | 3.14e-05 | 5.06e-05 | 0.00074256 | 0.000158 | 0.00226 | 0.00148 | 0.000331 | 2.56e-06 | 4.39e-06 | 0.000127 | 6.32e-05 | 3.025e-05 | 6.05e-06 | 3.87e-05 | 0.000316 | 0.00018355 | 3.57e-06 | 1.01e-05 | 2.24e-05 | 8.57e-06 | 1.34e-06 | 2.64e-06 | 8.01e-08 | 2.19e-06 | 6.46e-05 | 1.95e-07 | 7.91e-06 | 2.73e-05 | 8.62e-06 | 1.22e-05 | 9.56e-05 | 0.000187 | 1.18e-06 | 0.00024 | 4.18e-05 | 5.22e-05 | 4.8e-06 | 0.00023 | 0.0001618 | 0.000442 | 0.000232 | 5.19e-07 | 4.1e-10 | 4.79e-06 | 7.97e-06 | 7.8e-09 | 1.28e-05 | 2.2e-05 | 7.16e-08 | 2.22e-06 | 1.39e-05 | 7.28e-05 | 4.48e-07 | 3.29e-07 | 3.02e-07 | 6.34e-08
R/Qy PEC | 8.4086 | 0.069966 | 2.7429 | 2.455 | 19.03 | 959.458 | 957.33 | 6.944 | 589.395 | 0.2363 | 0.00387 | 0.65104 | 0.18463 | 1.258 | 1.7423 | 0.26912 | 0.7609 | 0.4067 | 0.889 | 0.11738 | 0.19749 | 16.096 | 0.00399 | 32.981 | 13.43 | 0.52906 | 0.1231 | 4.4418 | 1.5821 | 0.93106 | 0.000138 | 0.00147 | 10.87 | 3.772 | 1.49 | 7.26 | 38.028 | 0.539 | 4.577 | 59.369 | 12.253 | 0.00101 | 0.0016 | 0.00121 | 0.001625 | 0.02925 | 12.747 | 0.000228 | 0.0147 | 4.2819 | 0.026584 | 8.3185 | 0.00144 | 0.00116 | 0.5075 | 0.9127 | 1.9022 | 1.1935
R/Qz PEC | 1.26e-05 | 2.33e-05 | 3.19e-09 | 1.96e-07 | 7e-05 | 1.15e-07 | 2.51e-05 | 2.21e-05 | 1.31e-05 | 1.3e-08 | 1.29e-08 | 4.33e-05 | 0.0001025 | 2.87e-06 | 5.15e-08 | 1.19e-07 | 7.93e-05 | 1.06e-05 | 1.41e-06 | 3.61e-06 | 7.71e-05 | 5.1e-06 | 1.34e-06 | 5.44e-06 | 1.029e-08 | 1.96e-05 | 8.59e-06 | 4.006e-05 | 1.616e-06 | 2.47e-06 | 3.3e-06 | 3.179e-06 | 1.182e-07 | 4.85e-05 | 5.03e-09 | 1.48e-06 | 3.06e-06 | 0.000128 | 9.35e-08 | 2.01e-07 | 2.65e-07 | 7.27e-07 | 9.4e-05 | 1.43e-07 | 6.95e-07 | 1.41e-07 | 5.2e-10 | 4.59e-06 | 1.19e-06 | 7.31e-06 | 2.96e-07 | 1.018e-06 | 2.4e-06 | 2.32e-08 | 0.00012765 | 2.23e-07 | 2.32e-07 | 6.73e-08
Chart: Freq [GHz]
Q_ext PEC | 5637.32 | 5637.49 | 6775.24 | 24448.7 | 24448.1 | 125914 | 125900 | 18959.6 | 324854 | 235319 | 519989 | 129474 | 129366 | 59416.3 | 361013 | 15985.9 | 15756.1 | 9870.59 | 64373.1 | 1179.6 | 1129 | 859.135 | 5810.44 | 650.251 | 107.392 | 107.919 | 8430.28 | 5319.34 | 445.599 | 430.477 | 303.902 | 333.019 | 2269.31 | 10845.2 | 137.104 | 159.452 | 230.063 | 238.851 | 164.137 | 736.846 | 208.258 | 219.891 | 368.973 | 387.91 | 1367.88 | 1443.12 | 635.094 | 104659 | 133252 | 822.083 | 92.742 | 461.8 | 335.585 | 5345.33 | 459.906 | 612.915 | 1032.38 | 510.362
Chart: Freq [GHz]
Q_ext PEC | 5637.32 | 5637.49 | 6775.24 | 24448.7 | 24448.1 | 125914 | 125900 | 18959.6 | 324854 | 235319 | 519989 | 115152 | 115463 | 59416.3 | 361013 | 15500 | 15756.1 | 9870.59 | 64373.1 | 1179.6 | 1129 | 859.135 | 5810.44 | 650.251 | 107.392 | 107.919 | 8430.28 | 5319.34 | 445.599 | 430.477 | 303.902 | 333.019 | 2269.31 | 10845.2 | 137.104 | 159.452 | 230.063 | 238.851 | 164.137 | 736.846 | 208.258 | 219.891 | 368.973 | 387.91 | 1367.88 | 1443.12 | 635.094 | 104659 | 133252 | 822.083 | 92.742 | 461.8 | 335.585 | 5345.33 | 459.906 | 612.915 | 1032.38 | 510.362
Chart: Freq [GHz]
R/Qx PEC | 0.0001789 | 0.0018688 | 3.14e-05 | 5.06e-05 | 0.00074256 | 0.000158 | 0.00226 | 0.00148 | 0.000331 | 2.56e-06 | 4.39e-06 | 0.000127 | 6.32e-05 | 3.025e-05 | 6.05e-06 | 3.87e-05 | 0.000316 | 0.00018355 | 3.57e-06 | 1.01e-05 | 2.24e-05 | 8.57e-06 | 1.34e-06 | 2.64e-06 | 8.01e-08 | 2.19e-06 | 6.46e-05 | 1.95e-07 | 7.91e-06 | 2.73e-05 | 8.62e-06 | 1.22e-05 | 9.56e-05 | 0.000187 | 1.18e-06 | 0.00024 | 4.18e-05 | 5.22e-05 | 4.8e-06 | 0.00023 | 0.0001618 | 0.000442 | 0.000232 | 5.19e-07 | 4.1e-10 | 4.79e-06 | 7.97e-06 | 7.8e-09 | 1.28e-05 | 2.2e-05 | 7.16e-08 | 2.22e-06 | 1.39e-05 | 7.28e-05 | 4.48e-07 | 3.29e-07 | 3.02e-07 | 6.34e-08
R/Qy PEC | 8.4086 | 0.069966 | 2.7429 | 2.455 | 19.03 | 959.458 | 957.33 | 6.944 | 589.395 | 0.2363 | 0.00387 | 0.65104 | 0.18463 | 1.258 | 1.7423 | 0.26912 | 0.7609 | 0.4067 | 0.889 | 0.11738 | 0.19749 | 16.096 | 0.00399 | 32.981 | 13.43 | 0.52906 | 0.1231 | 4.4418 | 1.5821 | 0.93106 | 0.000138 | 0.00147 | 10.87 | 3.772 | 1.49 | 7.26 | 38.028 | 0.539 | 4.577 | 59.369 | 12.253 | 0.00101 | 0.0016 | 0.00121 | 0.001625 | 0.02925 | 12.747 | 0.000228 | 0.0147 | 4.2819 | 0.026584 | 8.3185 | 0.00144 | 0.00116 | 0.5075 | 0.9127 | 1.9022 | 1.1935
R/Qz PEC | 1.26e-05 | 2.33e-05 | 3.19e-09 | 1.96e-07 | 7e-05 | 1.15e-07 | 2.51e-05 | 2.21e-05 | 1.31e-05 | 1.3e-08 | 1.29e-08 | 4.33e-05 | 0.0001025 | 2.87e-06 | 5.15e-08 | 1.19e-07 | 7.93e-05 | 1.06e-05 | 1.41e-06 | 3.61e-06 | 7.71e-05 | 5.1e-06 | 1.34e-06 | 5.44e-06 | 1.029e-08 | 1.96e-05 | 8.59e-06 | 4.006e-05 | 1.616e-06 | 2.47e-06 | 3.3e-06 | 3.179e-06 | 1.182e-07 | 4.85e-05 | 5.03e-09 | 1.48e-06 | 3.06e-06 | 0.000128 | 9.35e-08 | 2.01e-07 | 2.65e-07 | 7.27e-07 | 9.4e-05 | 1.43e-07 | 6.95e-07 | 1.41e-07 | 5.2e-10 | 4.59e-06 | 1.19e-06 | 7.31e-06 | 2.96e-07 | 1.018e-06 | 2.4e-06 | 2.32e-08 | 0.00012765 | 2.23e-07 | 2.32e-07 | 6.73e-08
2- copper ring system
4- copper ring system
2- copper ring system
4- copper ring system

## Slide 48: QMiR Elettra 3 cav System + Tapers + 4CR
Cav.2
Cav.1
Chart: Freq [GHz]
Chart: Freq [GHz]
4- copper ring system
2- copper ring system

## Slide 49: QMiR Elettra 3 cav System: QL Comparison
Cav.2
Cav.1
Chart: 

## Slide 50: QMiR Elettra 3 cav System + Tapers + CR Steel
Chart: Freq [GHz]
Cav.2
Cav.1
Chart: Freq [GHz]
Copper tapers (150 mm)+2 rings
Steel tapers (150 mm)+2 rings

## Slide 51: QMiR Elettra 3 cav System + Tapers + CR Steel
Chart: Freq [GHz]
Chart: Freq [GHz]
Cav.2
Cav.1
Copper tapers (350 mm)+2 rings
Steel tapers (350 mm)+2 rings

## Slide 52: QMiR Elettra 3 cav System + Tapers + CR Steel
Chart: Freq [GHz]
Chart: Freq [GHz]
Cav.2
Cav.1
Copper tapers (450 mm)+2 rings
Steel tapers (450 mm)+2 rings