## Slide 1
Wrap Up – WG 2 Numerical Simulations for SRF Cavities
Thomas Flisgen
Workshop on Higher Order Modes in Superconducting Cavities (HOMSC25)
06 - 08 October 2025
DESY, Hamburg, Germany

## Slide 2: Wrap Up WG 2 - Numerical Simulations for SRF Cavities
Overview on concatenation methods, which are an important tool to determine HOMs in cavity chains, but sometimes difficult to get a good description of individual segments (Thomas Flisgen)
HOM power estimations for SHINE (Hard X-ray Free-Electron Laser Facility using 1.3 GHz 9-cell superconducting), [frequency-dependent] dielectric properties of absorber material is a critical issue (Jie Xi Zhang)
SIBC for a multilayer superconductor-insulator-superconductor approach as a cost-effective and higher-performing alternative to bulk niobium SRF cavities (Aaron Gobeyn)
Statistical analysis of HOMs: Method to model and analyze the spread of higher-order mode (HOM) parameters caused by mechanical imperfections in superconducting cavities, enabling prediction of resonant RF losses and informing design for stable, efficient operation of high-current accelerators (Andrei Lunin)
Assessment of HOMs in 915 MHz SRF cavities for industrial linacs, showing that stable, high-current operation is achievable without in-cell HOM couplers, enabling simpler, more efficient cavity designs for high-power applications (Alex Castilla Loeza)

## Slide 3: Wrap Up WG 2 - Numerical Simulations for SRF Cavities
Numerical simulation methods for analyzing HOM couplers in TESLA-type SRF cavities using S-parameter analysis (3D model and circuit model), optimization, and multipacting studies (Sosoho-Abasi Udongwo)
Presentation of ECHO code family and the underlying theory for accurately modeling wake fields and impedances in diverse accelerator geometries, highlighting recent developments, capabilities, and applications in complex component analysis (Igor Zagarodnov)