## Slide 1: XFEL Operator Training
Low Level Radio Frequency (LLRF)
Marco Diomede, for the DESY LLRF team

## Slide 2: Contents
Introduction
What an operator should know
Exceptional cases and how to react

## Slide 3: 1. Introduction
What is LLRF?
RF cavities: equivalent circuit and main parameters
Cavity tuning and coupling
LLRF and HPRF system overview

## Slide 4: Introduction
LLRF system
LLRF : measures and controls
  the accelerating field inside the cavity
  the bandwidth of the cavity
  the resonant frequency of the cavity
Low Level Radio Frequency: Low Level means low power (i.e. < 1Watt)
Our task: digital control of accelerating fields inside the cavities
    Normal conducting
      Gun 1.3 @ GHz
      TDS Injector @ 3.0 GHz
      TDS BC2 @ 3.0 GHz
    Super conducting cavities
      A1 – A25 @ 1.3 GHz
      AH1 @ 3.9 GHz

## Slide 5: Cavity as an Electrical System
The standard RLC model (simplified)
( 1 )
( 2 )
( 1 ) 
( 1 ) & ( 2 ) 
2nd order linear differential equation has a solution in the form of

envelope
carrier

## Slide 6: Cavity as an Electrical System
The envelope equation
t
 is the cavity time constant
it depends on the cavity bandwidth
VCAV : envelope
cavity half bandwidth
(i.e. half of the cavity bandwidth)
Notes: Could present one demo here of filling a cavity with low Ql and with high Ql, observe the time constant for the fill and for the fall.

## Slide 7: Cavity as an Electrical System
Cavity behaves as a band pass filter
  Center frequency f0
  Half bandwidth f1/2
In the frequency domain

## Slide 8: Cavity as an Electrical System
Cavity behaves as a band pass filter
  Center frequency f0
  Half bandwidth f1/2
We can define detuning as the difference between the cavity center frequency (f0 = resonance frequency) and the frequency of the RF drive (fRF)
In the frequency domain

## Slide 9: Tuner examples
Saclay type (EuXFEL)
Motor tuner (coarse)
Piezo tuner (fine)

## Slide 10: Cavity “fine” tuning
Lorentz Force detuning
Use of piezo in pulsed mode
Lorentz force detuning compensation using piezo
Example from FNAL 2007
R. Carcagno et al. SRF 2007
Detuning increases with square of gradient
Source:
L. Lilje et al.
EPAC 2006
Piezo stimulus:
Frequency
Delay
AC amplitude
DC offset
resonance build up

## Slide 11: Cavity coupling
Coupling power in and out of a cavity
Input coupler
  An antenna carries power from an RF source to the cavity
  The strength of the input coupler is adjusted by changing the penetration of the center conductor
Output coupler (pick up)
  the transmitted power probe (fixed coupler) picks up power transmitted through the cavity
Cavity unloaded quality factor
External quality factor modified by the coupler antenna position
Measurable “resulting” quality factor ( loaded Q)

## Slide 12: Cavity coupling
Q0 = unloaded quality factor
  Measured without the cavity power coupler
  Is a direct indication of the power dissipated in the cavity walls (high Q0  low losses)
Qext = external quality factor
  Can be changed when moving the coupler antenna
  Impacts how the incoming RF power couples into the cavity
  High Qext means slow response time, but less power required to reach high gradient
QL = loaded quality factor
  “Resulting” or “Effective” quality factor
  Is what can be measured during operation
  Changes in Q0 are masked by Qext
Understanding unloaded, loaded and external coupling
~ 106
~ 1010
~ 106

## Slide 13: LLRF System
Cavity response to a square pulse
Feed Forward
Forward drive
VMAX = steady state cavity voltage
VCAV
QL affects the cavity rate of filling and cavity bandwidth
QL is there
QL is there
QL affects the cavity maximum voltage
(for a given forward power)
Flat RF region that can be used for beam acceleration

## Slide 14: LLRF System
Adjust amplitude of the forward drive to match the set point gradient at the beginning of the beam time
Feed Forward
Forward drive
Cavity set point
Cavity voltage
OVC amplitude!

## Slide 15: LLRF System
Feed Forward
Adjust the drive during the beam time to maintain a flat accelerating gradient
Forward drive
Cavity set point
Cavity voltage
OVC ratio!

## Slide 16: Introduction
Where are we involved?
  In every RF station
  29 LLRF systems
TDS-INJ
TDS-BC2
reserved for tests
LLRF Systems

## Slide 17: Introduction
RF Stations in the injector
LLRF Systems
A1 and AH1 share the same LLRF crate

## Slide 18: Introduction : LLRF Station Overview
XTL RF station: semi-distributed LLRF system
DCM
Drift Compensation Module
REFM
RF Reference Module
LOGM
Local Oscillator Generation Module
PSM
Power Supply Module
PZ16M
Piezo Driver Module

## Slide 19: 2. What an operator should know
LLRF tasks of the XFEL operator:
  Turn an RF station ON / OFF
  Adjust the vector-sum voltage / phase
  Tune cavities, if necessary
  Adjust output vector correction and ratio, if necessary
  Set a certain phase as on-crest phase

## Slide 20: What an operator should know
Check amplitude and phase set point, RF control settings and flat tops
LLRF overview

## Slide 21: What an operator should know
Check waveform profiles (open loop, glitches, etc…
i.e. deviation from set point)
RF Amplitudes

## Slide 22: What an operator should know
Navigate to the main LLRF panel of a particular RF station: INJ, L1, L2, L3
LLRF selector

## Slide 23: What an operator should know
Voltage setpoint
Phase setpoint
Ramp station with FSM
Check for ON,
FSM should be green
FSM recovery voltage
Quench notifications
ALL these settings should be enabled*
* exception gun
Cavity tuning indicator
(should be green)
Drift compensation module (DCM)
Not green:
OK for operation but drifts are not compensated
elog entry  LLRF
Ramp-up
Ramp-down
(open loop)
Piezo
Not green:
OK for operation but piezos are not working
elog entry  LLRF
Non-LLRF systems!
Scalar/Table mode

## Slide 24: What an operator should know
Slopes active (yellow) : i.e. RF slope across the flat top
Error message area
(it self-clears after 5 minutes after the error is gone)
Not green:
Might lead to RF pulse cuts
elog entry  LLRF
Not green:
Operation might still be possible
elog entry  LLRF
Limiters
Main status

## Slide 25: What an operator should know

## Slide 26: What an operator should know

## Slide 27: What an operator should know
Color code
Operation probably not possible
Operation still possible!
LLRF color code

## Slide 28: What an operator should know
Special case GUN
Note that for the gun, the following features are greyed out and should stay disabled:
Feed-forward correction
Learning FF

## Slide 29: What an operator should know
Special case GUN
More familiar

## Slide 30: What an operator should know
Drive with FF only (i.e. open loop) no feedback trying to minimize error between signal and set point
Linear scaling of amplitude and phase drive to minimize error (automation)
Enables cavity tuning using piezos (including Lorentz force detuning)
Drive with FB (closed loop)
Applies small corrections to FF to compensate for systematic errors
Learns from pulse to pulse to adapt these small corrections
Re-initialize what has been learnt so far (i.e. start from empty correction)
Applies small correction to the drive to compensate for the presence of beam (i.e. scales with beam parameters)

## Slide 31: What an operator should know
Changing RF amplitude set point
Change is less than 100 MeV ?
Do it in closed loop
Do it in open loop
After adjustment limiters are triggering ?
Done
Revert to previous SP and try in open loop
Open the loop and adjust SP
Adjust OVC amplitude and ratio
Check tuning and adjust OVC phase
Close the loop
Dial in new SP
YES
YES
NO
NO
Note:
Changing SP phase does not require so much care, but should be also done progressively (i.e. steps of 10 deg.)

## Slide 32: What an operator should know
Changing RF amplitude set point in open loop (1/4)
Ampl. and Phase readouts lower than SP
LLRF system diagram
Only FF

## Slide 33: What an operator should know
Changing RF amplitude set point in open loop (2/4)

## Slide 34: What an operator should know
Changing RF amplitude set point in open loop (3/4)

## Slide 35: What an operator should know
Changing RF amplitude set point in open loop (4/4)
To close the loop
✓
✓
✓
✓
✓
✓

## Slide 36: What an operator should know
Procedures

## Slide 37: What an operator should know
Tuning cavities (1/2)

## Slide 38: What an operator should know
Tuning cavities (2/2)
Some cavities should NOT be tuned (greyed out)
Cavity detuning [Hz]
Piezo voltage (DC bias [V])
Click “Tune”
Relax piezo DC voltage
Shows tuning [Hz] and piezo DC bias [V]
both should converge to 0
“relax piezo DC voltage” is enabled by default
Some error message may pop up
You can choose to ignore once or twice but if problem persists, call expert

## Slide 39: What an operator should know
FSM
Not directly LLRF but belongs to RF operation
Turn the station on/off
(When possible) RF trips involving LLRF, Modulator, Klystron and Coupler interlock & quench are automatically recovered by FSM (no action needed!)
The FSM log can tell what is/was the problem

## Slide 40: What an operator should know
RF station color code
Station OFF
FSM is ON
Station ON FSM is ON
FSM is OFF
Station DOWN
FSM is ON
Station OFF beam
Station ON beam
Note 1:
Sometimes, the station is operational but the color indicator on the main display shows yellow/red instead of green
 Simply disable / re-enable FSM to force a status refresh
Station ON
Station OFF
FSM ON
FSM OFF
Station TRIPPED
Note 2:
The Status “FSM ON and station in service” is still represented with a green circle but with a label on top (L3 panel)
 Unusable stations are now visible from the L3 panel, also the Energy Manager should give this information

## Slide 41: What an operator should know
Energy Manager – Energy control
You can set the total RF energy -> It regulates the off-crest phases in L3

## Slide 42: What an operator should know
Energy Manager - automatic recovery from failure in L3
When enabled, if an RF trip is not recoverable within the defined timeout, the RF station is placed off-beam and the magnets scaled (possible to roll back if the station is recovered)

## Slide 43: What an operator should know
Setting the on-crest phase
The phase at which the max energy is measured is defined as on crest phase and corresponds to the “new” 0 phase setting in the LLRF controller

## Slide 44: What an operator should know
Setting the on-crest phase
For L3 this can also be done “parasitically” with the Energy Manager L3 Phase Scan (slow) -> fine tuning

## Slide 45: What an operator should know
Vector Sum Set Point configurations
2 RF energy configurations are actually foreseen:
Reduced-Energy (beam energies up to 14.0 GeV) -> VS SP 665 MV almost everywhere
High-Energy (beam energy of 16.3 GeV) -> Max achievable voltage
The purpose of the Reduced-Energy mode is to
reduce power consumption (lower modulator HV)
lower the radiation level in the tunnel (e.g. less MTCA issues)
The Maximum SPs are embedded in the LLRF server and they are updated at every change of configuration according to these tables: https://xwiki.desy.de/xwiki/short/b083a

## Slide 46: What an operator should know
How to deal with failing RF stations
How to deal with failing RF stations: https://xwiki.desy.de/xwiki/short/a43a1
HPRF problems at AH1 → MIN expert on call
Quadrupole &
(also LLRF mailing-list)
(also 1.3 GHz mailing-list)
Have a generic RF mailing-list?
(in BKR)
Recognize the root cause
If you are not sure, please inform all the possible groups (not only LLRF!)

## Slide 47: What an operator should know
LLRF on-call 5588
9 experts, 1 available 24/7 every week
llrf-expert@desy.de
Send log book entry to LLRF expert list
    Write your name / initials
    Edit the title and description
    Use the Tag fields (at least Location)
LLRF on-call service
Christian
Mariusz
Julien
Marco
Matthias
Valeri
Martin
Patrick
Max

## Slide 48: 3. Exceptional cases and how to react
Probe limiter – pulse cut
KLM limiter – pulse cut
Output/feedback limiter
Cavity quenches
Zombie station
Lost PCIe connection

## Slide 49: Exceptional cases and how to react
Pulse cuts due to gradient limiters
RF pulse is shorter
Limiter indicator is red
What to do:
Document in log book and send to LLRF
Open/close loop
Lower the gradient if possible
Note:
Pulse cuts are displayed on the main panel (limiter / KLM)
The beam is cut if the RF pulse is cut
4. If you want, you can check what is the limiting factor
(see next 2 slides)

## Slide 50: Exceptional cases and how to react
Pulse cuts due to gradient limiters
RF pulse is shorter
Check if a specific cavity is the reason for the cut

## Slide 51: Exceptional cases and how to react
Pulse cuts due to KLM limiters
RF pulse is shorter
If all cavity limiters are green, the cut probably comes from the Klystron Lifetime Management (KLM) system.
In any case,
Document in log book and send to LLRF
Lower the gradient if possible
8

## Slide 52: Exceptional cases and how to react
Limiter is red (but no cut)
If this output limiter is red:
1. SP is too high
or
2. LLRF drive parameters need to be rechecked
What to do:
Document in log book and send to LLRF
Try open/close loop
Lower the gradient if possible

## Slide 53: Exceptional cases and how to react
Cavity quench (1/2)
What to do:
Document in log book and send to LLRF
Lower the Voltage SP if needed
Note:
Place the quench panel instead of the main panel in the log book (more information)

## Slide 54: Exceptional cases and how to react
Cavity quench (2/2)
Repetitive quenches
Problem description:
  The FSM tries to recover a station after a quench, ramps up to the same gradient and quenches again
  After 3 tries, the FSM gives up
What you can try
  Lower the recovery gradient in the FSM window (-10 MV ?)
Quench during ramp up
Problem description
  (After a quench) the RF station trips due to quenches taking place at a much lower gradient
  Chances are the QL computation got corrupted during the quench, hence corrupting the quench detection mechanism
What you can try
  Disable the FSM, ramp up the station slowly (i.e. 10 MV steps) by hand, and re-enable the FSM

## Slide 55: Exceptional case and how to react
“Zombie” station
What to do:
Document in log book and send to LLRF
Agree with LLRF on-call and run coordinator when best to recover the station
The llrfCtrl server is not responsive
Chances are the hardware is still working
BUT
Likely the quench detection is no longer working
MANAGER (and / or) SUBORDINATE “zombied”
SUBORDINATE “zombied”

## Slide 56: Exceptional case and how to react
PCIe connection is lost
What to do:
Document in log book and send to LLRF
Agree with LLRF on-call and run coordinators when best to recover the station
PCIe connection with the board is lost
If it involves boards 4, 11 and 12, the station cannot operate
BUT
In the other cases, the station might work till fix
Main Status panel

## Slide 57: Summary
LLRF tasks of the XFEL operator:
  Turn an RF station ON / OFF
  Adjust the vector-sum voltage / phase
  Tune cavities, if necessary
  Adjust output vector correction and ratio, if necessary
  Set a certain phase as on-crest phase
Special cases
  Pulse cut
  Limiter notification
  Quench
  Zombie stations
Opportunity for hands-on:
  LLRF maintenance ~every Tuesday
  off-beam stations -> ask LLRF team (& RCs)
Document (elog) what you find not normal
  Please include your name, title and description!
Thanks to Julien for the material

## Slide 58
Marco Diomede
MSK
marco.diomede@desy.de
1615
Thank you
99.9% LLRF availability

## Slide 59: Backup slides

## Slide 60: Introduction
LLRF and RF operations
Low Level Radio Frequency: Low Level means low power (i.e. < 1Watt)
Our task: digital control of accelerating fields inside the cavities
    Normal conducting gun 1.3 GHz
    Super conducting cavities 1.3 GHz and 3.9 GHz (AH1)
Other tasks often labelled as LLRF
  Frequency control (cavity tuning)
  Bandwidth adjustments (QL)
  Quench detection
  Trip recovery
Modulator + Klystron
RF power coupler
LLRF

## Slide 61: Introduction : LLRF Station Overview

## Slide 62: What an operator should know
Check for server failures (all should be green!)
Good way to catch a “zombie” station
A17 shifted OFF beam

## Slide 63: What an operator should know
Error messages
Error message area:
Currently only used for multi-flat top settings but might be extended in the future
The error message latches. First try to reset, if persists, call LLRF expert
Sum of server errors should be 0 (green)
If not, elog entry to LLRF