## Slide 1: Muon Collider RF
Simon Albright
With material from:
Heiko Damerau
Christine Vollinger
Eric Montesinos
Frank Gerigk
Michela Neroni

## Slide 2
RF is almost everywhere, and directly/indirectly includes many subjects:
High power vacuum electronics
FPGA and DSP development
Analogue signal processing
Beam dynamics
Electromagnetic modelling/design/manufacture
…

## Slide 3: Full RF system
LLRF
HLRF
Cavities
Beam
Magnetic field
Voltage functions
…
Low power Level RF:
The “brain”
mW scale signals
Specifies what the RF should do to control the beam
High power Level RF:
Amplifies mW signals to kW/MW scale
Drives RF power into the cavity
Beam Measurement

## Slide 4: Contents
Longitudinal Beam Dynamics
RF Cavities
Beam Loading
RF Power Amplification

## Slide 5: Longitudinal Beam Dynamics

## Slide 6: Beam RF Interaction
Individual particles gain (or lose) energy as:
These particles lose energy
These particles gain energy

## Slide 7: Acceleration
Accelerating on-crest:
Most efficient use of the voltage
Very little margin of error
Can lead to banana shaped bunches
Frequently used in linacs
Accelerating off-crest:
Allows larger beams beam
Easier to control and mitigate errors
Obligatory in rings

## Slide 8: Synchrotron Layout
RF
Not RF
Not RF
Not RF
Not RF
Not RF
Not RF
Not RF
Each beam will see:
16 RF cavities
27 km of other stuff

## Slide 9: Synchrotron Motion

## Slide 10: Synchrotron Motion
Not RF

## Slide 11: Synchrotron Motion
Given enough time, particles will oscillate from the head to the tail and back again
Change of phase
(not RF)
Change of energy
(RF)
If the motion is slow enough, discrete steps in energy and phase can be approximated by a continuous function
If not, things can get a little spicy

## Slide 12: Key Takeaways
RF Is used to change the beam energy
particles at different positions in the bunch will gain/lose different amounts of energy
High and low energy particles drift within the bunch
Motion is discretised, small steps are needed to preserve stable motion

## Slide 13: Cavities

## Slide 14: Electromagnetic Pendulum
Cavities are effectively a harmonic oscillator; energy is added by RF power amplifiers and is lost to the cavity walls and extracted by the beam
The electric field is (typically) parallel to the beam direction
The magnetic field is (typically) perpendicular to the beam direction
Beam

## Slide 15: RLC Circuit
R
C
L
RF power source
V
Cavity gap voltage
Main terms of interest:
RShunt: Resistive impedance at the resonant frequency
ω0: Resonant angular frequency, given by L and C
Q: Quality factor, energy loss per RF period

## Slide 16: Quality Factor
Low Q:
High bandwidth
Fast decay
Fast filling
High Q:
Low bandwidth
Slow decay
Slow filling

## Slide 17: Key Parameters
Steel
Cu
Nb
(4K)
Moderate Q
Moderate RShunt
Low Q
Low RShunt
Enormous Q
Enormous RShunt
Peak Voltage: Scales with frequency (weakly), risk of sparking if too high
Frequency: Scales with size, high is good for V/m, low is good for large beams
Q: Influences frequency range and rate of energy loss/gain
R/Q: Defined by geometry, defines how easy it is to add voltage

## Slide 18: Types of Cavity
(Old) PSB: 3-8 MHz
Linac4: ~300 MHz
TESLA: 1.3 GHz
CLIC prototype: ~10 GHz

## Slide 19: Key Takeaways
Cavities are resonators that store RF energy
Cavity geometry defines R/Q, independent of material
High-Q cavities lose and gain energy very slowly
Many designs of cavities exist, all optimised for different conditions

## Slide 20: Beam Loading

## Slide 21: RLC Circuit
R
C
L
RF power source
V
Cavity gap voltage
Beam current

## Slide 22: Beam Induced Voltage

## Slide 23: Beam Induced Voltage
Drop in voltage due to beam passage
Proportional to R/Q and beam current
Cavity refilling (Q)

## Slide 24: Cavities that aren’t Cavities
Vacuum pumping manifold of the CERN Proton Synchrotron
Multiple resonant frequencies in the 1 – 1.5 GHz range
Suspected of causing beam instabilities
Proposed beam scraper for the CERN SPS
Strong modes predicted at 0.9 and 1.3 GHz
Design modified to suppress them

## Slide 25: Key Takeaways
The beam acts as an additional current source in the cavity
Beam induced voltage counteracts RF voltage and acts back on the beam
Almost anything exposed to the beam acts as a cavity and careful design choices are needed to avoid negative effects

## Slide 26: Power Amplification

## Slide 27: Vacuum Tubes
Vacuum tubes:
High electron current generated by a cathode
Low power signals applied to screen modulate the current
High AC-current electron beam on the anode provides high power signal
Limited in frequency and power
Very durable and reliable

## Slide 28: Solid State
Solid state:
Pairs of transistors, one to amplify the positive side, the other to amplify the negative side
Low power but modular
Modularity gives reliability, one broken transistor does not bring down the entire RF system
Gradually replacing vacuum tubes in many contexts
DC

## Slide 29: Klystrons
Klystron:
High current electron beam passes through an RF cavity
Lower power input RF energy modulates the beam
Bunches form as the beam travels along the klystron
Electron bunches deposit energy in the second cavity (beam loading) producing high power output RF
Very high power and available at a lot of frequencies (small tuning range)

## Slide 30: Key Takeaways
Variety of options for Power amplification, best solution depends on the application:
  Vacuum tubes: Durable, Radiation tolerant, can absorb power transients
  Solid-State: Reliability through modularity
  Klystrons: Highest power
Like cavities, no one-size fits-all solution

## Slide 31: What matters where?

## Slide 32
High proton beam power calls for high RF power
Very short and intense muon bunches lead to significant beam loading
Strong magnets next to cavities increase risk of sparking
Need very high voltage for fast acceleration
Fast synchrotron motion in the RCS needs care