## Slide 1: EuXFEL Operator Training Injector beam optics measurements
Matthias Scholz
March 18, 2025

## Slide 2: First things first
The width of the beam (in horizontal or vertical plane) at a certain position in the beamline depends on two things: The so-called beta function at the position and the emittance.
A screenshot from the camera OTRC.59.I1in the XFEL injector

## Slide 3: First things first
Matching means, that the actual electron beam parameters fit to the design optics of the lattice (given by the position and strength of magnets). In other words, the beam’s size at different positions in the accelerator is as designed.
The lattice is designed such that the electron beam’s quality in the undulator beamlines is as good as possible for lasing.
Beta functions (“beam sizes’) in the EuXFEL injector
Strengths of quads
Position of the cathode
I1 matching section

## Slide 4: First things first
Matched and mismatched beams in I1
Changed the strengths of two quads in A1 and AH1
The beam sizes are different from what we need for successful operation

## Slide 5: Emittance and Twiss-parameters
The beam orientation is described with the Twiss-parameters .
The “slope” of the ellipses are a signature of convergent or divergent beams.
A beam which does not have the same orientations (with respect to design optics) is called “mismatched” even if the emittance is the same.
This, can actually be measured (transverse beam sizes) e.g. with a screen or wire!

## Slide 6: Emittance
Area covered by particles in phase space is called emittance
We can assume an elliptical distribution
Emittance is conserved in linear optics (Liouville’s theorem) => beam behaves like an incompressible liquid => focusing the beam will increase its divergence
Small beams with little divergence as required for SASE lead to small emittance requirements.

## Slide 7: Emittance and Twiss-parameters
smaller emittance and no mismatch
same emittance with mismatch
The beam orientation is described with the Twiss-parameters
The “slope” of the ellipses are a signature of convergent or divergent beams.
A beam which does not have the same orientations (with respect to design optics) is called “mismatched” even if the emittance is the same

## Slide 8: Emittance and beam size measurements
momentum
position
beam size

## Slide 9: Emittance and beam size measurements
momentum
position
beam size
momentum
beam size
Δ phase advance *
* This is only true in the so called normalized phase space, but for simplicity's sake, let's keep it that way.

## Slide 10: Emittance and beam size measurements
momentum

## Slide 11: How to determine emittance and Twiss parameters
However, we know how <X2> is transformed from 0 to 𝓲 using the transfer matrix elements Rkl
We do the measurements in section with no bending magnets and assume that the transfer matrix elements R16 and R26 are zero.
and
We can only measure <X2>, the squared rms beam size 𝝈2.
-> not enough…
The definition of the emittance and the Twiss parameters at position 0 using the second beam moments.
𝓲

## Slide 12: How to determine emittance and Twiss parameters
However, we know how <X2> is transformed from 0 to 𝓲 using the transfer matrix elements Rkl
The definition of the emittance and the Twiss parameters at position 0 using the second beam moments.
and
We can only measure <X2>, the squared rms beam size 𝝈2.
-> not enough…
can be measured
Transfer matrix elements -> well known
three unknowns
𝓲

## Slide 13: Calculation of beam moments
Lets make 3 measurements with different transfer matrices!
can be measured
Transfer matrix elements -> well known
three unknowns
Done. All 3 required beam moments can be calculated.
and 3 equations

## Slide 14: Fit of beam moments
Calculating the beam moments with 3 measurements does not result in any error estimations!
-> Preferably more than 3 measurements should be made.
The beam moments can be determined by a least square fit:
known
fit parameters
and
minimize

## Slide 15: Measurement methods
How to make at least 3 different measurements with different transfer matrices between a reference position and the measurement position.
reference
position
S
screens
quads
4 screen method
reference
position
S
screen
quads
quad scan
R (𝓲)
Different transfer matrix due to 𝓲 = 1,…,N quad settings
R (1)

## Slide 16: Single quad scan
Depending on the beam optics it is often not possible to scan both planes at the same time.
A very small beam size in the injector can lead to a beam blow up due to space charge.

## Slide 17: Single quad scan and scan step sizes
Many thanks to Bolko for the nice and explanatory drawing 
If equally large steps are selected for the magnetic strength, this can potentially lead to doubtful measurement results.
The measurement result of the emittance in the example on the right hand side is absolutely dominated the one measurement taken in the beam waist.

## Slide 18: Multi quad scans
Using more than one quadrupole has the advantage that:
  The beam size at the screen can be kept constant for all measurement steps. No small beams are necessary that might be blown up by space charge.
  Both transverse planes can be scanned over a wide range in the same measurement (advantage over most single quad scans).
  Many measurement steps are possible thus measurement errors in single measurements can be found and neglected (advantage over multi-screen method).

## Slide 19: Prepared quad scan for the EuXFEL injector

## Slide 20: Optics matching in the injector using screen stations and multi knob quad scans

## Slide 21
The measurement result can be directly used to match the beam in the respective section.
Optics matching in the injector using screen stations

## Slide 22: Beam optics measurements downstream L3
Final beam optics measurements and corrections at the end of the main linac.
This measurement can be carried out using either screens or wire scanners.
It ensures, inter alia, an effective collimation in the following section.

## Slide 23: Prepared quad scan for L3

## Slide 24: Measurement results for quad scans with wires
Signals from all wires and for all measurement steps
Normalized phase spaces and beam sizes as well crucial scan parameters from the measurement.
<- Measurement steps ->
<- Detectors ->
Blue intensity traces indicate that the data from the respective detector is used for the evaluation.
Thus, saturated signals should be presented in black, which means they are not considered in the evaluation.
The upper plot is shown twice, one plot for each plane.

## Slide 25: Beam optics measurements downstream L3
A quadrupole scan using :
Two different beam optics
Three different wire scanners (or screen stations)
Electron beam profiles

## Slide 26: Optics matching in L3
The beam optics measurement presentation is the same as for the screen measurements.
The measurement result can used to match the beam in L3.

## Slide 27: Multi quad scan GUI
Select a beamline section
Select the measurement device: Screens or wires? The default device is automatically set for each beamline section.
Select the preferred cycling procedure.
Increment: only every nth step of the measurement will be taken.
Chose beam optics after measurement: either design values or beam optics used before the measurement.
Start the scan
It is necessary to change matching quads, wire scan detectors or something else? Press ‘edit config file’.
Access to the prepared quad scan files.
Access to all quad scan measurement data.
New button: load and plot old measurements. Opens a file selector GUI.
Tools Advertising

## Slide 28: Measurement results for quad scans with screens
Well know measurement presentation after a quadrupole scan using screen as measurement devices.
Match using last results
The matching routine uses either the last measurement or the last re-evaluation of the measurement data.
Typical result after matching calculation. This plot is only shown if the algorithm found a solution.
Tools Advertising

## Slide 29: Deselecting single measurements
After deselecting the first two measurement steps
Be careful with the deselection of measurement steps and with the following evaluation of the data!
This functionality must only be used to deselect measurements steps that went clearly wrong (e.g. no beam).
It must not be used to deselect ‘unwanted’ measurement steps to improve e.g. emittance size or beam optics matching!
The first two measurement steps were taken steps without beam.
It is possible to evaluate only a selection of the taken data steps.
Write all step numbers that should into that field and press ‘Evaluate again’.
You can use MATLAB type vector definitions like [3:7] = [3 4 5 6 7].
Tools Advertising

## Slide 30: Tomographic reconstruction of transverse phase spaces
momentum
position
beam size
Even more information about the beam can be obtained by using not only the beam sizes but also the profiles.
The transverse phase spaces can be reconstructed using a tomographic algorithm and the profiles from different ‘angles’.
Tomographic reconstruction of the horizontal phase space for the center slice.

## Slide 31: Tomographic reconstruction of the hor. phase space using a quad scan

## Slide 32: Tomographic reconstruction of the hor. phase space using a quad scan

## Slide 33: EuXFEL Lyso screens
It turned out that measured emittances sizes depended on the beam size on the screens.
In addition, the beam spots one the screens were not gaussian shaped but looked like smoke rings.
y
x
It was not clear if the beam looks like that or if the LYSO screens can not display the bunches correctly.
No others screens were available in the machine.
It turned out that it was a quenching effect of the scintillators.
That effect could be reproduced in simulations.
Most of the screen have been or will be replaced with YAP or GGAG.
Beam size
Beta functions at screen