## Slide 1: Silicon Pixel detectors for Relativistic Heavy Ion Collisions The present, the future and some dreams
M. Deveaux, GSI

## Slide 2
Relativistic heavy ion physics – how we search
Qualitative picture.
Ions collide. Heavy quarks are formed
in early collisions.
“Fireball” establishes (magically) a thermal
equilibrium and acts like a gas.
QGP is formed: Hadrons loose binding.
Fireball establishes
Energy is exhausted, Fireball starts to
expand. Still formation of matter. Medium
acts collectively like a gas cooling down.
Hadronization: Quarks find
partner and form hadrons.
Chemical freeze out: Composition
of particles no longer determined
by thermal equilibrium.
Thermal freeze out: Kinetics
of particles no longer determined
by thermal equilibrium.
This is what we want to study.
This is what arrives in the detector.

## Slide 3
Relativistic heavy ion physics – how we search
What you want to access:
Properties of the medium at highest energy density.
What you can access:
Kinetics of particles of the cooled down medium => in collision frame.
Composition of particles of the cooled down medium.
“Probes”:
  Particles from early collisions, e.g. charm quarks (precious but rare).
  Leptons from the hot phase (don’t cool down but a lot of background).
  Collective properties (e.g. density fluctuations).
What do you need:
Detectors suited for high precision tracking at low momentum.
Detectors being sensitive for rare probes in front of heavy ion background.
Sensitivity is essential, therefore DMAPS.

## Slide 4
MAPS – the hope and limitations
Hybrid pixels (LHC / CMS)
 | Hybrid pixels (2001) | MAPS (2001)
Single point resolution | ~ 30 µm | ~2 µm
Material budget | ~ 500 µm Si | ~ 50 µm Si
Time resolution | 25 ns | ~10 ms
Radiation hardness | ~1015 neq/cm² | 1012 neq/cm²
More sensitivity
More statistics
We need both
Massive improvement required… and was reached.
MAPS Hybrid

## Slide 5: The state of the art – MIMOSIS, the pixel sensor of CBM.
MIMOSIS-1, 60µm thick
>20V HV top bias
Capacitor blocks HV
 | MIMOSIS (TJ180nm)
Pixels | 504 x 1024
Pixel size | 27 x 30 µm²
Time binning | 5 µs
Sensor type | Fully depleted, 20 V top bias
Rate (average, peak) | 20 MHz/cm², 80 MHz/cm²
Control | I2C
Readout | 8 x 320 Mbps (GBTx compatible)
p-stop
First proposed by H. Pernegger et al.,
2017 JINST 12 P06008
Derived from ALICE - ALPIDE
Curtesy CBM-MVD collaboration
(IPHC, GU Frankfurt, GSU)

## Slide 6
MIMOSIS prototypes - Performance
ALPIDE-like
+ 0.5 µm for longer
pixel dimension
Optimal number of fired pixels/particle (about 2.5)
Dark rate typically <1010/pixel (2 Hz/cm²)
driven by individual hot pixels.
Also demonstrated:
Tolerates >1014 n/cm² + 5 MRad @ room temperature.
Tolerates exposure to > 20 MeV cm²/mg ions
Work in progress
So, we have the perfect sensor, but…
Curtesy CBM-MVD collaboration
(IPHC, GU Frankfurt, GSU)

## Slide 7
It’s the infrastructure, stup..!
J. Sonneveld for ALICE, PoS(HardProbes2023)077
S. Siddhanta for ALICE, NIM-A Vol. 931 (2014) P 1147ff
Pictures: ALICE ITS-2 ladder
In DMAPS detectors, material
is determined by the supporting
infrastructure.
Must minimize this infrastructure.
Idea to reduce the infrastructure:
Build air – cooled, self supporting, bended stations
from one or few wafer-size sensors.
=> Material budget close to 50µm thin sensors.
Pushed forward by ALICE-ITS3.
So, we have the perfect detector, but…
Sensor
Other
stuff

## Slide 8
Scaling up existing solutions
The ALICE ITS3 is small, what about scaling up?
Example ALICE3 outer tracker (~60m²):
Want speedup to 100ns time stamping (x50).
Air cooling – power should remain <50 mW/cm².
60 m² detector => 30 kW => 25kA.
Need to stabilize voltage to roughly .
Assume 5m to power supply and copper:
23 cm diameter cable, ~3700 kg mass.
This is not exactly a small current.
This is not exactly a massless detector.
Solution so far:
Limit time resolution and rate capability
of the sensors to minimize power.
What if we aim for ~10ns and 100 MHz/cm²?
OCTOPUS Meeting Prague, Sept. 3-5 2025
LHC magnet failure: 12kA

## Slide 9
Pixel powering options
Power seems to scale with
Obvious: Big pixels safe power.
3rd DRD3 week, NIKHEF Amsterdam, 2-6 June 2025
pitch
DPTS
~3x
Data extracted from IEEE TRANSACTIONS ON NUCLEAR SCIENCE, VOL. 70, NO. 9, SEPT. 2023
Welcome to the “power wall”.

## Slide 10
DPTS
TOWER–0.18µm, p-stop (MIMOSIS-1)
TPSCo 65 nm (DPTS)
Going beyond the power wall: Radiation tolerance vs. pitch
DPTS: G. A. Rinella et al., arXiv:2212.08621v4
MIMOSIS-1: H. Darwish et al, proceedings of 20thTrento workshop (2025), under preparation
Others: M. Deveaux, 2019 JINST 14 R11001
Using big pixels will reduce power but compromise rad. tolerance.
=> Not really an option.
MIMOSIS

## Slide 11
Going beyond the power wall – Time walk correction
Time walk correction
M. Deveaux,
rough estimate
Signal 65nm (?)
Signal 180nm (?)
Disclaimer: Pixel-to-pixel
variation not accounted for.
25 ns
Uncertainties considered:
Jitter, ToT uncertainty of 44 e
Idea:
Time walk depends deterministically on signal => Measure signal with ToT, correct offline.
May reduce analogue power by ~10x (t.b.c). Jitter remains.
Can’t do ToT on pixel => Send start and stop signal separately => 2x data rate.

## Slide 12
Going beyond the power wall – LGADs
Most analog power is spent in pre-amplifier of pixel.
Idea: Replace pre-amplification by low gain avalanche amplification in the sensing node.
Amplification layer
Consequence:
Injected signal increases by LGAD gain (typically 5 – 30x).
Time walk and jitter is naturally reduced => No increased amplifier power required.
Feasibility for TJ180nm being demonstrated by DRD3/CASSIA project (there are many other projects).
10 x
e

## Slide 13
Digital pixel power, example MIMOSIS-1/2 (TJ180 nm)
Offset
Irrad.
Data cost [power/hit]
Work in progress
MMOSIS-1/2
Power dissipation is composed from:
Analog power (analog front-end).
Static power (increases with irradiation).
Data cost:
  ~0.7 mW/MHz for MIMOSIS @~24 bit/hit.
  Reduced by lower operation voltage.
  Increased by higher number of bits/hit.
  Precision timing – expect higher cost.
Analog & data power cost increases with increasing rate capability.
Possible solution:
Optimize for low data cost (as always).
Switch-off unnecessary ressources (reduce static power).
Static power
OCTOPUS Meeting Prague, Sept. 3-5 2025
Curtesy CBM-MVD collaboration

## Slide 14
Reduce static power (pixel matrix readout).
So far: Priority encoder (ALPIDE, MIMOSIS), excellent for frame readout.
Possibly better: Arbiter readout.
Rules of individual cell:
If (signal@input) {
  Forward address with highest priority to downstream cell.
  Wait for clear signal from downstream cell.
  Clear upstream cell with highest priority
  }
In case of data collision: Process next signal immediately
Advantages: Fully Asynchronous
No clock needed -> Less power, no clk driven delay.
Best possible response speed (limited by line and transistor delays).
Scalable: Each cell may serve N input lines.
Data collision => hit delayed but not lost.
Today’s estimate: Should require <<10mW/cm² @ 100 MHz/cm².
E. Aguénounon et al., Sensors 2021, 21(12), 3949; https://doi.org/10.3390/s21123949
J. Soudier et al., NIM-A Volume 1067, October 2024, 169663
Additional power saving: Switch-off unnecessary resources where ever possible.

## Slide 15
The dream: Save power on the system level
More sensitivity (low power)
More statistics (high power)
What is the best choice for 2025-2030?
One must fit all...
2030:
Versatile sensor
Statistics Sensitivity
Today:
Power vs. Performance: Hardwired
What is the best choice for
Sensor 403 in Detector A?
Tune depending on position & application.
OCTOPUS Meeting Prague, Sept. 3-5 2025
Approach being followed up by the
DRD3 – MANTA collaboration.

## Slide 16
A wild dream (?): 3D integrated sensors
Amplification layer
e
Optimized MAPS/LGAD sensing node possibly
with analogue front-end
Minimize “analogue power”
Through silicon vias
Optimized digital process with low core
voltage and high density.
=> Reduce “data cost”
Distribute electronics over two layers
Minimize pixel pitch.
Small pitch => High rad. tolerance.
Multi-tear sensors have the potential to be the next big thing…
… unfortunately for >10 years already.
A next attempt is started within DRD 7.6b (talk of M. Caselle, this workshop)

## Slide 17
How to get rid of copper (or aluminum) – serial powering
Idea:
Serial powering allows using higher voltages => lower currents.
Voltage regulator:
Provides stable voltage to sensor.
Must be provided with sufficient current for max. sensor power (Imax).
Bypasses (burns) remaining current to feed consecutive sensor.
Chain current must be Imax.
System power is given as
Easy if:
Device power is determined by “static power”.
Data transport forms small (few 10%) additional contribution.
Advantages of the concept (despite complexity) are obvious.
Voltage
regulator
Voltage
regulator
Voltage
regulator
12V
GND
Sensor
Sensor
Sensor
10x
Imax
I(t)
What about tomorrow?
Stella Orfanelli, ACES 2018

## Slide 18
How to get rid of copper (or aluminum) – serial powering
MIMOSIS:
still: (at low rate).
P
t
Data
transport
Data
transport
Data
idle
Data
idle
Data
idle
Thermal limit
Future sensors will show data streams of ~Gbps/cm² => “Data cost” may dominate power budget.
Data power may be pulsed (e.g. read buffer until empty) => Power spikes.
relevant for conventional powering.
sensor power relevant for serial powering.
May differ substantially.
If conventional powering – few action needed (as for MIMOSIS).
If serial powering => Must flatten power curve over time (optimized data transport… ) => new design philosophy.

## Slide 19
Serial powering – data transport…
Serial powering (“simple”)
DAQ
AC coupling
Data
Serial powering (advanced(?))
12V
Voltage
regulator
Sensor
Sensor
Sensor
Sensor
Optical
Data
DAQ
Voltage
regulator
Sensor
Sensor
Sensor
Sensor
Optical
Data
Voltage
regulator
Sensor
Sensor
Sensor
Sensor
Optical
Data
GND
DAQ
DAQ
Slave
Slave
Master
Combining serial powering with Master-Slave data readout (as realized in ALPIDE)
and optical links might be interesting.

## Slide 20
A wilder dream
Amplification layer
e
Optimized MAPS/LGAD sensing node possibly
with analogue front-end
Minimize “analogue power”
Optimized digital process with low core
voltage and high density.
=> Reduce “data cost”
Through silicon vias
Monolithic optical transceiver
Optical fiber
Monolithic Optical Transceiver – Followed up by the Helmholtz Innovation pool project SOPHIE (DESY, KIT, GSI)
Light feed in
Voltage steered modulator

## Slide 21
Summary and conclusion
Future detectors in Relativistic Heavy Ion physics have to:
Perform precision tracking/vertexing at low momentum
  Need lowest material budget.
Reconstruct particles like open charm
  Need best possible vertexing capability, ~5 µm spatial precision.
Need time stamping of ~1ns at rates of >100 MHz/cm² and rad. hardness of ~1015neq/cm².
Detectors would preferably be air-cooled to reach material budget goals.
Low power dissipation is driving design constraint.
Serial powering might be required for bigger systems.
Technological approaches include:
Next generation sensor readout based on fixed priority arbiter.
Integration of time walk correction based on time-over-threshold.
Tuning power vs. performance locally for best system performance.
LGAD charge amplification in MAPS.
Monolithic optical transceivers.
Light weight and low power serial powering…
2 tier sensors (digital tier for low power data processing/transport).
Followed up by DESY+GSI (DRD3/OCTOPUS and MANTA
Followed up by GSI + DESY (DRD3/MANTA)
Followed up e.g. by GSI (DRD3/CASSIA)
Followed up by DESY + KIT + GSI (HELMHOLTZ/SOPHIE)
Not covered
Combining those elements might create outstanding next generation instruments for future research.
Followed up by GSI (ALICE3)
Followed up by KIT (DRD7.6b)