## Slide 1: 4D Particle Tracking with LGAD Strip Sensors and the DOGMA Readout System
Yevhen Kozymka for the HADES LGAD Team at the 11th annual MT Meeting

## Slide 2: Low Gain Avalanche Diode Detectors (LGADs)
Thin silicon detectors optimized for timing performance
  high electric field in gain layer (> 300 kV/cm)
    intrinsic signal amplification
    large signals with short rise times (< 1 ns)
Bulk gain optimization
  high gain also amplifies noise
    shot noise rises faster than signal
    leads to signal fluctuations (jitter)
    deteriorates timing performance
  LGADs are operated at relatively low gain (G 10-30)
Source: [1]

## Slide 3: Front-end electronics
Amplification based strategy
GSI amplification board for LGAD/diamond
  128 channels
  AC coupled
  Single- or double-sided readout
  60 ps for MIPs
  < 30 ps for C ions
  Voltage gain: 400
AC coupling
Stage 1
Stage 2
128-channel readout board
Pad diamond sensor
Strip LGAD sensor

## Slide 4: DOGMA Readout Framework
Best effort DAQ paradigm
Automatic fast reintegration after reboot
  Higher reliability and fault tolerance
  Enables use of commercial and cheap FPGAs
Optical data transmission and < 10 ps RMS clock
  No GND issues due to galvanic isolation
  Scaleable
Arbitrary system size due to no handshake latency
Ethernet protocol for easy and cheap upgrades
Keep it Small and Simple
  Easy to maintain for small teams

## Slide 5: DOGMA Readout Implementation
Dogma Control Module
  Communication with DOGs
  Trigger and clock distribution
  Add-ons for more ports possible
DiRICH5d2 modules
  32 channel readout
1 GbE connection to switch
10 GbE data to servers
Switches can be added
 Used during beam time
DOGs
DCM
Source: [2]

## Slide 6: DOGMA Readout Electronics
Pre-amplifier
Main FPGA
  Discriminator, TDC, DAQ, ethernet, slow control, etc.
Satellite/threshold FPGA
JTAG connector
Physical reset button
Power connector
SFF optical ports
  DCM and switch labelled

## Slide 7: 4D Tracking iCT Setup
 Talk by F. Ulrich-Pur at 12:30
2 m long frame to fix modules
PCBs fixed to plexiglass pane
6 layers with 2 X-Y-tracking LGADs each
45 channels per LGAD, 540 channels total
Mouse placed between layers 2 and 3
90 cm ToF path between layers 4 and 5
CAD model of setup, distances not adjusted
CAD model of one layer
Laser alignment

## Slide 8: CBM T0 Performance Study
 Talk by M. Kis / J. Pietraszko tomorrow at 10:30
Diamond layer placed behind iCT setup
Read-out connected after scope analysis
Single-sided 6 x 6 pad sensor with aluminium metallization
Efficiency analysis at different beam energies

## Slide 9: 4D Setup Performance
Full analysis chain
  Time over threshold normalization
  Time walk correction
  Cluster identification
Best timing performance so far
  60 ps for 800 MeV protons
Tomography of sacrificed mouse
  4D tracking algorithms currently WIP
Methods for diamond study developed
DAQ issues encountered
  Lower DAQ rate
  SEU data corruption

## Slide 10: Outlook
Two beam times at MedAustron in Dec./Jan.
  Live mouse radiography
  Diamond irradiation level study
Cold box construction to demonstrate < 50 ps with MIPS
Setup for laser driven beam at ELI-NP
  Vacuum operation
  Shielding concerns
DOGMA improvements
  DAQ rate investigation
  SEU prevention

## Slide 11: Thank you for your attention!

## Slide 12: References
Sadrozinski, Hartmut F-W et al. (2017). “4D tracking with ultra-fast silicon detectors”. In: Reports on Progress in Physics 81.2, p. 026101. DOI: 10.1088/1361-6633/aa94d3
The DOGMA DAQ System. dogma.gsi.de
Ulrich-Pur, F. et al. (2022). “Feasibility study of a proton CT system based on 4D-tracking and residual energy determination via time-of-flight”. In: Physics in Medicine & Biology. ISSN: 0031-9155, 1361-6560. DOI: 10.1088/1361-6560/ac628b
Johnson, Robert P (2017). “Review of medical radiography and tomography with proton beams”. In: Reports on Progress in Physics 81.1, p. 016701. ISSN: 0034-4885, 1361-6633. DOI: 10.1088/1361-6633/aa8b1d
Ulrich-Pur, F. et al. (2023). “First experimental time-of-flight-based proton radiography using low gain avalanche diodes”. In: Physics in Medicine & Biology. DOI: 10.1088/1361-6560/ad3326