## Slide 1
Ph. Pfäfflein, F. M. Kröger, D. A. Müller, J. Walch, M. O. Herdrich,
S. Allgeier, M. Friedrich, D. Kreuzberger, A. Abeln, H. Hadenfeldt, P. Kuntz,
Günter Weber, D. Hengstler, A. Fleischmann, Chr. Enss, Th. Stöhlker and many more…
Adaption of Metallic Magnetic Calorimeters to Precision X-ray Spectroscopy at Ion Storage Rings

## Slide 2
The demonstrated energy resolution of cryogenic microcalorimeters has seen large improvements over the last decades …
… making microcalorimeters a very promising detector technology for x-ray science.
Spectroscopic performance at 6 keV
Cryogenic Microcalorimeters for Precision X-Ray Spectroscopy
Temperature change
Operation at low temperature (T < 0.1 K):
→ small specific heat
→ large temperature change
→ low thermal noise
Spectral resolution of semiconductor detectors
1 – 2 orders of magnitude improvement

## Slide 3
Microcalorimeter Arrays for High-resolution X-ray Spectroscopy - maXs
maXs-100 design parameters | 
Active area: | 100 mm2 (64 pixels, 1.25 x 1.25 mm2 each)
FWHM at 60 keV: | <50 eV
Efficiency at 100 keV: | 17 % (50 µm) – 35 % (100 µm)
Operating Temperature: | <20 mK
maXs-100
developed within
by Chr. Enss, A. Fleischmann et al.
Metallic Magnetic Calorimeter (MMC)
Cryostat
Gas Handling
Control System
maXs Detector
1 cm
Notes: Area comparable to high res semiconductor detectors

## Slide 4
Microcalorimeter Arrays for High-resolution X-ray Spectroscopy - maXs
Metallic Magnetic Calorimeter (MMC)
Cryostat
Gas Handling
Control System
maXs Detector
1 cm
50 eV
Spectral resolution almost a factor 10 better
than with a semiconductor hard x-ray detector.
241Am
Notes: Area comparable to high res semiconductor detectors

## Slide 5
Microcalorimeter Arrays for High-resolution X-ray Spectroscopy - maXs
Metallic Magnetic Calorimeter (MMC)
Cryostat
Gas Handling
Control System
maXs Detector
1 cm
CRYRING@ESR
Notes: Area comparable to high res semiconductor detectors

## Slide 6
MMC Setup at CRYRING@ESR
180° detector
0° detector
CRYRING electron cooler
3.5 m
P. Pfäfflein et al., Phys. Scr. 97, 114005 (2022)
U91+
U91+ + e- → U90+ + X rays

## Slide 7
U91+ beam
10 MeV/u
maXs
180°
maXs
0°
e- beam
30 mA
Radiative recombination followed by photon emission
U90+ ions
P. Pfäfflein et al., Phys. Scr. 97, 114005 (2022)
U90+ ions
stopped by particle detector
Coincidence
condition
P. Pfäfflein et al., Atoms 11, 5 (2023)
Spectroscopy Setup and Experimental Technique at CRYRING@ESR

## Slide 8
X-Ray Spectroscopy of Heavy He-like Systems
He
U90+
Δ(w-x) = 74 eV
Δ(y-z) = 142 eV
Y. S. Kozhedub et al., Phys. Rev. A 100, 062506 (2019)
A. Gumberidze et al., PRL 032712 (2004)
K2
K1
≈100 keV
1s2p 1P1
1s2p 3P2
1s2p 3P0
1s2p 3P1
z
x
w
y
1s2s 1S0
1s2s 3S1
1s2 1S0
He-like Uranium
No precision spectroscopy data
for L → K transitions
available for He-like systems
with Z > 54.
Data taken from P. Indelicato, J. Phys. B: At. Mol. Opt. Phys. 52, 232001 (2019)
±100 eV
Heavy He-like systems:
Most fundamental atomic system to study many-body interaction at extreme field strengths (aZ ≈ 1).

## Slide 9
Δ(w-x) = 74 eV
Δ(y-z) = 142 eV
Y. S. Kozhedub et al., Phys. Rev. A 100, 062506 (2019)
K2
K1
He
U90+
X-Ray Spectroscopy of Heavy He-like Systems
A. Gumberidze et al., PRL 032712 (2004)
z
y
x
w
For high-Z systems a spectral resolution of <100 eV FWHM is necessary to resolve the n=2 level structure and benchmark state-of-the-art theory.
This cannot be achieved with conventional semiconductor detectors. Thus, a new experimental approach is needed.
≈100 keV
1s2p 1P1
1s2p 3P2
1s2p 3P0
1s2p 3P1
z
x
w
y
1s2s 1S0
1s2s 3S1
1s2 1S0
He-like Uranium
No precision spectroscopy data
for L → K transitions
available for He-like systems
with Z > 54.
Heavy He-like systems:
Most fundamental atomic system to study many-body interaction at extreme field strengths (aZ ≈ 1).

## Slide 10
Preliminary Results
z
y
x
w
180°
0°
z
y
x
w
Preliminary Results
[1s1/2,2s1/2] 1S0
[1s1/2,2p1/2] 3P0
w (E1)
x (M2)
z (M1)
[1s1/2,2s1/2] 3S1
[1s1/2,2p3/2] 3P2
[1s1/2,2p1/2] 3P1
[1s1/2,1s1/2] 1S0
[1s1/2,2p3/2] 1P1
74 eV
142 eV
y (E1)
Results 2021 beam time: U90+ Ka (L → K) transitions
Ka2 transitions resolved for the first time in a heavy He-like system.
☺
About 150 Ka photons were recorded in each detector with DEFWHM < 100 eV.
Ka2
Ka1
Ka2
Ka1

## Slide 11
Results 2021 beam time: U90+ Ka (L → K) transitions
Sum of both spectra in the emitter frame.
Maximum likelyhood adjustment of four Voigt-shaped peaks (including natural line width) in both detectors to obtain the line positions.
P. Pfäfflein et al., Phys. Rev. Lett. 134, 153001 (2025)

## Slide 12
Results 2021 beam time: U90+ Ka (L → K) transitions
First high-precision data on Ka transitions in a high-Z system (Z > 54). No indication of a systematic deviation.
☺
P. Pfäfflein et al., Phys. Rev. Lett. 134, 153001 (2025)

## Slide 13
Comparison of the present measurements and theoretical predictions of the transition energies as well as the ground state energy.
D: Drake, P: Plante, C: Cheng, K: Kozhedub (versus reference Artemyev et al.)
Still far away from 1 eV accuracy
Results 2021 beam time: U90+ Ka (L → K) transitions
Experimental accuracy not sufficient to distinguish between different theoretical treatments. Uncertainty is mainly stemming from statistics, thus we need more photons.

## Slide 14
2025 surprise: instabilities due to accelerator operation
HOT FIX:
Mitigating measures with help of GSI Detector Laboratory.
Hardening/optimization of the detector system needs frequent field tests in the harsh environment of accelarators/storage rings.

## Slide 15
Thank you for your attention :-)
And many thanks to all the colleagues involved in this work.