## Slide 1: Status of the Pulsed Electron Lens for Space Charge Compensation at GSI
K. Schulte-Urlichs, GSI
MT Meeting, 05.11.2025

## Slide 2: Motivation
Space charge represents a major intensity limitation in larger circular accelerators
R&D to increase the primary beam intensity and thus accelerator efficiency for FAIR operation
Electron Lens for SCC
  Counter defocusing self-SC with electrons
  Modulate e-beam to follow bunch profile
  Linear compensation
    Uniform transverse profile
    linear fields avoiding resonance creation
  Symmetry typically requires several lenses
Strategy
  Design of dedicated e-lens for SIS18
    Design shall be compatible with SIS100
  SIS18 e-cooler as test bed for e-gun and collector to demonstrate the concept
Electron Lens Prototype for Space Charge Compensation (SCC)
Modulation to match bunch profile
SCC scheme
Synchrotron | dQ
PS Booster | up to -0.69
PS | up to -0.39
SPS | up to -0.21
AGS Booster | up to –0.3
AGS | up to -0.25
JPARC RCS Booster | up to -0.35
JPARC Main Ring | up to -0.4
ISIS SR | up to -0.4
SNS SR | up to -0.15
Fermilab Booster | up to -0.6
SIS18 | up to -0.5
SIS100 | up to -0.3 (planned)
Er
courtesy of P. Spiller, Talk, IPAC24, WEBD3

## Slide 3: Design of Modulated Electron Gun
Requirements of design result from the SIS18 cycle:
  400 kHz to 1 MHz to follow longitudinal bunch profile
    grid modulation to reduce load, 3 kV on grid
    two different types of modulation grid
  up to 15 A @ 35 kV for SCC
  modulator design
    prototype within ARIES WP16
    technical concept was developed
  transverse, homogeneous beam density profile
    immersed in solenoidal field of up to 0.4 T
    despite elliptical cross section of bunch, round cross section was chosen
Evaluation of transverse beam density profile
kurtosis:
kurtosis: 1.97
kurtosis: 1.99
normalized current density
evaluation of kurtosis
Electrode design with target grid
Electrode design with honey comb grid

## Slide 4: Design of Modulated Electron Gun
Status of rf-modulated E-Gun:
Preparation of preliminary e-gun design with two different grids by GSI
  flexible set-up to exchange grids
  BaO dispenser cathode 311XM to meet current density requirements 4 A/cm2
Production contracted in April of this year
E-gun is currently being redesigned by NTG
Expected delivery in May 2026
Commissioning at GSI test stand
E-gun layout by NTG (current status)
Evaluation of dielectric strength
E-gun design by GSI

## Slide 5: Design of Low Loss Collector
Design Challenges:
collector is operated on a HV platform and has bias potential DU with respect to cathode to reduce power loss
beam potential increases by deceleration
  leads to reflection of beam for low DU between e-gun and collector
  DU=10 kV required for conventional design
magnetic cusp field helps to rapidly expand beam
  reduce beam potential
  distribute beam over large area
  reduction of power deposition by ~50%
Collector integrated into cusp field
B
z / mm
Velocity ratio of electrons in cusp field
Peak power deposition
E-lens is only used in the beginning of the SIS18 cycle, this reduced the power deposition by ~0.3.
Secondary electron mitigation
SEE backflow:
Iback,total=11.1mA
collector efficiency: >99.9%

## Slide 6: Design of Low Loss Collector
Design of collector chamber
Collector Parameters |  | 
Electron current max. | 15 | A
Collector bias potential max. (represents max. electron energy) | -5.5 | kV
Beam modulation frequency | 400 – 1000 | kHz
Inner collector radius max. | 215 | mm
Outer collector radius | 242 | mm
Beam radius | ≥ 215 | mm
DC power deposition | 82.5 | kW
Power deposition within cycle, max. | 20 | kW
Collector area | 1452 | cm2
Max. magnetic field | 0.4 | T
Collector chamber height | 66 | mm
Design of collector magnets
Technical Challenges:
chamber must have a small height compared to the diameter
separate cooling channels are required to allow deducing beam power distribution from the temperature of the water backflow
requires the use of advanced manufacturing methods

## Slide 7: Test Bench at GSI
Test bench set-up:
commissioning of e-gun and collector
  demonstration of extraction currents up to 15 A and beam profile
reusage of equipment as power supplies, vacuum pumps and solenoids from 100 keV COSY e-cooler @ FZ Jülich
used in different stages according to the experimental requirements
  stage 1
    existing collector with power depostion up to 10 kW and smaller aperture compared to beam diameter
    preparation of transverse and longitudinal beam diagnostics
  stage 2
    commsioning of low loss collector
    characterization of e-beam and operation modii
stage 1
Gun: 2.4A @ 8.5kV
collector: 9.5kW
Electron beam trajectories

## Slide 8: SIS18 E-Cooler as Test Bed
Modification of SIS18 E-Cooler:
E-Cooler is in Sector 10 of SIS18
Electron cooler has a maximum B-field of 0.15 T in the interaction section and 0.4 T in the gun and collector branches
simulations indicate that cooler field magnitude is feasible for demonstration experiments
The design of the electron gun and collector has been adapted so that it can be integrated into the cooler.
  An additional solenoid is provided to adjust the collector system to the length of the beam tube.
next step: planning of demonstration experiments with “single lens”
SIS18 e-cooler
Modified SIS18 e-cooler set-up
Concept study: beam transport simulations

## Slide 9: Outlook
Preparation of demonstration experiments
Set-up of test bench at GSI
Commissioning of rf-modulated e-gun
Construction of low loss collector
Modification of SIS18 e-cooler and machine experiments
Design of demonstrator electron lens is under preparation in parallel

## Slide 10
Special thanks to all contributors to this project:
M. Droba2, M. Kirk1, O. Meusel2, D. Ondreka1, J. Rausch2 , P. Rottländer1, P. Spiller1, K. Thoma1,2
1GSI Helmholtzzentrum für Schwerionenforschung GmbH,
2Goethe-University Frankfurt
Thanks for your attention!