## Slide 2: Deployment and Development of MicroTCA at ESS
PRESENTED BY faye chicken

## Slide 4
Layer Architecture of ESS Control Systems
ESS Main Control Room
Experiment workstations
other human interfaces
EPICS
Timing System
Fieldbus
Personnel Safety Systems
H2O Flow
He Flow
RF
Proton
Neutron
Temp
Electricity
Mech. Movement
Machine Protection
Device signals
Remote
I/O
Controller
PLC
EPICS
IOC
EPICS
IOC
Controller
etc.
PLC
MicroTCA
System
Ether
CAT
MicroTCA
System
Remote
I/O
Alarms
EPICS
IOC
Config.
Tools
Device
Electronics
Remote
I/O
Techncal Network
Data on
Demand
Event
Generator
Fast Beam
Interlock System
NICOS
DMSC
PSS
PLC
Chopper
Power Supply
Sensor
Motor
Pump
Flowmeter
PSS
GUIs
Device
Electronics
Switch
Sensor
Sensor
EPICS
IOC
EPICS
IOC
Archiver
Magnetic
Equipment
GUIs
Alarm Server

## Slide 5: Control Systems deployed at ESS

## Slide 6: MTCA at ESS
  Have ≅250 MTCA systems in production
  Supporting Timing Distribution, LLRF, Beam Instrumentation and Fast Beam Interlock for Machine Protection.
  Many systems are now mature and running for significant time without issue
  >70% migrated to ESS Linux OS

## Slide 8: Alarm Service

## Slide 9: Replacement of Arc Detector Controls
Analog readout of the arc detectors on the RF distribution chain.
Whenever there is an arc inside cavities, they want to be able to correlate with LLRF data. Need the classic “scope” application to properly acquire these signals. Currently one oscilloscope in each RF station to digitize the signals and integrate to EPICS
Migration to MTCA based system to use hw from IOxOS
  IFC_1420 (modified for DC)
  RAA_1471 RTM

## Slide 10: Replacement of Modulator Controls System
Currently running on NI CompactRIO HW
Change to use:
  nVent 5U (baby) Chassis
  NAT-PM-AC600D
  NAT-MCH-PHYS80
  IOxOS IFC_1412
    ADC_3117
    DIO_3118

## Slide 11: Next Steps for 2026
BOD2 and BOT and production of first neutrons
Complete migration of MTCA systems to ESS Linux OS (Yocto)
Development of Arc-Detector system using IOxOS IFC and new RTM
Conversion of Modulator controls from CompactRIO to MTCA

## Slide 12: Conclusions and lessons
Knowledge sharing is key; avoid brain drain and costly roadbumps
Collaboration is important; EPICs community has shown how impactful
Make full use of deployment tools from other groups/facilities
Good relationships with suppliers is critical; for questions/information but also product development
“If I had asked people what they wanted, they would have said faster horses.”
- Henry Ford

## Slide 13: End