## Slide 1: Update on the development and deployment of the MicroTCA based detector controller, NGCII
Mathias Richerzhagen, Matthias Seidel, Alexander Rüde,
Max Engelhardt, Omar Sqalli

## Slide 2: Abstract: In the time since the last MicroTCA workshop we have achieved laboratory first-light with the final two detector families to be supported by our MicroTCA.4 based general detector controller, NGCII. Besides CCDs, the workhorse detector for ground-based astronomy, we have also brought up Geosnap, a fully digital detector transmitting its pixel data through high-speed digital signals. Meanwhile, we are in the process of preparing CMOS detector systems for large scale deployment. We are developing test tooling for post-production testing, estimating the need for, and starting the procurement of spare parts, and are in the process of performing final environmental tests for CMOS detector specific systems.

## Slide 3: It moves!

## Slide 4: System Overview
MicroTCA Based Detector Controller - Recap
Detector
Interface
Network
Interface
AC or DC
Power

## Slide 5: Detector Status

## Slide 6: Analog CMOS Detectors
  Detector performance fully validated in 2023 and 2024
  Need to deliver ~25 Systems in 2026 and 2027
HAWAII-xRG Hybrid CMOS / SAPHIRA eAPD CMOS

## Slide 7: Analog CMOS Detectors
  All assembly and testing done in-house.
  Very limited external delivery.
HAWAII-xRG Hybrid CMOS / SAPHIRA eAPD CMOS
Prototype
Pre-Series
Series
  Assembly and testing done by external contractor.
  External delivery within Europe.
  Considered “Series” if environmental testing passes
  Assembly and testing done by external contractor.
  External delivery.
Managed by technology
development programme
Managed by directorate of engineering
Manufacturing Readiness Review
Environmental Test
We are here

## Slide 8: Analog CMOS Detectors
  Thermal Test (In-House):
  ✅High-Temperature Operation (+40°C)
  ✅Low-Temperature Operation (+0°C)
  ✅Cold Start (−10°C)
  ✅Survival (−5°C to +45°C)
Environmental Test
  EMC Immunity Test (External Test Site):
  ✅IEC61000-4-2 Electrostatic Discharge (8kV/15kV)
  ✅IEC61000-4-8 Power Frequency Magnetic Field
  ✅IEC61000-4-3 Electromagnetic Field
  ✅IEC61000-4-4 Burst
  ✅IEC61000-4-6 Conducted RF
  EMC Emission Test (External Test Site):
  ✅CISPR 11 Radiated Emission

## Slide 9: Fully Digital Detectors
Geosnap 2K x 2K Mid-IR (13.5µ) Detector
Detector Head
With ROIC
NGCII
Controller
8x 1.6Gbps

## Slide 10: Fully Digital Detectors
Geosnap 2K x 2K Mid-IR (13.5µ) Detector
Test Pattern Image
Visible Light Mask Image
First time reading fully-digital detector at ESO, enabled by MicroTCA

## Slide 11: Analog CCD Detectors
  First light achieved!
  3e−RMS noise observed
    Same as previous controllers
  Different parameters than other controllers
  Very analog detector control, complex debugging necessary and ongoing.
What a selection! – This is a subhead for an emotional addition to the headline

## Slide 12: Miscellaneous

## Slide 13: Self-Test Software
Everything linked by ESO-Global Asset Tags
Integrated Test System
© xnimrodx – Flaticon
© Payungkead – Flaticon
© Icongeek26 – Flaticon
© Freepik – Flaticon
1
2
3
Web-Browser Client
PyTest Based
Test Server
SSH Tunnel through
Detector Workstation
Device-under-test
With Loopback Plug
S3 Report Storage
Bucket
IBM Maximo Inventory
+ JIRA Ticket System

## Slide 14: Shopping List
We’d like to buy a few mechanical parts!
500x FMC Filler Panel
100x Mid-Size to Full-Size Adapter
250x Native R2x Air Filter
30x Native R2x Spare Fan Tray

## Slide 15
@ESOAstronomy
@esoastronomy
@ESO
european-southern-observatory
@ESOobservatory
Mathias Richerzhagen
mathias.richerzhagen@eso.org