## Slide 1: Few-femtosecond IR pump-UV probe spectroscopy in liquid phase
İdil Şimşek
Koç University, Turkey
DESY group: FS-ATTO
DESY Summer Programme, Hamburg

## Slide 2: Ultrafast dynamics in liquid
Aim: Studying the effects of the liquid environment on chemical reactions in biological systems
Hemoglobin & iron tris bipyridine
Pump-probe spectroscopy
Few-fs time resolution
NCBI PubChem, CID 6857601. Retrieved Sept 8, 2025.
| Few-femtosecond IR pump-UV probe spectroscopy in liquid phase | İdil Şimşek, 10.09.2025

## Slide 3: Pump-probe spectroscopy
Aim: seeing how the absorption feature of the sample changes when it’s excited.
Pump pulse (IR) excites the sample
Probe pulse (UV) captures the optical response
The delay between the pump and the probe is adjusted with each measurement
Adapted from Giovannetti et al., Research Square Preprint (2025), DOI: 10.21203/rs.3.rs-6745336/v1
| Few-femtosecond IR pump-UV probe spectroscopy in liquid phase | İdil Şimşek, 10.09.2025

## Slide 4: Generation of short pulses
Time-bandwidth product:
Broader spectrum = shorter pulse
Things to discuss:
  Pump
  Probe
  Delivery system
| Few-femtosecond IR pump-UV probe spectroscopy in liquid phase | İdil Şimşek, 10.09.2025
Rockenstein et al., Univ. Hamburg Lab Manual (May 2024).

## Slide 5: Pump: Photoexcitation of Fe complex
Iron Tris Bipyridine Absorption Spectrum
Auböck & Chergui, Nature Chem 7, 629–633 (2015).
| Few-femtosecond IR pump-UV probe spectroscopy in liquid phase | İdil Şimşek, 10.09.2025
NIR Pump Spectrum
Giovannetti et al., Research Square (2025), Supplementary Info.

## Slide 6: Probe: Generation of UV light
| Few-femtosecond IR pump-UV probe spectroscopy in liquid phase | İdil Şimşek, 10.09.2025
Fundamental beam
(700-800 nm)
Third harmonic
(~233-267 nm)
“Components of electromagnetic spectrum,” PrimaLuceLab (2025).
.
response of a medium towards an EM field:
Nonlinear Optics
ω
ω
3ω

## Slide 7: Probe: Generation of UV light
Wanie et al 2024 J. Phys. Photonics 6 025005
| Few-femtosecond IR pump-UV probe spectroscopy in liquid phase | İdil Şimşek, 10.09.2025
Wanie et al 2024 J. Phys. Photonics 6 025005

## Slide 8: Delivery system: Flow cell
Aim: liquid sample delivery in vacuum
No dispersion
Advantages:
Isolated system from vacuum
Easy liquid control
Disadvantages:
Needs a window, requires UV-transparent materials
Small aperture, losing counts
Nasri et al., Poster, Universität Hamburg & DESY (2025).
| Few-femtosecond IR pump-UV probe spectroscopy in liquid phase | İdil Şimşek, 10.09.2025

## Slide 9: Delivery system: Flow cell
Results: [Fe(bpy)3]2+
| Few-femtosecond IR pump-UV probe spectroscopy in liquid phase | İdil Şimşek, 10.09.2025
Plotted data is courtesy of FS-ATTO group.

## Slide 10: Delivery system: Flow cell
Results: [Fe(bpy)3]2+
| Few-femtosecond IR pump-UV probe spectroscopy in liquid phase | İdil Şimşek, 10.09.2025
Plotted data is courtesy of FS-ATTO group.
Water
Iron complex in water

## Slide 11: Conclusion
Few-femtosecond UV pulses: allow investigation of molecular dynamics on their native time-scale
A way of generating UV light: Third harmonic generation
Proof of concept for studies of iron complexes
| Few-femtosecond IR pump-UV probe spectroscopy in liquid phase | İdil Şimşek, 10.09.2025

## Slide 12: Acknowledgements
CFEL-ATTO, Germany
Ana Lambert-Bernal
Sabine Rockenstein
Kai-Fu Wong
Linda Oberti
Lorenzo Pratolli
Keerthana Ravi
Fatemehsadat Ghaffari
Ana Oliveira e Silva
Oliviero Cannelli
Terry Mullins
Aurelien Sanchez
Kate Robertson
Felix Ritzkowsky
Katinka Horn
Ammar Bin Wahid
Agata Azzolin
Marc Seitz
Sergey Ryabchuk
Vincent Wanie
Andrea Trabattoni
Erik Månsson
Francesca Calegari
Special thanks to our supervisors!
THANK YOU!
| Few-femtosecond IR pump-UV probe spectroscopy in liquid phase | İdil Şimşek, 10.09.2025

## Slide 13: SUPPLEMENTARY SLIDES

## Slide 14: Generation of UV Light
Harmonic Generation as a Route to UV - Theory
response of a medium towards an EM field:
the second-order polarisation contribution when we have two fields:
second harmonic generation (SHG)
sum-frequency generation (SFG)

## Slide 15: Generation of UV Light
Harmonic Generation as a Route to UV - Theory
We select the frequencies to survive via phase matching.
The SFG field needs to be in phase with the fundamental field, i.e.,
so that
This condition boils down to
and can be fulfilled by adjusting the angle of the crystals used for generation.
Third harmonic generation:
1) high and high fundamental beam intensity
2) SHG (ω → 2ω) + SFG ( ω + 2ω → 3ω)
SHG
SFG

## Slide 16: Generation of UV Light
first BBO
second BBO
fundamental beam (700 nm)
second harmonic (350 nm)
third harmonic (~233 nm)
second BBO*
first BBO*
HWP
calcite plate
*BBO ≡ Beta-Barium Borate
Harmonic Generation as a Route to UV - Cascaded Approach Experimental Setup and Results

## Slide 17: Generation of UV Light
Harmonic Generation as a Route to UV - Experimental Setup with Delay Stage
spectrometer
second BBO
first BBO
HWP
delay stage
fundamental beam (800 nm)
second harmonic (400 nm)
third harmonic (~267 nm)
dichroic mirrors

## Slide 18: Generation of UV Light
Resonant Dispersive Wave (RDW) Emission: Towards Tunable UV - Theory
Because of nonlinear effects, the spectrum broadens and there is dispersion which are compensated by the chirped mirrors outside.
In RDW, rather than using chirped mirrors to compensate for the dispersion, we configure the system so that the compensation happens inside the waveguide.
Travers et al. 2019, Nat. Phot. 13 547 (2019)

## Slide 19: Generation of UV Light
Resonant Dispersive Wave (RDW) Emission: Towards Tunable UV - Experimental Results
Silletti et al. 2025, APL Photon. 10, 026818 (2025)
Results:
very short pulse
easily tuneable across UV unlike the direct or cascaded third harmonic generations!

## Slide 20: Liquid Jet
Advantages:
Reduced sample damaging
Controlled thickness and size
Long stability
Challenges:
Clogging
Pressure and temperature conditions
Advantages & Challenges

## Slide 21: Liquid Jet
Aim: understand the properties of aqueous solutions
Sample: Water & [Fe(bpy)3]2+
Requirements:
In vacuum
Ultrathin
Introduction
Giovannetti et al., Research Square Preprint (2025), DOI: 10.21203/rs.3.rs-6745336/v1

## Slide 22: Liquid Jet
Liquid Jet Stage Setup
Conical catcher
Heater
3D stage manipulator
Micronit Chip
Flat sheet jet

## Slide 23: Liquid Jet
Setup of the Vacuum Chambers
Experimental Chamber
Catcher Bottle
HPLC
Glass Door
Gate valve
Turbomolecular Pumps
Reservoir
Membrane Pump
Sample
Vacuum Pump
Extension Chamber
Light Source

## Slide 24: Liquid Jet
Results: Water
All data that we plotted is courtesy of FS-ATTO group.

## Slide 25: Liquid Jet
Matlab Script
Python Script

## Slide 26: Liquid Jet
Results: Water FFT
All data that we plotted is courtesy of FS-ATTO group.

## Slide 27: Liquid Jet
Results: [Fe(bpy)3]2+
All data that we plotted is courtesy of FS-ATTO group.

## Slide 28: Liquid Jet
Results: [Fe(bpy)3]2+ FFT
All data that we plotted is courtesy of FS-ATTO group.

## Slide 29: Flow Cell
Results: Water
All data that we plotted is courtesy of FS-ATTO group.

## Slide 30: Flow Cell
Results: Water FFT
Reference Spectrum for Water
All data that we plotted is courtesy of FS-ATTO group.

## Slide 31: Comparison
Water
[Fe(bpy)3]2+
Flow Cell

## Slide 32: Comparison
Water
Iron Bipyridine
Liquid Jet
Flow Cell

## Slide 33: Comparison
Water
Iron Bipyridine
Liquid Jet
Flow Cell

## Slide 34: Liquid Jet
Results: Water FFT