## Slide 1: RF Technology for fundamental physics Hands-on instructions 3: Cavity field measurement with beads-pulling method and VNA
Akira Miyazaki

## Slide 2: Pill-box cavity modes
TMmnl
m |  |  | 
0 |  |  | 
1 |  |  | 
2 |  |  | 
m |  |  | 
0 |  |  | 
1 |  |  | 
2 |  |  | 
TEmnl
m |  |  | 
0 |  |  | 
1 |  |  | 
2 |  |  | 
m |  |  | 
0 |  |  | 
1 |  |  | 
2 |  |  | 

## Slide 3: Resonant cavity perturbation: Slater’s theorem
Material perturbation
Shape perturbation
Inserting a dielectric material shifts resonant frequency proportional to the fields
dielectric  pure measure
  Sapphire, Teflon, etc
material  pure measure
  Ferrite?
Deform the cavity wall at
E-field region: push in  lower frequency
H-field region: push in higher frequency
(energy conservation of work against Lorentz force)
Inserting a metal = decreasing the volume

## Slide 4: Frequency Perturbation  field measurement
VNA
Metal sphere with a radius
Metal sphere with a radius
Ellipsoidal bead could resolve field components
This is possible if we measure a resonator with a well-defined resonant frequency

## Slide 5: Non-resonant perturbation: Lorentz reciprocity
If the resonance is unclear and resonant frequency cannot be identified, change in reflection coefficient is
C.W. Steele. “A Nonresonant Perturbation Theory”. In: IEEE Transactions on Microwave Theory and Techniques 14.2 (1966), pp. 70–74
This w/ and w/o perturbation is useful even for non-resonators
Original field
perturbed field
Change in reflection coefficient is given by field and current integrated over the volume of the perturbing object

## Slide 6: List of interesting experiments
Redo 1-port calibration (review of Hands-on 2)
Identify fundamental mode and scan the field via the bead
Reconstruct the field distribution from the frequency shift
Reconstruct the field distribution from the reflectivity shift
Compare with the analytical solution
Try to measure higher order modes?