## Slide 1: Bunch Compression at the SwissFEL Injector Test Facility
Bolko Beutner
13.3.2014
SwissFEL Meeting

## Slide 2
Introduction
Bunch Compression Theory
Measurements at the SwissFEL Injector Test Facility
Conclusions
Contents

## Slide 3
Introduction

## Slide 4
FEL performance is determined by the peak current and the emittance – the charge density in 6D.
Low emittance and high peak current beams are required in the undulators, but not available at feasible electron sources.
Typically long beams are produced with low emittance and the compressed later.
Therefore compression should not dilute emittance to much (i.e. Space Charge Forces).
FEL Performance
Beam Requirements for SASE:
SASE Performance:

## Slide 5
Early compression would lead to high charge density beams at low energies which would increase the emittance.
Late compression would require the transport of long bunches trough the linac without emitance dilution, which is difficult (RF-curvature, wake fields, …)
Multi-stage-compression
  2 stages in case of LCLS, FLASH, and SwissFEL
  3 stages in case of xfel.eu
Were to compress the beam?
BC1
BC2

## Slide 6
Bunch Compression Theory

## Slide 7
Basic Principle
with

## Slide 8
Energy Chirp Generation

## Slide 9
Linear Compression

## Slide 10
Linear Compression with Uncorrelated Energy Spread
Typically the “full” compression is avoided…
each particle i has an individual “random” energy offset

## Slide 11
Simple Compression Setup
E0,k1,0 deg
E1,k1,phi
total energy E
Is this Ok?

## Slide 12
Nonlinear compression
E0,k1,0 deg
E1,k1,phi
total energy E
This is NOT Ok!
Can we tune the T566-term to compensate the E1 quadratic-term?
No since

## Slide 13
Linarised Compression
E0,k1,0 deg
E1,k1,phi
E2,k2,180deg
total energy E

## Slide 14
Energy Compensation
E0,k1,0 deg
E1,k1,phi
E2,k2,180deg
total energy E
Compensation of energy loss is required while the slope must be maintained.

## Slide 15
Energy Compensation
E0,k1,0 deg
E1,k1,phi
E2,k2,180deg
total energy E
Compensation of energy loss is required while the slope must be maintained.

## Slide 16
(Almost) General Solution for Single Stage BC
If x-band is not operated “anti-on-crest” an additional linear compression term plays a role.
E0,k1,0 deg
E1,k1,phi
E2,k2,180deg
total energy E
head

## Slide 17
Initial chirp from the gun affects the compression (“aR56”-term). An adjustment of FINSB02 phase proved useful to correct for it.
Adjust phase to remove incoming chirp
longitudinal axis
longitudinal axis
energy axis
energy axis
head
tail

## Slide 18
X-band is compensating the quadratic terms from:
  initial curvature
  Second order contributions in S-band RF (E0 and E1)
  T566-components in BC1
  T566-components in BC2 and Energy Collimator
  RF curvature from the C-band RF
  Quadratic chirp generated by self field interactions
Multi-Stage Compression
E0,k1,0 deg
E1,k1,phi
E2,k2,180deg
total energy E
BC 1
BC 2
Energy Collimator

## Slide 19
Multi-Stage Compression
head
tail
Coherent Synchrotron Radiation
Previous talks:
Operation Modes and Longitudinal Layout for the SwissFEL Hard X-Ray Facility
http://indico.psi.ch/conferenceDisplay.py?confId=308
Bunch Compression Optimization for SwissFEL
http://indico.psi.ch/conferenceDisplay.py?confId=1248
head
tail
Longitudinal Space Charge
tail
head
Longitudinal Wake Fields
  Forces generated by self field interactions have an effect on the compression but is affected by compression as well. Analytic calculations are very difficult.
  => Self-Consistent Tracking
  Iterative semi-analytic procedure to setup compression:
Peak current [A]
Iteration step

## Slide 20
Measurements at the SwissFEL Injector Test Facility*
*with contributions from the SwissFEL Injector Commissioning Team

## Slide 21
BC Movable Girder
alpha [deg] | B[T] at 200MeV | R56[mm]
0 | 0 | 0
1 | 0.0466 | -2.767
2 | 0.0931 | -11.07
3 | 0.1397 | -24.90
4 | 0.1861 | -44.27
5 | 0.2326 | -69.17
xfel.eu

## Slide 22
Bending angle needs to be set up to achieve a certain R56.
Analytic formula results can be checked with measurements.
BC Angle Setup
R56
longitudinal position
head
tail

## Slide 23
Compensation of magnetic fields with trim coils
Dispersion correction using orbit correctors either manually or with an SVD based method
BC Field Correction
f(x)=-26.6110258+1.50357605*x-0.018499*x**2 => Average geomagnetism of 28.4 uT
F10BC-MCRX10: = 0.20 A F10BC-MCRX20: = 0.24 A F10BC-MCRX30: = 0.24 A F10BC-MCRX40: = 0.23 A
Correction of position in dipole 4
Correction of angle at dipole 4

## Slide 24
Scan of downstream BPM position vs. quad current – position with “zero” slope is the optimum position.
After the BC girder is aligned the orbit offsets in the BC BPMs are removed.
BC Beam-Based-Alignment

## Slide 25
X-band Setup
X-band position/orbit setup:
Alignment of X-band cavity to minimise emittance growth and wake fields.
horizontal [micron]
vertical [micron]
Voltage [V]
Wake field monitor
Projected Emittance vs. beam offset in X-band

## Slide 26
Calibration of energy gain of each structure against the RF input power using the spectrometer.
RF Power Calibration

## Slide 27
Set RF phases of all stations with scan tool to nominal. This is low energy spread for FINSS, on-crest for the FINSB01-04 and 180deg in FINXB.
Measure beam energy after FINSB02 (FINSB034 and FINXB off)
Set on-crest beam energy with FINXB off to nominal
Match Optics
Setup Procedure
FINSB03
FINXB

## Slide 28
All calculations are done in a small GUI
Required energy gains (losses) in the RF structures are calculated
A calibrated RF power setup of the voltages is used for setup
As a backup an procedure using the spectrometer dipole can be used to set the RF without precise calibration of the voltage vs. power
Calculate RF Parameters

## Slide 29
Phase Space Linearisation in WLHA
head
head
head
on-crest
xband off
xband on
Spike is resolution limited

## Slide 30
Longitudinal Measurements with TDC
Longitudinal bunch profiles are measured using the TDC.

## Slide 31
After carefully machine set-up bunch compression factors can just be “dialled” in.
“Blind”-setup is in principle possible but a TDC is still increasing the reliability (i.e. initial chirp removal or measurement)
Compression Measurements

## Slide 32
Slice emittance increases for compression factors higher than about 5-6.
Uncorrelated (slice) energy spread increases for compressed beams.
Examples:
First Observations

## Slide 33
Due to the conservation of longitudinal emittance the energy spread scales with the compression factor.
Off-axis longitudinal fields in the transverse deflector increase the uncorrelated energy spread. This effect is not dominant in WLHA
Energy Spread and Compression
longitudinal position
energy

## Slide 34
For chirped electron beams the vertical spot size (the longitudinal resolution) generates artificial energy spread contributions.
Energy Spread and Compression
vertical axis (longitudinal)
horizontal axis (energy)
slope S
vertical resolution/ spot size
The measurement is dominated by the
.

## Slide 35
Slice and projected emittance increases about linear (?) with the compression factor .
Slightly stronger increase in the horizontal plane.
  => CSR?
Emittance vs. Compression Factor

## Slide 36
While the projected emittance, in both planes, depend on the energy
the slice emittance is conserved.
Emittance vs. Energy

## Slide 37
Emittance vs. BC Angle
The compression factor was kept constant while the bending angles, and thus the R56, were varied. => varying energy chirp
Emittance is clearly diluted at higher angles. => CSR interactions (?)

## Slide 38
To identify contributions from dispersion the beam is accelerated on both flanks of the RF wave.
Energy spread is the same but the sign of the chirp is reversed.
Emittance is only diluted in case of compression.
Dispersion?
phase
voltage
compressed beam
de-compressed beam

## Slide 39
The emittance growth can be mitigated by adapting the optics along the chicane.
Emittance growth due to CSR is affected by the optics in the chicane.
More studies are required...
Optics

## Slide 40
Conclusions

## Slide 41
Procedures for the operation and setup of the Compression were developed and tested.
Bunch Compression at the SwissFEL Injector Test Facility is successfully used and in agreement with the theory.
Confirmation of the basis for the SwissFEL compression design.
Effects from compression on energy spread can not be determined due to chirp
Beam emittance, or their measurement, is growing stronger then expected.
  CSR is a likely candidate, but the effect is too strong
  Initial correlations in the beam
  ….
Emittance growth studies require more studies.
  Laser studies
  Comparison horizontal vs. vertical plane
  …
Summary and Outlook

## Slide 42
Thank You for Your Attention!
Special Thanks to:
Masamitsu Aiba, Simona Bettoni, Gian Luca Orlandi , Eduard Prat, Thomas Schietinger
and to the
WLHA Team