meets

---
Prologue
SHiP is an approved CERN experiment
“Approved” means that CERN agreed to refurbish the Beam Dump Facility in the ECN3 experimental hall
Now formation of detector collaboration
Many components in very preliminary state in many aspects
This concerns in particular layout of Scattering and Neutrino Detector (SND, see later)
Possible application of our SiW ECAL R&D in real experiment
Relevant physics case

---
Silicon Tungsten electromagnetic calorimeter
Optimized for Particle Flow:
Jet energy resolution 3-4%, Excellent photon-hadron separation
Basic Requirements:
Extreme high granularity
Compact and hermetic
(inside magnetic coil)
Basic Choices:
Tungsten as absorber material
X0=3.5mm, RM=9mm, lI=96mm
Narrow showers
Assures compact design
Silicon as active material
Support compact design
Allows for pixelisationRobust technology
Excellent signal/noise ratio: 10 as design value
The SiW ECAL in the ILD Detector
- O(108) cells
- “No space”
=> Large integration effort
All future e+e- collider projects feature at least one detector concept with this technology
Decision for CMS HGCAL based on CALICE/ILD prototypes

---
Silicon Tungsten electromagnetic calorimeter – Example ILD
Ecal alveolar structure
PCB+FEE
1.2 – 2.8mm
Sensor: ~500µm
Sandwich calorimeter
26 layers (+/- 4)
Thickness: ~20cm, 24 X0/1λI
Pixel size ~5x5 mm2
Expected elm. energy resolution 15-20%/√E
8.2- 13.5mm

---
SHiP Physics case
The SHiP experiment will search for a broad range of feebly interacting particles such as:
• Light Dark Matter
Heavy Neutral Leptons (HNLs)
• Dark photons
• Dark Scalar Higgs-like particles
• Axion-like particles (ALPs)
In addition SHiP will allow for a rich set of tests of Standard Model physics in with neutrinos
Relevant for today:
Neutrino Physics
LDM

---
SHiP Schematic Layout
Andrei Golutvin
SHiP Spokesperson

---
ShiP Calorimetry

---
ShiP Calorimetry

---
SHiP Schmatics

---
Scattering and Neutrino Detector (SND)?

---
A SiW Ecal for SND?
Questions
How many SiW Ecal layers and where?
Rear part of target or MTC or both
Knowing that an SiW Ecal layer is not cheap
Require serious optimisation study

---
Hadware development for SHiP
Test of demonstrator planned in 2026
Stack of 15 18x18x0.5 cm3 ASUs (Active Signal Units)
Currently under construction
Would terminate R&D cycle mainly oriented toward
Linear Colliders
Opportunity for SHiP staff to get familiar with “our” calorimeter?
Development of new ASUs will start in 2026
... centered around next generation of ASICs (CALOROC)
Debugging of CALOROC and development of readout chain
Initially generic work but adaptation for SHiP will be kept in mind
Expect first new ASUs ~beginning of 2027
Provided funding
Strong synergies with work in DRD Calo and EU project OTELLO
(if approved)
Mechanics
Dedicated study on mechanical housing
Need to understand mechanical interfaces
36cm
36cm

---
Optimisation How - Co-design?
What does it mean in practice?
It means creating a full parametric model of the detector, plugging in a surrogate model of the physics, and a differentiable model of the data reconstruction and inference extraction
Then you can iteratively modify the detector parameters following the gradient of the utility function – like in a NN
Detector parameters x
Utility evaluation and derivatives dU/dx
x x + λ dU/dx
Reconstruction and inference
Physics surrogate model
Tommaso Dorigo, DRD Calo Meeting, April 2025
Dumbed down version of an optimization pipeline
A fiirst proposal worked out with the help of Tommaso Dorigo and Andre
Would first need to get familair with SHiP software
Identification of (benchmark) physics channels
Understand concretely how apply co-design for ShiP

---
Next steps – ShiP <-> CALO5D (DRD Calo)
Identify relevant physics benchmark channel for detector optimisation
Typically neutrino scattering (rich final state) and LDM scattering
In parallel try to develop a plan on the detector optimisation study
Implementation of first layers into ShiP simulation
First thoughts on how to implement Co-design in SHiP?
Optimisation can be directed to performance and/or cost
Maintain connection to goals of CALO5D
SHiP also wants to use Particle Flow for even reconstruction!
Energy range O(10 GeV)
Timing hasn’t been explored
Can we abstract ideas develop in CALO5D to configurations other that collider detectors?)

---
Summary
SHiP covers relevant questions of particle physics and is (among) most powerful experiment(s) for feebly interacting
particles for decades to come (at least in the low mas range < 10 GeV)
SHiP as potential application of SiW ECAL
Detector optimisation for SHiP would have to start soon, i.e. now!
In our case how many Ecal layers and where it’s best to place them
A nice use case to learn/apply the principle of Co-design?
We would however start exactly from zero!
Development for SHiP could/should leverage on R&D in DRD Calo
Building up on R&D for Linear Colliders, synergies with hardware development for FCCee
Synergies with other similar experiments (that may take data before SHiP)!?

---
Backup

---
SiW Ecal Technological prototype – Elements of (long) layer
Interconnection
(IJCLab)
HV Supply
(IJCLab, LLR)
ASIC SKIROC2(a)
(OMEGA)
Wire Bonded or
In BGA package
(IJCLab, U Tokya, LLR)
    ASIC+PCB+SiWafer
        =ASU
        Size 18x18 cm2
(IJCLab, U Tokyo, OMEGA, LLR, SKKU)
Connection between 2 A.S.U.
Digital readout
SL-Board (IJCLab)
 Si Sensors
  glued
onto PCB
Pixel size
5.5x5.5 mm2
(IFIC, CERN)
The beam test set ups comprised mainly short layers consisting of one ASU and a readout card each
7 A.S.U.
~1500mm
total
“end” PCB