## Slide 1
Symposium
Precise quantum detectors in space, time and energy – semi- and superconductors in particle and condensed matter physics
2. DPG-Herbsttagung, 9. Sept. 2025 100 Jahre Quantenmechanik

## Slide 2: Norbert Wermes Physikalisches Institut Universität Bonn
Symposium Introduction: Semiconductor quantum sensors/detectors in Particle Physics – a success story
2. DPG-Herbsttagung, 9. Sept. 2025 100 Jahre Quantenmechanik

## Slide 3: Short history - 1
It was clear since 1950’ies ... for particle detection need “thick” depleted Si with milliseconds free carrier lifetime
Ge (cooled)
better than Si
2-5 mm
X-ray or gamma
At first: metal on Si => surface barrier detectors -> preferred until about 1980 (no thermal processing needed)
Later: thermal diffusion of dopants through oxide windows, later ion implantation was introduced

## Slide 4: Short History - 1
In 1979: Josph Kemmer (MPI) showed that using MOS technology & ion implantation
=> e/h lifetimes ≈ O(ms) came in reach and in addition microstructuring was possible
NA11/CERN 1980
Klanner, Lutz & Kemmer
NA11/CERN (H8)
1980
Heijne, Hyams, Jarron, ...
birth of the microstrip
detector
surface barrier
Si implant
device
measurements of decay lengths (< mm) possible
=> lifetime measurements in ps-range
e.g. charmed mesons (1981-86)
NA11

## Slide 5: Short history (2) ... ~1982 – 2000 −> now
Silicon detectors became tremendously important for particle physics to detect heavy quarks/leptons
identification of b, c and 𝜏
precise lifetime measurements (ps)
Z0 decay widths like Γ𝜏𝜏 , Γbb
discoveries: top quark (t ➝ b) H ➝ bb̄, 𝜏𝜏
H1@HERA
microstrip BST
microstrips
CCD pixels
(hybrid) pixels
SLD@SLC
CCD vertex detector
hybrid pixels
OPAL@LEP
@ LEP, HERA, ...
and Tevatron, LHC
@ SLC
@ LHC

## Slide 6: pp ➝ WH ➝ 𝜈e + bb̄
ν
e
22 collisions
piling up
7 cm
primary
secondary
vertex
Notes: 12 interactions ... currently about 40-50 ... in a few years about 200

## Slide 7: Spin-off to medical imaging: radiography with “counting” pixels
2x2 chips (CdTe) – 64 x 64 pixels
200x200 µm2
1.3 x 1.3 cm2
MPEC
1997 - 2001
spectral imaging
medipix.web.cern.ch/mars-bio-imaging
2024/25
(Image: MARS Bioimaging Ltd)
3D image of a human wrist
Medipix Collaboration
256 x 256 pixels, 55 x 55 µm2
1.4 x 1.4 cm2
founded 1997
M. Löcker, UBonn
Medipix3

## Slide 8: Current and new developments - 1
(a) Monolithic pixels
  hybrid pixel cell (one pixel)
Sensor
Readout
  (D)MAPS (depleted) monolithic active pixel sensors
(b) Picosecond timing with silicon (pixels)
Lampis et al.,
JINST 18 (2023) 01, C01051
presentation
Precision Timing with Silicon Detectors
Nicolò Cartiglia (Univ. di Torino)

## Slide 9: Current and new developments -2
(c) Devices operating at the single quantum level
(d) ”Ultra” ... in many aspects ...
presentations
Quantum sensor systems for enhanced precision particle detection
Michael Doser (CERN)
High-performance superconducting nanowire single photon detectors Val Zwiller (KTH Stockholm)
1
2
3
4
5
like SNSPDs
Photon  Electron / Hole
Ion / molecule  Phonons at surface
Charged particle  Coulomb interaction with electrons or nuclei
monolithic, high spatial resolution, highly efficient
and ultra thin ...
ALICE ITS3
- the ultimate paper wrap pixel detector Magnus Mager (CERN)
presentation
Notes: SNSPD = Superconducting nanowire single photon detector

## Slide 10: Symposium talks
Precision Timing with Silicon Detectors (25 min) Nicolò Cartiglia (Univ. di Torino)
Quantum sensor systems for enhanced precision particle detection (25 min)
Michael Doser (CERN)
High-performance superconducting nanowire single photon detectors (25 min)
Val Zwiller (KTH Stockholm)
ALICE ITS3 - the ultimate paper wrap pixel detector (25 min) Magnus Mager (CERN, Geneva)