## Slide 1: Differentiable Physics-Based Feedback for Adaptive Laser Pulse Shaping
8th Round table on Deep Learning @ DESY
Denis Ilia1,2, Ingmar Hartl1, Christoph Mahnke1, Federico Pressacco1, Henrik Tünnermann1
1 Deutsches Elektronen-Synchrotron, Notkestrasse 85, Hamburg, Germany
2 Universität Hamburg, Luruper Chaussee 149, Hamburg, Germany
Desy, Hamburg, 14/11/2025

## Slide 2: Expanding EuXFEL capabilities for new science
Laser pulse shaping for improved electron beam quality
EuXFEL mid\long term goals:
Higher photon energies > 25keV
Higher duty cycle (20% lower gun gradient)
Both require reduced emittance, which can be achieved by linearizing space charge forces through laser pulse shaping
  Pellegrini, C., in Physica Scripta. T169. 014004. (2016)
Photocathode
UV Laser pulses
Electron bunches
Space-charge forces

## Slide 3: Temporal pulse shaping is challenging
NEPAL laser system
Spectral attenuation and phase control
Conditions
High-dimensional control space
Ideally, without non-linearities
Non-linearities distort pulse during propagation.
Problem Find desired filter for target output
Approach
Physics-based differentiable model

## Slide 4: Physics-based differentiable model
A framework for ultrafast pulse propagation in fibers and laser systems
    7 physics-based modules:
      NLSE for pulse propagation (1D)
      Coupled eqs. for SHG process (2D)
      Rate equations for steady-state fiber amplifier
    Implemented in PyTorch:
      Fully differentiable
      GPU accelerated
Fewer parameters than Neural Network models, but Split-step Fourier Method solver on large grids requires substantial memory.

## Slide 5: A gradient-based feedback method
From optimizing models to real-systems
Real
Laser system
Differentiable laser model
System Identification
Control optimization
Sliding window with last B measurements
Measured output:
Control input:
Model predicted output:
Target output :
Model tunable parameters :
Computational resources
GPU: A6000 (48 GB)
Run time: ~28 min/iteration (~ typically 25 hrs with 50 its)
Memory usage: ~35 GB with

## Slide 6: Experimental results
Shaping UV output of photoinjector laser
Front-end
Oscillator
Power amplifier
Solid state amplifier
FH generation
SHG
Solid state amplifier
Solid state amplifier
AMP
WS
AMP
SHG
UV
Convergence is reached after approximately 50 iterations, closely matching the target shape.

## Slide 7: Conclusion and future works
Summary
Developed a gradient-based model for laser pulse shaping: fully functional, minor refinements ongoing
Next Steps
Development of laser shaping procedure for operations
  Feedback algorithm requires good hardware with direct access to DOOCS control system (to our knowledge not easily possible with Maxwell).
  Operational challenges due to long convergence time
Integration with NN-based approach for electron beam optimization
  Physics-based models here scales unfavorably to exploit differentiability.