## Slide 1: AIDA Infrastructure for very forward calorimeters
10/28/2011
Designers: In collaboration with:
Eric David François-Xavier Nuiry
Christophe Bault Andrea Catinaccio

## Slide 2: Overview
PH-DT collaboration
AIDA very forward calorimeter design
Mechanical frame
Tungsten support
Si detector support
Tungsten procurement
Mechanical frame machining

## Slide 3: PH-DT collaboration
Eric David
Designer
Christophe Bault
Designer
Francois-Xavier Nuiry
Engineering support
Andrea Catinaccio
Engineering support

## Slide 4: Calorimeter mechanical design
Multi-parts structure ST0372459
Able to work with 2mm and 1mm gap between tungsten plates
255mm
212mm
368mm
200mm

## Slide 5
Stainless steel frame
3 spacers
3 holders
Mechanical frame
3 Comb slots
Plan support slot
Calorimeter mechanical design

## Slide 6
Left comb
Top comb + spring (x2)
Bottom comb
Right comb + spring
Left plan
25mm
250mm
Combs
Calorimeter mechanical design

## Slide 7: How to mount tungsten plates
Open 2 top combs
Insert the first Tungsten
Insert all Tungsten + Si detectors
Close the 2 top combs

## Slide 8: C=2mm between each tungsten
Tungsten plate 125*145
C=2
A=3.5
Sensor
~10.5
 We work with an offset of 5.5mm
Gap=5.5
Gap=5.5
Gap=5.5
Gap=5.5
Gap=5.5
Gap=5.5
~2.5
Electronic board
Gap=5.5
No sensor In this gap
No sensor In this gap
No sensor In this gap
No sensor In this gap
Sensor
~10.5
~2.5
Electronic board
Sensor
~10.5
~2.5
Electronic board
BEAM
C=2

## Slide 9: C=1mm between each tungsten
Tungsten plate 125*145
C=1
A=3.5
Sensor
~10.5
Gap=4.5
 We work with an offset of 4.5mm
Gap=4.5
Gap=4.5
Gap=4.5
Gap=4.5
Gap=4.5
Gap=4.5
~2.5
Electronic board
Gap=4.5
Gap=4.5
No sensor In this gap
No sensor In this gap
No sensor In this gap
No sensor In this gap
Sensor
~10.5
~2.5
Electronic board
Sensor
~10.5
~2.5
Electronic board
BEAM
No sensor In this gap
New set of combs!

## Slide 10
Mechanical frame: overview
Horizontal beam
Vertical beam
The black box around will be designed soon.
This box will also hold services.

## Slide 11: The tungsten holder
Permaglas frame
Tungsten
Combs
Glass fibres in epoxy resin

## Slide 12
The tungsten holder
Ground
Spring

## Slide 13
W
3.5
W
J
A
C
J=C+D-(A+B)
A=3.5 +/-25μm
B=2 +/-2μm
C=5.5 +/-20μm
D=2 +/-2μm
Jmax = 5.520+2.002-3.475-1.998=2.049mm
W
3.5
W
J
A
B
J=B-A
A min=3.475mm
A max=3.525mm
B min=5.480mm
B max= 5.520mm
J max= 5.520-3.470= 2.05mm
J min= 5.480-3.530= 1.95mm
B
D
Tungsten + permaglas assembly

## Slide 14: The existing electronic board, is inserted in the Permaglas frame [RESARM company]
PCB Board
Permaglas frame
Comb

## Slide 15: The existing electronic board, in the Permaglas frame
The PCB should be machined before loading the Si detector

## Slide 16: Tungsten procurement
Main supplier: Cime Bocuse (Plansee) (France)
 | Tungsten min W 99.97% | Densimet W min 90% | Inermet W min 90%
Magnetism | Paramagnetic | Ferromagnetic | Paramagnetic
Other components |  | Ni + Fe | Ni + Cu (0%Fe)
ρ | 19.3 | from 17 to 18.8 | from 17 to 18.0
Ability to machine | Hard | Nearly like steel | Good machinability
Cost / Kg | ~770€(standard plate) ~15510 € for 30 plates | ~220 € Only rod shapes, no plates | Not available
Cost after machining At CERN |  |  | 
Cost after machining At Cime Bocuse | 3500€ for 1 machined plate 45000€ for 30 machined plates | 3492€ for 4 machined plates | Waiting for a new quote, very soon!
Tungsten alloys are 4 time cheaper than pure tungsten

## Slide 17: Tungsten procurement
Other supplier: (USA)
 | SD185 W min 97%
Magnetism | Ferromagnetic
Other components | Ni (2.1%) + Fe (0.9%)
ρ (g/cc) | 18.5
Ability to machine | Quite good
Cost / Kg | ~500 $ / plate ~500$ / kg
Cost after machining At CERN | -
Cost after machining | ATI cannot machine it for us We would need to machine it at CERN

## Slide 18: Mechanical frame manufacturing
Potential suppliers:
Leman Avionics SA (~5000CHF) [Structural frame]
Resarm (answer week 44) [Permaglas machining]
Call for tenders done buy the CERN Main Workshop (answer week 44) [For all quotes]
Different quotations:
Structural frame Permaglas machining Springs Combs
Structural frame only

## Slide 19: Next Step...C=0.5mm
The idea:
We use the same tungsten plates
We could use the same Permaglas frame (in white in this picture)
We glue the Si detector + the read-out on the Permaglas frame
We could realise a sliding kinematic between each tungsten plate, in order to reach the 0.5mm gap between each W plate.
A new mechanical frame is mandatory

## Slide 20
Silicon sensor
Flexible part
Connector for the read out
Rigid part (PCB)
Next Step...C=0.5 mm
The most important for us:
Realising a flexible link between the sensor and the read out.
Something similar to this example:

## Slide 21: Summary
The C=2 solution is designed.
The C=1 solution is designed.
The black box around have to be designed.
(the concept is founded Standard structure used for electronics racks)
We will soon determined the total price of this detector (W + frame)
[First Approx ~ 40 KEuros].

## Slide 22: Appendix 1: Additional information about the frame
Tungsten plate 125*145
C=2
A=3.5
Gap=5.5
C=2mm
 We work with an offset of 5.5mm
C=1mm
 We work with an offset of 4.5mm
Tungsten plate 125*145
C=1
A=3.5
Gap=4.5
Distance before next
tungsten
Distance before next
tungsten
BEAM

## Slide 23
Tungsten plate 125*145
A=3.5
Sensor
~10.5
 We work with an offset of 5.5mm
Gap=5.5
Gap=5.5
Gap=5.5
Gap=5.5
Gap=5.5
Gap=5.5
~2.5
Electronic board
Gap=5.5
Sensor
~10.5
~2.5
Electronic board
Gap=5.5
No sensor In this gap
No sensor In this gap
No sensor In this gap
No sensor In this gap
C=2
Electronic board
Sensor
~10.5
~2.5
Electronic board
BEAM
What we can do with C=2mm:
Appendix 2: Additional information about the frame