## Slide 1: Equipment Protection for the Photon Beam Transport
Harald Sinn
WP73: X-ray Optics and Beam Transport
April 17 2012, 1st XFEL Accelerator Consortium Meeting

## Slide 2: Photon beam transport: Active protection
Orange color: Beam Transport and X-ray optics
Beam loss monitor
Notes: ----- Meeting Notes (4/4/11 16:59) -----

## Slide 3: Active system: X-ray Beam Loss Monitor
BLM photo-multi-plier
BLM photo-multi-plier
CVD diamond or YAG
X-rays
optical light
DN100
DN 40
to shutter experiment hall
Can stop beam within pulse train
Under discussion with WP 17 & 74

## Slide 4: Photon beam transport: Passive Protection
Orange color: Beam Transport and X-ray optics
slit ≈ 250 m behind source
Notes: ----- Meeting Notes (4/4/11 16:59) -----

## Slide 5: Passive Protection: Slit (only slow T-monitors)
SRA- slit by Germano Galasso (XFEL) and ALCA
beam
B4C, water-cooled,
4° incidence angle

## Slide 6: Reaching Tmelt during pulse trains
FEA simulations done by Fan Yang 2012
Example: Graphite beam stop at SASE1,2,3 295 m from source point (B4C very similar)
= single shot
1 Joule
= e.g. 1000 x 1 mJ pulses per train

## Slide 7: Damage Levels SASE1&2

## Slide 8: Proposed Beam Modes
*Limited by electron dumps
+ Diagnostics non-FEL mode (Mode0): shift Mode 1 to Mode 2 when undulators open
Number of allowed pulses per train at different bunch charges:
 | < 0.1 nC | < 0.25 nC | < 1 nC | > 1 nC
Mode 1 (Alignment …) | 1 | 1 | 1 | 1
Mode 2 (C-Window …) | 600 | 200 | 30 | 1
Mode 3 (Mono, Slits …) | 2700 | 1350 | 200 | 10
Mode 4 (Full beam) | 2700 | 2700 | < 2700* | < 900*

## Slide 9
Machine Protection System (RS422 inputs only)
Injector
Machine Vacuum
Beamline Vacuum PLC
Limit switches
RS 422 monitor devices
Beam Transport PLC
Beckhoff online?
Mode 1-4 OK
Fast valve closes on trip
Vacuum trip
Vacuum trip
All valves out?
Attenuators in
Beam stops in
Si mono in
Thermal, sound, water, intensity, and loss monitors
Trip,
Mode 1-4
Screens in
K-mono in
Beam stops in, Shutters in
(limit switches)
Undulator PLC
Beckhoff online?
Set beam mode
Trip beam
Distr. mirrors
Mode 3
Mode 1
adjust
Mode
≤ 3 undulators closed
change Mode 12
Experiment 1
Experiment 2
Experiment 3
decrease
Mode
Equipment Protection System
High Level Control System
Personal Interlock SASE 1,2,3
active protection
passive protection

## Slide 10: De-coupling of experiments
SASE1
SASE2
2 MID
11 SPB
SASE3
14 SQS
1 HED
10 FXE
15 SCS
3
12
13 SQS2
SASE5
SASE4
7
8
9
4
5
6
MPS needs to know which branch is active
MPS needs to know where pulse lases (requires R&D)
Beam Transport PLC needs to know which experiment
active (max 10 Hz switching)

## Slide 11: Preferred Beam Modes
*Limited by electron dumps
Number of allowed pulses per train at different bunch charges:
HED MID FXE SPB SQS SCS
 | < 0.1 nC | < 0.25 nC | < 1 nC | > 1 nC
Mode 1 (Alignment …) | 1 | 1 | 1 | 1
Mode 2 (C-Window …) | 600 | 200 | 30 | 1
Mode 3 (Mono, Slits …) | 2700 | 1350 | 200 | 10
Mode 4 (Full beam) | 2700 | 2700 | < 2700* | < 900*

## Slide 12: Summary Equipment Protection
Active and passive protection systems
Definition of beam modes necessary
Beam Modes Beamlines ≠ Beam Modes Accelerator
Different Experiments will run different modes
Experiments will change modes during run time
Damage test needed when operation starts and improves
Thank you for your attention!