## Slide 1: FE Gruppe.
Electronics development at DESY (Hamburg)
Mathias Reinecke
Workshop on Fast Beam Conditions Monitoring DESY Zeuthen, 3.2.2012

## Slide 2: Contents
People in the FE electronics groups
Current Projects / Focus of Activities
Optical data transfer (old project)

## Slide 3: People at FE
FE
M. Zimmer
A. Schröder
FEA
M. Zimmer
H. Arpe
K. Diekmann
C. Kosinski
F. Krivan
I. Shevyakov
P. Vetrov
Q. Xia
FEB
P. Göttlicher
W. Baatz
K.-H. Gooßen
T. Pwalam
M. Reinecke
P. Smirnov
L. Steffen
H.J. Wentzlaff
M. Zeribi
FEC
K. Hansen
I. Diehl
J. Hampe
P. Kavalakuru
H. Klär
D. Müntefering
M. Randall
C. Reckleben
J. Szymanski
A. Titze
A. Venzmer
E. Wüstenhagen

## Slide 4: Kernkompetenzen von FE
Main Activities | FEA | FEB | FEC
PCB circuit design and layout | x | x | x
fast FPGA - based data acquistions xTCA, PXI, 10G-Ethernet, fast serial links, VHDL | x |  | 
processing of sensitive analogue- and detector signals |  | x | x
ASIC-Development (Analog, Mixed-Signal, Digital) |  |  | x
hybrid module assembly, chip bonding |  |  | x
low- and high-level software (µC, LabView) | x | x | x
complex measurements techniques | x | x | x
System design (EMC, Grounding etc.) | x | x | x
ECAD Service for Mentor Graphics and CADENCE | x |  | x

## Slide 5: Data acquisition module DAMC2
xTCA for Physics as extension of the standard
  Extension of specifications from running experience and customers advice.
  Double height, extendable by Rear-Transition-Modul (µRTM)
  Separation of data acquisition and I/O, firmware can be adapted to task
  Board is foreseen for many different appliccations!

## Slide 6: µRTM Modules for FLASH II and XFEL
µRTM Modules for:
Beam Position Monitor in test at FLASH II
Machine Protection System in production.
Beam Halo Monitor to be finished in 2012.
Beam Loss Monitor scheduled for 2012.
Typical tasks: multichannel A/D conversion and additional functions.
Hardware: FEB, Firmware: FEA

## Slide 7: Readout-Module for XFEL - detetcors
Versatile Readout Module as Mezzanine - Card
  Input digital data rate up to 100 GBit/s / Up to 4x 10GBit Ethernet outputs
  Applications: AGIPD, MEDIPIX and CMOS - Imager for XFEL
Spezielles Carrierboard für jeden Detektor
Sensor
Digitalisierte Signale
Power
Slow
Control
Steckverbindung
Daten
Signal-anpassung
Digitales Readout Modul
FPGA
Virtex5
8 GB RAM
2 SODIMM
PHY / SFP+
Bis 4 x
10 GBit
Ethernet
Offline Computing
PHY / SFP+
PHY / SFP+
PHY / SFP+
146 Pairs/ 700 Mbit/s

## Slide 8: Analogue, hadronic Calorimeter (AHCAL)
Research for the ILC:
48 layers steel/tungsten - detector. 2600 channels per layer.
Almost 4 million channels in the barrel. 1/16 HCAL module: > 24t.
FEB: concept- and prototype development within the CALICE collaboration.
4m

## Slide 9: AHCAL – Prototype Electronics
SiPM
Szintillator
144 Stück auf Rückseite
High integration level:
„As thin as possible“
36 cm
HBU2

## Slide 10: Adaptive Gain Integrating Pixel Detector (AGIPD)
FEB
FEA
High-speed camera for XFEL:
1 MegaPixel for 12keV-photons
Dynamic range: 0, 1, 2, … up to 20000 photons
Full frames all 222ns.
No data compression. => DAQ data rate: 80GBit/s.
64 ADCs (14bit, 50MS/s)
Further FEB contribution:
Slow Control and Configuration:
ARM9 microcontroller

## Slide 11: Hydrostatic Leveling System (HLS)
HLS for vertical position determination of accelerator components using ultrasound.
PETRA III: 130 metering points in operation for 1.5 years. Achieved accuracy: ~1µm.
Full system delivered.
Earthquake at the Salomon Islands
HLS Prototype
CE certified

## Slide 12: ASIC Development and Microelectronics
Analogue, digital and mixed-signal Circuits
  CADENCE
  130 nm CMOS process by IBM
  350 nm BiCMOS process by AMS
Assembly, Interconnection and Packaging
  Various bonding techniques
  Quality assurance (pull, electrical, optical test)
  3D-packaging
Characterization
  Probe station based ATE system
  Measurement equipment up to 20 GHz

## Slide 13: Hybrid Module and System Design
24,1 x 25,1 x 22,4 cm3
32 Sensoren (128 x 256 pixel)
256 ASICs.
FEC: 64 x 64 channel ADC
XFEL Pixeldetektor DSSC:
8 x 8 channel ADC
prototype ASIC

## Slide 14: Optical data transmission system
Data transfer in a Silicon-Drift-Detector setup (for HASYLAB in 1998).
Data Rate: 2.5GBit/s
Channel-Coding, multiplexing of data, laser-biasing, clock -and data recovery in dedicated functional blocks.
Tested up to 20km with BER < 10^(-13)
Tx
Rx

## Slide 15: Optical data transmission system
Analogue, optical data transmission
  Temperature sensitivity (temperature control necessary?).
  Settling time of optical signal fast enough?
  Radiation induced degregation of optical power. Lifetime limited by radiation. Channel-to-channel variation of optical power.
  No ADC in front-end
Digital, optical data transmission
  Needs more space in front-end (ADC, channel coding)
  High data-rate, “no” temperature problems. Lifetime limited by radiation.
  Many channels can go through single fiber (WDM) to back-end.
Electrical transmission
  Galvanic separation has to be set up, EMC (sens. detector) has to be considered.
  Moderate data rate possible.