## Slide 1: BCM1F 4 LHC Status and Challenges
Bernd Dehning
CERN BE/BI
Histograming of loss events synchronous with revolution period
Event triggered beam loss measurements
BCM1F 4 LHC upgrade considerations
Loss electronic developments at CERN

## Slide 2: HERA Scraping Beam with Wires
HERA
  Bunch spacing 96 ns
  Samples taken every 21 ns
No coasting beam halo
  3 samples with zero intensity (left, top)
Partially coasting halo
  Inter bunch samples measure intensity (left, middle)
Only coasting halo
  No observation of bunch structure (left bottom)
Strong coasting component at begin of fill (centre top)
Bunched halo only minutes later (centre, middle)
With retracted wire diffusion of coasting component into cleaned area (centre bottom), SPS?
Effect caused by RF system noise, faulty amplifier
Halo Intensity
Inner wire
Outer wire
Outer wire
wire ~ 4 sig
wire ~ 4 sig
wire ~ 6 sig
begin fill
4 min later
wire retracted

## Slide 3: Diamonds Signal over Threshold and Arrival Time Histogram
Measurement of bunch filling scheme with high dynamic range
Model reproduces measurements
Empty bunch region
Non
colliding bunche
bunch number
Courtesy S. Mueller

## Slide 4: Arrival Time Histogram from Losses downstream of Collimator
Counts
25 ns bunch spacing
Losses from beam approaching the LHCb experiment
Losses from beam and interaction debris from the LHCb experiment
Measurement set up allows details study of loss origin

## Slide 5: BCM1F2LHC
Only halo losses (no debris from collisions)
Halo (B1) from ARC and debris from experiment + halo (B2)
Halo (B2) from ARC and debris from experiment + halo (B1)
Halo from ARC and debris + halo from experiment, both beams
Different combination of losses at different location will allow halo formation studies
ARC halo is measured by detection of shower particles originating from collimator proton impact
Debris detected by shower particles originating form vacuum chamber aperture limitation
CERN Prevessin (865)
LHC P4
LHC P2
LHC P5
LHC P8

## Slide 6: BCM1F4LHC Topology
Slow control: HV, low voltage, test pulse locally with Ethernet multi purpose ADC – DAC unit
Centralised acquisition: VME crate, CAEN module, LINUX PC
LHC P4
LHC P2
LHC P5
LHC P8
CERN Prevessin (865)
Conceptional considerations
Amplifier near to the detector (sCVD) => fast signal amd low noise
Optical signal transmission => almost no cable lenght limitation => concentration of signal acquistion at one location (Prevessin 865)
Radiation tollerant design => placement of the detectors near to the loss location

## Slide 7: 4 Diamond BLMs for Observation at LHC (event triggered)
ATS/Note/2011/048 (TECH), B. Dehning et al.
Chemical Vapor Deposition (CVD) diamond
IP7 collimators (TCP) – one per beam
    All sizable local losses are also seen at collimators
Injection regions – one per beam
40 dB amplification
2 GHz upper limit
Dose up to 1 MGy
Risetime 180 ps
Pulse width 300 ps
Fall time 400 ps
SNR of 5 with 1.6 fC
Courtesy E. Griesmayer

## Slide 8: LHC: 152 bunches, 150ns bunch spacing (3/10/2010 12h48)
Time
Loss signal
due to macro particle collision
loss due extraction kicker imperfection
Notes: Figure
25:
The
10
ms
buffer
(1
ms/div)
shows
the
characteristics
of
the
event
and
the
turn-­clock
signal
of
LHC
(89.2
us).
The
dump
causes
a
high
pulse
at
the
end
of
the
loss
pattern.

## Slide 9: LHC: 152 bunches, 150ns bunch spacing (3/10/2010 12h48)
Loss signal
Time
Diamond signal
Ionisation chamber
(40 us integration time)
Notes: Figure
26:
Zoom
factor
101
(100
us/div):
the
time
structure
of
the
bunch
trains
can
be
estimated.
The
corresponding
measurement
from
the
ionization
chambers
is
shown
at
the
bottom
and
shows
an
excellent
agreement
between
the
DBLM
and
the
ionization
chambers.

## Slide 10: LHC: 152 bunches, 150ns bunch spacing (3/10/2010 12h48)
Time
Loss signal

## Slide 11: LHC: 152 bunches, 150ns bunch spacing (3/10/2010 12h48)
Time
Loss signal

## Slide 12: LHC: 152 bunches, 150ns bunch spacing (3/10/2010 12h48)
Time
Loss signal
About 20 particle per pulse

## Slide 13: Post Mortem Data (some examples)
PM application: BLM data of 0.082 sec
online available
Longer PM buffer: BLM data of 1.72 sec
offine available
43000 values (40 us)
2000 values (40 us)
Loss in a bending magnet
Monitors
Time
BEAM

## Slide 14: BCM1F4LHC Upgrade Considerations
Keep topology like implemented
Time over threshold detection in front end will allow:
  histograming synchronous to revolution period of MIP events
  Pulse high spectrum analysis (dynamic between 2 to 3 orders of magnitude)
  Detection of rare multi MIP signals (dynamic between 2 to 3 orders of magnitude)
  Digital signal transmission
Reduction of peaking time (higher double pulse resolution, lower MIP detection jitter)
Use GBT for transmission
Data acquisition in single FPGA directly connected to optical fibres
Thresholds setting done by slow control unit locally using Cu cable

## Slide 15: The BLM Acquisition System (Experiments and LHC)
Real-Time Processing BEE
FPGA Altera’s Stratix EP1S40 (medium size, SRAM based)
Mezzanine card for the optical links
3 x 2 MB SRAMs for temporary data storage
NV-RAM for system settings and threshold table storage
Analog front-end FEE
Current to Frequency Converters (CFCs)
Analogue to Digital Converters (ADCs)
Tunnel FPGAs: Actel’s 54SX/A radiation tolerant.
Communication links: Gigabit Optical Links.
Range 1 pA to 1 mA
Radiation tolerant to 500 Gy
SEE tested
New: direct Ethernet read out at front and back-end foreseen

## Slide 16: Advanced Current to Frequency Converter Principle
LHC current to frequency converter:
only positive signals (limitation in case of signal under shoots)
500 Gy radiation tolerance
Integrator
Comparator
Reference current source
f = Iinput / (Iref * Tref)

## Slide 17: Advanced Current to Frequency Converter Principle
LHC current to frequency converter:
only positive signals (limitation in case of signal under shoots)
500 Gy radiation tolerance
Integrator
Comparator
Reference current source
f = Iinput / (Iref * Tref)

## Slide 18: Advanced Current to Frequency Converter Principle
LHC current to frequency converter:
only positive signals (limitation in case of signal under shoots)
500 Gy radiation tolerance
Integrator
Comparator
Reference current source
f = Iinput / (Iref * Tref)

## Slide 19: Advanced Current to Frequency Converter Principle
LHC current to frequency converter:
only positive signals (limitation in case of signal under shoots)
500 Gy radiation tolerance
Integrator
Comparator
Reference current source
f = Iinput / (Iref * Tref)
Development for LHC BLM system upgrade, optical link GBT

## Slide 20: Fully Differential Current to Frequency Converter Principle
Fully differential Integrator
Input switch
Specifications:
  Dynamic range 7 orders integration window 2 us 1nA to 200mA
  Dynamic range 9 orders integration window 1 s 10pA to 200mA
A status signal selects in which branch of a fully deferential stage the input current is integrated.
Two comparators check the differential output voltage against a threshold, whenever is exceeded, the status signal changes to the complementary value (0 ! 1 or 1 ! 0) and the input current is integrated in the other branch.
Discrete components: not radiation tolerant
Development for injector BLM system upgrade, optical and Ethernet link

## Slide 21: Fully Differential Current to Frequency Converter Diagram
Input 50 ohm resistor split in two: 47 + 3 ohm
Re-routing on the ADC buffer amplifier
CFC
switches
for CFC
ADC
shunt
resistor
input
switches
ADC shunt or
CFC operation

## Slide 22: Fully Differential Current to Frequency Converter Diagram
Input 50 ohm resistor split in two: 47 + 3 ohm
Re-routing on the ADC buffer amplifier
CFC
switches
for CFC
ADC
shunt
resistor
input
switches
ADC shunt or
CFC operation

## Slide 23: Fully Differential Current to Frequency Converter
Top: PSpice simulation of CFC part of circuit
Bottom: first PCB circuit results
To be used for the beam loss system in the CERN pre-accelerators

## Slide 24: Acquisition System Specification for Diamond Signal
Detector |  |  |  | 
Pulse | Amplitude | Max. | 2 | V
 |  | Min. | 1 | mV
 | width |  | 5 | ns
 | time jitter |  | 1 | ns
 | noise level | below | 1 | mV
Double pulse resolution |  |  | 20 | ns
Digitalisation of the signal |  |  |  | 
ADC (min) |  |  | 10 | bit
 | range | Max. | 1 | V
 | sampling |  | 500 | MHz
 | bandwidth |  | 250 | MHz
Buffer |  |  | 1.00E+007 | words
Trigger | input |  | TTL | 
Histogramming of arrival times |  |  |  | 
Threshold DAC |  | min | 0.5 | mV
 |  |  | 10 | bit
Reference frequency |  | min | 10 | kHz
 |  | max | 2 | MHz
 |  |  | TTL | 
Histogram |  |  | 5.00E+004 | bins
Signal frequency |  | max | 10 | MHz
Two data sets should be available:
Signal versus time
Number of signals over threshold versus arrival time
Market survey has been started
Signal to be measured
Oscilloscope features
Histogram of time of arrival
Next project: compact diamond signal
acquisition system; industries - CERN

## Slide 25: Summary
The revolution period synchronised loss histrograming is regarded as essential for LHC halo studies (collimation – luminosity optimisation)
Non periodic signals need to be measurable (UFO)
MIP and multi-MIP events occurring in LHC
For injector and LHC BLM upgrades electronics is under development, experience is and will be available for:
  optical link design and data treatment (CRC, …)
  Direct Ethernet read out of front and back-end electronics
  FPGA firmware design – digital and analog signal treatment

## Slide 26
Reserve Slides

## Slide 27: CMS BCM1F Monitor System (histogram of loss arrival time)
Radiation tolerant ASIC amplifier and laser diodes
Detector and electronics mounted in a few centimeter case
VME based CAEN module acquisition system
  ADC 500 MHz
  Scalar
  TDC
Next project: increase of dynamic range and transmission link optimisation
DESY Zeuten – CERN BE/BI
See Elena Castro talk

## Slide 28: Post Mortem Data (some examples), Zoom
Loss from primary event
+
dump system loss

## Slide 29: Diamond and Radiation Hardness
Top: sCVD shifted to the left to show that it follows the same degradation parameterization as pCVD
Bottom: sCVD irradiation loss: 20 % of initial signal
drop of signal to noise from 26 to 7
1.5 E17 1/cm2 (MIP)
From
“Fast beam conditions monitoring
(BCM1F) for CMS” by N/Bernardino Rodriguess, …
From:
W.Trischuk & RD42, “Resent advances in
diamond detectors”
No data are available at temperatures below 100 Kelvin

## Slide 30
Christoph Kurfuerst, CERN BE-BI
Integration over length of spill (400 ms)
Leakage current below 1 pA
Test of radiation tolerance foreseen for June & Nov. 2011 (dose: 1MGy, few E15 prot/cm2)
Signal integration over 0.6 seconds
Average response of
single particle

## Slide 31: Si Studies with Pulsed LASER (100 ps duration) I
CVD 500 um thickness

## Slide 32: Si Studies with Pulsed LASER (100 ps duration) II
Drift velocity is constant up to 40 Kelvin
Drift velocity variation (saturation to 300 K) for holes by a factor 3 and for electrons by a factor 2.4
Saturation plateau shows some variation (hypothesis shallow energy level capture charges)
General: for steady state irradiation and radiation damaged material polarisation effects expected.

## Slide 33: 1.8 Kelvin Loss Detection – MIP response (20 GeV Protons)
Diamond (sCVD)
Si at 4.2 K
Si at 1.8 K
Open questions: radiation hardness, DC current value, non linearity effects for high losses

## Slide 34
ALPHA source
sCVD

## Slide 35: Poly and single crystalline CVD (Diamond) Detectors
10 mV/div
10 mV/div
20 mV/div
stopped after few um
traverse the detector
pCVD faster but less signal compared to sCVD
Courtesy to E. Griesmayer, CIVIDEC