## Slide 1: Fast Beam Monitoring in ATLAS (BCM)
The original BCM
  Mechanical Design
  Readout capabilities
  Results from 2010-2011 running
Upgrade to add spatial information (DBM)
William Trischuk
University of Toronto
on behalf of the ATLAS-BCM group
February 2, 2012

## Slide 2
The Beam Conditions Monitor Mission
Primary goal: Protect ATLAS and the LHC machine
  Tevatron beam ~10 MJ (bus at 120 km/h)
  LHC beam ~1.4 GJ (an A380 at takeoff)
Protons
Protect against beam accidents
  Monitor backgrounds during injection
  Montior losses during abort
  Detect instabilities early
  Warn of deteriorating conditions
  Abort the beam if necessary
Secondary goals
  Monitor collision rate
  IP location and shape
A 1m long melted stretch of Tevatron collimator

## Slide 3
The ATLAS BCM Collaboration
A. Svetek
M. Deliyergiyev
M. Fischer
H. Merritt
J. Moss
H. Jansen
E. Jiankowski
N. Venturi

## Slide 4: The ATLAS Beam Conditions Monitor
ATLAS will use time-of-flight to distinguish collisions from lost beam particles
4m separation gives 12ns time-of-flight: optimal
Pixel space-frame support at ± 1.9m
Use CVD diamond sensors
  10x faster signals and 10x more radiation tolerant than silicon
Use GaAs amplifiers with 1ns rise-time, 5ns baseline restoration

## Slide 5
The BCM in ATLAS

## Slide 6
The BCM Installation
Half of BCM modules on ATLAS Pixel support frame
BCM module support mechanics designed in Toronto

## Slide 7
The BCM Detector Modules
pCVD diamond sensors (10x10 mm2, 2x500m thick)‏
  Withstand doses > 1015 p/cm2
Fast & short signal (FWHM~2ns, rise time<1ns)‏
Count hits above two thresholds:
  ½ MIP (for luminosity measurements
  100 MIPs (for beam protection)
BOTTOM
  Agilent MGA-62653 500Mhz (22 dB)‏
pCVD diamond
  Mini Circuits GALI-52 1 GHz (20 dB)‏

## Slide 8
Must provide independent beam background assessment
Also provides luminosity and trigger information for ATLAS
The BCM Readout
ATLAS
Cavern
USA-15 (Counting room)
Control room

## Slide 9
BCM Abort Post-mortem
Provide fast feedback (within 5 minutes of abort) to CERN CC
  After every abort (about 3000 per year)
Normally look like:
Single MIP
Hundred MIP
1000 turns
100 turns
vs. Time
vs. BCID

## Slide 10
Two Aborts Seen – 2+ Years of Operation
Two aborts seen (July 31, 2011, August 18, 2011)
Both corroborated by LHC machine beam loss monitors
  Typical of unidentified falling objects seen elsewhere in machine
  Approaching danger levels for SCT and Pixel detectors

## Slide 11
Two Aborts Seen – 2+ Years of Operation
Two aborts seen (July 31, 2011, August 18, 2011)
Both corroborated by LHC machine beam loss monitors
  Typical of unidentified falling objects seen elsewhere in machine
  Approaching danger levels for SCT and Pixel detectors

## Slide 12
BCM: ATLAS Default Luminosity Monitor
Since early 2011 the BCM is ATLAS’ default luminosity monitor
  Provides robust rate measurements
  Negligible backgrounds
  Operates when other systems are not active
Used during all Van de Meer scans
  Measure few % variations in bunch currents
  Reproducibily and reliably

## Slide 13
BCM Luminosity Maps
A or C
A and C
Only A
Only C

## Slide 14
BCM: Luminosity Stability
Two independent lumi measurements (BCMH (ref), BCMV (o))
  Stable over months (left) Stable against pile up (right)
One of the keys to ATLAS stated 3.4% absolute luminosity uncertainty

## Slide 15
Build on success of BCM – include pixel readout pattern
  Install with service quarter panel (nSQP) replacement
  Four 3-plane stations on each side of ATLAS-IP
nSQP replacement sets installation date – Februrary 2013
DBM: 3.2<η<3.5
The Diamond Beam Monitor (DBM)

## Slide 16
DBM
BCM
Pixel
BPSS
DBM Location

## Slide 17
27 sensors ``in hand’’ from IBL demonstrator work
  Most need thinning
  5 FE-I3 sensors will be cut to give 15 DBM sensors
  4 DBM sensors ready for bump-bonding
  4 (thick) built into I4 modules
All currently meet DBM specifications
DBM Sensor Inventory

## Slide 18: First four DBM modules
Four DBM modules built at IZM
  21x18 mm2 pCVD from DDL
  FE-I4 ATLAS IBL pixel chip
  336x80 = 26880 channels, 50x250 μm2
Largest ASIC/diamond flip chip assembly
X-ray after
bump bonding
Diamond + I4
I4 only
Module on
test board
4 modules after flip-chipping
First noise map of a DBM module
X-ray perfect
Noise map uniform
  Indication of success
HV issues due to IZM metallization up to edge

## Slide 19
Three Testbeam campaigns
  July, late August, October
Learning about FE-I4 performance
  Calibration/tuning for low thresholds unique to diamond
  Achieved 1000 e threshold (needed for irradiated silicon)
Use testbeam data to tune charge model
Run1394 1000e Threshold
October 2011
DBM: Module Testbeam Studies

## Slide 20
Projective telescope design now being prototyped
  Integrate cooling circuit in a simple way
  Ensure DBM is thermally neutral, but modules can run at 40C
DBM: Support Mechanics

## Slide 21
Full GEANT model available
Geometry forces us to focus on z,q reconstruction
Momentum resolution weak anyway => precise pixel in r
50 µm in Φ
σz ~4 cm
50 µm in r
σz ~0.6 cm
DBM: Simulation/Reconstruction

## Slide 22
Fast beam monitoring is very successful in ATLAS
  BCM is default luminosity monitor
  Abort algorithm in place since 2010
    No false positives
    Responded as expected in two UFO events near Pt. 1
  Expect to arm the BCM abort during 2012 running
Planning an upgrade with spatial resolution
  DBM design is finalised
  Modules under construction
  Will install in long shutdown
  Ready to augment BCM information in 2014 running
Summary