## Slide 1: Data Acquisition System of the Belle II Pixel Detector
Takeo Higuchi (KEK)

## Slide 2: Belle II Detector in a Nutshell
Central drift chamber with smaller cell size and longer lever arm
2-layer DEPFET pixel
Electromagnetic calorimeters barrel: CsI(Tl) endcap: pure CsI
Ring image Čerenkov counters
KLμ detector
barrel: RPC endcap: scintillator + SiPM
More elaborated hardware trigger
Time of propagation counters
4-layer DSSD
Fast and broad-band data acquisition system
Large scale mass storage system

## Slide 3: Belle II Vertex Detectors
4-layer DSSD (SVD)
Beam pipe
2-layer DEPFET pixel (PXD)
DEPFET: thin sensor (75 µm)
unique worldwide
SVD
PXD
Side view
Detector | Layer # | R | # ladder
DEPFET (PXD) | 1 | 1.4 cm | 8
 | 2 | 2.2 cm | 12
DSSD (SVD) | 3 | 3.8 cm | 7
 | 4 | 8.0 cm | 10
 | 5 | 12.0 cm | 12
 | 6 | 13.5 cm | 16
Significant resolution improvement
Belle
Belle II
pβsin(θ) [GeV/c]
0.4
2.0
0
0.8
1.2
1.6
100
20
50
[µm]
30mm
15mm
PXD+SVD
Vertex resolution in beam direction
200

## Slide 4: Full-Size Mockup of the PXD

## Slide 5: PXD Readout System (Front-End)
DCD
DHP
DHH
Switcher
~20 cm
10-20 m
Power
control
Data
Patch-panel
CDAQ I/F Trigger timing
Opt.
Power Supply Slow control
Half ladder 768 rows x
250 cols
x(half+half)
x(fwd+bwd) x10-ladders
= 7680000 px
Total of 8M pixel readout in 20µs
Opt.
Cu

## Slide 6: Pixel Charge Readout
Row-by-row readout (rolling shutter mode)
  Row is select with external gate (controlled by SWITCHER).
  Current corresponding to the row is readout.
Readout time
  The entire PXD is readout in 20µs (100ns per row).

## Slide 7: Pixel Charge Readout
Four-fold parallel readout
Pixel (75x50μm²)
Gate ON
Gate OFF
4
Digitizer (DCD)
…
250 cols
…
2 x 768 rows

## Slide 8: On-Ladder ASICs
Drain Current Digitizer (DCD)
  256 analog inputs per DCD chip.
  Signal digitization in 8-bit resolution.
  Serialized data output to DHP.
  Measured signal dispersion = 1.7 ADC-units (RMS).
Data Handling Processor (DHP)
  On-ladder data size reduction by zero suppression with corrections for common mode noise and pedestal fluctuations.
  Measured link speed to downstream receiver over 15m cable = 1.6Gbps.
Layout of the DCD chip
3.2x5.0mm²
256-input- pad area
Logic area
Layout of the DHP chip
  Signal control for the row-wise pixel readout.
  JTAG configuration.
2bytes/px

## Slide 9: Interface to the Level-1 Trigger
Data Handling Hybrid (DHH)
  The DHH merges 4 incoming data streams from DHPs to a single stream, then stores the data to its memory.
  When a level-1 trigger arrives, the DHH moves the stored data to downstream modules with data reformatting.
VME-6U sized module
DHP
DHP
DHP
DHP
DCD
DCD
DCD
DCD
DHH
PXD ladder
Virtex6 FPGA
2GB DDR2
Level-1 trigger & System clock
Triggered data output
4x1.6Gbps

## Slide 10: Data Handling Hybrid (DHH)
Snapshot of the DHH
2x Infiniband to receive data from DHP chips
2x SFP+ to output data to downstream receivers
SFP+ to interface DHH controller
2x RJ45 to receive level-1 triggers and JTAG signals
Virtex6 FPGA (XC6VLX75T-FF784)
Up to 2GB DDR2 memory slot
Measured output bit-error-rate @ 6.25 Gb/s links: < 10⁻¹⁵

## Slide 11: PXD Readout System (Back-End)
Readout modules
RoI finding logic
1st Layer EVB
HLT
2nd Layer EVB
SW
HLT decision
…
SVD
COPPER
Readout
PC
CDC
COPPER
Readout
PC
DATCON
DHH
DHH
DHH
DHH
PXD
GbE
RocketIO over opt.

## Slide 12: DHH Readout
DHH readout module (ATCA system)
  x4(x2) optical inputs from x4 DHHs and x4 GbE outputs to the 2nd layer event builder.
  More elaborated data size reduction using externally determined region-of-interest (RoI).
  The ATCA system comprises of a buffer for RoI-determination latency (5secs at maximum).
Block diagram of the ATCA module

## Slide 13: ATCA System – Carrier Board
Carrier board houses 4 computing nodes
  4 AMC connectors to I/F computing nodes.
    “Computing” node performs data size reduction based on RoI information.
  Virtex-4 FPGA for arbitration of 4 computing nodes.
  Peripherals
    2GB DDR2 memory.
    512Mb flash memory.
    x2 GbE ports.
    x16 RocketIO I/F to backplane.
Carrier board in ATCA form factor
4x AMC slots

## Slide 14: ATCA System – Computing Node (CN)
Computing node is in the AMC form factor
  4Gbps link speed is achieved with 200MHz clock.
  Measured bit-error-rate is < 4x10⁻¹⁴ at 4Gbps link.
  Measured memory-access speed is 400MHz for read/write at 200MHz clock.
2x2GB DDR2
AMC connector to I/F the carrier board
Virtex-5 FPGA
2x SFP+ (6.25Gbps) to I/F DHH
GbE port to I/F EVB
4GB memory for up to 5-second RoI-finding latency

## Slide 15: ATCA System – System Assembly
40 x [ 4x computing-node + carrier-board ]
6.25Gbps (GTX)
LVDS
Full-mesh backplane
Drawn by Illustrator

## Slide 16: RoI-Based Data Size Reduction
RoI-based data size reduction
  PXD RoIs externally determined by track finding algorithm are informed to the ATCA module; the computing nodes (FPGA) within the ATCA module abandon PXD-hit signals out of the RoIs before sending the hit signals to the 2nd level event builder.
  Data size reduction by a factor of 10 is expected.
x
x
x
x
x
x
x
… Survived pixel hits after zero suppression by the DHP.
Reconstructed track
… RoI associated to the reconstructed track.
x
… Pixel hits within the RoI, which should be recorded.
PXD ladder

## Slide 17: RoI↔PXD-Hit Matching on the CN
MC-gend. random pixel hit; MC-gend. signal pixel ht
  Implemented firmware works up to 31 RoIs per event.
  No error after processing of 1.9x10⁶ random hit events; 1.2x10⁵ signal hit events
MC-gend. realistic pixel hit with Touschek BG added
  DHP and DHH output-format decoder is implemented to the firmware.
  No problem observed as well.
FPGA on the computing node examines pixel hits and output only associated hits to the RoIs.

## Slide 18: RoI Finding in PC Farm
SW
HLT decision
HLT
SW
HLT decision
HLT
High Level Trigger (HLT)
  HLT reconstructs tracks→RoIs from SVD and CDC hit signals.
PXD
Readout modules
RoI finding logic
1st Layer EVB
2nd Layer EVB
SVD
COPPER
Readout
PC
CDC
COPPER
Readout
PC
DATCON
DHH
DHH
DHH
DHH

## Slide 19: High Level Trigger
HLT functionalities
  RoI finding by track reconstruction.
  Event rate reduction by a factor of 3.
HLT = PC farms
  10 PC-farm units, each of which comprises of 150 CPU cores.
  Uniformed software framework for online and offline data analysis will be provided.
  The system is under development; it will be ready by the end of this year.
HLT R&D setup
96 cores
Storages

## Slide 20: RoI Finding in DATCON
Data concentrator (DATCON)
  We are studying possibility of SVD-only track and RoI finding in a FPGA on the “DATCON” module.
x1902 readout chips (APV25)
x40 (FINESSE + COPPER)
‘FADC+PROC’
Analog-to-digital conversion, data size reduction, and hit time finding module
FINESSE transmission board
SVD
FPGA
Opt. link
Opt. link
Opt. link
Opt. link
Opt. link
ATCA modules
DAT CON

## Slide 21: New Idea on Hit Recovery
Hit recovery
  A track with pt<75MeV/c cannot be reconstructed by the SVD sololey because of its small curvature. → No associated RoI is generated. → Corresponding PXD hit will be totally lost.
  PXD+SVD track finding may salvage these PXD hits.
ATCA modules
DHH
DATCON
PXD+SVD track finding CPU
PXD
SVD
Central DAQ

## Slide 22: Backup Solution for DHH Readout
PCI-express cards receive data from DHH.
Link-speed study with a prototype card
DHH
DHH
DHH
DHH
2nd Layer EVB
RX card on PCIe
RX card on PCIe
RX card on PCIe
RX card on PCIe
…
PCs RX-card readout with RoI-based data size reduction
PXD
  ML605 (Virtex-6 (LX240T) evaluation kit)
  Capability of PCIe Gen2 (x4).
  x2 FMC connectors to optional daughter card
ML605
OPT4 Board
Virtex-6
PCIe
FMC
FMC
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
Loopback optical link
PC
x4 Aurora 5Gbps x8 PCIe 2.5Gbps
11.84Gbps achieved
GbE

## Slide 23: Backup Solution for DHH Readout
A newly developed PCI-express card
  The card has just delivered to KEK a month ago; we start a test of this card soon.
Virtex-6 (XC6VLX75T)
DDR3 4GB buffer for accidental block of PCI-express
x2 SFP+ modules to receive DHH outputs
x2 RJ45 connectors to alert buffer full
PCI-express x4 Gen2
The card can be a next Belle-II DAQ platform.

## Slide 24: Communication with the 2nd EVB
Processed Data → Event Builder
AMC computing nodes
UDP/IP over HDL stack
2nd Layer EVB
TCP/IP over GbE
UDC/TCP converter
Preliminarily >118MB/s is achieved 
Processed Data → Event Builder
AMC computing nodes
TCP/IP on PowerPC core
2nd Layer EVB
~26MB/s 
Requirement: 33MB/s

## Slide 25: PXD R&D Milestones
1/10 SVD + partial PXD
Evaluation of PXD6 (test production) | Oct. | 2011
Start final (PXD9) production | May | 2012
DAQ / power / cooling ready for test | Jan. | 2013
“Telescope test” at DESY (full DAQ + slow control) | Fall | 2013
All ASICs produced | Feb. | 2014
Finish final DEPFET production | Apr. | 2014
Finish assembly of PXD | Apr. | 2015
DAQ / power / cooling ready for installation | Jul. | 2015
PXD installed on beam pipe at KEK | Sep. | 2015

## Slide 26: Summary
Data stream of the Belle II PXD from pixels to an event building system has been presented.
The full size of PXD output is 16MB/event. We design the PXD DAQ that can reduce the data size to a manageable level.
A telescope test of 1/10 SVD + partial PXD is planned in fall 2013 at DESY. It is a quite important milestone toward the successful operation of PXD DAQ.

## Slide 27: Backup Slides

## Slide 28: Belle II Collaborating Institutes
As of Feb, 2012
AUSTRALIA | Univ. of Melbourne
 | Univ. of Sydney
 | HEPHY, Austrian Academy of Sciences
CHINA | Institute of High Energy Physics
 | Peking Univ.
 | Univ. of Science and Technology of China
CZECH | Charles University in Prague
GERMANY | Deutsches Elektronen-Synchrotron
 | Karlsruhe Institute of Technology
 | Ludwig Maximilians University Muenchen
 | Max-Planck-Institut fur Physik Muenchen
 | Technical Univ. of Munich
 | Univ. of Bonn
 | Univ. of Giessen
 | Univ. of Goettingen
 | Univ. of Heidelberg
INDIA | Indian Institute of Technology Guwahati
 | Indian Institute of Technology Madras
 | Institute of Mathematical and Sciences
 | Panjab Univ. Union Territory
 | Tata Institute of Fundamental Research
KOREA | Gyeongsang National Univ.
 | Hanyang Univ.
 | Korea Institute of Science and Technology Information
 | Korea Univ.
 | Kyungpook National Univ.
 | Seoul National Univ.
 | Yonsei Univ.
MALAYSIA | Univ. of Malaya
POLAND | Institute of Nuclear Physics PAN
RUSSIA | Budker Institute of Nuclear Physics
 | Institute for High Energy Physics
 | Institute for Theoretical and Experimental Physics
SAUDI ARABIA | Univ. of Tabuk
SLOVENIA | Univ. of Ljubljana
 | Univ. of Nova Gorica
SPAIN | Istituto de Fisica Corpuscular
TAIWAN | Fu Jen Catholic Univ.
 | National Central Univ.
 | National Taiwan Univ.
 | National United Univ.
U.S.A. | Indiana Univ.
 | Luther College
 | Pacific Northwest National Laboratory
 | Univ. of Cincinnati
 | Univ. of Hawaii
 | Univ. of South Alabama
 | Virginia Polytechnic Institute and State Univ.
 | Wayne State Univ.
VIET NAM | Institute of Physics
 | Vietnamese Academy of Science and Technology
JAPAN | High Energy Accelerator Research Organization
 | Nagoya Univ.
 | Nara Women's Univ.
 | Niigata Univ.
 | Nuclear Physics Consortium
 | Osaka City Univ.
 | Toho Univ.
 | Tohoku Univ.
 | Tokyo Metropolitan Univ.
 | U-Tokyo
 | Yamagata Univ.
PXD R&D is contributed by colored institutes.

## Slide 29: DEPFET
Theory of operation
  A p-channel FET resides on a completely depleted silicon bulk.
  A deep n-implant creates a potential minimum for electrons under the gate.
  Signal electrons accumulate in the internal gate and modulate the transistor current (gq ~ 400pA/e⁻).
  Accumulated charge can be removed by a clear contact.
Depleted p-channel FET
Fully depleted → Large signal, fast signal collection
Low capacitance, internal amplification → Low noise
Transistor on only during readout → Low power

## Slide 30: Thinning Technology
Sensor wafer bonded on “handle” wafer.
Rigid frame for handling and mechanical stiffness
50μm thickness produced.
Full-sized Belle II matrices have been produced.
Electrical properties tested successfully.

## Slide 31: Test Production of Sensors
Front side
Thinned back side
First thinned (50µm) DEPFETs ever.

## Slide 32: Tests of Thin DEPFET Sensors
DUT: 32x64 pixel, Belle II type pixel size 50x50 µm²
100ns row read out time S/N = 17:1 (will improve, not yet optimal bias setting due to current DCD design)
Landau curve from ⁹⁰Sr source

## Slide 33: Clustering ASIC (DCE3)
DCE3 mini-chip with 256 clustering nodes
  Power: 165mW @ 400MHz.
  Bonding adapter ready.
  Clustering carrier board will be ready soon.

## Slide 34: DHP Output Format
Frame header (32bits)
  The frame header is always sent at every start of a new frame independently of a level-1 trigger.
  Data type (3bits)
  Chip ID (8bits)
  Frame ID (16bits)
  Reserved (5bits)
Row header (16bits)
  The row header is only sent when hit data are available in the active row.
  Flag (1bit)
  Row address (9bits)
  Common mode (6bits)
Data word (16bits)
  Flag (1bit)
  Column address (7bit)
  ADC data (8bit)

## Slide 35: DHH Output Format
Packet 1 (128bits)
  Header ID0(16bits), error-code(8bits), DHH-ID(6bits)
  Trigger information (32bits)
  Time tag (64bits)
Packet 2 (32bits)
  Header ID1(16bits), error-code(6bits), data-type(2bits), DHH-ID(6bits), DHP-ID(2bits)
Data body
  Same as the DHP output format.

## Slide 36: Expected Data Rate
Occupancy assumption = 3%
Design maximum level-1 trigger rate = 30kHz (ave.)
8Mpixel x 3% x 16bits x 30kHz = 103Gbps
  We have 40 DHH-links → 2.6Gbps per DHH-to-downstream-link

## Slide 37: Prototype ATCA System
2xSFP+ I/F with DHH
GbE output to 2nd level EVB
4x
FPGA programming I/F (IPMC)
Computing FPGAs
Switching FPGA
Virtex4 FPGAs
Linux runs on embedded PowerPC in the FPGA
For the optical links
6.25Gbps links
Aurora 8B10B encoding
are confirmed to work well.

## Slide 38: ATCA/CN Buffer Management
List of
Free Blocks
PXD/DHH → Pixel Data
HLT Trigger → ROI data
Event Builder ← Processed Data
Lookup:
PXD Data Blocks
Get free block,
write data to memory,
store ptr in lookup
HW Registers
Read FIFO
HW Registers
Write FIFO
IP Core
RoI selection
DDR2 memory
get free block, write ROIs to memory, get pixel ptr from lookup, feed both ptr to IP core
Read both ptr to IP core
write processed data
to Ethernet free blocks,
Links between cores inside the FPGA are being established.
UDP/IP over GbE

## Slide 39: RoI-Finding Latency
RoI-finding latency = 5secs in the worst case
  To allow up to 5-second RoI-finding latency, 4GB online buffer per DHH is required assuming 2.6Gbps/link with a margin factor.
3.2GHz
Intel Xeon,
e-time/core.
[ms]
Elapsed time distribution for Belle track finding

## Slide 40: Trigger Timing Distribution
Tree-structured trigger timing distribution
  The system is getting well matured.
  Clock jitter requirement: <20ns; achieved: <15ns.
~1100 destinations