## Slide 1: Belle II Overview
Yutaka Ushiroda (IPNS, KEK)
DESY-KEK Meeting
Mar. 20, 2012

## Slide 2: Role of Flavour Factories in coming 10 years

## Slide 3: Keystones of Flavour Factory
High luminosity lepton collider with well controlled background
Good detector of low material

## Slide 4: SuperKEKB and Belle II
e- 7GeV 2.6 A
e+ 4GeV 3.6 A
Target: L = 8x1035/cm2/s
SuperKEKB
Colliding bunches
Damping ring
Low emittance gun
Positron source
New beam pipe
& bellows
Belle II
New IR
TiN-coated beam pipe with antechambers
Redesign the lattices of HER & LER to squeeze the emittance
Add / modify RF systems for higher beam current
New positron target / capture section
New superconducting /permanent final focusing quads near the IP
Low emittance electrons to inject
Low emittance positrons to inject
Replace short dipoles with longer ones (LER)

## Slide 5: Belle II Detector
electron (7GeV)
positron (4GeV)
KL and muon detector:
Resistive Plate Counter (barrel outer layers)
Scintillator + WLSF + MPPC (end-caps, inner 2 barrel layers)
Particle Identification
Time-of-Propagation counter (barrel)
Prox. focusing Aerogel RICH (fwd)
Central Drift Chamber
He(50%):C2H6(50%), Small cells, long lever arm, fast electronics
EM Calorimeter:
CsI(Tl), waveform sampling (barrel)
Pure CsI + waveform sampling (end-caps)
Vertex Detector
2 layers DEPFET + 4 layers DSSD
Beryllium beam pipe
2cm diameter

## Slide 6: Status of Belle 1
Beam Pipe and Vertex Detector extraction: on Nov. 10, 2010
Belle Detector Roll-out: Dec. 9, 2010
End-caps, CDC, B-ACC, TOF extraction: in Jan. 2011

## Slide 7: Belle II Collaboration
17 countries/regions, 62 institutes, ~400 collaborators (Jan. 2012)
+2 countries, 4 institutes (Mar. 14, 2012)

## Slide 8: German Institutes
DESY
Univ. of Goettingen
Univ. of Bonn
Univ. of Giessen
Univ. of Heidelberg
Karlsruhe Institute of Technology(KIT)
Ludwig Maximilians University (LMU)
Max-Planck-Institut fur Physik
Technical Univ. of Munich (TUM)
9 institutes, ~50 people
2nd largest (JP, 12 inst. ~130 people)

## Slide 9: DEPFET for Belle II
total of 8 Mpx
Layer | radius (mm) | px size (mm2) | thickness (mm) | half ladder rows×cols | half ladder size (mm×mm) | #ladders
1 | 14 | 50x55 | 75 | 768×250 | 70×15 | 8
2 | 22 | 50x75 | 75 | 768×250 | 85×15 | 12
Mechanical mockup

## Slide 10: Principle of DEPFET
Each pixel is a p-channel FET on a completely depleted bulk
A deep n-implant creates a potential minimum for electrons under the gate (“internal gate”)
Signal electrons accumulate in the internal gate and modulate the transistor current (gq ~ 400 pA/e-)
Accumulated charge can be removed by a clear contact (“reset”)
Rolling shutter mode (column parallel) for matrix operation
20 µs frame readout time
Low power (only few lines powered); 0.1W/cm2
Air-cooling sufficient

## Slide 11: Real merit for B physics (esp. t-dep. CPV)

## Slide 12
Country | Funding Agency | Member (Abbreviation) | Representative
Czech Republic |  | Charles University Prague (PRA) | Zdenek Dolezal
China | CAS | Inst. for High Energy Physics (IHEP) | Zhen’An Liu
Germany | BMBF | University of Bonn (BON) | Norbert Wermes
 |  | University of Göttingen (GOE) | Ariane Frey
 |  | University of Heidelberg (HEI) | Peter Fischer
 |  | University of Karlsruhe (KAR) | Thomas Müller
 |  | University of Gießen (GIE) | Sören Lange
 |  | University of Munich (LMU) | Jochen Schieck
 |  | Technical University Munich (TUM) | Stephan Paul
 | DESY | DESY Hamburg (DES) | Carsten Niebuhr
 | MPI | MPI for Physics, München (MPI) | Hans-Günther Moser
Japan | JSPS | Struct. Biol. Research Center (KEK) | Soichi Wakatsuki
Poland |  | Inst. of Nucl. Phys,, Krakow (KRA) | Maria Rozanska
Spain | Ministerio de Ciencia e Innovación | CSIC-CNM Barcelona (CNM) | Enric Cabruja
 |  | University of Barcelona (UBA) | Angel Dieguez
 |  | CSIC-IFCA Santander (IFC) | Ivan Vila Alvarez
 |  | CSIC-IFIC Valencia (IFV) | Carlos Lacasta
The DEPFET Collaboration

## Slide 13: Weak Point of DEPFET Collaboration
have never built and installed a full DEPFET detector into a real HEP detector complex as a system
  Practical constraint in space, …
  Integration with others
  …

## Slide 14: Role of DESY-KEK (1): Mechanical Integration of PXD
Dry volume, cooling pipe, cables
Coupled with Mechanics of Interaction Region and Vertex Detector as a whole
  SVD Group needs help on Mechanical Design
  Lack of Mechanical Engineer at KEK
    Official request sent out to IPNS/Mechanical Engineering Group several months ago, but …
[Software effort] Alignment of tracking detectors (CDC/SVD/PXD)
  Coupled with mechanical design
    Overlap of sensors
    Support and positioning of ladders

## Slide 15: Role of DESY-KEK (2): Integration of data flow from PXD
Huge data from PXD must be reduced

## Slide 16: Data rate comparison
Experiment | Event Size [kB] | Record rate | 
 |  | [Hz] | [MB/s]
Belle II | 300 | 6,000 | 1,800
ALICE(HI) | 12,500 | 100 | 1,250
ALICE(pp) | 1,000 | 100 | 100
ATLAS | 1,600 | 200 | 320
CMS | 1,500 | 150 | 225
LHCb | 25 | 2,000 | 50
Event size is small
Record rate is so high and cannot be low!

## Slide 17: Role of DESY-KEK (3): GRID-based distributed computing
KEK alone cannot handle our huge data
Help needed for the sake of analyzers in remote sites
MC Production
and Ntuple Production
MC Production (optional)
Ntuple Analysis
Raw Data Storage and Processing
Belle II
detector

## Slide 18: Belle II Construction Schedule
JFY 2014
Machine operation starts
JFY2012 (April-March)
Belle rotation
JFY2013
Installation of KLM
Physics run starts in end of CY 2015