## Slide 1: Summary of SuperKEKB/Belle II session
Yutaka Ushiroda (IPNS, KEK)
DESY-KEK Meeting
Mar. 20, 2012

## Slide 2: Role of Flavour Factories in coming 10 years

## Slide 3: SuperKEKB and Belle II
e- 7GeV 2.6 A
e+ 4GeV 3.6 A
Target: L = 8x1035/cm2/s
SuperKEKB
Colliding bunches
Damping ring
Low emittance gun
Positron source
New beam pipe
& bellows
Belle II
New IR
TiN-coated beam pipe with antechambers
Redesign the lattices of HER & LER to squeeze the emittance
Add / modify RF systems for higher beam current
New positron target / capture section
New superconducting /permanent final focusing quads near the IP
Low emittance electrons to inject
Low emittance positrons to inject
Replace short dipoles with longer ones (LER)

## Slide 4: Belle II Detector
electron (7GeV)
positron (4GeV)
KL and muon detector:
Resistive Plate Counter (barrel outer layers)
Scintillator + WLSF + MPPC (end-caps, inner 2 barrel layers)
Particle Identification
Time-of-Propagation counter (barrel)
Prox. focusing Aerogel RICH (fwd)
Central Drift Chamber
He(50%):C2H6(50%), Small cells, long lever arm, fast electronics
EM Calorimeter:
CsI(Tl), waveform sampling (barrel)
Pure CsI + waveform sampling (end-caps)
Vertex Detector
2 layers DEPFET + 4 layers DSSD
Beryllium beam pipe
2cm diameter

## Slide 5: Belle II Collaboration
19 countries/regions, 66 institutes, ~400 collaborators
9 German institutes (2nd largest)

## Slide 6: DEPFET for Belle II
total of 8 Mpx
Layer | radius (mm) | px size (mm2) | thickness (mm) | half ladder rows×cols | half ladder size (mm×mm) | #ladders
1 | 14 | 50x55 | 75 | 768×250 | 70×15 | 8
2 | 22 | 50x75 | 75 | 768×250 | 85×15 | 12
Mechanical mockup

## Slide 7
Country | Funding Agency | Member (Abbreviation) | Representative
Czech Republic |  | Charles University Prague (PRA) | Zdenek Dolezal
China | CAS | Inst. for High Energy Physics (IHEP) | Zhen’An Liu
Germany | BMBF | University of Bonn (BON) | Norbert Wermes
 |  | University of Göttingen (GOE) | Ariane Frey
 |  | University of Heidelberg (HEI) | Peter Fischer
 |  | University of Karlsruhe (KAR) | Thomas Müller
 |  | University of Gießen (GIE) | Sören Lange
 |  | University of Munich (LMU) | Jochen Schieck
 |  | Technical University Munich (TUM) | Stephan Paul
 | DESY | DESY Hamburg (DES) | Carsten Niebuhr
 | MPI | MPI for Physics, München (MPI) | Hans-Günther Moser
Japan | JSPS | Struct. Biol. Research Center (KEK) | Soichi Wakatsuki
Poland |  | Inst. of Nucl. Phys,, Krakow (KRA) | Maria Rozanska
Spain | Ministerio de Ciencia e Innovación | CSIC-CNM Barcelona (CNM) | Enric Cabruja
 |  | University of Barcelona (UBA) | Angel Dieguez
 |  | CSIC-IFCA Santander (IFC) | Ivan Vila Alvarez
 |  | CSIC-IFIC Valencia (IFV) | Carlos Lacasta
The DEPFET Collaboration

## Slide 8: Challenges in PXD integration
Beam Background Suppression
Mechanical Integration
  Dry volume, cooling pipe, cables
  Integration with Beam Pipe SVD, QCS
DAQ integration
Distributed Computing
Need help from DESY people

## Slide 9: DESY joined Belle II in Nov. 2011

## Slide 11: Agenda of parallel session

## Slide 12: Mechanical Integration
Dedicated meeting at DESY on 12-13 Apr.

## Slide 13: Thermal issues

## Slide 14: Background Simulation
Yuri Soloviev stayed at KEK for one month (short-term invitation program)
and learnt Belle II background simulation (especially synchrotron radiation) from scratch
HER e- beam
LER e+ beam
Be
Ti
Ti
SR must not hit Be part.
SR is desired not to hit Ti part.

## Slide 18: Belle II Construction Schedule
JFY 2014
Machine operation starts
JFY2012 (April-March)
Belle rotation
JFY2013
Installation of KLM
Physics run starts in end of CY 2015

## Slide 19: Principle of DEPFET
Each pixel is a p-channel FET on a completely depleted bulk
A deep n-implant creates a potential minimum for electrons under the gate (“internal gate”)
Signal electrons accumulate in the internal gate and modulate the transistor current (gq ~ 400 pA/e-)
Accumulated charge can be removed by a clear contact (“reset”)
Rolling shutter mode (column parallel) for matrix operation
20 µs frame readout time
Low power (only few lines powered); 0.1W/cm2
Air-cooling sufficient

## Slide 20: Real merit for B physics (esp. t-dep. CPV)

## Slide 21: Weak Point of DEPFET Collaboration
have never built and installed a full DEPFET detector into a real HEP detector complex as a system
  Practical constraint in space, …
  Integration with others
  …