## Slide 1: FLASH at DESY in Hamburg
FLASH
PETRA III
XFEL

## Slide 2: FLASH at DESY in Hamburg
Primarily a Photon User Facility
  since 2005
Single-pass high-gain SASE Free-Electron Laser
  SASE = self-amplified spontaneous emission
Photon wavelength range from vacuum ultraviolet to soft x-rays
Femtosecond range pulses with high brilliance
FLASH II, a second undulator beam line is in preparation
SCRF Linac started life as a test-bed for a linear collider (TESLA Test Facility)
  Beam time available for ILC experiments
  Currently unique facility in the world (integrated systems testing)
Notes: 2

## Slide 3: FLASH layout after the upgrade 2009/2010
315 m
Bunch Compressor
Bypass
Undulators
sFLASH
Bunch Compressor
5 MeV
150 MeV
500 MeV
1200 MeV
Accelerating Structures
Diagnostics
FEL Experiments
RF stations
LOLA
RF Gun
Laser driven photo injector
Diagnostic Sections
FEL Experimental Hall
TESLA type superconducting accelerating modules
Fixed gap SASE undulators
Experimental Hall
sFLASH Undulators
3.9 GHz module

## Slide 4
Tour tomorrow at 10:15

## Slide 5: FLASH as a VUV laser
6 undulator modules, total length 27 m
  Fixed gap of 12 mm, permanent NdFeB magnets, peak field B = 0.48 T K = 1.23, period λu = 27.3 mm
  Gain length Lgain = 2.5 ± 0.3 m (@13 nm)
Requirements for electron bunches
Peak current > 2 kA
Emittance (slice, norm.) < 1 mm mrad
Energy spread (slice, rel.) < 10-3
Notes: 5

## Slide 6: SASE Parameters for 4.4 nm
Preliminary data for 4.4 nm:
Energy 140 µJ (max.)
Peak power ~ 2 GW (estimate)
bandwidth 0.25 % rms
Peak Brilliance B ~ 1030 - 1031 photons/s/mrad2/mm2/0.1%bw
preliminary

## Slide 7: Experimental Hall
Visible Laser
FIR -Beamline
Plane Grating
Monochromator
BL3
unfocused (5 -10 mm),
optional multilayer mirror
in experiment for few to
sub-μm focus
BL2
20 μm focus
BL1
100 μm focus
PG2
50 μm focus,
monochromatized
PG1
sub-10 μm focus,
monochromatized
2-stage Raman-
Spectrometer

## Slide 8: 9mA Experiments at TTF2/FLASH
 |  | XFEL | ILC | FLASH design | FLASH experiment
Bunch charge | nC | 1 | 3.2 | 1 | 3.0 (typical 1.0)
# bunches |  | 3250* | 2625 | 7200* | 2400
Pulse length | ms | 650 | 970 | 800 | 800
Current | mA | 5 | 9 | 9 | 9
TTF2/FLASH: unique worldwide facility
ACC 4-7

## Slide 9: Primary Objectives
Long-pulse high beam-loading (9mA) demonstration
  800ms pulse with 2400 bunches (3MHz)
  3nC per bunch
  Beam energy 700 MeV ≤ Ebeam ≤ 1 GeV
Original primary goals
  Demonstration of beam energy stability
    Over extended period
  Characterisation of energy stability limitations
    Operations close to gradient limits
  Quantification of control overhead
    Minimum required klystron overhead for LLRF control
  HOM absorber studies (cryo-load)
*Recent Goal* operation with “flat gradients”
Major challenge for FLASH !
  Pushes many current operational limits
Primarily a LLRF experiment

## Slide 10: Context
Relevant to ILC, XFEL, FLASH
  ILC: International GDE stated milestone for systems test
    Primary driver: important and visible deliverable for international effort
  XFEL: Close collaboration with world-wide LLRF groups
    Focus (potentially accelerate) development and planning for XFEL
    “Operation at limits” experience provides important Input for future XFEL development
  FLASH: Addresses many operational issues
    Automated exception handling and recovery
    Better characterisation of machine
    Towards routine high-power long-pulse operation for users.
International collaboration (ILC-GDE driven)
  ANL, DESY, FNAL, KEK, SLAC, …
  >40 registered on mailing list
  Direct international participation in machine shifts and data analysis
Notes: Comment concerning MAC.

## Slide 11: Focus on ACC6 and ACC7
Operation with Gradient Spread
  From single RF source
  now baseline
Specifically: achieving constant gradients for each individual cavity during beam pulse
  to within few percent
  close to gradient limits
ACC6
ACC7
31.5 MV/m
40.0
35.0
30.0
25.0
20.0
15.0

## Slide 12: ILC: Maximising Energy
ILC baseline parameter: 31.5±20% MV/m accelerating gradient (25-38 MV/m)
Full individual cavity Pfor and QL control foreseen
  but not cheap!
  FLASH only has QL adjustment
  Flat gradient solutions IB dependent!
(Positive) slopes on individual cavity gradients ‘eat away’ gradient overhead
Goal: <3% change in V over flat top
  including during turn-on
±20%

## Slide 13: ILC: Beam Dynamics
Random cavity misalignments (tilt) acav
Transverse kick to the beam
  time dependent due to voltage ‘slope’ Va(t)
Resulting oscillations causes emittance growth
  different for different bunches along train
Cavity alignment pitch: 300 mr RMS
gey = 30 nm
1.5% RMS ‘voltage tilt’ → 1 nm gey growth
(for entire ILC linac)
Note: D(gey ) ∝ DVa(t)2
Tolerance similar to quench limit overhead (few %)

## Slide 14: FLASH: Flat Gradients (Feb 2012)
2400 bunches @ 3MHz
Average charge qb ~1.5nC (~4.5mA)
800ms flat top pulse
(could not increase qb due to beam loss)
Detuned:
ACC6 C5 C6 (low gradient)
ACC7 C1 (piezo tuner broken)
Average cavity gradient: 28.2 MV/m
(23-33 MV/m)
Gradient (MV/m)
RMS ‘flatness’ ~0.02%

## Slide 15: Flat Gradient Solution (Feb 2012)
Raised ACC6-7 vector sum to 380 MV
  close to quench limits of several cavities
Flat gradients iteratively achieved by automated adjustment of individual QL
  RMS ‘tilts’ ~0.2% achieved!
Other (critical) key tools
  LFD piezo compensation server
  LLRF quench-protection system

## Slide 16: Limits achieved (380 MV)
limiting cavity
Gradient (MV/m)

## Slide 17: Gradient “Tilt” Stability
13 cavities plotted
Each data point is average over
RMS over flat-top divided by average voltage.
100 pulses averaged (20 seconds)
Scale is equivalent relative rms for 1% voltage change over flat-top (tilt)
[= 1% / (2*sqrt(3)) ~ 0.29%]
sflat-top/Vavg in %
hours

## Slide 18: FLASH: Stability
15 consecutive studies shifts (120hrs), and with no downtime
Time to restore 400us bunch-trains after beam-off studies: ~10mins
Energy stability with beam loading over periods of hours: ~0.02%
Individual cavity “tilts” equally stable
Energy stability over 3hrs with 4.5mA
~0.02% pk-pk
9 Feb 2011

## Slide 19: Recovery/Boot-strap Scenario
With no beam (loading) tilts appear on cavities
  Would reduce vector sum / RF to avoid quench
Progressive restoration of beam pulse allows QL tuning without quench
  initial DV too small to quench
  short pulse tuning enough to go to longer pulses
  After that small corrections needed

## Slide 20: Other important observations
Quench recovery
  Major quench (~intentional) required time to allow automated piezo system to re-tune cavities (minutes)
  After cavity tuning, full 2400 bunches restored instantaneously
    no machine trips or instabilities
Beam-off crash test
  Intentionally killed laser (beam) to test LLRF response
  Quench protection system and beam-loading compensation system worked correctly to prevent quenching

## Slide 21
HV of klystron was decreased from 108 kV to 86.5 kV.
4.5 mA beam was used.
Filling time was adjusted to have ~rectangular output.(500us ->660us)
Operation point is about -7% (in power) from saturation.
RF Power Overhead
operation point
Filling Flat-top
Saturation (1.58MW)
RF output with “bump” set-table
Operation(1.48MW)
7%
S. Michizono KEK
ILC specific

## Slide 22
Amplitude stability was x2 worse at near sat. because of the limitation of rf.
But 0.05%rms in amplitude can satisfy the requirements (~0.1% in amplitude)
Phase stability was almost same between nominal and near saturation.
Stabilities at nominal and near saturation
VS amplitude
VS phase
S. Michizono (KEK)
Possible to operate at 7% below saturation

## Slide 23: Future
Currently one more dedicated run in 09.12
  Primary goal: 6mA 800 us
  (Last possibility for 9mA ?)
  Final results possibility for GDE TDR
Q1 2013 shutdown for FLASH 2 installation
  FLASH 1 Undulator Bypass will be removed
Still expect possibilities for further ‘long bunch train, high beam-loading experiments’
  Possibly in collaboration with STF and NML