## Slide 1: Photon Beam Transport
WP73
Harald Sinn
PPR1-2012, April 19, 2012

## Slide 2: Achievements since last PPR (Nov. 2011)
Contract on mirror prototype was signed on February 28th :
2 nm PV figure error, 80 cm long mirror, weakly bendable, adaptive design and water cooled.
(FEA ongoing, CDR expected mid June)
From F. Yang, E.XFEL

## Slide 3: Mirror chamber development
DR in January, FEA reveals problem with sensitivity to air pressure variations, tender expected in June.
1 bar = 6 microns
± 40 hPa = ± 240 nm = ± 480 nrad
SASE2: 660 m × 480 nrad × 2 = ±0.6 mm hor. beam motion depending on weather
T. Noll, HZB, A. Trapp E.XFEL

## Slide 4: SASE3 monochromator (CDR update)
experiment hall
VLS G1, G2, (M4)
M1
M2
M3a,b,c
M5
M6
horizontal focus
vertical exit slits
Top view
Side view
SCS
281
283.9
300
301
339
341
374
400
417
SQS
open

## Slide 5: SASE3 mono and resolution
800 eV +/- 160 meV
ΔE = 60 meV
800 eV/60 meV = 13.000
Next step: wavefront calculations + technical design concept
Ray tracing by R. Follath, HZB

## Slide 6: Equipment protection system
Concept
Devices
Under discussion with MPS group, WPs 74,17&76,
Presented in XFEL meeting on Feb. 8, 2012

## Slide 7: Other achievements since Nov. 2011
3D CAD placeholder model updated including E-racks
Started E-crate allocation plan
Signed contract on Hard X-ray Monochromator
First vibration studies in tunnels
Interferometer test setup reached 100 nrad stability
Prototype pump station build up
Prototype SR-Aperture received
Shutter requirements determined (WP35), collaboration with DESY started on design
Damage studies on gratings
CDR for gas attenuator
DESY FSBT design,
F. Yang E.XFEL

## Slide 8: WP73 team
Shafagh Dastjani
Jerome Gaudin
Fan Yang
Idoia Freijo
Liubov Samoylova
Harald Sinn
Martin Dommach
Jens Linnemann
Antje Trapp
Nicole Kohlstrunk
Alexander Bartmann
Raul Villanueva
Daniele La Civita (ALS)
Xiaohao Dong (Soleil)
x-ray optics
design
vacuum
students
WP-73
Timo Korsch starts 1.5.2012
New !

## Slide 9: Next plans
Get out mirror chamber design
Make progress on mirror prototype
Progress on hard + soft X-ray mono
Design of 3.5 km beam transport, IKC Poland (?)
Design of beam stops, apertures
Vacuum test setup in Hera Süd
Build-up and test of gas attenuator
Damage experiment on metal–coated mirrors
Technical Design Review in September 2012

## Slide 10: Concerns: Where to put Spilt & Delay line?
IKC from Uni Münster: Split & Delay Line
Not clear, which experiment will use it and in which tunnel & beam transport it should go
(requires collision checks, infrastructure, controls)
SASE 2, XTD6