## Slide 1: 10Gb Ethernet and beyond on FPGA Workshop UDP/IP Implementation and Data streaming
Rob Halsall
European XFEL/DESY
25 May 2012

## Slide 2: XFEL
1M Pixel, 2B/Pixel,4.5Mhz, 512 Samples, @10Hz
10Gbyte per Second per Megapixel rate
16 x 10G Links off detector per Megapixel
10G Ethernet using UDP protocol
Scalable to multiple Megapixels – 160 x 10G Links
Switch & Farm
Train Builder
Detector
10g Switch
10g server
10G
10G
10G

## Slide 3: XFEL LPD Quadrant Prototype
LPD Quadrant
  256K Pixels
  512 ASICs
Embedded Readout
  4 x FEMs
  4 x 10G Links

## Slide 4: XFEL LPD FEM
Front End Module
  128 ASIC
  480 Way LVDS
  2 x SP3 I/O FPGA
  V5 FXT 100 FPGA
  SODIMM DRAM
  Dual 10G FMC (DESY)
  1GE LAN
  RJ45 LVDS Timing
16 per M Pixel
Embedded in Detector Head

## Slide 5: XFEL Train Builder
  Train Builder Prototype
    4 x V5FXT100 FPGAs
    4 x DESY dual 10G FMC
    Mindspeed X-point
      80x80 @ 6.5G
    8 x 4GB SODIMM DDR2 Modules
    1 Pair per 0.5 Mpixel
    ATCA form factor
  Builds Images for Farm
    8 x 10 Gbit/s
    Scale up to 160x160
Notes: Optical fibres

## Slide 6: PC Side
10G Switch
  Arista
10G NICs
  Mellanox/Chelsio
Linux Servers
  Supermicro

## Slide 7: XFEL
0.25 M Pixel Train Builder
  Train builder receives image trains spread across 4 inputs synchronously
  4 Outputs send complete image trains
Scale to 160 x 10G Links
  Requires external 4 x 160 x 160 Xpoint Module
FEMs
Train Builder
FEMs
PC
SWITCH
PC
PC
SWITCH
PC
Train Builder
Detector
N x 512
N x 512

## Slide 8: FEM FPGA Firmware
ASIC Pipeline Emulation
ASIC Slow Ctrl
ASIC Fast Commands
SP3 Confign
FPGA
ASIC Data Rx
Processor Embedded
Software
DDR2
10Gb Link
C&C Timing & Veto
SP3 Top I/O
(80%)
SP3 I/O
FPGAs
Virtex5 Main FPGA
LPD
Super
Module
Clock & Controls
ASIC Simulated Data
DATA
CTRLS
128 ASICs
PC
Virtex 5 FPGA
RS232
R
R
R
R
GbE
UART
MatLab
Python

## Slide 9: Core TB Firmware
Aurora
Core
0
XPOINT
4 TX PAIRS
4 RX PAIRS
4 TX PAIRS
4 RX PAIRS
Aurora
Core
1
XAUI
Core
0
XAUI
Core
1
Power PC
Memory Controller
Subsystem
4 TX PAIRS
4 RX PAIRS
4 TX PAIRS
4 RX PAIRS
XTAL
PLL
XTAL
PLL
DUAL
10G PHY
FMC
PHY
SFP+
PHY
SFP+
TB FPGA
UDP
Core
Power PC
Memory Controller
Subsystem
UDP
Core
‘XCTRL’
DDR2 SDRAM
DDR2 SDRAM

## Slide 10: FEM/TB Firmware
PHY
XAUI
SFP
UDP
PPC
AUR
PHY
XAUI
SFP
UDP
PPC
AUR
FPGA 1
XP
RAM
RAM
PHY
XAUI
SFP
UDP
PPC
AUR
PHY
XAUI
SFP
UDP
PPC
AUR
FPGA 2
RAM
RAM
PHY
XAUI
SFP
UDP
PPC
AUR
PHY
XAUI
SFP
UDP
PPC
AUR
FPGA 3
RAM
Detector
FPGA
GIGE
RAM
PHY
XAUI
SFP
UDP
PPC
AUR
PHY
XAUI
SFP
UDP
PPC
AUR
FPGA 4
RAM
RAM
PHY
XAUI
SFP
UDP
PPC
AUR
PHY
XAUI
SFP
UDP
PPC
AUR
FPGA 5
RAM
RAM
PHY
XAUI
SFP
UDP
PPC
AUR
PHY
XAUI
SFP
UDP
PPC
AUR
FPGA 6
RAM
RAM
PHY
XAUI
SFP
UDP
PPC
AUR
PHY
XAUI
SFP
PE
PPC
AUR
FPGA 7
RAM
RAM
PHY
XAUI
PE
PPC
AUR
PHY
XAUI
SFP
PE
PPC
AUR
FPGA 8
RAM
RAM
SFP
PHY
XAUI
UDP
PPC
RAM
ASIC
RX
SFP
PHY
XAUI
UDP
PPC
RAM
TB
ASIC
RX
FEM
SFP
FPGA
FPGA

## Slide 11: 10G IP Library
  Local_Link
    LL_FIFO, LL_MUX, LL_DEMUX
    LL_GEN, LL_CHK
  RDMA
    RS232_RDMA
    RDMA_SER_SPLIT
    RDMA_PAR_BUS_SPLIT
    RDMA_REG
  Aurora
    LL_10G_AURORA
  Video
    LL_VID_GEN
  X10G
    LL_10G_UDP
LL-10G-AURORA
LL 64
XAUI
RDMA
156.25MHz
32
156.25MHz

## Slide 12: 10G UDP IP
Used in
  FEM & TB FEM
Features
  LL FRAME <-> UDP PKT STREAM
  FPGA <-> FPGA - FPGA <-> PC
  RDMA Programmable
  Rx IP, PORTS, MAC
  Tx MAC, IP PORT LUT
  IFG…
  No Handshake/flow control
  No resend
LL-10G-UDP
LL 64
XAUI
RDMA
156.25MHz
32
156.25MHz

## Slide 13: Local Link transport via UDP
UDP Header | 42B
Detector Data | 8K
Frame Number | 4B
SOF/EOF Packet No | 4B
LL 10G
  Tx Channel splits Local Link frame into 8K Byte UDP packets
  Adds a LL frame number & a packet number
  SOF & EOF Flags in top bits of packet number
  Rx channel re-assembles packet stream into a Local Link frame
UDP Header | 42B
Detector Data | 8K
Frame Number | 4B
SOF/EOF Packet No | 4B
LL Header | 8
Detector Data | 2M+
LL Trailer | 8
Index

## Slide 14: FEM -> TB - UDP Train
UDP Header | 42
Detector Data | 8K
Frame Number | 4
Packet No 1,2,3… | 4
UDP Header | 42
Detector Data | 8K
Frame Number | 4
Packet No 0 | 4
UDP Header | 42
Detector Data | 8K
Frame Number | 4
Packet No 1,2,3… | 4
UDP Header | 42
Detector Data | ≤8K
Frame Number | 4
Packet No N | 4
First UDP Packet
N x Data UDP Packet
Last UDP Packet
Local Link Frame
SOF
EOF
LL Header | 8
Detector Data | 2M+
LL Trailer | 8
Local Link Frame
LL Header | 8
Detector Data | 2M+
LL Trailer | 8
Index
FNUM

## Slide 15: TB -> PC - UDP Packet Format
Detector Header | 
Detector Data | 8M
Trailer | 8B
Detector Data | 8M
Trailer | 8B
Detector Data | 8M
Trailer | 8B
Detector Data | 8M
Trailer | 8B
Detector Data | 8M
Trailer | 8B
Detector Data | 8M
Trailer | 8B
Packet trailer
  Frame/Packet Count +sof/eof
Overwrite next packet over trailer of previous packet
No copies to remove trailer
Re-assembles Local Link Frame in memory
Some copying may be required to fix out of order and missing packets but at a low rate

## Slide 16: UDP TB -> PC - Trailer Format
31 |  |  |  |  |  |  | 24 |  |  |  |  |  |  |  | 16 |  |  |  |  |  |  |  | 08 |  |  |  |  |  |  |  | 00
Frame Count |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SOF | EOF | Reserved |  |  |  |  |  | Packet Count |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Frame Count 2^32 frames => 10 years
  @10Hz
Packet Count 2^24 => 128 Gbyte Max Frame Size
  8192 Bytes/pkt
SOF/EOF flags + 6 bits reserved
  e.g. SOP/EOP/RESEND/,…
Same Format as Header Mode…

## Slide 17: 10G UDP Block Tx Path
Simplified view of Transmit packet processing
  Local Link Frame contains train data
  Local link frame header contains index to MAC, IP, PORT in LUT
  Entire local link frame packet stream sent to the address indexed in the LUT – ‘farm mode’
  Power PC or firmware can set this for each train
  The addresses could simply loop or be sourced from broadcasts
ll fifo
hdr
trl
xtr
ll pkt
splitter
ll pkt
hdr/trl
insert
ll pkt
chks
len
chks
len
ll pkt
ll frm
MAC
IP
PORT
LUT
Index
extract
ll pld
mac
ip
port
ll hdr/trl
Packet
Engine
index
xgmii-tx
64
64D+8C
64
64
64
64
64
8k pipe

## Slide 18: 10G UDP Block Rx Path
Simplified view of Receive packet processing
  Re-assembles Packet stream into Local Link Data Frame using trailer info
  Extracts MAC, IP, PORT info
  Provides MAC, IP & PORT Filter
  Currently Receives from a single address
LL FIFO
PKT
COMBINE
UDP
EXTRACT
xgmii-Rx
64D+8C
64
64
64
64
ENET frame
Sync
align

## Slide 19: Slice Test Design
XAUI
LL-10G
UDP
+FM
LL-MUX
LL-MON-IP
LL-GEN
LL64
LL64
LL64
Tx
PowerPC
LL64
LL-VID
XAUI
LL-10G
UDP
+FM
LL-MUX
LL-MON-IP
LL-GEN
LL64
LL64
LL64
Tx
PowerPC
LL64
LL-VID
SEQ
RDMA
trig_0
done_0
trig_n
done_n
1
8

## Slide 20: Slice Test
Firmware
  10G UDP with Farm Mode exists VHDL
Software
  UDP Local Link Frame Receive exists python -> c/c++ boost
  UDP 10G Setup exists Matlab -> python
ML510
FEM
TB
10G
Server
Server
10G Switch

## Slide 21: Test Bench
FEM + DESY 10G FMC
ML510 ‘TB’ + DESY 10G FMC

## Slide 22: Tools
Subversion
    Structure
    Libraries
    Documentation
    Tool compatibility
    ISE, EDK, ISIM, PlanAhead…
Linux
    Design & DAQ

## Slide 23: Summary/Plans/Future
10G Ethernet successful so far...
Complete Testing of 10G UDP IP ‘Farm Mode’
Complete Testing/Development of Train Builder at RAL
Train Builder Slice Tests at DESY in July
Consider Simple Re-send capability
Porting to Xilinx K7/V7 10G direct/DDR3 SDRAM
Longer term 40G Ethernet & iWarp/RDMA & ROCE interest
Ordered Xilinx & HTG K7/V7 Dev Boards
Have Mellanox 40G Ethernet NICs

## Slide 24: Questions