## Slide 1: High speed data recording - software
Djelloul Boukhelef (XFEL)
25.05.2012
10Gb Ethernet and beyond on FPGA Workshop
The Cluster of Research Infrastructures for Synergies in Physics is co-funded by the partners and the European Commission under the 7th Framework Programme Grant Agreement 283745
Notes: How to edit the title slide
Upper area: Title of your talk, max. 2 rows of the defined size (55 pt)
Lower area (subtitle): Conference/meeting/workshop, location, date, your name and affiliation, max. 4 rows of the defined size (32 pt)
Change the partner logos or add others in the last row.

## Slide 2: Outline
Introduction
Slice test
  Test measurements
Software
  UDP Feeder (TB emulator)
  PCL application
  Some preliminary test results
Summary

## Slide 3: Purpose of slice test
Timeline: 2010-2012 – evaluation, development and testing of hardware and software components
Hardware level
  Link bandwidth: Do we see the full wire speed (10Gbps)
  UDP behavior: Packets loss
  Network performance: Concurrent read and write operations
Software level:
  Develop the software: Feeder (emulation) and PC layer
  Effect of concurrent processing on read/write activities
  Device/DeviceServer model, configurability: is s/w framework good?
Outlook:
  Complete software suite: processing, formatting
  Test 10GB/s disk write
Notes: Proof of concept
  Capability to handle 10GB/s data rate: read data from train builder, process/format, and send it to the computing and storage devices.
  Identify issues/bottlenecks, solve them: Error situations (UDP packet loss), speed-up data transfer, data format (HDF5, Wrona)…
Dimensioning and tuning
  Measure processing capabilities on the PC layer including data compression and rejection
  Assess scalability of the processing and storage system
  Ability to run multiple concurrent experiments, investigate usage of shared resources and data access protection
  Test different data storage hardware configurations, find the proper balance between capacity and access speed
  Identify data access patterns and improve access performance accordingly
  …

## Slide 4: System architecture

## Slide 5: Software status

## Slide 6: Purpose
Proof of concept
  Ability to handle 10GB/s data rate: read data from train builder, process/format, and send to the computing and storage layers
  Use the EXFEL homogenous software framework
Development
  Write the necessary software components: read., processing, formatting, write …
  Identify issues/bottlenecks: e.g. error situations (UDP packet loss), speed-up data transfer…
Test and tuning
  Measure the processing capabilities of the PC Layer
  Test different software and hardware configurations, find the proper balance between scalability, performance, and reliability

## Slide 7: Software architecture - overview
Two applications are under development
  Train builder emulator
  PCL node application
Data-driven model (push)
  Start PC nodes
    Wait for data
  Start UDP feeder
    Wait for timer signal
  Start timing system
Communication model
  1-to-1, N-to-N
UDP feeder 2
Node 1
Node 2
PC Layer
Node n
UDP feeder 1
UDP feeder m
Train builder emulator
UDP
Timing system

## Slide 8: UDP feeder
Train generator
  Circular train buffer
  Trains are generated at the beginning (offline)
Train dispatcher
  PCL nodes directory (configurable)
  At every timer signal, select next train and next channel
  Divide the train into packets and send them using UDP
Train buffer (Circular)
Train generator (file, random)
Nodes directory
Next train
Next channel
Train data
Serialization through UDP
1
3
2
4
Internal structure
Timer

## Slide 9: Train serialization
Images desc.
Images data
000
001
002
003
.
.
.
Train structure (configurable)
  Header, images & descriptors, detector data, trailer
Implementation
  Plain vanilla UDP
  The train is divided into chunks of 8k (configurable)
Packet structure
  Adhere to Rob’s proposal
SoF=1
EoF=1
Header
Trailer
Body
Data 8129 bytes
# Frame 4b
# Packet 3b
1b
SoF, EoF

## Slide 10: PC Layer node
Processing pipeline
  Multithreaded application
Design aims
  Performance
  Configurability
  Reliability
T1
T1
Train reader
UDP
Train queue
token
Train formatter (HDF5)
Train writer
TCP
Available buffer slots
Reject
Free
Storage layer
Train builder
Reconstruct
Train buffer
Pre-allocated memory
Processing
T1
T2
T2
T2
Read
Process
Write

## Slide 11: Network-wide timer service
Listener Thread
TCP
Member (name, channel)
Register
Unregister
Groups
(name, rate, timeout,…)
Timer Threads
TCP
Notifyer Thread
Time events queue

## Slide 12: Data structures and algorithms
Concurrent queue
  Lightweight inter-thread communication
  Wraps std::queue
  Use “condition variable” to reduce access contention
Multi-threading: Thread class
  Virtual runLoop()
  Define pre-processing: in()
  Processing: process()
  Post-processing: out()
Examples: producer, consumer, pipeline, multicaster, …

## Slide 13: Inter-thread Communication fabric
Pluggable modules
  Run-time flexibility
  Initial application settings
  On-the-fly reconfiguration: Enable/disable, insert/remove/replace modules
Idea:
  Pipe-like naming convention
  Create typed-queues
  Build a networked queue
  Plugins is the glue: source/sink/error queues
  Practical/theoretical framework

## Slide 14: Implementation and test
Device/Device server model
  Homogenous software framework
  Highly configurable components
  Our applications are already Devices (DeviceServers will be integrated soon)
Implementation
  One feeder can feed one PCL node
  Up to 8 feeders run in parallel: 8 (full size) trains per second
Some results (very preliminary)
  MTU=1500: 1 train sent/received in 0.98 sec
  MTU=9000: 1 train sent/received in 0.86 sec
  Running time: few minutes
  No processing, no TCP out-streaming
1
5
2
3
4
6
7
8

## Slide 15: Unidirectional tests
UDP:
  Send buffer size=128K  8.39 Gbps
    Packet loss: 80% (128K) ~ 0.01% (1M)
    With CPU affinity: 20% (128K) ~ 0.01% (1M)
  Send buffer size=256K~1M  9.61 Gbps
    Packet loss: 67% (128K) ~ 0.03% (1M)
    With CPU affinity: 0.3% (128K) ~ 0% (1M)
  Send buffer size=4M  13Gbps send / 8.4Gbps receive
    Packet loss: 35%
    Why: driver’s send queue overflow (tx-queue-len should be increased)
    Default Linux kernel behavior: Does not return ENOBUFS error “The output queue for a network interface was full. This generally indicates that the interface has stopped sending, but may be caused by transient congestion. (Normally, this does not occur in Linux. Packets are just silently dropped when a device queue overflows.)”. From man

## Slide 16: Performance tuning
Buffers sizes
  As big as possible on the receiver side
Time profile
  Fine grained (frame level): Considering the maximum NIC throughput (frame/sec)
  Coarse-grained (train level):
CPU affinity
  Bind the UDP reader thread to the right CPU core
Tuning the kernel parameters (IRQ, TX queue length)
  TX queue length: as long as possible on the sender
  IRQ binding: Reduce context switching (20-30% of CPU improvement - fasterdata.es.net): To be investigated.
  Interrupt grouping ? To be investigated.

## Slide 17: Experimental study
Results
  Running time: 10mn ~few hours
  UDP stream (# packets): 106 ~3.5x108
  Packet loss rate: 10-7~10-8
Time (us)
Frequency (#packets)
Packets
Delays (ns)
Very slow (rare)
Slow (5%)
Fast (>95%)
Time delay between packets

## Slide 18: Considering the time profile
Sending profile: send a bunch of packets then have break.
  maximum throughput vs. minimum (no) packet loss
Frame rate (fps):
  Packet size = 8192*8 = 65536 bits
  Preamble = 64 bits
  Inter-frame gap (IFG) = 96 bits
  Frame rate = 10Gbps/65696 = 152216 fps = 138580 fps (jumbo frame)
  Frame size = 65696 bits

## Slide 19: Some results (very preliminary)
Lost packets = [1285301 1285302 1285303 ] # packet received: 100000000 # packet lost : 3 Delay (us) Max: 5152.525 Min: 1.478 Avg: 7.495 Total time (sec): 749.545
Lost packets = [0 1 2 …130 131 2364451905 ] # packet received: 3500000000 # packet lost : 133 Delay(us) Max: 10814.772 Min: 1.479 Avg: 7.510 Total time (sec): 26284.9
Set CPU affinity of the reader thread the same as eth5 IRQ
Bunch = 27 Gap = 50 us
Bunch = 27 Gap = 52 us
Packet loss: 3.8 10-8 2.85 10-10 (exclude first packets)

## Slide 20: Summary
Preparation of the slice tests (1st part)
  Network, PC layer hardware are configured
  Software for data readout under test
Hardware:
  Full link bandwidth: 9.93Gbps
  Plain vanilla UDP: very low packet loss rate (ongoing!)
  Concurrent read and write on dual NIC
Software
  UDP Feeder and PCL (readout) software with some processing (Adler checksum) and TCP out streaming
  Device implementation (DeviceServer, full configuration will be done)
Outlook
  Test the impact of concurrent processing on read and write

## Slide 21
Thank you!