## Slide 1: Pixel Beam Telescope - Online Monitor
Michał Wysokiński
AGH University of Science and Technology, Krakow, Poland
Supervisor: Igor Rubinsky
Timing, Tests and Optimisation

## Slide 2: 0. General Introduction
one of the four great experiments at the LHC
ATLAS Experiment

## Slide 3: 0. General Introduction
Most famous for the new boson discovery:
ATLAS Experiment

## Slide 4: 1. Test beams
Test beams are used for determinig properties of new cutting edge detector systems
They use devices called telescopes
DESY test beam

## Slide 5: 2. Pixel Telescopes for test beams
Telescopes work like a normal camera
Pixel telescopes

## Slide 6: 2. Pixel Telescopes for test beams
What do we want to measure with the telescope?
beam
Check whether a device works or not and measure its properties:
- resolution
- etc...

## Slide 7: 2. Pixel Telescopes for test beams
Pixel telescopes
Telescope arm
Telescope arm
DUT
DUT – Device Under Test

## Slide 8: 2. Pixel Telescopes for test beams
„Datura” telescope
6 telescope planes
MIMOSA 26 sensors:
  1152x576 pixels = 0.7 Mpix
  „pictures” are taken every 115.2 µs
  binary readout
Sensors are usually cooled to 15°C (to stabilize their performance in time)

## Slide 9: Architecture
2. Pixel Telescopes for test beams

## Slide 10: Architecture
2. Pixel Telescopes for test beams

## Slide 11: 3. Goals
Make the Online Monitor as robust and fast as possible (make it a real-time tool).
Add new features for users’ convenience.
Test it with the real data.
Goals

## Slide 12: Preliminary analysis
4. Starting Point
We are here

## Slide 13: Preliminary analysis
4. Starting Point
We are here
We want to be here

## Slide 14: Preliminary analysis
4. Starting Point
Threshold impacts the event size [hits/event]
significantly.

## Slide 15: Profiling
I started with profiling...
  Profiling – analysis of how much time is spent in different functions and how many times they are being called
...and I was about to find out that my start would not be very simple...
4. Starting Point

## Slide 17: Questions I asked myself after seeing a few callgraphs
Which functions are the most crucial for the performance?
Will structural optimisations be enough? Or new algorithms will have to be developed?
3. Starting Point

## Slide 18: 1) Which functions are the most crucial for the performance?
Clusterisation
Correlation
?
3. Starting Point

## Slide 19: 1) Which functions are the most crucial for the performance?
3. Starting Point
What is the root of all evil in the Online Monitor?
Answer: C++ STL dynamic vectors

## Slide 20: 1) Which functions are the most crucial for the performance?
What is the root of all evil in the Online Monitor?
Answer: C++ STL dynamic vectors
Solution: Accept it, because changing it is impossible without rewriting the entire application
3. Starting Point

## Slide 21: Will structural optimisations be enough? Or new algorithms will have to be developed?
This version of the Online Monitor was originally developed within the ATLAS pixel test beam group
It is very good but there is always something to improve, so I decided to investigate the algorithms
4. Starting Point

## Slide 22: Previous clusterisation algorithm
How does the previous clusterization algorithm work?
It compares every single hit with the rest from the same plane - O(n2)
5. Clusterisation

## Slide 23: How does the previous clusterisation algorithm work?
5. Clusterisation
Telescope Plane 1
Telescope Plane 1
Is there a way to optimise this?

## Slide 24: New clusterisation algorithm
Let’s sort all hits
Now we can look only for the nearest neighbours
O(n*log(n) + n)
5. Clusterisation

## Slide 25: Performance
Did it help?
4. Clusterisation
We want to be somewhere here

## Slide 26: Previous correlation algorithm
How does the previous correlation algorithm work?
It correlates all clusters between every two planes - O(n2)
5. Correlation

## Slide 27: How does the previous correlation algorithm work ?
5. Correlation
Telescope Plane 1 Telescope Plane 2
Telescope Plane 1 Telescope Plane 2
Is there a way to optimise this?

## Slide 28: New correlation algorithm
Let’s try to reconstruct all tracks first
Then we could use reconstructed tracks to get information about correlations
... and in addition to that we now know how many tracks (roughly) we have in a single event
O(n*log(n))
5. Correlation

## Slide 29: How the new correlation algorithm works ?
5. Correlation
Telescope Plane 1 Telescope Plane 2
Telescope Plane 1 Telescope Plane 2
Telescope Plane 1 Telescope Plane 2

## Slide 30: Changes in Plots
5. Correlation
Old Correlation Plot
New Correlation Plot
All clusters are being correlated.
Only clusters with associated tracks are being correlated.

## Slide 31: Performance
Did it help? 2GeV beam (2 kHz)
5. Correlation
We want to be somewhere here
Adding new functonalities usually makes application slower but in this case we have a speed up!

## Slide 32: The only solution left was to skip the incoming events.
6. New features

## Slide 33: Performance with skipping 90 % of events
6. New features

## Slide 34: Summary
The Online Monitor:
  became a real-time tool
  has new data quality monitoring functionalities
  conducts self-analysis about its performance
We took data necessary for the performance study of the telescope.
7. Summary

## Slide 36: BACKUPS

## Slide 37: Tracks per Event plot in the Online Monitor
5. Correlation