## Slide 1: Sample preparation, characterization and delivery for Free Electron Laser protein serial crystallography experiments
Kirill Baranov
supervised by
Henry Chapman
Francesco Stellato

## Slide 2: Summary
FEL crystallography
Sample preparation
Sample characterization
Sample delivery

## Slide 3: I. FEL crystallography
X-ray crystallography gives
the majority of biological structures
BUT
It needs crystals of sufficient size
PROTEIN STRUCTURE PROTEIN FUNCTION
Number of structures
in PDB databank
Notes: Number of structures in PDB databank

## Slide 4: I. FEL crystallography
-High brilliance 1012 photons/pulse in ~1 μm2 Small objects Weak scattering objects -Short pulses: <10 fs pulses (up to 120 Hz) Diffraction before destruction Pump-probe measurements -Short wavelength: LCLS goes up to 10 keV High resolution measurements

## Slide 5: I. FEL crystallography
In diffract-before-destroy experiments fresh sample must be continuously injected

## Slide 6: II. Sample preparation
Small crystals are necessary for FEL experiments: protocols to grow micron-sized crystals or to crush big ones are developed
Lysozyme microcrystals
are grown in different
conditions
(pH, salt concentration,
temperature, buffers)

## Slide 7: II. 1. Lysozyme batch crystallization
Sample | LYSOZYME_A | LYSOZYME_B | LYSOZYME_C | LYSOZYME_D | LYSOZYME_E
Protocol | 2 M NaCl 0.1 M amm. ac. | 2 M NaCl 0.1 M amm. ac. 0.09 M ac. acid | 2 M NaCl 0.1 M amm. ac. 0.17 M ac. acid | 2 M NaCl 0.1 M amm. ac. 0.34 M ac. acid | 2 M NaCl 0.1 M amm. ac. 0.67 M ac. acid
pH | 7 | 6 | 5.5 | 5.5 | 5
Sample | LYSOZYME_F | LYSOZYME_G | LYSOZYME_H | LYSOZYME_I
Protocol | 0.9 M NaCl 0.34 M ac. acid | 0.9 M NaCl | 0.45 M NaCl 0.08 M NaOH | 0.9 M NaCl 0.15 M NaOH
pH | 4 | 8 | 12 | 13
BUFFER_1: 2 M NaCl, 0.1 M ammonium acetate
BUFFER_2: 0.9 M NaCl

## Slide 8: III. Sample characterization
Optical microscopy
  Crystal concentration
  Size distribution
X-ray diffraction

## Slide 9: III. 1. Optical microscopy
LYSOZYME_H_F_4
0.43 M NaCl
0.08 M NaOH
50 g/l HEWL;
0.5 µm pre-filtered;
pH 12
temperature 4°C

## Slide 10: III. 1. Counting crystal
LYSOZYME_H_F_4
Vdroplet = 2 µl
Sdroplet surface = 6 mm2
#/10 000 µm2 = 160
(6 mm2/0.01 mm2) * 160 #/2 µl = 50 000 #/µl = 5*107 #/ml
put a uniform droplet of known volume;
measure the surface of the droplet.;
count the number of crystals in different parts of the droplet;
calculate the total number of crystals.

## Slide 11: III. 1. Crystal shape and size distribution
Crystals of different sizes and shapes are observed:
Needles - length: from less than microns to a few hundreds microns, width: from microns to 30 microns;
Tetrahedrons - up to about 20 microns;
Aggregates (maybe containing small crystals) – up to 100 microns.

## Slide 12
LYSOZYME_M_F_4:
0.09 M NaCl
0.01 M NaOH
50 g/l HEWL;
2 µm prefiltered;
pH 11
temperature 4°C
III. 1. Crystal shape and size distribution
Crystal density is high, about 106 #/µl here.
Most part of crystals are needles.

## Slide 13: III. 1. Crystal shape and size distribution
LYSOZYME_G_F:
0.9 M NaCl
50 g/l HEWL;
0.5 µm prefiltered;
pH 8
temperature 20°C

## Slide 14: III. 1. Crystal shape and size distribution
LYSOZYME_G_F:
0.9 M NaCl
50 g/l HEWL;
0.5 µm prefiltered;
pH 8
temperature 20°C

## Slide 15: III. 1. Crystal shape and size distribution
LYSOZYME_H_F_4:
0.43 M NaCl
0.08 M NaOH
50 g/l HEWL;
0.5 µm prefiltered;
pH 12
temperature 4°C

## Slide 16: III. 1. Crystal shape and size distribution
LYSOZYME_D:
1.84 M NaCl
0.1 M amm. ac.
0.34 M ac. acid
50 g/l HEWL;
pH 5.5
temperature 20°C

## Slide 17: III. 1. How to get small crystals
When crystals are too big for serial crystallography experiments, protocols to crush them can be applied.
Manual grinding
Vortexing with glass beads

## Slide 18: III. 1. Crystal shape and size distribution
LYSOZYME_G:
0.9 M NaCl
50 g/l HEWL;
pH 8
temperature 20°C
This sample was vortexed with beads for 10 minutes – all big crystals are gone.

## Slide 19: III. 2. Electron microscopy
It allows to get high-resolution pictures of small objects.
Problems because of specimen charging and salt crystals formation.
LYSOZYME_P_F_4
(20/8/2012):
0,85 М NaCl
0,0005 М NaOH
50 g HEWL;
2 µm prefiltered;
pH 11
temperature 4°C

## Slide 20: III. 4. Dynamic Light Scattering
Gives information on size of particles in suspension
LYSOZYME_E:
1.81 M NaCl 0.1 M amm. ac. 0.67 M ac. acid
50 g/l HEWL;
pH 5
temperature 20°C

## Slide 21: III. 2. X-ray diffraction
X 11 beamline at DORIS
Room temperature measurements
MAR detector
15 keV beam
Detector distance: 330 mm
Resolution at the corner: 1.15 Å
Diffraction up to high resolution
LYSOZYME_H_F_4 :
0.43 M NaCl
0.08 M NaOH
50 g/l HEWL;
0.5 µm prefiltered;
pH 12
temperature 4°C
3 Å
Notes: X 11 beamline at DORIS

## Slide 22: III. 2. X-ray diffraction
X 11 beamline at DORIS
Room temperature measurements
MAR detector
15 keV beam
Detector distance: 330 mm
Resolution at the corner: 1.15 Å
Diffraction up to high resolution
LYSOZYME_H_F_4 :
The sample was grinded for 10
minutes and filtered using a 2 µm filter.
4 Å
3 Å

## Slide 23: IV. Sample delivery
To deliver protein crystals into FEL (or synchrotron) x-ray beam gas focused virtual nozzles are used.
Nozzle making
Nozzle testing with and without crystals

## Slide 24: IV. 1. Nozzle making
To produce jetting nozzle one needs to follow this protocol:
1. A glass capillary is shrunk by fire to match the inner capillary shape;
2. Cleaning and sharpening of inner glass capillary;
3. Inner capillary should fit the exit hole of the tube very well. The end of the capillary should be close enough to the end of the tube to obtain a stable and small jet.
Virtual nozzle
Outer tube
Inner capillary
Notes: 2. -> passive

## Slide 25: IV. 1. Nozzle making
Inner fiber too far from the end of the glass tube
Inner fiber very close to the tip
Inner fiber too far out from the end of the glass tube

## Slide 26: IV. 2. Nozzle testing without crystals
NOZZLE_3
Configuration 1 Outer tube tips out
Jetting with water
50 µm
Water pressure
62 psi
Gas pressure
297 psi
Gas pressure
297 psi

## Slide 27: IV. 2. Nozzle testing with crystals
NOZZLE_3:
Jetting with LYSOZYME_A:
2 M NaCl 0.1 M amm. ac.
50 g/l HEWL;
pH 7
temperature 20°C;
2 µm filtered
NaCl crystal growth on the nozzle observed
after 20 minutes jetting

## Slide 28: Conclusions
Lysozyme is successfully crystallized; pH, temperature and salt concentration, effects are studied;
Sample | LYSOZYME_H
Protocol | 0.45 M NaCl 0.08 M NaOH
pH | 12
T | 4°C
The best sample for FEL protein serial crystallography has high pH, low salt concentration, hold in low temperature and shall be prefiltered after mixing and vortexed before using.

## Slide 29: Conclusions
X-ray diffraction measurements showed that the crystals diffract to high resolution;
Nozzles to inject micro crystals are produced and tested.