## Slide 1: FLASH Reaching the Transition Metals
DESY Summer Student Program
Valeri Vardanyan
Supervisor: Bart Faatz

## Slide 2: FLASH Layout
Beam parameters | 
Beam Energy | 0.38 – 1.25 GeV
Normalized emittance (proj.) | 1.4 – 3 mm mrad
Energy spread | 0.2 MeV
Peak Current | 2.5 kA
Bunches per second | <8000
Bunch Charge | 0.07 – 0.7 nC
Undulator parameters | 
Period | 27.3 mm
Segments length | 4.5 m
Number of segments | 6
Focusing Structure | F0D0
5 MeV
150 MeV
450 MeV
1250 MeV
RF-Gun
FLASH1
FLASH Accelerator
Fixed Gap Undulators
Radiation | SASE
Wavelength | 4.2 – 44 nm
Pulse duration (FWHM) | 10 – 500 fs
Peak power | 1 – 5 GeV
Bandwidth | 0.5 – 2 %
Number of pulses | < 8000
Peak Brilliance | 1028 – 1031
Pulse Energy | 1 – 500 uJ

## Slide 3: FLASH Upgrade: FLASH II
5 MeV
150 MeV
450 MeV
1250 MeV
RF-Gun
FLASH1
FLASH Accelerator
FLASH2
Fixed Gap Undulators
Variable Gap Undulators
Beam parameters | 
Beam Energy | 0.5 – 1.25 GeV
Normalized emittance (proj.) | 1.4 – 3 mm mrad
Energy spread | 0.5 MeV
Peak Current | 2.5 kA
Bunches per second | <8000
Bunch Charge | 0.02 – 0.7 nC
Undulator parameters | 
Period | 31.4 mm
Segments length | 2.5 m
Number of segments | 12
Focusing Structure | F0D0
New tunnel for undulator
New Hall for experiments

## Slide 4
FLASH Upgrade: FLASH II
Radiation | SASE
Wavelength | 4 – 60 nm
Pulse duration (FWHM) | 10 – 500 fs
Peak power | 1 – 5 GeV
Bandwidth | 0.5 – 2 %
Number of pulses | < 8000
Peak Brilliance | 1028 – 1031
Pulse Energy | 1 – 500 uJ
Expected beam parameters
Tunability > factor 3

## Slide 5: FLASH Layout: Proposed
Main Undulator
3.0 nm 1.5 nm
2.6 nm 1.3 nm
2nd harmonic afterburner
Main Goal: Reach Transition metals with circular polarization at FLASH
Cu: 1.33 nm
Ni: 1.45 nm
Co: 1.59 nm
Needed: energy upgrade to 1.6 GeV or higher and new undulator
Possible intermediate step:
Energy upgrade to 1.4 GeV (easy to achieve) and a new undulator
Energy upgrade to 1.467 GeV (at the limit) with the existing one.
Reach same wavelengths at reduced pulse energy at the 2nd harmonic (to be explained later)
Questions:
Do we get enough pulse energy and short enough pulses for the experiments with this intermediate step
5 MeV
150 MeV
450 MeV
1250 MeV
RF-Gun
FLASH1
FLASH Accelerator
FLASH2
Fixed Gap Undulators
Variable Gap Undulators

## Slide 6: Harmonic Generation
Main Undulator
Afterburner
Power at end (SASE Radiation with GW spikes).
Power at beginning (normal synchrotron radiation): smooth at kW level.
800 W
10 GW
Power growth along the main undulator.

## Slide 7: Harmonic Generation
Main Undulator
Power growth along the main undulator.
Bunching along the main undulator at fundamental harmonic.
Bunching along the main undulator at 2nd harmonic.
Afterburner
Afterburner

## Slide 8: Harmonic Generation
Afterburner
800 W
10 GW
Power growth along the main undulator.
Main Undulator
80 MW

## Slide 9: The Simulation Code

## Slide 10
The Simulation Code
Genesis 1.3
Simulates Interaction of electrons and radiation field.
Assumes small bandwidth with radiation in the forward direction
Solves ODEs by 4th order Runge-Kutta method for particle dynamics and PDEs by method of finite differences for radiation.
Time dependent simulations!

## Slide 11: Results for 1.4 GeV, 1.5 nm
Undulator period main | 30 mm
K main | 0,7
Undulator period afterburner | 18,8 mm
K afterburner | 0.4417
Pulse energy, 10 fs | 0.4 (uJ) | 0.7 (uJ)
Pulse length, 10 fs | 34 (fs) | 35.7 (fs)
Pulse energy, 30 fs | 1.9 (uJ) | 2.8 (uJ)
Pulse length, 30 fs | 99.3 (fs) | 93.8 (fs)
30 fs
30 fs
After 2.5 m Afterburner Undulator After 5 m Afterburner Undulator

## Slide 12: Results for 1.4 GeV, 1.3 nm
Undulator period main | 26 mm
K main | 0,7
Undulator period afterburner | 17,4 mm
K afterburner | 0.3464
Pulse energy, 10 fs | 0.1 (uJ) | 0.18 (uJ)
Pulse length, 10 fs | 36.5 (fs) | 31.1 (fs)
Pulse energy, 30 fs | 0.68 (uJ) | 1.04 (uJ)
Pulse length, 30 fs | 90.27 (fs) | 89 (fs)
30 fs
30 fs
After 2.5 m Afterburner Undulator After 5 m Afterburner Undulator

## Slide 13: Results for 1.467 GeV, 1.5 nm
Undulator period main | 27,3 mm
K main | 0,9
Undulator period afterburner | 19,7 mm
K afterburner | 0.505
Pulse energy, 10 fs | 0.29 (uJ) | 0.56 (uJ)
Pulse length, 10 fs | 42.4 (fs) | 42.8 (fs)
Pulse energy, 30 fs | 1.25 (uJ) | 1.84 (uJ)
Pulse length, 30 fs | 113.8 (fs) | 119.7 (fs)
30 fs
30 fs
After 2.5 m Afterburner Undulator After 5 m Afterburner Undulator

## Slide 14: Results for 1.575 GeV, 1.3 nm
Undulator period main | 27,3 mm
K main | 0,9
Undulator period afterburner | 19,7 mm
K afterburner | 0.505
Pulse energy, 10 fs | 0.29 (uJ) | 0.5 (uJ)
Pulse length, 10 fs | 42.6 (fs) | 42.6 (fs)
Pulse energy, 30 fs | 1.3 (uJ) | 1.9 (uJ)
Pulse length, 30 fs | 105.5 (fs) | 114.1 (fs)
30 fs
30 fs
After 2.5 m Afterburner Undulator After 5 m Afterburner Undulator

## Slide 15: Conclusion
We can make radiation at the wavelengths for transition metals.
Level of 0.1 to 2 uJ.
Pulse duration of 30 to 120 fs.

## Slide 16
Danke Schöne