## Slide 1: Ptychographical measurements of biological specimen
Supervisor: Alke Meents
Karolina Stachnik
Hamburg, 6 September 2012

## Slide 2: Outline
Coherent Diffractive Imaging
Ptychography – lensless imaging
Experimental setup
Ptychographical Iterative Engine
Applications
Conclusions

## Slide 3: Fresnel Coherent Diffractive Imaging
A tool for structure analysis on the nanoscale
CDI experiment:
  Zone plate – creation of divergent beam incident on the sample
  OSA – removal of other diffracting orders from the zone plate
  a coherent plane wave illuminating sample
C. A. Larabell, K. A. Nugent, Imaging cellular architecture with X-rays
Notes: Current Opinion in Structural Biology, Volume 20, Issue 5, October 2010, Pages 623-631

## Slide 4: Coherent Diffractive Imaging
Result of measurements:
  Diffraction pattern the the Fraunhofer far field
Lensless imaging – resolution ultimately limited only by the wavelength of the radiation
Direct reconstruction of the original optical transmission function of the specimen
Phase problem: measured real-valued intensity – amplitude information only, phase lost
Iterative phase retrieval methods
  Alternations between real and Fourier space with certain boudary constraints

## Slide 5: Ptychographical Coherent Diffractive Imaging (pCDI)
Ptychography (from the Greek ”πτνξ” meaning ”fold”)
First proposed by Hoppe and Hegerl in 1970s
Diffraction patterns recorded from a series of overlapping beam positions
M. Dierolf et al., Ptychography and lensless X-ray imaging

## Slide 6: Ptychography
Prerequsite for pCDI: localized and mainly coherent illumination
Parameters:
  Data: real-valued intensity
  Positions of illumination function
Sample illuminated at e.g. 15x15 overlapping positions spaced by certain stepsize
Overlap of about 70% causing high increase of image resolution in reconstruction process
M. Dierolf et al., Ptychography and lensless X-ray imaging

## Slide 7: Sample image and some diffraction patterns
Oliver Bunk et al., Influence of the overlap parameter on the convergence of the
ptychographical iterative engine

## Slide 8: Reconstructions for different relative overlaps
Relative overlap (5x5 object positions)
10%
60%
100% (conventional iterative phase retrieval)
Oliver Bunk et al., Influence of the overlap parameter on the convergence of the
ptychographical iterative engine

## Slide 9: Experimental setup
polarization
direction
FZP
OSA
sample
PILATUS 6M
detector
FZP – Fresnel Zone Plate
OSA – Order Sorting Aperture

## Slide 10: Experiment design – crucial parameters
Focal length of the zone plate:
Sample-to-detector distance: 636 cm
Beam defining pinhole | 150 μm
Zone plate diameter | 150 μm
Order sorting aperture | 10 μm
OSA
FZP
CS
BDP

## Slide 11: P11: Ptychography
Flight
tube

## Slide 12: Ptychographical Iterative Engine
Phase retrieval algorithms
The probe: complex-valued probe function
The object: complex-valued object function
The resulting exit wave – complex-valued diffraction pattern
Recorded real-valued far field intensities
First iteration of the phase retrieval: random guesses of the probe and the specimen

## Slide 13: Algorithm of reconstruction
The superresolution algorithm:
  Specimen and probe reconstructions
  Significant improve of their resolution (extrapolation of the recorded deffraction patterns beyond the aperture of the detector)
A. M. Maiden, M. J. Humphry, F, Zhang J. M. Rodenburg, Superresolution imaging via ptychography

## Slide 14: Applications
The lily pollen images reconstruced using two versions of ptychographical iterative engine (PIE):
  (a), (b) – extended PIE
  (c), (d) – superresolution PIE
Modulus
Phase
A. M. Maiden, M. J. Humphry, F. Zhang, J. M. Rodenburg, Superresolution imaging via ptychography

## Slide 15: Applications
The image of the bee’s leg (the amplitude)
  (a) PIE
  (b) parallel PIE
A. M. Maiden, J. M. Rodenburg, An improved ptychographical phase retrieval algorithm for diffractive imaging

## Slide 16: Conclusions
Ptychography as a lensless imaging
Quite simple experimental setup
Optimal overlap – high increase in resolution in comarison to other methods
Ptychographical algorithms for solving phase problem and reconstruction process
Promising method for nanoscale bio-imaging

## Slide 17: Acknowledgments

## Slide 18
Thank you for your kind attention!