## Slide 1: State-of-the-art in Hadronic Calorimetry for the Lepton Collider
José Repond
Argonne National Laboratory
2012 Nuclear Science Symposium
Anaheim, CA
October 28 – November 3, 2012

## Slide 2
What to measure at a future Lepton Collider
● Single charged particles → YES → use the tracker
● Single photons → YES → use the ECAL
● Single neutral hadrons → ???
● Hadronic jets → YES → how?
Dijet masses
Not necessarily with a calorimeter with the best
possible single particle energy resolution
Detector optimized for PFAs
But with a detector providing the best possible
jet energy and dijet mass resolution
YES
ECAL
HCAL
γ
π+
KL

## Slide 3
Attempt to measure each particle in a event/jet individually
Implications for calorimetry
● Need a calorimeter optimized for photons: separation into ECAL + HCAL
● Need to place the calorimeters inside the coil (to preserve resolution)
● Need to minimize the lateral size of showers
● Need the highest possible segmentation of the readout
● The role of the HCAL reduced to measure the part of showers from neutral hadrons
leaking from the ECAL
● Need to minimize thickness of the active layer or the depth of the HCAL
Two performance measures of a hadronic calorimeter optimized for PFAs
Particle Flow Algorithms
Energy resolution for Identification of energy deposits
single neutral hadrons (minimize confusion)
Χ

## Slide 4
The absorber
Steel
Discussion has boiled down to three choices Tungsten
Crystals
Element | ρ [gcm-3] | X0 [cm] | λI [cm] | λI /X0
Fe | 7.87 | 1.758 | 16.8 | 9.6
W | 19.30 | 0.350 | 9.94 | 28.4
e.g. BGO | 7.13 | 1.118 | 22.3 | 20.0
Sampling
Given space restrictions, best choice not obvious
~2 cm Fe-absorber corresponding to 1.2 X0 or 0.13 λI sampling
~1 cm W-absorber corresponding to 2.9 X0 or 0.10 λI sampling
Have been tested
Impact on measurement of electromagnetic sub-showers

## Slide 5
R&D for PFA Hadronic Calorimeters
Fe
Fe
Fe
W
W
Scintillator tiles
RPC
GEM
RPC
μMegas
2-bit
1-bit
Fe
16-bit

## Slide 6
The large prototypes
Needed to contain hadronic showers

## Slide 7
Electronic readout
Silicon Photomultipliers (SiPMs)
Digitization with VME-based system (off detector)
Tests at DESY/CERN/FNAL
with Iron absorber in 2006 - 2009
Tests at CERN
with Tungsten absorber 2010-2011
Description
38 active layers
Scintillator pads of 3 x 3 → 12 x 12 cm2
→ ~8,000 readout channels
Complemented by a Scintillator strip tail-catcher (TCMT)
Large Prototype I
Scintillator – AHCAL
1st use in large system

## Slide 8
Large Prototype II
RPC – HCAL (DHCAL)
Description
54 active layers
Resistive Plate Chambers with 1 x 1 cm2 pads
→ ~500,000 readout channels
Main stack and tail catcher (TCMT)
Electronic readout
1 – bit (digital)
Digitization embedded into calorimeter
Tests at FNAL
with Iron absorber in 2010 - 2011
Tests at CERN
with Tungsten absorber 2012
1st time in calorimetry

## Slide 9
Large Prototype III
RPC – HCAL (SDHCAL)
Description
48 active layers
Resistive Plate Chambers with 1 x 1 cm2 pads
→ ~430,000 readout channels
Electronic readout
2 – bit (semi-digital) → 3 thresholds
Digitization embedded into calorimeter
Power pulsing
Tests at CERN
with Steel absorbers 2012
1st use in large system

## Slide 10
Some of the many results…

## Slide 11
Response – Scintillator - AHCAL
Steel -Absorber
Tungsten -Absorber
Linear response to hadrons at the <1% level
Under-compensating: e/h ~ 1.2
-- Electrons
Linear response up to 10 GeV
(higher energies still being analyzed)
5mm scintillator + 10 mm W
→ Compensation : e/h ~1
Should be linear: but is it necessary?

## Slide 12
Response – (Semi) - Digital HCALs
Should be linear: but is this necessary?
Over-
Compensation
Steel – DHCAL
e+ - uncalibrated
π+ - uncalibrated
Tungsten – DHCAL
e+ – well described by power law αEβ
π+ - appear to be linear up to 25 GeV
30% fewer hits compared to steel
Non-linear response
to both e± and hadrons
Both well described by
power law αEβ
Badly over-compensating
e/h ~ 0.9 – 0.5
→ need smaller readout pads
Steel – SDHCAL (1-bit mode)
Functional form a priori not known, but needed for energy reconstruction
uncalibrated
uncalibrated
Deviations from
linear response
due to finite
readout pad
size

## Slide 13
Resolutions
For PFAs this is only part of the story…
Steel – DHCAL
Steel – SDHCAL
Tungsten – DHCAL
Without containment cut
With containment cut
Not corrected for
non-linearity
(expected to be a +(3±2)% correction)
Resolution
~ 25% worse
than with steel
Corrected for
non-linearity
Correction for non-linearity applied
Measurements using either 1 or 3 thresholds
Improvement at higher energies with 3 thresholds

## Slide 14
Software compensation – Scintillator AHCAL
Apply different weights to ‘hadronic’ or ‘electromagnetic’ sub-showers
based on energy density
Large improvement (~20%)
Stochastic term 58%/√E → 45%/√E
Similar stochastic terms of
Steel – DHCAL and ‘raw’ AHCAL
→ Resolution dominated by sampling
Software compensation should also work
for the DHCAL: how well?
The power of imaging calorimeters

## Slide 15
Leakage correction
Select showers (80 GeV π) starting in first part of AHCAL
Apply corrections depending on
Interaction layer (shower start)
Fraction of energy in last 4 layers
The power of imaging calorimeters
Mean value restored
RMS reduced by ~24%

## Slide 16
Shower shapes
The power of imaging calorimeters
Identification of
layer with shower start
Comparison with various hadron shower models

## Slide 17
Timing measurements
Measurement of shower timings using
Scintillator pads or
RPC with pads
Positioned downstream of
Steel stack or
Tungsten stack
Comparison with hadron shower models
Average 60 GeV shower in 4D
Use reconstructed interaction
point in Tungsten - AHCAL
The power of imaging calorimeters

## Slide 18
R&D beyond current prototypes
Embedded readout for AHCAL
1 m2 μMegas as alternative to RPCs
32 x 96 cm2 GEMs as alternative to RPCs
Ultra-thin 1-glass RPCs
High-rate RPCs

## Slide 19
And now to something completely different

## Slide 20
Dual Readout
The idea
Typically, compensating calorimeters feature poor em resolution
Dual readout measures both
Scintillation light (ionization by any charge particle)
Cerenkov light (predominantly produced by electrons and positrons)
And so reconstructs fem (the electromagnetic fraction of a hadronic shower)
and corrects for the different electromagnetic and hadronic response
on an event-by-event basis
Several different approaches
DREAM
Fiber readout
CALTECH/FNAL
Crystals/glass
ADRIANO
Fiber readout with
scintillating glass/plastic
20 GeV π
simulation
Correction
40 → 22%/√E
Experimental proof still needed

## Slide 21
Summary
Scintillator Analog HCAL First use SiPMs in large prototype
Demonstration of software compensation
Demonstration of leakage corrections
Detailed measurements of shower shapes
RPC-Digital HCAL First large prototype with embedded electronics
First digital pictures of hadronic showers
Record channel number in calorimetry
Demonstrated viability of concept of digital calorimetry
RPC-Semi-Digital HCAL First use of power pulsing
Demonstrated benefit from 3 thresholds (semi-digital)
Further R&D Many different activities

## Slide 22
Summary
of the summary
These are only prototypes
For real detector x50
Technical feasibility of imaging hadron calorimetry proven
new endeavor
Measurement of hadronic showers with unprecedented spatial resolution ongoing
Detailed comparison with GEANT4 based MCs → valuable information for further tuning
Further work needed to design/build modules for a colliding beam detector
ILD
SiD

## Slide 23
Backup slides

## Slide 24
Validation of PFA performance
Shower separation
Showers reconstructed with
PandoraPFA
Excellent agreement with
simulation
GEANT4 can be trusted to
optimize detector design for
PFA performance